Form C2

LIGO VACUUM BAKE OVEN PROCEDURE AND CHECK LIST

Oven:  A     B     C     D     VSA                Load # ___________                    Date: ___ /___ /____

Load Contents: ________________________________________________________________

Cap Torqued:  ______  ft/lbs  ______  ft/lbs  ______ ft/lbs _____ ft/lbs

Metal Valve Open:     Y     N     Vent Valve Closed:     Y     N         TP on:     Date:___/___ Time:___:___

TP on:     Date:___/___ Time:___:___

TP on:     Date:___/___ Time:___:___

TP on:     Date:___/___ Time:___:___

Pressure: ________ Torr	Date:___/___ Time On:___:___

Pressure: ________ Torr	Date:___/___ Time On:___:___

NOTE: Do not turn heat on when pressure is above 5E-5 Torr.

AUTO/MANUAL:		Heat on:   Date:___/___ Time:___:___

Ramp Time:     Oven:____ Hrs,    Pumpline:____Hrs

Soak Time:      Oven:____ Hrs,    Pumpline:____Hrs

BAKE TEMPERATURE o (C):

Oven: ______   PumpLine: ______      Turbo Pump Heat On:     Y     N

TEMPERATURE o (C):

|  | P-Line | End | Body | Cap | Date & Time | P(Torr) |
| --- | --- | --- | --- | --- | --- | --- |
| 1. |  |  |  |  |  |  |
| 2. |  |  |  |  |  |  |

TP Heat Off:     Y     N       Temp Cont. sw Off:     Y     N         Reset PROG off:     Y     N

DEGAS:

Fil On?     Y     N	       W/Dycor# ____	Date:___/___ Time On:___:___ Time Off:___:___

Date:___/___ Time On:___:___ Time Off:___:___

Date:___/___ Time On:___:___ Time Off:___:___

Date:___/___ Time On:___:___ Time Off:___:___

PURGE:	N2       AIR

Comments:____________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

LIGO Form F030015-00-V  (02/03)

# Comments

This form was basically rearranged but generally the same as the original.