Laser Interferometer Gravitational Wave Observatory

- LIGO -

CALIFORNIA INSTITUTE OF TECHNOLOGY

MASSACHUSETTS INSTITUTE OF TECHNOLOGY

Specification		        LIGO-E960022- B- E		       03/13/2003

LIGO Vacuum Compatibility,

Cleaning Methods and Qualification Procedures

LIGO Systems Engineering

This is an internal working note

of the LIGO Project.

California Institute of Technology		Massachusetts Institute of Technology

LIGO Project - MS 51-33						LIGO Project - MS 20B-145

Pasadena CA 91125							Cambridge, MA 01239

Phone 626.395.2129								Phone 617.253.4824

Fax 626.304.9834								Fax 617.253.7014

E-mail: info@ligo.caltech.edu					E-mail:  info@ligo.mit.edu

| CHANGE RECORD |
| --- |
| Revision | Date | Authority | Pages Affected | Item(s) Affected |
| A | 28 January 2000 | Initial Release | All | All |
| B | 13 March 2003 | DCN E030125 | All | All |

| Organization/Group | Name | Signature | Date |
| --- | --- | --- | --- |
| System Engineering and Chair, LIGO Vacuum Review Board | Albert Lazzarini |  |  |
| LIGO Vacuum Review Board | Fred Raab |  |  |
|  | David Shoemaker |  |  |
|  | Rainer Weiss |  |  |
|  | John Worden |  |  |
| Project Manager | Gary Sanders |  |  |

TABLE OF CONTENTS

Nomenclature and Acronyms. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	 5

1.	Scope	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	 6

1.1		Purpose 	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	. . . . . 	 6

1.2		Content		. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	 6

1.3		Vacuum Review Board	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	. . . . .	 6

2.	Applicable Documents	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 7

3.	Vacuum Compatible Material Usage in LIGO. . . . . . . . . . . . . . . . . . . . . . . . . . .	. . . 8

3.1		Material Approval Process	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	. . . 8

3.2		Component Qualification	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	. . . . . 	 8

4.	Cleaning and Preparation of Materials Procedures	. . . . . . . . . . . . . . . . . . . . . . .	 9

4.1		Commercially Produced Components. . . . . . . . . . . . . . . . . . . . . . . . . . .	. . . . .	 9

4.2		Internally Produced Components	. . . . . . . . . . . . . . . . . . . . . . . . . .	. . . . . . . .	 9

5.	Handling and Storage Procedures	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	10

6.	Qualification and Screening Tests for Materials and Components. . . . . . . . .	. . 	11

6.1		Initial Qualification & Screening	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	11

6.1.1	High Power Exposure Tests of Cavity Mirrors. . . . . . . . . . . . . . . . . . .	 . . . .	12

6.1.2	Outgassing Screening Tests	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	13

6.1.2.1	Bake Out	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	 . . . .	13

6.1.2.1.1	Vacuum Bake	. . . . . . . . . . . . . . . . . . . . . . . . . . . . .	 . . . . .	 . .	13

6.1.2.1.2	Air Bake. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	 . . . . . . .	14

6.1.2.2	Residual Gas Analysis	. . . . . . . . . . . . . . . . . . . . . . . . . . . . .	 . . . .	14

6.2		QA Screening	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	15

Appendix  A	Cleaning and Baking Procedures for Approved and

Provisionally Approved Materials. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	16

Appendix  B	Cleaning and Baking Procedures for Approved Sub-Assemblies	. . .	 . .	20

Appendix  C	Forms	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 	22

C1: Parts Cleaning Request. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	23

C2: LIGO Vacuum Bake Oven Procedure and Check List. . . . . . . . . . . 	24

Appendix  D	Calculation of Vacuum Load	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	25

LIST OF FIGURES

Figure 1:		Exposure Test Setup. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .12

Figure 2:		Typical Vacuum Bake Test Set 	. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	14

Figure 3:		Geometrical arrangement of source, mirror, and pumping system. . . . . . . .	27

# Figure 4:		Schematic for the calculation. .. . . . . . . . . . . . . . . . . . . . . . . . .. . . . . . . . . . .31

# Figure 5:		Relation between the surface coverage and the equilibrium pressure

# for the Dubinin-Radushkevich theory. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	33

LIST OF TABLES

Table 1:		Applicable Documents. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	 7

Table 2:		Parameters for estimating contaminant buildup on LIGO optics. . . . . . . . .	26

Table 3:		Physical Constants. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	26

Table 4:		Typical values for water on hot rolled 304L stainless steel. . . . . . . . . . . . . .	32

Table 5:		Sample parameters leading to 200 day equilibration time. . . . . . . . . . . . . . .	32

NOMENCLATURE AND ACRONYMS

ADP		Ammonium Di-hydrogen Phosphate [(NH4)H2PO4]

AMU		Atomic Mass Unit

CO2 		Carbon Dioxide

DI			Deionized Water

FDR		Final Design Review

HC		Hydrocarbons

HF			Hydrofluoric acid

JPL		Jet Propulsion Laboratory

KDP		Potassium Di-hydrogen Phosphate [KH2PO4]

LIGO		Laser Interferometer Gravitational Wave Observatory

LOS		Large Optics Suspension

OFHC		Oxygen Free High-Conductivity Copper

NEO		Neodymium Iron Boron

PFA		Perfluoroalkoxy fluoropolymer (Du Pont)

PTFE		Polytetrafluorethylene (Du Pont)

PZT		Lead-Zircomate-Titanate

RGA		Residual Gas Analyzer

RTV		Room Temperature Vulcanizing Silicone Elastomer

SEI		Seismic Isolation System

TBD		To Be Determined

UHV		Ultra High Vacuum

1.		SCOPE

1.1	Purpose

The goal of this document is to provide reasonable assurance against the inadvertent introduction into the LIGO vacuum envelope of material which could contaminate optics and/or produce excess phase noise by forward scattering.

This document sets forth certain procedures and standards by which material to be used in LIGO interferometers may be qualified and assayed for compatibility in operation with high-power resonant cavities inside an ultra-high vacuum (UHV) system.

All items to be installed inside LIGO vacuum equipment or onto beam tube pump ports shall conform to this policy for selection of components and exposed materials, for preparation, handling, testing and storage prior to assembly and during assembly. These items are considered Class A hardware. For definition of Class A hardware, refer to LIGO-M990034 (Section 5).

It is intended that the total optical contamination produced by detector components placed into the LIGO vacuum envelope shall be limited to < 0.5 ppm/yr/optic absorption and < 10 ppm/yr/ optic scatter.

1.2	Content

All materials/parts (commercial and custom designed) must undergo vacuum outgassing and contamination evaluation to ensure compatibility with operation in high-power laser cavities within UHV systems.

Certain materials needed to fabricate LIGO interferometers, although used in other UHV applications, need to be evaluated for possible deleterious effects which their outgassing products may produce on high reflectivity mirrors while these mirrors are under laser irradiation at power levels of tens of kW. A determination of the rate of increase of optical losses by exposure of test cavity mirrors to substances in question shall be the basis for vacuum qualification whenever possible for such substances.

It is also necessary to ensure proper cleaning of components fabricated from acceptable materials. Cleaning of LIGO components shall be performed in accordance with recognized and accepted cleaning practices. Some of these cleaning procedures are generic and baking will be carried out generally at the maximum temperature permissible for a given material: other procedures have been developed to handle specialized or oversized components that could otherwise not be cleaned.

1.3	Vacuum Review Board

Outgassing data and, whenever possible or necessary, optical loss data of materials/parts shall be submitted to the Vacuum Review Board for review and acceptance. The Vacuum Review Board must approve tested materials/parts before they may be included in the LIGO vacuum compatible materials approved list (E960050). The Vacuum Review Board members are selected by the Systems Engineering and the Detector Systems group management.

The Vacuum Review Board will recommend the disposition of issues where policy and schedule are in conflict. This document will be updated as irradiance exposure data become available.

2.		Applicable Documents

The documents cited in Table 1 have been used to develop some of these guidelines and serve as reference material.

| Table 1: Applicable Documents |
| --- |
| Document Title | ID Number |
| LIGO Project Management Plan | LIGO-M950001 |
| LIGO Project System Safety Plan | LIGO-M950046 |
| LIGO Project QA Plan | LIGO-M970076 |
| LIGO Configuration Management Plan | LIGO-M950005 |
| LIGO Vacuum Compatible Materials List | LIGO-E960050 |
| Stanford Synchrotron Radiation Project User Specifications for Vacuum Systems and Components which Interface with the SPEAR Vacuum System | LIGO-E870001 |
| Detail Specification for General Cleaning Requirements for Spacecraft Propulsion Systems and Support Equipment | LIGO-E740001 |
| LIGO Seismic Isolation System: Fabrication Process Specification | LIGO-E970063 |
| Material, Process, Handling and Shipping Specification for Fluorel Parts | LIGO-E970130 |
| Material, Process, Handling and Shipping Specification for Welded Diaphragm Bellows | LIGO-E970129 |
| Material, Process, Handling and Shipping Specification for Damped Coil Springs | LIGO-E970131 |
| Specification for the LIGO Bakeout Ovens | LIGO-T980008 |
| Small Optics Cleaning Procedures | LIGO-E990034 |
| Large Optics and COC Cleaning Procedures | LIGO-E990035 |
| Cleaning Procedures for LIGO Commercial Optics (Other Than Core or IO Optics) | LIGO-E000007 |
| Process Specification: CO2 Cleaning Procedures | LIGO-E990316 |
| Cleaning and Baking Viewports | LIGO-E990190 |
| LIGO Hanford Observatory Contamination Control Plan | LIGO-M990034 |
| Viton Spring Seat Vacuum Bake Qualification | LIGO-T970168 |
| Outgassing Documents from 1988-1992 | LIGO-T920009 |

3.		Vacuum Compatible Material Usage in LIGO

3.1	Material Approval Process

LIGO maintains an updated list of materials considered safe to use in LIGO vacuum systems. This approved list is LIGO-E960050. New material must go through the prescribed screening process before it may be added to this list. The screening process is described in Section 6 of this document. The vacuum data of the tested materials/parts will be compared to the LIGO vacuum outgassing and contamination requirements before being included in the LIGO vacuum compatible materials approved list.

In cases where any of the cleaning procedures cannot be followed due to considerations such as material durability or sensitivity to elevated temperatures, a waiver shall be completed and submitted to the Vacuum Review Board for consideration and approval. The waiver shall be accompanied by an alternative preparation procedure which has been demonstrated to achieve the desired cleaning effects.

3.2	Component Qualification

- A component or subassembly is itself considered approved if all its exposed materials are approved and if its pre-installation treatment is consistent with the preparation procedures for those materials.

- All blind holes and trapped volumes shall be explicitly vented to avoid virtual leaks; provision for cleaning such volumes adequately (e.g., by solvent flushing) shall also be considered in the design process.

- A material is considered "exposed" unless it is encapsulated fully and hermetically within another material. All designs using hermetic containment must be approved specifically by the Vacuum Review Board.

- Components composed of materials from a single class are to be prepared, handled and stored according to the corresponding procedure for that class.

- Irreducible subassemblies comprising more than one material class are to be prepared and handled according to the most stringent subset of procedures consistent with all materials involved.

- A Qualification and Screening Test Report must be written for the candidate material/ component after completion of tests. This report must include the amounts of materials, outgassing rates (approved or not), residual gas analyses and RGA scan data, molecular species that is outgassed, amount of hydrocarbons outgassing, and surface contamination information if available. A material usage list must be compiled for every subassembly or component that is placed in the vacuum and be included in the report. This information shall be available by the FDR of the subject system or subsystem. The material usage list for each assembly shall be updated to maintain it current.

- The Qualification and Screening Test Report and associated raw data (e.g., RGA scans) shall be processed as follows:

  - File original with the LIGO QA Officer.

  - Submit a copy to the requester of the qualification tests.

  - Submit a copy to the LIGO Document Control Center.

4.		Cleaning and Preparation of Materials Procedures

All materials/parts (both commercial and LIGO-produced) must be scrutinized for vacuum cleanliness compatibility before being accepted for utilization with the LIGO vacuum system.

4.1	Commercially Produced Components

If a vendor is required to provide clean components, then the vendor shall use recognized UHV practices. The vendor shall submit to LIGO a description of the practices for prior approval by LIGO as part of the quote or proposal for the work in accordance with the procurement process.

For commercially produced components with potentially many materials used in the construction, a detailed accounting of all materials and the amounts used shall be submitted for review. It may be necessary for some components to require certifications (per article or serial number) for the materials employed in their manufacture, so that material substitutions by the manufacturer are visible to LIGO. The vendor shall notify LIGO of any material substitutions which occur after the agreed-upon list of materials has been determined. LIGO QA shall have oversight to ensure such notification is obtained. Where practicable, a first article screening using an RGA scan and outgassing measurement shall be performed by LIGO prior to receiving shipment of all other components.

4.2	Internally Produced Components

LIGO shall clean in accordance with documented procedures all components produced internally. Cleaning procedures shall be defined for all materials on the LIGO approved materials list. Present procedures are listed in Appendix A. These will be updated periodically. The LIGO approved materials list includes:

Generic materials:

- Metals

- Ceramics and glasses

- Hard crystalline minerals, excluding electro-optical elements

Fabricated materials:

- LIGO optical components

- Composite Assemblies

- Commercially purchased mechanical assemblies

- Electronic Components

- Suspension Sensor/Actuator Head assemblies

There are also provisionally approved materials being used in prototype interferometers. It is permissible to incorporate provisionally accepted materials in LIGO interferometer designs; however before the designs may be actually implemented, promotion of their constituent materials to the accepted materials list must be performed in accordance with the procedures set forth in this document. Provisionally approved materials list includes:

- Silicone rubber (see notes in Appendix A, item F)

- Solder, lead/tin (Kester 6337) (see also Appendix A, item H)

- Sm-Co permanent magnets

- PZT piezoelectric ceramics

- Hygroscopic crystalline optics

5.		Handling and Storage Procedures

Latex gloves are to be worn for handling, assembly and installation of cleaned or partially cleaned parts. Unless otherwise indicated, gloves are to be changed when proceeding to handle components at different stages of processing.

Tools and fixtures which may contact cleaned parts in assembly or transport are to be cleaned and baked as Class B material. (See Class B processing procedure, Appendix A, Section 3.)

Processed parts awaiting installation or further assembly will be triple wrapped for storage or shipping as follows:

(a) Wrap the part(s) with UHV quality aluminum foil.

(b) Place each part(s) in an anti-static bag fabricated from Ameristat poly sheet and cleaned to Class 100.

(c) Compress the bag tightly around the part(s) to purge excess air. Tie wrap the bag for closure, or use a bag with a zipper.

(d) Two labels must be used on the outer layer of all bagged components: (i) a warning label stating: "UHV CLEAN PART -- HANDLE ONLY WITH PROPERLY GLOVED HANDS" and (ii) an identification label. If the labels are not self-adhesive, then they shall be affixed with tape. All empty fields on the ID label shall be filled in with the relevant information; use “N/A” rather than leaving a field blank.

(e) Place the part(s) in a second anti-static polyethylene bag, as specified above, remove excess air, and heat seal or tape shut, making sure both labels are visible.

(f) Place the double bagged part(s) in an appropriate shipping container, using care to not puncture or cut the bags. Seal the shipping container closed. Attach a label with the LIGO part number (drawing number(s), including revision letter) and serial number(s) to the outside of the container.

The shipping containers must be such that they insure that the double bags do not get punctured and that the parts are properly supported during transit.

For a list of approved contamination supplies and vendors refer to LIGO-M990034, Appendix 1.

Small parts may also be stored in stainless steel or glass containers which are cleaned and prepared in the same way as vacuum equipment.

Tables and work areas for cleaning, packing/unpacking, assembly, alignment and testing of cleaned parts are to be lined or covered with fresh contamination-free foil or Ameristat immediately before starting work. Ameristat shall not be used if a solvent incompatible with the film is involved in the assembly or cleaning process. Final assembly of any small subassembly or component intended for installation in LIGO shall be assembled under a Class 100 laminar flow bench. Assemblies too large for handling on laminar flow benches shall be unwrapped and assembled in portable clean rooms assembled around open chambers.

6.		Qualification and Screening Tests for Materials and Components

Tracking and control of material usage in LIGO has two aspects:

- Initial determination that a particular material (or component assembly if it cannot be disassembled) is benign with regard to its effect on optical surfaces and interferometer excess phase noise caused by forward scattering. This shall be done by exposing mirror surfaces in test resonant cavities with resonant optical power representative of the worst-case LIGO irradiances. A corroborating RGA scan of the material, whenever possible, shall be recorded in order to develop a database containing both optical effects and related outgassing measurements.

- QA screening of components fabricated from approved materials. The basis of such screening shall be the measurement of hydrocarbon outgassing of the subject components using RGA scans after appropriate vacuum preparation. The RGA levels for a pre-determined and specified group of species masses which represent hydrocarbon fragments shall be compared to those obtained in the material qualification step. Excess RGA levels shall indicate inadequate cleaning and preparation of the component under test. Reliance on RGA scans for screening is required to provide a faster process to accommodate fabrication schedules.

6.1	Initial Qualification & Screening

All candidate materials must satisfy the criterion of screening and qualification testing before being considered for addition to the vacuum compatible “approved” or “provisionally approved” list. The distinction between approved and provisionally approved materials lies at present with lack of definitive data for provisional materials about their behavior in mirror cavities at LIGO irradiance levels.

The high power exposure (qualification) test of cavity mirrors and screening test are described in detail in the following paragraphs. Materials which are intrinsically free of organic compounds (after suitable cleaning) may be excluded from laser cavity testing.

6.1.1		High Power Exposure Tests of Cavity Mirrors

The purpose of the exposure test is to evaluate the candidate material for optical contamination potential under high laser power in the presence of high reflectance mirrors. Outgassing can lead to contamination of the optics with the result of increased optical losses and ultimately failure due to heating. The amount of outgassing is less important than the molecular species that is outgassed. There are two test procedures in the exposure test, which are briefly described below; a complete procedure shall be developed. Efforts to date have been directed at developing comparison tests between empty cavities and cavities exposed to candidate materials. A typical cavity setup is shown in Figure 1.

Figure 1: Exposure Test Setup

The qualification procedure includes the following steps:

- Vacuum bake candidate materials according to the procedure for that material, then cool and take an RGA scan to quantify the outgassing. The scan must be calibrated against one or more standard leaks.

- Run an optical exposure test at > 150 kW/cm2 in a resonant cavity to qualify material at the level of optical losses discussed in Section 1.1. The run shall be the shorter of 2 months or when a measurable effect is observed.

- If the candidate material is deemed safe for incorporation into LIGO designs, then subsequent components made of this material shall be screened in the manner described below.

6.1.2		Outgassing Screening Tests

There are two steps of the screening test:

- a bakeout for driving volatile substances (HCs) off the component; and

- a residual gas analysis (RGA).

6.1.2.1	Bakeout

The default bakeout procedure shall be conducted under vacuum. With large components, which it may not be feasible to bake under vacuum, an air bake will be considered acceptable providing cautions are taken to preclude contamination from the ambient air.

All bakes shall be performed in LIGO-approved ovens; these may be located at vendors.

6.1.2.1.1	Vacuum Bake

Vacuum baking of the candidate component/material is performed to obtain hydrocarbon and other outgassing data information. The typical vacuum bake test setup is shown in Figure 2.

Typical testing procedures are:

- Prepare a sample of candidate component/material to be tested.

- Prepare a “Parts Cleaning Request” form (see Appendix C, Form C1), as an example, for Caltech specific vacuum preparation. Follow the cleaning methods and handling procedures in Sections 4 and 5 above according to the type of material, and indicate the procedures on the form.

- Prepare a “LIGO Vacuum Bake Oven Procedure and Check List” (see Appendix C, Form C2). Provide the component/material baking time and temperature and any requirements for temperature ramptime or soaktime. Baking temperatures shall follow written procedures discussed in Sections 4 and 5.

- Perform a system calibration according to the defined procedure.

- Perform a vacuum bake of candidate component/material.

At the end of the vacuum bake period, obtain a record of the partial pressures of suspect HC masses to document results.

Figure 2: Typical Vacuum Bake Test Set

6.1.2.1.2	Air Bake

The air bake procedure for large in-vacuum components which cannot be handled otherwise is set forth in E970063, LIGO Seismic Isolation System: Fabrication Process Specification. It applies to all similar components in LIGO.

6.1.2.2	Residual Gas Analysis

Cleaning and baking of components/materials must be followed by a residual gas analysis. This analysis shall be performed and documented according to LIGO defined procedures.

6.2	QA Screening

All components fabricated from approved materials and which are intended for installation into the LIGO vacuum envelope shall be screened to ensure that proper preparation of the subject components has been achieved. This screening follows the procedure outlined in Section 6.1.2, Outgassing Screening Tests.

In cases where a large number of components are to be screened, it may be permissible to perform a statistical sampling of components instead of 100% testing. However in this case, it must be assured that the results of the screening test for the sampled article are determined to be acceptable before any intervening untested articles are integrated into LIGO. In this way a screening failure can be tracked to all potentially affected articles. The sampling frequency shall be submitted for approval by the Detector Cognizant Engineer to the Vacuum Review Board.

In the event that a component fails the screening test, it must either be re-processed or if there are sufficient reasons, a request must be made of the Vacuum Review Board for a waiver. In the case of a screening test failure with statistical sample, it must be assumed that all intervening untested articles are also suspect and must thus be reprocessed unless it can be shown that the reason for failure is specific to the failed article.

Appendix A - Cleaning and Baking Procedures for Approved and Provisionally Approved Materials

1.  Approved Materials

These procedures are consistent with:

1) a materials bakeout at the maximum temperature possible; and,

2) achievement of the summed mass pressure limit.

Any deviation from these procedures must be cleared with the Vacuum Review Board with an approved waiver. Ultrasonic cleaning shall be done in a unit comparable to the system presently in use at MIT.

A.	Metals:

- For all small metal parts do the following:

  - Machine all sides.

  - Ultrasonic clean in Liquinox for 10 minutes.

  - Rinse in distilled water at least 3 times, changing the rinse water every time.

  - Ultrasonic clean in methanol for 10 minutes.

- Subsequent to the above steps bake the metal as follows:

  - Stainless Steel

    - Bake in vacuum at 200 C( for 48 hours.

  - Aluminum

    - Bake in vacuum at 120 C( for 48 hours.

- SEI damped springs shall be cleaned per the procedure outlined in E970131.

- SEI large in-vacuum components shall be cleaned per the procedure outlined in E970063.

NOTES:

- In the case of gross contaminants, the above may be proceeded by an acid bath (i.e., 3% Protex solution (diluted with distilled water) for aluminum or 2% Gosh solution for stainless steel), or an appropriate degreasing agent such as trichloroethane or acetone. Follow these steps with a DI water rinse. Then clean as in A.

- Stainless steel brushes and pads could be used. Cotton swabs, wetted with methanol, must be used after cleaning blind holes to test for cleanliness.

Solvents must be reagent grade.  Methanol is the preferred solvent. Isopropanol and/or acetone may be substituted.

.

B.	Ceramics and Glasses:

- Clean off contaminants with Liquinox and water, be sure to rinse thoroughly.

- Ultrasonic clean in methanol for 10 minutes.

- Soak in isopropyl alcohol for 10 minutes, agitating regularly.

- Bake in a vacuum at 120 degrees C for 48 hours.

C.	LIGO optical components:

- Clean and bake LIGO core and IO optical components according to Process Specification E990034 and/or E990035.

- Clean LIGO optical components other than core or IO optics to Process Specification E000007.

- Clean installed optics utilizing a CO2 cleaning system according to Process Specification E990316.

D.	Fluorel - Viton:

- Seals and O-rings:

  - Wipe with clean, dry lens tissue or polywipe.

  - Bake in vacuum for 48 hours at 120 degrees C.

- At least 24 hours prior to installation, process all Fluorel or Viton seals and O-rings as follows:

  - Soak 10 minutes in DI water.

  - Dry with cleanroom wipes.

  - Place on a class 100 flowbench for 24 hours to dry.

  - Wrap for transport to the installation.

- Molded castings:

  - Follow procedure in LIGO-T970168.

  - Then, at least 24 hours prior to installation, process as in Fluorel-Viton above.

  - Wrap for transport to the installation.

E.	Teflon and PFA 440 HP

- Parts requiring high dimensional tolerances are not to be made of Teflon

- Cleaning of parts made of PFA 440 HP not requiring high dimensional tolerances:

  - Ultrasonic clean in acetone for 10 minutes.

  - Ultrasonic clean in methanol for 10 minutes.

  - Bake in vacuum at 120 C for 48 hours.

F.	NEO 35 - permanent magnets:

- Ultrasonic clean in methanol for 10 minutes.

- Bake in vacuum at 80 C for 48 hrs.

When the magnets became part of a magnet/standoff assembly, after sanding, and prior to bonding, clean using a CO2 cleaning system (LIGO-E990316).

2.  Provisionally Approved Materials (3/1998)

A.	Silicone rubber:

- Small pieces, less than 1.5 cm thick:

  - Soak in methylene chloride for 4 days, changing solvent every 24 hours.

  - Let air dry at room temperature (under fume hood) for 48 hours.

  - Bake in vacuum oven for 10 days at 200 Degrees C.

- Large pieces: Not allowed.

NOTE: This material may be used in LIGO in isolated evacuated vessels which do not communicate directly with the LIGO vacuum envelope (e.g., low-power reference cavities).

B.	Solder: Lead-tin (Kester 6337)

- Same as metals, but flux is to be removed first by spraying Deflux solution.

C.	Perkin Elmer Vacseal:

- Ultrasonic clean in methanol for 10 minutes.

- Bake in vacuum at 80 C for 48 hrs.

D.	Sn-Co permanent magnets:

- Ultrasonic clean in methanol for 10 minutes.

- Bake in vacuum at 80 C for 24 hours.

.

E.	PZT piezoelectric ceramics:

- Ultrasonic clean in methanol for 10 minutes.

- Bake in vacuum at 80 C for 24 hrs.

F.	Ryton:

- Ultrasonic clean in methanol for 10 minutes.

- Bake in vacuum at 120 C for 48 hrs.

G.	Hygroscopic crystalline optics:

- Spot clean mounting fixtures with toluene to remove shipping material residue; cleaning shall be under a fume hood.

NOTE: DO NOT BAKE CRYSTAL

NOTE: DO NOT LET SOLVENT CONTACT CRYSTALS; DO NOT EXPOSE CRYSTALS TO SOLVENT FUMES -- KEEP OPEN CONTAINERS OF SOLVENT AT LEAST 1m FROM CRYSTALS. KEEP CONTAINERS CLOSED WHENEVER POSSIBLE.

H.	Peek connectors/Kapton cabling/wire harnesses:

- Ultrasonic clean in methanol for 10 minutes.

- Bake in vacuum at 200 C for 48 hrs.

3.  Class B Cleaning Procedure

Follow cleaning procedures in Sections 1 and 2 above and airbake instead of vacuum bake, at the specified temperatures for a minimum of 24 hours for all listed materials.

Brass Cleaning

- Use acetone first with clean room cloth and a bottle brush (for internal threads) or wool (preferably stainless steel or brass wire brush or steel wool) over the threaded areas.

- Ultrasonic clean in methanol or isopropyl for 10 minutes at room temperature in a fume hood.

- Blow the parts with dry N2

- Wrap in UHV aluminum foil

NOTES:

1.	Do not use water or water-based cleaners since this will cause an oxide layer on the brass part.

2.	DO NOT vacuum bake brass since it may contaminate the vacuum oven with lead. For the same reason, do not air bake part either.

Appendix B - Cleaning and Baking Procedures for Approved Sub-assemblies

A.	LOS Cleaning Procedure:

- Use flashlight and inspect every cavity; if contaminated send out for another pickle and passivate (using local vendor who has experience in handling and wrapping per our procedures).

Note:  A few areas of reddish surface contamination (rust) in the interior is acceptable.

- Check all threaded holes with UHV cleaned and baked silver-plated, stainless screws to confirm that the threads are clear; if necessary chase the threads with a clean tap using no lubricant except DI water or approved solvents.

- Wipe all exposed surfaces with a clean room cloth (not a clean room paper/tissue) and isopropanol.

- Flush thoroughly with DI water using stainless steel brushes; turn the structure end-over-end and on all sides to get as much of the particulates in the interior cavities out.

- Blow dry (as much as possible) with N2 (do not allow the water to sit and dry).

- Wipe the exposed surfaces again with a clean room cloth (not a clean room paper/tissue) and isopropanol to see if any particulates have been flushed out of the cavities and onto the exterior; flip the structure end-for-end.

- Vacuum bake at 200( C for 48 hours.

- Spot check after the vacuum bake for particulates as the structure is turned end-for-end; wipe any particulates off with a clean room cloth (not a clean room paper/tissue) and isopropanol.

B.	Composite Assemblies

B.1	Commercial Stages:

- Disassemble and clean parts in ultrasonic cleaner with Liquinox for 10 minutes.

- Rinse in DI water.

- Clean in ultrasonic cleaner with methanol for 10 minutes.

- Replace all plastic parts with appropriate metal or Teflon replacement part (Teflon PFA 440 HP pieces).

- Remove Teflon parts and clean thoroughly.

- Reassemble stages.

- Bake in vacuum at 120oC for 24 hours.

B.2	Electronic Components:

- Clean with Liquinox solution and rinse with DI water.

- Bake in vacuum at highest temperature compatible with manufacturer's maximum rating.

B.3	Sensor/Actuator Head Assemblies

- 1st. Assembly: Ceramic body, Teflon tape and Teflon coated wire

  - Ultrasonic clean in methanol for 10 minutes.

  - Soak in isopropyl alcohol for 10 minutes agitating regularly.

  - Bake in vacuum at 200oC for 48 hours.

- Complete Assembly:

  - Ultrasonic clean in methanol for 10 minutes.

  - Soak in isopropyl alcohol for 10 minutes agitating regularly.

  - Bake in vacuum at 80oC for 48 hours.

B.4	Sensor /Actuator “Pigtail” Cables

- Ultrasonic clean in methanol for 10 minutes.

- Bake in vacuum at 120(C for 48 hours.

B.5	Cleaning and Baking Viewports

- Refer to LIGO-E990190.

Appendix C - Forms

Form C1: 	Parts Cleaning Request

Form C2: 	LIGO Vacuum Bake Over Procedure and Check List

Form C1

PARTS CLEANING REQUEST

Requestor: ___________________________  Phone _________________	Date _________

Parts Description, Drawing # _______________________________________Rev#_________

___________________________________________________________________________

Used In (next higher assembly) __________________________________________________

Material:	Al		SST	CST				Bronze

Macor	Teflon	Viton				Glass

Other: ______________________________________________________

Special Handling: _____________________________________________________________

____________________________________________________________________________

Baked In Oven: ____________	Load # ____________		Temp.: ___________ ( C

Date In ___________________	Date Out __________________

Quantity: ____________

No. of Units: __________ and/or (as appropriate) total surface area 	______________ cm2

Describe total quantity required per LIGO interferometer:  _______________________________

____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Baked By: ________________________________

Form C1.  Parts Cleaning Request

Form C2

LIGO VACUUM BAKE OVEN PROCEDURE AND CHECK LIST

Oven:  A     B     C     D     VSA                Load # ___________                    Date: ___ /___ /____

Load Contents: ________________________________________________________________

Cap Torqued:  ______  ft/lbs  ______  ft/lbs  ______ ft/lbs _____ ft/lbs

Metal Valve Open:     Y     N     Vent Valve Closed:     Y     N         TP on:     Date:___/___ Time:___:___

TP on:     Date:___/___ Time:___:___

TP on:     Date:___/___ Time:___:___

TP on:     Date:___/___ Time:___:___

Pressure: ________ Torr	Date:___/___ Time On:___:___

Pressure: ________ Torr	Date:___/___ Time On:___:___

NOTE: Do not turn heat on when pressure is above 5E-5 Torr.

AUTO/MANUAL:		Heat on:   Date:___/___ Time:___:___

Ramp Time:     Oven:____ Hrs,    Pumpline:____Hrs

Soak Time:      Oven:____ Hrs,    Pumpline:____Hrs

BAKE TEMPERATURE o (C):

Oven: ______   PumpLine: ______      Turbo Pump Heat On:     Y     N

TEMPERATURE o (C):

|  | P-Line | End | Body | Cap | Date & Time | P(Torr) |
| --- | --- | --- | --- | --- | --- | --- |
| 1. |  |  |  |  |  |  |
| 2. |  |  |  |  |  |  |

TP Heat Off:     Y     N       Temp Cont. sw Off:     Y     N         Reset PROG off:     Y     N

DEGAS:

Fil On?     Y     N	       W/Dycor# ____	Date:___/___ Time On:___:___ Time Off:___:___

Date:___/___ Time On:___:___ Time Off:___:___

Date:___/___ Time On:___:___ Time Off:___:___

Date:___/___ Time On:___:___ Time Off:___:___

PURGE:	N2       AIR

Comments:____________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

Form C2. LIGO Vacuum Bake Oven Procedure and Check List

Appendix D -- Calculation of Vacuum Load

In order to account for the anticipated load on the LIGO vacuum system arising from the introduction of LIGO Detector components into the chambers, it is necessary to develop an accounting system to track the contribution made to the partial pressure gas load by individual detector subsystem components.

D.1	Database

This could be done by assembling a suitably designed database in which the results of all screenings and high-power exposure tests will be logged. The database shall be searchable/ listable according to any of its entries. As a minimum, the database shall contain the following data:

Inventory data:

- Material, exposed surface area, material volume.

- Subsystem and system comprising material.

- Location, by chamber, of component material.

Physical data:

- Approximate distance to nearest mirror and indication whether there is a direct viewing path.

- Approximate orientation of surface to mirror surface -- needed to estimate viewing factor.

- Pumping speed for HCs in specific location.

Measured data:

- Outgassing rates, by mass number for important complex HC masses.

- Ringdown and frequency shift data: (absorption + loss) and loss rates: ppm/yr.

- Source of information -- LIGO document number or other traceable reference.

Derived quantities:

- Partial pressure by mass.

- Predicted accumulation on target mirror, monolayers/yr and estimated (absorption + loss) and loss rates: ppm/yr, where possible or relevant.

D.2	Estimation of Material Buildup

Optical performance degradation of the LIGO interferometers from material contamination within the vacuum vessels involves three elements: an outgassing source (“culprit”), a target mirror (“victim”), and a path. The outgassing source is most simply characterized by the set of parameters: {A, Ji, mi, i, ai}. A(m2) is the source surface area exposed to the vacuum, Ji(W/m2) is the outgassing rate for the ith species of contaminant, having mass mi(AMU), i is the affinity for the species to adhere to a (clean) vacuum surface (0 <i < 1), and ai is the characteristic linear dimension of a molecule of species i (molecular area ~ ai2). The vessel is maintained at ultrahigh vacuum by a pumping system characterized by a pumping speed for the ith species, Si (m3/s). The target mirror is characterized by the parameters: {dm,, Am}. dm(m) is the distance between mirror surface and outgassing source,is the orientation of the surface normal to the mirror relative to the line-of-sight to the contamination source and Am(m2) is the mirror surface area. These parameters are summarized in Table 2.

| Table 2: Parameters for estimating contaminant buildup on LIGO optics |
| --- |
| Parameter | Symbol | Value or Units (SI) | Value or Units (CGS) | Conversion Factor, : CGS = SI |
| Outgassing rate for species i | Ji | (N-m)/m2/s or W/m2 | torr-liter/cm2/s | 133.32 |
| Source area | Ai | m2 | cm2 | 10-4 |
| Species molecular weight | mi | AMU | - |
| Sticking affinity | i | 0< i <1 | - |
| Molecular linear dimension | ai | m | cm | 10-2 |
| Distance to mirror | dm |  |  |  |
| Mirror area | Am | m2 | cm2 | 10-4 |
| Mirror orientation |  | - |
| Pumping speed for species i | Si | m3/s | liter/s | 10-3 |
| Partial pressure for species i | Pi | N/m2 or Pa | torr | 133.32 |
| Rate of increase of optical losses with time |  | ppm/yr |

.

Table 3: Physical Constants

| Physical Constants |
| --- |
| Boltzmann constant | k | 1.38 10-23 J/K | 1.38 10-16 erg/K | 10-7 |
| Atomic Mass Unit 12C standard: 12 AMU = 12 gm / NA) | AMU | 1.66 10-27 kg | 1.66 10-24 gm | 10-3 |
| Avogadro's Number | NA | 6.023 1023 | - |
| Ambient Temperature, 27oC | T0 | 300 K | - |

Figure 3 depicts schematically the geometrical arrangement of a source, mirror, and pump system.

Figure 3: Geometrical arrangement of source, mirror, and pumping system

As shown in the figure, there are (at least) two mechanisms by which contaminants can migrate to a mirror surface: a direct path and an indirect, or diffuse, path involving the equilibrium partial pressure of contaminant species in the vacuum vessel. The following discussion uses statistical mechanical description derives from discussions found in O’Hanlon’s A User’s Guide to Vacuum Technology, 2nd Ed., Wiley Interscience. It may also be reconstructed from material found in Reif’s Statistical and Thermal Physics, McGraw-Hill. This derivation assumes that equilibrium has been achieved and does not take into account partial pressure gradients which may be present.

Viewed from the mirror surface, the contaminant flux has a direct component and indirect component determined by the material partial pressure.

[1]

The direct component is given by:

[2]

The indirect component is given by:

[3]

The partial pressure is proportional to the outgassing rate-area product and inversely proportional to the system pumping speed:

[4]

Stot is the total pumping speed, which may include the pumping provided by the (otherwise clean) vacuum chamber walls:

[5]

[6]

D is given in eq. [2] above. The worst case is given by chamber 0, in which case the contaminants do not adhere to the chamber walls and the only pumping action is provided by the pumping system itself. In this limit, the molecular flux incident on the mirror surface at room temperature is given by:

[7]

Note that d scales weakly as AMU1/4: using S  1000 liter/s, the distance scale where the two contributions become comparable for AMU=36 is d  3 cm, and for AMU = 500 d  5 cm.

The rate accumulation of material on a surface depends on the physical dimensions of a molecule, ai. A simple model-independent estimate of this dimension may be obtained by considering a substance’s molecular weight and density. Many hydrocarbon have densities which are comparable to that of H2O,  gm/cm3 (at least they will not differ from this value too greatly). The molecular volume is estimated by:

[8]

This yields . For AMU = 36, this yields ai = 3.9  and

or 1.5 10-15cm2. Using this dependence of molecular size on molecular weight (assuming a constant density of ~1 gm/cm3), the following expression obtains for the rate of monolayer buildup:

[9]

For    1   and S0 = 1000 liter/s, this yields:

[10]

This represents a worst-case estimate because it assumes that all molecules adhere to the mirror surface and remain there indefinitely. T980008, “Bake Oven Requirements and Conceptual Design,” Appendix 1, discusses the effect of considering surface dwell time for contaminating molecules.

Eq. 10 will be implemented in the database which predicts the buildup of material on mirrors from outgassing products.

D.3	Extrapolation of Optical Losses in LIGO from High-power Cavity Tests

The least model-dependent estimate of the potential for mirror contamination in LIGO comes from in-situ exposure of resonant cavities to samples of materials. Extrapolation of laboratory test results to LIGO will be performed as follows.

Assume that the ratio of loss buildup to material buildup, , is an intrinsic property of the material under evaluation. Here  is the rate of increase of optical loss (absorption or absorption-plus-scatter) in ppm/yr per optical surface and  is the material buildup rate in monolayer/yr. Then, using equation 10 (and reintroducing the pumping speed dependence into numerator and denominator), the extrapolation from a laboratory-scale measurement to LIGO follows:

[11]

Note that if either the setup or the LIGO installation for the material does not have a direct view of the mirror, then the corresponding term in Eq. 11 will be equal to zero.

D.4	Determination of Outgassing for Highly Condensible Organic Molecules

The calculations required to determine the surface coverage of a condensible gas are not as straightforward as estimating the surface coverage for an almost noncondensible gas. The surface coverage is not determined by merely calculating the flux onto the surface and multiplying by the product of the accommodation coefficient times the exposure time. The surface adsorbs and re-emits molecules and when out of equilibrium has an enormous pumping or emission capacity that dwarfs the pumping speed of the system. Hence, the simple technique of estimating the outgassing rate of a substance by measuring the partial pressure of the gas, multiplying by the pumping speed of the system and dividing by the exposed area of the substance can result in substantial errors if the system is out of equilibrium. The estimated outgassing rate is smaller than the actual rate.

A better approach is to use the Dubinin-Radushkevich adsorption theory (Refer to LIGO- T920009). In this theory at equilibrium, the surface coverage is given by

is the surface coverage in monolayers or torr liters/cm2 while  is the maximum surface coverage. At this coverage the equilibrium vapor pressure is P0. T0 is the average molecular binding energy to the surface expressed as a temperature and T is the temperature, both in K. The figure indicates the parameters used to apply the theory to our measurements. A substance with outgassing rate J (torr liters/sec cm2) is placed in the vacuum system. The emitting area of the substance is As. The surface area of the vacuum system (including the stuff placed inside of it) is Asys. The pumping speed out of the vacuum system is F (liters/sec) and the pressure throughout the volume of the system, V (liters), is P (torr).

Figure 4: Schematic for the calculation. A substance that outgasses a condensible material has a surface area As, in the figure located in a sidearm of the system, though this is not essential to the model. The surface of the system initially has no surface loading of this material. The question is how to estimate the surface loading of the system as a function of time.

If one can assume that the pressure in the system is appropriate to the surface coverage given by the Dubinin-Radushkevich adsorption theory, the system is in a “dynamic” equilibrium on the collecting surface. There is still a net flow from the sample to the surface so there is no global equilibrium. Under these assumptions, the particle conservation equation is

which can be rewritten in terms of the system parameters as

The first order differential equation for the evolution of the pressure in the system becomes

where

When the system is initially exposed to the source, the surface coverage is small and the

dynamical equilibrium pressure is small. The denominator of the pressure derivative equation is dominated by the surface term and the numerator by its surface term. The time it takes for the system to come to pumping speed equilibrium where and is approximately given by:

In order to determine the surface adsorption parameters, , P0 and T0 it is useful to measure the pressure changes vs. time by accumulation methods and to determine the equilibrium pressure under different pumping speeds and temperature. Typical values for water determined from the beam tube project are given in Table 4.

| Table 4: Typical values for water on hot rolled 304L stainless steel |
| --- |
| T0 | 1.0x104 K |
|  | 100 monolayers = 2.8x10-3 torr liters/cm2 |
| P0 | 1.0x10-3 torr |
| J(300K) | 1.0x10-8 /t (hours) torr liters/sec cm2 |

An example calculation for a source in one of the LIGO instrumentation tanks might give an equilibration time of 200 days using typical parameters given in Table 5.

| Table 5: Sample parameters leading to 200 day equilibration time |
| --- |
| T0 | 104 K |
| T | 300 K |
| J | 10-9 torr liters/sec cm2 |
| P0 | 10-3 torr |
|  | 100 monolayers = 2.8x10-3 torr liters/cm2 |
| F | 103 liters/sec |
| Asys | 106 cm2 |
| As | 104 cm2 |

Figure 5 shows the relation between the surface coverage and the equilibrium pressure for the Dubinin - Radushkevich theory. The enormous range in pressure for a small change in surface coverage is the fundamental reason for the vacuum “stiffness” of the process.

Figure 5: Relation between the surface coverage and the equilibrium pressure for the Dubinin - Radushkevich theory

# Footnotes

Latex gloves from Ansell Edmont (AccuTech-Ultra Clean 91-300)

Branson Ultrasonics Corp. (Tel: +1.203.796.0400) Model 8210(latest model as of March, 1998: #8510) has a 5.5 gal. tank (19.5"x18"x6"). Transducer output is 320 watts @ 40khz. The tank can also be heated.

Standard Liquinox solution is 1 tablespoon in 1 gallon of water.

# Comments

Original read "Vacuum Standards Board."  Changed per Albert Lazzarini throughout document to "Vacuum Review Board."

"and Baking. . ." added.

Added to list.

Added to list.

Added to list.

Added to list.

Originally read Page 4, Section 5.  Deleted "page 4" to allow for revisions of document M990034 which may place section 5 on a different page.

Used acronym rather than "ultra-high vacuum" since it was included on the acronym list.

Added hyperlinks for all listed documents which calls up the latest version submitted to the DCC. Check that these are indeed the latest versions and, if not, that subsequent versions are submitted.

Added to list - referenced in document.

Added to list - referenced in document.

Used to be part of (e) as second half of paragraph.

Original read: "Obtain a "Parts Cleaning Request" (see Appendix B Form B1 form) from Detector Systems for pre-bake cleaning.  Follow the cleaning methods and handling procedures in Sections 4 and 5 above according to the type of material, and indicate the procedures on the form.

Original read: "Obtain a LIGO vacuum bake overn procedure and check list" (see Appendix B form B2) from Detector Systems. Provide the component/material baking time and temperature and any requirements for temperature ramptime or soaktime.  Baking temperatures shall follow written procedures discussed in Sections 4 and 5.

NOTES was reformatted.  Original had a paragraph and one isolated bullet.

Added to Applicable Table list.

"steel" added.

Original read "Name."

This line was added.

This form was basically rearranged but generally the same as the original.

Added to Applicable Documents List.

# Text boxes

(

(

(