LIGO Laboratory / LIGO Scientific Collaboration

LIGO-T0900645-v2	aLIGO	September 2010

PSL spare concept

Peter King, Peter Weßels, Benno Willke

Distribution of this document:

LIGO Scientific Collaboration

This is an internal working note

of the LIGO Laboratory.

| Albert-Einstein-Institut Callinstraße 38 Hannover, D-30167 Federal Republic of Germany Phone (05 11) 762 2229 FAX (05 11) 762 2784 | California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 FAX (626) 304-9834 E-mail: info@ligo.caltech.edu |
| --- | --- |
| Laser Zentrum Hannover Hollerithallee 8 Hannover, D-30419 Federal Republic of Germany Phone (05 11) 27 88 0 FAX (05 11) 27 88 100 E-mail: info@lzh.de | Massachusetts Institute of Technology LIGO Project – NW22-295 185 Albany St Cambridge, MA 02139 Phone (617) 253-4824 FAX (617) 253-7014 E-mail: info@ligo.mit.edu |
| LIGO Hanford Observatory P.O. Box 159 Richland, WA 99352 Phone (509) 372-8106 FAX (509) 372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone (225) 686-3100 FAX (225) 686-7189 |

http://www.ligo.caltech.edu/

# Purpose of this document

The purpose of this document is to define the general spares plan for the aLIGO PSL subsystem. The underlying concept is presented followed by a detailed list of spare parts.

# Spare strategy

The general spare strategy assumes, that enough spare components have to be available to cover a 10 year period. (The spare strategy does not cover components that need to be exchanged on a regular basis like laser diodes, chiller filters and DI cartridges etc). Furthermore it is assumed, that a knowledgeable person is available at each LIGO site to perform the following tasks:

- change a laser diode box

- align the 35W front end laser

- change a laser head in the 200W laser

- align the 200W high power laser and the high power Faraday isolator

- replace a control module and adjust the filter parameters

- perform general optics replacement and modematching procedures

- perform general computer administration tasks

User manuals are provide for the lasers and the diagnostic breadboard to guide the alignment tasks.

The following questions guided the choice of spare:

- How high is the risk of failure?

- How easy is it to get a replacement after the fact of a failure (of the shelf component, production lead time, detailed knowledge and training required to produce such a component, single supplier).

- Trade-off between faster replacement of pre-assembled components and costs.

Furthermore we assume that CDS components like computers, chassis, DA/AD/DIO cards anti-aliasing and anti-imaging filters etc. are covered by a LIGO wide spare concept.

# spare component list

We will have one full functioning 35W front end laser (including NPRO and electro-optical components) at each site. There will be no complete high power stage as a spare but separate units / components that compose the high power stage.

For the pump light fibers we follow the following rule:

- 2 spare front end fibers installed per laser

- one full bundle of 6 fibers available on spool at LHO (in case a full bundle is cut, …)

- 2 spare high-power-pumplight bundles (à 7 fibers) installed per laser

- 4 spare bundles on spool at LHO, 4 spare bundles at LLO

| component | LHO 1 | LHO 2 | LLO |
| --- | --- | --- | --- |
| NPRO | 1 |  | 1 |
| 35 W front end laser |  |  |  |
| complete front end laser | 1 |  | 1 |
| control box (not required for AdvLIGO Laser) | (see HPL stage) |  |  |
| FE additional optical components (FI, EOM, PD, optics) | 1 | 0 | 1 |
| chiller (not required for AdvLIGO Laser) | (see HPL stage) |  |  |
| fibers installed | 2 | 2 | 2 |
| fiber bundle on spool | 1 |  |  |
| HPL components |  |  |  |
| HPL electronics NeoLASE |  |  |  |
| control box / interlock box/ Beckhoff PC | 1 of each |  | 1 of each |
| oscillator diode box | 2 |  | 2 |
| power supplies | 3 |  | 3 |
| TEC electronics plus BUZ (for one diode box) | 2 |  | 2 |
| all 4 different laser heads, pre-aligned | 1 |  | 1 |
| Homogenizer | 4 | 4 | 4 |
| laser crystal | 5 | 5 | 5 |
| 45° dicroitic mirrors | 5 | 5 | 5 |
| birefringence compensation set (quarz rotator and 4f lenses) | 2 | 2 | 2 |
| output coupler | 5 | 5 | 5 |
| complete long range actuator with driver | 1 |  | 1 |
| PZT with mirror (charactrerized) | 2 | 2 | 2 |
| low power shutter | 1 |  | 1 |
| hp shutter | 1 |  | 1 |
| flipper with mirror/ solenoid (electromagnetic mount) | 2 | 2 | 2 |
| installed fiber bundel | 2 | 2 | 2 |
| fiberbundel on coil | 4 |  | 4 |
| 45° turning mirror / 100ppm | 5 | 5 | 5 |
| 45° turning mirror / HR | 5 | 5 | 5 |
| faraday isolator | 1 | 1 | 1 |
| thin film polarizer | 5 | 5 | 5 |
| calcite wedges | 2 | 2 | 2 |
| AR windows | 5 | 5 | 5 |
| Brewster plate / full assembly | 1 | 1 | 1 |
| Brewster plate | 5 | 5 | 5 |
| fitting and tubes |  |  |  |
| MACOR mechanincal components | 4 | 4 | 4 |
| laser head sealings / set | 1 |  | 1 |
| chiller set (rack with diode and Xtal chiller) | 1 | 0 | 1 |
| metric screw set | 1 |  | 1 |
| set of mirror mounts | 1 | 1 | 1 |
| set of lens mounts | 1 | 1 | 1 |
| cable set | 1 | 1 | 1 |
| DBB |  |  |  |
| set of PZT mirrors | 1 |  | 1 |
| Quadrant photodiode | 1 |  | 1 |
| reflection PD | 1 |  | 1 |
| transmission PD | 1 |  | 1 |
| control electronics | 1 |  | 1 |
| DBB-CCD | 1 |  | 1 |
| shutter | 2 | 2 | 2 |
| other PSL components |  |  |  |
| CCDs | 2 | 2 | 2 |
| high bandwidth PD | 2 | 2 | 2 |
| FSS rf diode | 1 | 1 | 1 |
| monitor dioden | 2 | 2 | 2 |
| ISS photodiode, inner loop | 1 | 1 | 1 |
| pumplight monitor electronics | 1 | 1 | 1 |
| high power AOM | 1 | 1 | 1 |
| PMC | 1 | 1 | 1 |
| mirrors , lenses, polarizers, retarding plates (low power) |  |  |  |
| mirrors , lenses, polarizers, retarding plates (high power) |  |  |  |
| high power beam dump | 1 | 1 | 1 |
| ISS high power AOM | 1 | 1 | 1 |
| high dynamic range cameras | 1 | 1 | 1 |
| power meters | 1 | 1 | 1 |
| LIGO scope (FSS components reuse from iLIGO) |  |  |  |
| reference cavity | 1 |  | 1 |
| rf EOM 21.5 MHz | 1 | 1 | 1 |
| Ion pump incl. controler | 1 |  | 1 |
| ISS outer loop (in vacuum assembly) | 1 | 1 | 1 |