| APPROVALS | DATE | REV | DCN NO. | BY | CHECK | DCC | DATE |
| --- | --- | --- | --- | --- | --- | --- | --- |
| AUTHOR: L. BARSOTTI | 3-19-10 |  |  |  |  |  |  |
| CHECKED: |  |  |  |  |  |  |  |
| APPROVED: D. SIGG |  |  |  |  |  |  |  |
| DCC RELEASE |  |  |  |  |  |  |  |

# Description

0.5” Ø Flat/Flat mirror @ 532nm

# Material

Corning HPFS 7980 (high purity fused silica, UV grade)

Grade 1G or better (Low inclusion class: <1 mm² cross section, 0.28 mm max. size;

Homogeneity not specified)

# Dimensions

0.5"Ø +.000/-.005" X .250" ± .020" tk., Plano / Plano

# Wedge

<60 arc seconds

# Surface Roughness

Side 1

Super polish

Surface Roughness: <1Å RMS in CA

Surface Quality: 10-5

Side 2

Commercial Polish

Surface Roughness: <5Å RMS in CA

Surface Quality:40-20

# Surface Figure

Side 1

Flat < λ/10 at 632.8 over central 80%

Side 2

Flat < λ/4 at 632.8 over central 80%

# Coating

Wavelength: 532nm

Angle of incidence: 30°- 45°

Side 1

R > 99.95% @ 532nm and AOI 30°- 45°, both s and p pol

Side 2

AR coating, R<0.1% @ 532nm and AOI 45°, both s and p pol

# Coating vendor to provide:

  - 1. Two spectrophotometer graphs of the reflectance and transmittance of the HR coatings; one covering the spectrum from 440nm to 1200nm; the other, with increased sensitivity, showing wavelengths from 450nm to 650nm.

            - 2. Spectrophotometer graphs of the reflectance of the AR coating taken as cited above.