Statement of Work

Fabrication of Machined Parts

for Advanced LIGO HAM Small Triple Suspensions

The following documents are incorporated into and made a part this purchase order.  Click on the following LIGO Document Control Center (DCC) links to access these documents or go on line to the LIGO Public DCC at https://dcc.ligo.org/ to access the DCC#.

# Scope

This Statement of Work (SOW) is for the fabrication of machined parts per the unique drawings included in this package for the Advanced LIGO HAM Small Triple Suspension (HSTS).

# Terms

| DCC # | Description |
| --- | --- |
| C080185-v1 | Laser Interferometer Gravitational Wave Observatory (LIGO) Commercial Items or Services Contract General Provisions California Institute of Technology “Institute”, LIGO Rev 11/12/08 |
| F0810001-v4 | Technical Direction Memorandum. |

# Quality Control

| DCC # | Description |
| --- | --- |
| Q0900001-v4 | Advanced LIGO Supplier Quality Requirements, dated 2/10/10, describes following contractor/supplier QA/QC actions for this procurement: |
|  | 3.1 Pre-Award Inspection |  | 3.9 Discrepant Material Storage |  | 4.4 Calibration Program |
|  | 3.2 Supplier In Process Quality Control |  | 3.10 Quality Records |  | 4.5 Critical Interface |
|  | 3.3 In Process Inspection |  | 3.11 Drawing and Specification Change Control |  | 4.6 Cleanliness |
|  | 3.4 Pre-Ship Inspection |  | 3.12 Welding Certification |  | 4.7 Packaging |
|  | 3.5 Receiving Inspection |  | 3.13 End Item Data Package (including Certifications of Compliance) |  | 4.8 Storage |
|  | 3.6 Discrepant Material |  | 4.1 Design Verification |  | 4.9 Transport |
|  | 3.7 Material Review Action |  | 4.2 Raw Material Procurement |  | 4.10 Customs |
|  | 3.8 Material Review Actions at Contractor |  | 4.3 Traceability of Materials |  |  |

For the above list the Supplier shall: 1) Identify the corresponding sections/paragraphs in their existing QA/QC system 2) meet or exceed the design requirements contained in the attached engineering documents for each area called out.

# End Item Data Package

At the time of delivery of the parts, the Supplier shall also provide the following data, as a minimum:

- Any as-built modifications (with approval of the LIGO Contracting Officer) as mark-ups to the drawings

- Material certifications

- Certificate or statement of compliance with all contract and drawing process restrictions.

- Dimensional & QC inspection reports—this shall include a report showing that parts have been inspected and fall within specified tolerances.

## Dimensional & QC Inspections

We have categorized the drawing list by the level of inspection we require.  The color coded key is found in Table 2.  The complete color coded drawing list can be found in E1000243.

Table 2.

| QTY | Non Critical Parts | Critical Parts |
| --- | --- | --- |
| 10 or Less | Level 2 | Level 1 |
| 10 to 50 | Level 4 | Level 3 |
| >50 | Level 4 | Level 3 |

Level 1: Inspect all parts, provide inspection report by serial number prior to shipping to LIGO

Level 2: Inspect all parts, provide inspection report on first and last only prior to shipment to LIGO

Level 3: Inspect 1st and last parts and random 30%, provide inspection report by serial number prior to shipment to LIGO

Level 4: Inspect 1st and last parts and random 10%, provide inspection report on first and last item only prior to shipment

If any setup changes are made to the tooling, treat the next item out of the unit as a “1st article”.

All Heli-coil threaded holes should be 100% gauged with appropriate gage tools according to Emhart Heli-Coil Product Catalog, HC2000, Rev 4.

# Included Document Hyperlinks

E1000243-v3 Table 1. Drawings list including: part number, revisions, descriptions, ship-to points,

quantities, and inspection levels.

E1000254-v2 Drawing Package. PDF Package containing all drawings associated with this fabrication

effort.

E0900364-v3 Engineering Specification. Specification covering metal components intended for use in

the Adv LIGO Vacuum System

3D CAD files are available upon request and are provided as reference only.  All parts are to be manufactured to the referenced 2D drawings.  If there are any discrepancies between the drawings and the CAD files, the drawings take precedence.

# Quantity Required

The total quantity required for each part by drawing number, and (if appropriate) type number, is indicated in E1000243.

# Delivery Requirements:

The deliveries are FOB at these destinations, i.e. the contractor has responsibility for shipping title and     control of goods until they are delivered and the transportation has been completed. The contractor selects the carrier and is responsible for the risk of transportation and for filing claims for loss or damage.

Shipping Locations: All parts are to be shipped to these locations in the quantities listed in E1000243

LIGO Livingston Observatory (LLO)                 LIGO Hanford Observatory (LHO)                                    
Attn: Mike Meyer and Tom Gentry                     Attn: Betsy Bland and Jodi Fauver
19100 LIGO Lane                                                127124 North Route 10
Livingston, LA 70754                                          Richland, WA  99354

Shipping Containers:

The contractor is responsible for providing shipping containers and transportation which protect these parts from damage from the transportation environment (weather, handling, accidents, etc.).  Edges of parts should be especially protected from damage during shipping.

## Delivery Schedule

All deliveries are to be completed 12 weeks ARO.  If this cannot be accommodated, please provide an alternative delivery schedule for consideration with your bid package.  Early and/or partial deliveries are welcome.

# Manufacturing

## 8.1 Precedence

The Statement of Work (SOW) sections below regarding processing or fabrication of the parts are meant to convey the scope and nature of the requested work.  If there is a conflict between this SOW and the drawing, the drawing has precedence.

## 8.2 Materials

Parts are mainly aluminum alloy (6061-T6, 2024-T351, 1100-H14), stainless steel (302, 304, 316).  The specific material alloys and/or grades are called out on the drawings.  (If aluminum is called out, but a specific grade or temper is not specified, use 6061-T6 aluminum.)  No materials may be substituted or added without prior knowledge and testing by LIGO.  Material certifications are required for all parts.

## 8.3 Machining for Use in Ultra High Vacuum (Clean)

- All parts are to be machined. (No as received, as rolled, as milled surfaces will be accepted.)  No grinding or lapping with abrasive wheels, cloth or stones is permitted.  No sanding of any type.   No parts shall be cast or molded.

- All machining fluids must be fully synthetic, water soluble (not simply water miscible) and free of sulfur, chlorine, and silicone.

- Thoroughly clean part to remove all oil, grease, dirt, and chips with soap and water.  Follow with solvent (acetone) wipe.  Pay close attention to tapped holes.  The use of Scotch-Brite is not allowed.

- The contractor is NOT responsible for cleaning or insertion of heli-coils and dowel pins.

- The contractor is NOT responsible for "Post-Machining Notes" on the drawings, i.e. special cleaning, etc.

## 8.4 Finishing

The required surface roughness (finish) is defined in the drawings.  If no call-out is on the drawing, the surface finishes should be 32 micro inches Ra.  If finish is called out on the drawing, it is Ra.  No coatings or applied finishes are to be used.

Localized scratches, digs and blemishes should be minimized and addressed through visual inspection and QA.

## 8.5 Marking

The majority of parts are to be serialized.  All necessary part identification requirements are found on the drawings.   Mechanically scribe, stamp, or engrave (no dyes or inks), or laser etch, these markings.

## 8.6 Helicoil

All heli-coil holes are to be machined according to the steps specified in the Emhart Heli-Coil Product Catalog, HC2000 Rev4, page 17. These steps include drilling, countersinking, tapping, and gauging the holes to the sizes specified on the LIGO part drawings. It is important that all holes are gauged after tapping to ensure they were prepared properly. See Section 4.1 for additional information regarding the inspection of heli-coil holes. 

Procurement and installation of heli-coils is NOT the responsibility of the contractor and will be done by LIGO.

# Text boxes

# LIGO LABORATORY

California Institute of Technology

1200 E. California Blvd.

Pasadena, CA  91125