Statement of Work

aLIGO TCS Ring Heater

Upper and Lower Assembly Components

The following documents are incorporated into and made a part this purchase order.  Click on the following LIGO Document Control Center (DCC) links to access these documents or go on line to the LIGO Public DCC at https://dcc.ligo.org/ to access the DCC#.

- Terms:

| DCC # | Description |
| --- | --- |
| C080185-v1 | Laser Interferometer Gravitational Wave Observatory (LIGO) Commercial Items or Services Contract General Provisions California Institute of Technology “Institute”, LIGO Rev 11/12/08 |
| F0810001-v4 | Technical Direction Memorandum. |

- Quality Control:

| DCC # | Description |
| --- | --- |
| Q0900001-v4 | Advanced LIGO Supplier Quality Requirements, dated 2/10/10, describes following contractor/supplier QA/QC actions for this procurement: |
|  | 3.1 Pre-Award Inspection |  | 3.9 Discrepant Material Storage |  | 4.4 Calibration Program |
|  | 3.2 Supplier In Process Quality Control |  | 3.10 Quality Records |  | 4.5 Critical Interface |
|  | 3.3 In Process Inspection |  | 3.11 Drawing and Specification Change Control |  | 4.6 Cleanliness |
|  | 3.4 Pre-Ship Inspection |  | 3.12 Welding Certification |  | 4.7 Packaging |
|  | 3.5 Receiving Inspection |  | 3.13 End Item Data Package (including Certifications of Compliance) |  | 4.8 Storage |
|  | 3.6 Discrepant Material |  | 4.1 Design Verification |  | 4.9 Transport |
|  | 3.7 Material Review Action |  | 4.2 Raw Material Procurement |  | 4.10 Customs |
|  | 3.8 Material Review Actions at Contractor |  | 4.3 Traceability of Materials |  |  |

For the above list the Supplier shall: 1) Identify the corresponding sections/paragraphs in their existing QA/QC system 2) meet or exceed the design requirements contained in the attached engineering documents for each area called out.

- End Item Data Package:

At the time of delivery of the parts, the Supplier shall also provide the following data, as a minimum:

- Any as-built modifications (with approval of the LIGO Contracting Officer) as mark-ups to the drawings

- Material certifications

- Dimensional & QC inspection reports—this shall include a report showing that parts have been inspected and fall within specified tolerances.

- Certificate or statement of compliance with all contract and drawing process restrictions.

- Scope and Included Documents:

The Institute is seeking a qualified firm to manufacture the components identified as "made-to-specification" (MTS) items in the formal drawing tree, LIGO-E1000295-v1. Components designated as "off-the-shelf" (OTS) will be provided by Caltech. Also, the formed Glass Rod Insulator (D1000682-v2) is being provided by Caltech. The list of drawings (by part number, revision and name) for particular MTS components is included in Table 1 of this document. The set of drawings is also included with this document.

Table 1. Drawings Associated with Particular MTS Components of each Assembly,

D1001838-v1 and D1001895-v1

| Item No. | Rev. | Description | Type | Source | Quantity |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Required | Spare | Total | Unit |
| D1001838 | V1 | aLIGO [TCS] UPPER SEGMENT RING HEATER ASSY | ASSY | MTS | 1 |  | 1 | EA |
| D1001679 | V1 | ALIGO TCS UPPER MONOLITH RH SHIELD | PRT | MTS | 1 |  | 1 | EA |
| D1000682 | V2 | [TCS] RH GLASS ROD INSULATOR | PRT | MTS | 1 | 1 | 2 | EA |
|  |  | NICHROME WIRE, 24 BNC [DIA .5 MM] | PRT | OTS | 19.8 | 19.8 | 40 | FT |
| D1001819 | V1 | RH ELEMENT RETAINER LEFT [9 O'CLOCK POSITION] | PRT | MTS | 1 | 1 | 2 | EA |
| D1001858 | V1 | RH ELEMENT RETAINER RIGHT [3 O'CLOCK POSITION] | PRT | MTS | 1 | 1 | 2 | EA |
| D1001849 | V1 | UPPER COPPER PLATE | PRT | MTS | 2 | 2 | 4 | EA |
| D1001850 | V1 | LOWER COPPER PLATE | PRT | MTS | 2 | 2 | 4 | EA |
| C-210 |  | SS SHCS-V #2-56 UNC 2A X .625 LONG | HW | OTS | 2 | 2 | 4 | EA |
| N-256 |  | SS HEX NUT #2-56 UNC 2B | HW | OTS | 2 | 2 | 4 | EA |
| FA-404 |  | SS FSHCS-V #4-40 UNC 2A X .25 LONG | HW | OTS | 4 | 2 | 6 | EA |
| CZ1105 |  | PFA COATED 28 AWG Cu WIRE, 2x 6 IN LENGTH | PRT | OTS | 12 | 12 | 24 | IN |
| 100170 |  | ACCUGLASS PIN CONTACT 100170, MALE TYPE T-1, CRIMPED | PRT | OTS | 2 | 2 | 4 | EA |
| D1001895 | V1 | aLIGO [TCS] LOWER SEGMENT RING HEATER ASSY | ASSY | MTS | 1 |  | 1 | EA |
| D1001680 | V1 | ALIGO TCS UPPER MONOLITH RH SHIELD | PRT | MTS | 1 |  | 1 | EA |
| D1000682 | V2 | [TCS] RH GLASS ROD INSULATOR | PRT | MTS | 1 | 1 | 2 | EA |
|  |  | NICHROME WIRE, 24 BNC [DIA .5 MM] | PRT | OTS | 19.8 | 19.8 | 40 | FT |
| D1001819 | V1 | RH ELEMENT RETAINER LEFT [3 O'CLOCK POSITION] | PRT | MTS | 1 | 1 | 2 | EA |
| D1001858 | V1 | RH ELEMENT RETAINER RIGHT [9 O'CLOCK POSITION] | PRT | MTS | 1 | 1 | 2 | EA |
| D1001849 | V1 | LOWER UPPER PLATE | PRT | MTS | 2 | 2 | 4 | EA |
| D1001850 | V1 | LOWER COPPER PLATE | PRT | MTS | 2 | 2 | 4 | EA |
| C-210 |  | SS SHCS-V #2-56 UNC 2A X .625 LONG | HW | OTS | 2 | 2 | 4 | EA |
| N-256 |  | SS HEX NUT #2-56 UNC 2B | HW | OTS | 2 | 2 | 4 | EA |
| FA-404 |  | SS FSHCS-V #4-40 UNC 2A X .25 LONG | HW | OTS | 4 | 2 | 6 | EA |
| CZ1105 |  | PFA COATED 28 AWG Cu WIRE, 2x 6 IN LENGTH | PRT | OTS | 12 | 12 | 24 | IN |
| 100170 |  | ACCUGLASS PIN CONTACT 100170, MALE TYPE T-1, CRIMPED | PRT | OTS | 2 | 2 | 4 | EA |

The solid models (SolidWorks Professional 2009) used to create the drawings and assemblies as well as e-drawings  can be made available to the contractor once an award is made. Further information to aid with assembly will be provided at the time of contract.

Finally, specific manufacturing guidelines for metal components (as in Table 1), which are intended for use in the aLIGO Vacuum System, are included with this document.

| E0900364-v3 | Metal components intended for use in the AdvLIGO Vacuum System |
| --- | --- |

  - Quantity Required

The total quantity required for each part, by drawing number, is indicated in Table 1. Note that the "Required Quantity" for each component is a direct indication of minimum number of parts required to make each Assembly. "Total Quantity" is considered a complete assembly kit, including spares.

The required delivery, under this Statement Of Work, is (1) total assembly kit, for each D1001838-v1 and D1001895-v1.

5.0  Delivery Requirements:

The deliveries are FOB at these destinations, i.e. the contractor has responsibility for shipping title

and control of goods until they are delivered and the transportation has been completed. The

contractor selects the carrier and is responsible for the risk of transportation and for filing claims for

loss or damage.

Shipping Location:

The parts are to be delivered to:

California Institute of Technology

Mindy Jacobson

PMA-LIGO, MS 18-34

391 S. Holliston St.

Pasadena, CA 91125

626.395.3209

Shipping Containers:

The contractor is responsible for providing shipping containers and transportation which protects these parts from damage from the transportation environment (weather, handling, accidents, etc.).  Mating edges of parts should be especially protected from damage during shipping.

6.0  Manufacturing:

### 6.1	Precedence

The Statement of Work (SOW) sections below regarding processing or fabrication of the parts are meant to convey the scope and nature of the requested work. If there is a conflict between the SOW and the drawing, the drawing has precedence.

### 6.2	Cleaning requirements for machining

- Machine all surfaces to remove oxides and mill finish.  Abrasive removal techniques are not acceptable.

- All machining fluids must be water soluble (not simply water miscible) and free of sulfur, chlorine, and silicone, such as Cincinnati Milacron Cimtech 410.

- Thoroughly clean part to remove all oil, grease, dirt, and chips with soap and water. Follow with solvent (acetone) wipe. Pay close attention to the tapped holes.

### 6.3	Material

Specific material grades are called out on each drawing. (If aluminum is called out, but a specific grade or temper is not specified, use 6061-T6 aluminum.)

Material certifications are required for all parts. Cast tooling plate is not permitted.

All materials specified on drawings or SOW have been approved for use in the UHV environment in LIGO. No materials may be substituted or added without prior knowledge and testing by LIGO.

### 6.4	Machining

All parts are to be machined. No grinding or lapping with abrasive wheels, cloth or stones is permitted.  No parts shall be cast or molded.

### 6.5	Finishing

The required surface roughness is defined in the drawings. Except as noted, no surface coatings or plating are required.

### 6.6	Marking

Unless too small, all parts must be marked with a part number, revision code and serial number at the location indicated on the drawing. Marking is to be accomplished by mechanically scribing, stamping or engraving (no dyes or inks). Otherwise, all parts are to be bagged and tagged with information that is to be engraved, as follows:

<drawing number> - <revision code>, <type number if applicable>

<unique 3 digit serial number starting at 001 for the first part and incrementing thereafter>

As an example:

D071314-V2

S/N – 001

The serial number must be a sequential 3-digit number, starting with 001, for each part. Also where indicated, mechanically scribe, stamp, or engrave (no dyes or inks) any additional markings called out on drawing sheets.

### 6.7	Hardware

All hardware indicated on the assembly drawings will be provided by Caltech.

# Text boxes

# LIGO LABORATORY

California Institute of Technology

1200 E. California Blvd.

Pasadena, CA  91125