Statement of Work

Fabrication of Output Faraday Isolator Assy for Advanced LIGO

The following documents are incorporated into and made a part this purchase order.  Click on the following LIGO Document Control Center (DCC) links to access these documents or go on line to the LIGO Public DCC at https://dcc.ligo.org/ to access the DCC#.

- Terms:

| DCC # | Description |
| --- | --- |
| C080185-v1 | Laser Interferometer Gravitational Wave Observatory (LIGO) Commercial Items or Services Contract General Provisions California Institute of Technology “Institute”, LIGO Rev 11/12/08 |
| F0810001-v4 | Technical Direction Memorandum. |

- Quality Control:

| DCC # | Description |
| --- | --- |
| Q0900001-v4 | Advanced LIGO Supplier Quality Requirements, dated 2/10/10, describes following contractor/supplier QA/QC actions for this procurement: |
|  | 3.1 Pre-Award Inspection |  | 3.9 Discrepant Material Storage |  | 4.4 Calibration Program |
|  | 3.2 Supplier In Process Quality Control |  | 3.10 Quality Records |  | 4.5 Critical Interface |
|  | 3.3 In Process Inspection |  | 3.11 Drawing and Specification Change Control |  | 4.6 Cleanliness |
|  | 3.4 Pre-Ship Inspection |  | 3.12 Welding Certification |  | 4.7 Packaging |
|  | 3.5 Receiving Inspection |  | 3.13 End Item Data Package (including Certifications of Compliance) |  | 4.8 Storage |
|  | 3.6 Discrepant Material |  | 4.1 Design Verification |  | 4.9 Transport |
|  | 3.7 Material Review Action |  | 4.2 Raw Material Procurement |  | 4.10 Customs |
|  | 3.8 Material Review Actions at Contractor |  | 4.3 Traceability of Materials |  |  |

For the above list the Supplier shall: 1) Identify the corresponding sections/paragraphs in their existing QA/QC system 2) meet or exceed the design requirements contained in the attached engineering documents for each area called out.

LIGO prefers to utilize the vendors existing QA/QC programs to the fullest extent possible consistent with the LIGO QA and QC requirements. All bidders are requested to submit a written description/plan of their existing QA/QC system with their quotes. The bidder must also submit QA/QC plans for managing subcontractor work and materials.

In the event that a prospective contractor lacks an existing quality system, the contractor/vendor shall develop and implement a quality assurance program in compliance with requirements negotiated at contract/PO award.

- End Item Data Package:

At the time of delivery of the parts, the Supplier shall also provide the following data, as a minimum:

- Any as-built modifications (with approval of the LIGO Contracting Officer) as mark-ups to the drawings

- Material certifications

- Dimensional & QC inspection reports—this shall include a report showing that parts have been inspected and fall within specified tolerances.

- Certificate or statement of compliance with all contract and drawing process restrictions.

4.0	Included Documents:

| DCC # | Description |
| --- | --- |
| E1000672-v1 | Output Faraday Isolator, Metal Mechanical Parts and Quantities, Overall Bill of Materials and all drawings |
| E0900364-v7 | LIGO Metal in Vacuum Specification |

5.0	Scope:

This SOW is for the fabrication of five (5) sets of machined parts for the Output Faraday Isolator.

6.0	Quantity Required:

Item 1-- First Article - One (1) set of Output Faraday Isolator parts.

One complete set of Metal Mechanical Parts consisting of 110 individual pieces as listed in E1000672 (see section 4.0).

Item 2-- Four (4) sets of Output Faraday Isolator parts.

Four complete sets of Metal Mechanical Parts consisting of 440 individual pieces as listed in E1000672 (see section 4.0).

7.0	Delivery Requirements:

The deliveries are FOB at these destinations, i.e. the contractor has responsibility for shipping title and

control of goods until they are delivered and the transportation has been completed. The contractor

selects the carrier and is responsible for the risk of transportation and for filing claims for loss or

damage.

Shipping Location:

Item 1:  First Article  One (1) set of Output Faraday Isolator parts.

LIGO Laboratory

California Institute of Technology

Attn: Michael Smith

MS 18-34

Pasadena, CA 91125

Item 2:  Four (4) sets of Output Faraday Isolator Parts

Ship two (2) sets to:

LIGO Livingston Observatory (LLO)
Attn: Chris Guido
19100 LIGO Lane 
Livingston, LA 70754

Ship two (2) sets to:

LIGO Hanford Observatory (LHO)
Attn: Gerardo Moreno

127124 North Route 10 
Richland, WA  99354

Shipping Containers:

The contractor is responsible for providing shipping containers and transportation which protects these parts from damage from the transportation environment (weather, handling, accidents, etc.).  Mating edges of parts should be especially protected from damage during shipping.

# 8.0 	Manufacturing:

## 8.1 Precedence

The Statement of Work (SOW) sections below regarding processing or fabrication of the parts are meant to convey the scope and nature of the requested work. If there is a conflict between the SOW and the drawing, the drawing has precedence. The parts are to be produced using the CAD models which will be provided to the contractor upon award. If there are discrepancies between the drawings and the CAD model, the model takes precedence.

## 8.2 Restrictions

- Machine all surfaces to remove oxides and mill finish.  Abrasive removal techniques are not acceptable.

- All machining fluids must be fully synthetic, water soluble (not simply water miscible) and free of sulfur, chlorine, and silicone.

- Thoroughly clean part to remove all oil, grease, dirt, and chips with soap and water. Follow with solvent (acetone) wipe. Pay close attention to tapped holes.

- No repairs shall be made unless approved in advance, and in writing, by LIGO Laboratory.

## 8.3 Materials

Material is specified on the drawings. All materials specified by drawings or SOW have been approved for use in the UHV environment in LIGO. No materials may be substituted or added without prior knowledge and testing by LIGO.  Cast tooling plate is not permitted.

## 8.4 Machining

All parts are to be machined. No grinding or lapping with abrasive wheels, cloth or stones is permitted.  No sanding of any type.   No parts shall be cast or molded.  Water soluble (not just water miscible) cutting fluid (lubrication) is to be used for all machining operations. The use of cutting fluids or lubricants, which contain sulfur, chlorine or silicone compounds is prohibited.

## 8.5 Finishing

Any required surface finish is defined in the drawings.

Localized scratches, digs and blemishes should be minimized.

## 8.6 Marking

Marking location is shown on the drawings.

All parts must be marked with a part number, revision code and serial number at the location indicated on the drawing. Marking is to be accomplished by mechanically scribing, stamping or engraving (no dyes or inks).

If not indicated in the drawing, mechanically scribe, stamp or engrave as follows:

<drawing number> - <revision code>, <type number if applicable>

<unique 3 digit serial number starting at 001 for the first part and incrementing thereafter>

As an example:

D0900026-v1

S/N – 001

The serial number must be a sequential 3-digit number, starting with 001, for each part.

Also where indicated, mechanically scribe, stamp, or engrave (no dyes or inks) any LABELS shown on drawing sheets.

- Delivery Schedule:

Our desired schedule is:

Item 1, First Article--4 weeks after receipt of order (ARO).

Item 2, 4 sets--6 weeks after receipt of order (ARO).

Early and/or partial deliveries are welcome. If this schedule cannot be accommodated, please provide an alternative delivery schedule for consideration with your bid package. Early and/or partial deliveries are welcome.

# Text boxes

# LIGO LABORATORY

California Institute of Technology

1200 E. California Blvd.

Pasadena, CA  91125