Compliance matrix for Quad suspension noise prototype design.

Ian Wilmut, Justin Greenhalgh and the SUS team

April  2008

This note gathers the performance requirements and key interface requirements and documents compliance to them, with cross-reference to other relevant documents.

Revision 01 March 2006 following RRR review – see M060041.

Revision 02 June 2006 following steady work on loose ends.

Revision 03 March 2008 in preparation for Quad Fabrication readiness review

Revision 04 April 2008 in preparation for Quad Fabrication Readiness Review (Machined parts and Blades)

# Introduction

This compliance matrix was originally put together for PDR #3 in Summer 2006. It was compiled to address all the requirements from the various requirements documents. Most of these were marked as “comply” and the few that were not had explanations attached.

In this update (04) the status information has been re-checked, and the document colour coded to reflect structural and suspension requirements, this has been done to facilitate quick review of just the structures or suspensions as the review has been split. The colour codeing scheme is as follows:

Grey: Unchanged since last review (PDR#3)

Light Blue: Relevant to structures but unchanged since PDR #3

Blue: Relevant to Structure review, and changed since the last review

Light Pink: Relevant changes have been made to Machining since PDR#3 but matrix is unchanged

Dark Pink: Relevant changes have been made to Machining since PDR#3 and matrix has changed

# Part 1 – complete listing of requirements in Design Requirements Documents.

| Document section | Parameter | requirement | Status | Notes |
| --- | --- | --- | --- | --- |

T010007-03 Cavity Optics suspension subsystem DRD, 7 Jun 2005,  Barton et al.

| 3.3 | Technical noise | No source must contribute to the gravity wave signal more than 10% of the “fundamental” requirements in T010075-00 | Comply | See 3.7, 4.2 and 6.7.2 below. |
| --- | --- | --- | --- | --- |
| 3.5.1 | Alignment | Longitudinal: +/- 3mm Transverse/vertical: +/- 1mm Pitch/yaw: +/- 0.1 mRad | Comply Comply Comply | See assembly procedure document T060040-06-K, latest version. Problems were encountered with perminant DC pitches, this has been solved and is being tested at LASTI |
| 3.5.1 | Actuator range | Must provide a range of +/- 1mRad Updated by document cited at right. | Comply | See T050271-00 (Fritschel, “Considerations regarding magnet strengths …”) for the detail. T060001-00 (Strain) showed how we will meet the requirements. |
| 3.5.2 | Earthquake stops or assembly jigs | Facilitate assembly | Comply | See assembly procedure T060040-04-K |
|  | Earthquake stops or assembly jigs | Immobilize optic | Comply | See end of assembly procedure T060040-04-K |
|  | Earthquake stops | Protect suspended parts during earthquake | Comply | See fuller description in T060139-00-K. |
|  | Earthquake stops | Protect suspended parts when wire/ribbon breaks | Comply |  |
| 3.6 | Structure resonances | No mode below 100Hz | Do not comply | 1st mode is ~54Hz, This has been given preliminary approval. See also below in E050159-00 item 1.1.4.3 |
| 3.7 | Reaction chain and actuator noise | Noise of the actuators | Comply | The design will meet the requirements as set out in T060067-00. |
|  |  | Control noise | Comply | As above. |
|  |  | Coupling of reaction chain noise via non-zero rate of change of force with distance | Comply | T060043 shows that we meet this requirement. |
|  |  | Fluctuating forces from scanning TCS if used | N/A | Scanning TCS not currently planned |
| 3.8 | Mass budget | Must agree with E040136-00 (Seismic Isolation System (SEI) Payload Mass Properties) or revisions | Comply | See mass breakdown in T060141-00-K Note that the Folding mirrors are not considered at this review. Agreed with DCC at RRR. |
| 3.9 | Interfaces |  |  | See detailed breakdown below |
|  |  | Note that the requirements below should be split between SEI and SUS – so the SUS should be given an isolation requirement, not a noise requirement. |
| 4.2 | Noise performance | Test mass internal mode longitudinal thermal noise | N/A | Not covered at this review. |
|  |  | Suspension longitudinal thermal noise | Comply | Covered in T010103-05 (summed with vert thermal) |
|  |  | Longitudinal and vertical seismic sqrt term | Comply | Covered in T010103-05 (presented separately, but when summed satisfy requirements). |
|  |  | Pitch noise | Comply | Not covered in T010103. A document is pending on pitch, yaw and transverse thermal and seismic noise. |
|  |  | Yaw noise | Comply | Not covered in T010103. See above. |
|  |  | Vertical thermal | Comply | Covered in T010103-05 (link above) (summed with long. Thermal) |
|  |  | Transverse thermal and seismic | Comply | Not covered in T010103. See above. |
|  |  | Longitudinal, vertical and transverse technical noise | Comply | See T060099-00-K (insert link) which describes the effects for various technical noise sources. |
|  |  | Roll noise | N/A | We are no longer planning to use sapphire. |

E010613-01-D Generic requirements & Standards for Detector subsystems, 9 June 2005, Coyne et al

| 4 | Documentation | Documents on DCC, drawings approved in accordance with E030350-A-D | Comply | See also further commentary in M050438-01. |
| --- | --- | --- | --- | --- |
| 6.2, 6.3 | Part numbers and serial numbers | LIGO drawing number marked on all parts | Comply | All detail drawings require marking of LIGO part number as in E030350-A-D |
| 6.4 | Co-ordinate system | As per T980044 | Comply | See also T040072-01-R which is specific to the quad. |
| 6.5.1 | Structural safety factor | Metals other than maraging steel 1.25 on yield, 1.4 on ultimate | Comply | See stress calculations in top stage PDS T050233-00-K, structure FEA document T060135-00-K, wire clamp PDS T060042-00-K. |
| 6.5.2 | Structural safety factor | Maraging steel FS + 1.8 | Comply | See blade PDS T060047. |
| 6.5.3 | Structural safety factor | Bonds FS of 2.0 | Comply | Magnets are used for holding flags. Ear bonds are using FS of 3 minimum. |
| 6.5.4 | Glass & ceramics | FS 3.0 | Comply | Ears and their bonds covered in PDR#2 and updates. FS well above 3 expected for laser-pulled ribbons. |
| 6.5.4.1.1 | Proof testing | Proof test all bonds and brittle structures. We note that the ribbon proof test requires to be done in an inert environment. The current procedure does not address this. | Will comply | Covered in ribbon, ear and welding review PDR#2. See updates for latest data. |
| 6.5.4.1.2 | Ribbon environment | Ribbons to be kept moisture free | Comply | See under T000053-03 section 2.8.6.2 below. |
| 6.7.1 | Cleaning | To LIGO specs | Comply | All components of final production will be cleaned by LIGO. These parts will be handled and treated in accordance with the LIGO specifications during manufacture. Welding technique is described in the RFQ. |
| 6.7.2 | Creep acceleration | Requirement here updated by blade committee document T040108-03. See also requirements in T000053-05 section 2.6.1 below. | Comply | Detailed in assembly procedure T060040-04-K, now gives 1 week at 120C (per T040108-03) rather than at 100C to 200C(per E010613) or at 110C per T000053 2.6.1 table 1. |
| 6.8.1 | Welding of metals | Various requirements specified | Comply | See T000053-03 section 2.8.3.4.2 below, and RFQ for weldments for exact detail. |
| 6.8.2 | Welding fused silica | TBD | Comply | Requirements further developed and reviewed in at PDR#2. See updates. |
| 6.8.3 | Dip brazing | No dip brazing | Comply |  |
| 6.9 | Finishes | Tooling protected against corrosion. In-vacuum components not to be anodized. | Comply | See T000053-03 section 2.8.3.1 below. |
| 6.10 | Threaded fasteners |  | Comply | See detail under T000053-03 section 2.8.3.3 below. All fastener holes are tapped either 0.005” oversize or have Nitronic helicoils, this allows the use of regular SS bolts throughout. Helicoils are used in locations of high load or multiple removals. |
| 6.11, 6.12 | Drawing and CAD standards | See E030350 | Comply |  |
| 6.16.1 | Vacuum parts preparation | See E960022-00-D | Comply | See under T000053-03 section 4.1 below. |
| 6.16.2, 6.16.3 | Packaging, marking | Appropriate to the parts, decent wooden crates, properly marked | Comply | Relevant standards will be used |
|  |  | Parts for in-vacuum use must use the right kind of wrapping | Comply | Note that such wrapping is not required BEFORE vacuum-quality cleaning. |
| 7 | Electrical standards |  |  | Covered at previous review PDR #1. See update documents on Birmingham website. |
| 7.4 | Cabling | See E960177-00. (Must also meet vacuum requirements) | Comply | Relevant for wiring over the SUS between actuators and interface with SEI. See PDR#1 update document T050112-01 on Birmingham website. |
| 8 | Vacuum compatibility | See E960022 (below) and E960050 (also below) | Comply |  |
| 9 | Acoustic requirements |  | N/A | Only applies to electronics drive units; covered by previous review PDR#1. ESD drives will be water cooled, see T050110-01 on Birmingham website. |
| 10 | Earthquake requirements | Limits given for maintaining operation (10.3), no damage (10.2) and maintaining structural integrity (10.1) | Comply | See section 2.6.1.2 of T000053-03 below which gives a static equivalent interpretation. |
| 11 | QA | Requirements for inspections, analysis, demonstration, similarity and test. | Comply | See section 3.4 of T000053-03 below |
| 12 | Reliability |  | Comply | See T000053-03 section 2.4 below |

T000053-04, Universal Suspensions subsystem DRD, Dec 2005, Dennis Coyne

| 2.1 | Fit | Must fit in the chamber without interfering with neighbouring components. See details in D050266-00 | Comply | Almost fits with envelope supplied by SYS only very localised violations at the bottom of the sleeve. An updated drawing will be provided. |
| --- | --- | --- | --- | --- |
| 2.2 | Interfaces external to LIGO |  | N/A |  |
| 2.3 | Interfaces internally | E030647 and extant RODAs | Comply | See also below for interfaces |
| 2.4 | Reliability | Failure rate 5 years per interferometer. |  | OSEMs have been covered by a separate review. There are no structural parts subject to fatigue, and creep in the highly-stressed parts (wires and blades) has been extensively studied; See T040108-03 (blade process spec). See comments on OSEM life in T060142-00-K. |
| 2.5 | Maintenance and repair – general |  |  | See also E040329-03 (Failure and repair) and T060116-00-K (FEMA) and T060040-04-K (assembly proc with repair scenarios) |
| 2.5.1 | Maintenance and repair – in-air | Less than 1 day | N/A | Electronics covered by separate review |
| 2.5.2 | Maintenance and repair – in –vacuum | Minimise the need for cartridge de-installation where possible | Comply |  |
| 2.5.2.1.1 | Fibres/ribbons | Suspension partially or fully removed from vacuum. Time to repair not to exceed two days | Comply | Covered in earlier review see updates and also latest assembly procedure T060040-04-K |
| 2.5.2.1.2 | Wires | Time to replace less than two days including cleanup | Comply | See T060040-04-K (assembly procedure) |
| 2.5.2.1.3 | Optic ears | Fifty days including bonding; two days with pre-bonded parts | N/A | Covered in earlier review see updates |
| 2.5.2.1.4 | OSEM | Replacement possible in situ, time not to exceed two days. | Comply | See T060040-04-K (assembly procedure) and T060116-00-K (FEMA) |
| 2.5.2.1.5 | Magnets | Replacement of optic plus magnet not to exceed 14 days. Replacement of screw-in magnet not to exceed two days | Comply | This has been superseded by the innovation of “magnetic bonding” for the flags. See T060122-00-K |
| 2.5.2.1.6 | Mechanical adjustments | Realignment goal 4 hours in situ | Comply | As far as we are aware this can be done; it depends on the extent of the alignment required and the metrology available. |
| 2.6 | Environment | Suspension assembled at observatory from easily shipped parts | Comply | The assembly process has been deigned with this in mind and we will supply assembly tooling. |
| 2.6.1 | Temperature and humidity | Storage of various items, only the first line applies in this review. | Comply | The only items which might subject to degradation are the maraging steel blades and the steel wires, which might rust. |
|  |  | Creep bake. | Comply | For the creep bake see E010613-01-D section 6.7.2 above. |
|  |  | In vacuum bake. Note additional request by email from Dennis Coyne May 9th 2006 requesting highest temperature possible. The target under discussion in preceding emails was 125C. | Comply | No temperature-sensitive parts in this review except wiring and magnets, but this new requirement was not reviewed as part of the electronics review PDR#1. See T050111-01 page 26. |
|  |  | Assembly | Comply | No special requirements. |
|  |  | Assembly with fused silica | Comply |  |
|  |  | Transport of parts – no special requirements | Comply |  |
|  |  | Transport of assembly (no fused silica parts) extra care and air-ride van | Comply | Movement stops are provided see T060139-00-K |
|  |  | Transport and handling (final assembly including mirrors) within facility | Comply | Not part of this review, although the suspension is designed so that it can be installed using special tooling and the crane. |
|  |  | Operation in-vacuum 23 +/- 2C | Comply | But note that most parts of the suspension will reach higher temperatures see T060115-01-K re thermal effects. |
|  |  | Operation external to vacuum 23 +/- 2C | Comply | No special requirements during assembly. |
| 2.6.1.2 | Seismic | Severe: 0.4g sideways and 1.1g vertically must cause no major damage | Comply | See T060118-00-K Which has a section on earthquake survival calculations. See FEMA document T060116-00-K |
|  |  | Moderate: 0.11g sideways and 1.03g vertical must cause no failures | Comply | Ditto |
|  |  | Minor ground motion – not defined | N/A |  |
| 2.6.1.3 | Magnetic fields | See ICD E050159-00. Suspension must fulfil design requirements with given fields and gradients. | Comply | See T050271-00 (revised force requirements) and T060001-00 (proposed response) Ref stress relive bake |
| 2.6.2 | Magnetic damping | Requirement not defined – there must be no eddy-current damping effects that violate the “technical noise” requirement. | Comply | See T060099-01-K (technical noise sources) section 2.10. |
| 2.6.3 | Electrostatics | (for objects near the optics) Requirement not defined | Comply | Earthquake stops will use silica tips |
| 2.6.4.1 | EMI compatibility | Various requirements | N/A | Covered in electronics review; key documents updated are T050111-01 (OSEMs); T050112-01 (electronics); T050110-01 (ESD) on Birmingham website. |
| 2.6.4.2 | Acoustic | Various requirements | N/A | Covered in electronics review; ESD drives will now use water cooling see T050110-01 on Birmingham website. |
| 2.6.4.3 | Mechanical vibration | Natural vibration amplitude not increased by more than 1dB with 1 m. | Comply | SUS not coupled directly to vacuum tanks. |
| 2.7 | Transportability | Transportable by commercial carriers; lifting provisions over 100 lbs; handling frames to be provided by SUS | Comply | The most delicate parts currently envisage d to ship are the PM and RM (Test mass not part of this review) and assembled top and UI masses. None of these are above 100 lbs unless multiple systems are assembled together. |
| 2.8.1, 2.8.2 | Electronics, electrics |  | N/A | Covered in electronics review. |
| 2.8.3 | Materials and processes |  |  |  |
| 2.8.3.1 | Finishes | Tooling protected against corrosion. In-vacuum components not to be anodized. Sliding surfaces to be avoided where possible, must only use approved lubricants. | Comply | No in-vacuum components have any surface treatment. Tooling will use non-corroding materials or mild steel parts which are surface treated eg by cadmium plating. |
| 2.8.3.2 | Fasteners | All imperial (E030350-A-D is cited) In vacuum fasteners to be treated as specficied in accordance with E030350 to prevent galling (oversize taps; silver plating; nitronic inserts) (note that the requirement has in fact been removed from E030350 and is now duplicated here and in E010613-01 generic requirements, section 6.10) | Comply | Specified on detail drawings |
| 2.8.3.3 | Materials for vacuum service | Must come from E960050-B or be tested | Comply | The material of the flexi-circuit is still under test. See T060137-00-K |
| 2.8.3.4.1 | Cleaning | Cleaning must be done to E960022-B | Comply | In-vacuum parts will be supplied laboratory clean to Caltech where they will be cleaned baked packed and shipped to LASTI. Tooling will be be cleaned in accordance with E960022-B, class B (Appendix A3) with the possible exception of scissors-jack for jacking sus assembly. |
| 2.8.3.4.2 | Welding | Various requirements specified. See also recent experience from SAS HAM as set out in email from Dennis Coyne of 23 May 2006 | Comply | See draft welding specification T060113-00-K. and Weldment RFQ |
| 2.8.4 | Component naming | Use the standard LIGO naming convention | Comply |  |
| 2.8.5 | Interchangeability | Only two or three OSEM designs | Comply | Currently only two are envisaged, the “LIGO-1” and “Birmingham” designs. However, the Birmingham design will come in two flavours, with and without sensors. |
|  |  | Magnet/Standoff/flag common to all suspensions | Comply |  |
|  |  | Electronics designs similar | N/A | Covered in separate review |
|  |  | Dog clamps single design | Variant | The dog-clamps for the quad suspensions will need to be much stiffer than those for the HAMs – see T050098 (Dennis at March 2005 LSC) |
| 2.8.6 | Safety | Hazard Analysis required per M950046-F section 3.3.2. | Comply | First draft at T060131-00-K The hazards include stored energy in blades, injury from lifting, injury from dropping, lasers during welding. |
| 2.8.6.1 | Personnel safety | lasers (for welding). SOP compliant with M0401112-07 (LLO), M020131-01 (LHO) and TBD (LASTI) | Will comply | An SOP will be produced for the ribbon pulling/welding machine. Glasgow have just delivered a similar system to Virgo for EGO, which complies with Glasgow University and EGO rules. |
|  |  | heavy items, | Comply |  |
|  |  | spring energy release | Comply |  |
|  |  | high voltage | N/A | High voltage was considered in a previous review. |
| 2.8.6.2 | Machine safety | Provide mass stops | Comply |  |
|  |  | Design FS | Comply | See under E010613-01-D section 6.5 above |
|  |  | Proof testing on all magnet bonds, ear bonds, ribbon welds | Comply | Ears and ribbons covered in previous review. See also under E010613-01-D section 6.5 above |
|  |  | Ribbons to be kept moisture free | Comply | Suitable storage will be provided. See assembly procedure T060040-04-K |
|  |  | Coil over-current | N/A | Covered in previous review. See T050111-01 (OSEMs); T050112-01 (electronics) on Birmingham website. |
| 2.8.7 | Human Engineering | Several factors listed for consideration in assembly procedures | Comply |  |
| 2.8.8 | Assembly and maintenance | Assembly possible in class 100 clean area | Comply |  |
|  |  | Alignment tooling provided | Comply |  |
|  |  | Installation | N/A | Not part of this review, but installation of controls prototype shows that it is feasible and we are working closely with LIGO on installation tooling. |
|  |  | Repair/replacement procedure and tooling | Comply | See also section 2.5.2 above. |
|  |  | Assembly procedures tested by “third parties” | Will comply as far as LIGO observatory staff can be made available. | Procedure has been developed between several groups, needs to be tested on the noise prototype. |
|  |  | “Cartridge” installation method | Comply |  |
| 2.9.1 | Specifications | ICDs | Comply | Reviewed in June 2005, UK comments in M050438-01 |
|  |  | OSEM and ESD | N/A | Covered by electronics review |
|  |  | Welded structure process spec | Comply | See draft welding specification T060113-00-K. and Weldment RFQ. |
|  |  | Suspension UHV cleaning and FTIR sampling spec | Comply | It is hoped that the weldment vendor will take on some of the cleaning duties, the spec they will be provided with is still subject to discussion |
| 2.9.2 | Design documents | Conceptual design T010103 and T010007 DRD to be kept up to date | Comply | Revised and reviewed in June 2005 |
|  |  | Installation and commissioning plans |  | Not covered by this review. |
| 2.9.3 | Engineering drawings | To E030350 | Comply | See comment in M050438-01 on the details of the UK compliance. |
| 2.9.4 | Procedures | OSEM assembly | N/A | Earlier review |
|  |  | Suspension assembly | Comply | T060040-04-K assembly procedure |
|  |  | Fiber/Ribbon welding | N/A | Earlier review |
|  |  | Ear bonding | N/A | Earlier review |
|  |  | Initial installation and setup | pending | Not UK deliverable but UK should have input. |
|  |  | Normal operation |  | Instructions required? |
|  |  | Normal and/or preventative maintenance | Comply | None envisaged |
|  |  | Troubleshooting guide | Pending | Recognise need. Has been developed during noise prototype assembly and installation. Will be improved during 1st article assembly. |
| 2.9.5 | Manuals | Requirements modified in forthcoming release of T000053, to include The following manuals shall be provided: OSEM Manual OSEM Drive/Readout Electronics Manual Electro-Static Drive Electronics Manual Suspension Controller and System Manual Each of these manuals shall include guidance on operational use, maintenance, repair, and troubleshooting, as appropriate. | Pending | The manuals will be provided. |
| 2.9.6 | Numbering | Documents use DCC | Comply |  |
| 2.9.7 | Travellers | Requirements not yet complete | Pending | Will be developed during noise prototype assembly/cleaning/installation |
| 2.10 | Test plans and procedures |  | N/A | Requirement not relevant to this review |
| 2.11 | Logistics | Spares etc | Comply | Numbers of spares have been agreed with SYS, embodied in UK Scope document M030162-A released by DCN E050036-00 |
| 3.2 | Reliability testing | OSEMS | N/A | Covered by electronics review |
|  |  | Ear bonds and ribbon welds | N/A | Covered by ear etc review |
| 3.3 | Configuration management | Must follow LIGO detector implementation plan | Intend to comply | Need to see the plan. We assume much of this will be covered by our compliance with E030350-A-D (Drawing standards) |
| 3.4 | Quality conformance | Requirements for inspections, analysis, demonstration, similarity and test. | Comply | Design at RAL is within a ISO 9001 QA system. LIGO QA procedure are followed for example in drawing approvals and by reviews. |
| 4.1 | Vacuum parts preparation | See E960022-00-D | Comply | All in-vacuum parts will be cleaned in US. Parts will be supplied to them to general lab clean standard. And will be machined with appropriate processes to enable cleaning. Structures may be supplied clean and RGA tested |
| 4.2, 4.3 | Packaging, marking | Appropriate to the parts, decent wooden crates, properly marked | Comply | Relevant standards will be used |

# Part 2 Key interface requirements

It would not be productive to list here all of the items in the several interface documents to which SUS-UK is party. There follows a listing of those requirements which the design team feel to be particularly relevant.

| Document section | Parameter | Requirement | Status | Notes |
| --- | --- | --- | --- | --- |

E050160-01 ICD SUS/UK – SUS/US Coyne et al. Draft four from Birmingham website, Sept 2005

UPDATED VERSION NOW LINKED HERE E050160-01

| Figure 1 and Figure 2 | Diagrams showing scope of provision | Embodied in diagrams. This is mostly not relevant for this review except for the “pigtails” | Comply |  |
| --- | --- | --- | --- | --- |
| Table 1 etc. | Table of OSEM connections | The pigtails must conform to the relevant tables at both ends. | Comply |  |

E050169-01 ICD SUS/UK – AOS Coyne et al, June 21, 2005.

| 1.1.1.1.1 | Compensator plate | Comp Plate is mounted to the end of the reaction chain of the ITM. | Comply | Note that the requirement is for the N-Ptype to be reconfigurable between ETM and ITM. |
| --- | --- | --- | --- | --- |
| 1.1.1.1.2 | Ring heater and radiation shield attachments | Heater and shield, mass up to 1.5kg each. | Comply | Has an adverse affect on natural frequency of structure. Note: Baffles no longer interface to structure |
| 1.1.1.1.2 & 1.1.1.1.4 |  | Must be able to mount heater and shield, with suitable view factor, | Comply | Being tested |
| 1.1.1.2 | Ring heater power | Expected to exploit unused wire in the D25 connectors | Unsure | Need to check if the D25 connectors are suitably rated. |
| 1.1.1.3 | TCS parasitic heating | TBD limit on heat into structure from TCS |  | See recent analysis in T060115-01-K |
| 1.1.3.1.2 | Obscuration by earthquake stops | Must not protrude more than 10mm from edge of optic | Comply | Note limit is assumed to be from edge of chamfer to maximise contact area. (Agreed with Coyne Dec 2005) |
| 1.1.6.1.1 | Alignment marks | Required per diagrams in ICD. | Comply | Shown on detail drawings. |
| Not yet included | Requirement to allow for SPI | Location of SPI not yet formalised | Intent is to comply | No provision in present design to allow for SPI |

E050168-00 ICD SUS/UK – COC Coyne et al, June 14, 2005.

| Table 1 | Optics sizes | Definitive sizes of optics | Comply |  |
| --- | --- | --- | --- | --- |
| 1.1.1.4 | Electrostatic coating | In discussion | Compliance anticipated | Need to agree who provides these. |
| 1.1.1.6 | Covers and Ergo arm | Covers will be provided for optics when not in use, in particular during assembly of SUS. The “Ergo arm” provided by COC will be used for handling the optics | Comply | Use of the covers and ergo arm is allowed for in the assembly procedure. |

E050159-00 ICD SUS/UK – SEI Coyne et al, June 14, 2005.

| Figure 1 and Figure 2 | Interface between pigtails and SEI | Required to conform to diagram | Compliance anticipated | Alternate diagram proposed – see above under Figure 1 & 2 of E050161-01 |
| --- | --- | --- | --- | --- |
| 1.1.1.2 | Envelope | Drawing supplied by SYS |  |  |
| 1.1.4.3 | Frequencies | > 200 Hz (upper), >100 Hz (lower), > 100 Hz (both) See also T010007-03 item 3.6. Beware duplicates modes. | NOT COMPLIANT but effects are understood to be acceptable | Requirements are discussed in T050005-01, and further interpreted in T050014-00. FEA of structures is in T060135-00-K. Feedback from LASTI and Brian Lantz indicate 1st mode of 77hz as tested to be acceptable. |
| 1.1.6.1 | SEI static range | Limits given for movements that can be achieved by SEI to move the whole SUS into alignment. | Comply | See alignment document T050103-00-K |

E050176-00 ICD SUS/UK – ISC, Coyne, June 2005

| 1.1.2.1 | Global control actuator requirements | All superseded by more recent documents T060067 “AdL Quad Suspension UK Coil Driver Design Requirements” and T050271-00 “Considerations regarding magnet strengths for the Advanced LIGO test mass quadruple suspensions” (Not sure about the ESD requirements) | Comply | Key documents updated are T050111-01 (OSEMs); T050112-01 (electronics); T050110-01 (ESD) on Birmingham website. |
| --- | --- | --- | --- | --- |
| 1.1.2.2 | Violin modes | Above 400 Hz and quality factor above 1010 | Comply | See T010103-05 for violin modes and T050267-00 for further discussion. Mecanical provision exists and Nick Lockerby agrees there is adequate provision (verbal) |
| Not yet included | Gap between Test mass and reaction mass | We will set the gap to 5mm +/- 0.25mm. If necessary this will involve mounted the RM at a small angle. And we note the requirement that we do not align the RM with the interferometer. See also email from KAS 26 May 2006 | Comply | Assembly procedure T060040-04-K. Additional provision has been added to allow looking at the side of the optics with microscopes to help this. |

# Part 3 relevant RODAs and other areas

Relevant RODAs

See http://www.ligo.caltech.edu/~coyne/AL/project_management/RODA/RODA_status.htm

| M040005-01.pdf |  | CP location, dimensions and mass baselined | Comply | Noise prototype and final design are subtly different but both comply. |
| --- | --- | --- | --- | --- |
| M040088-01.pdf |  | OSEM counts etc | Pending | Needs updating to reflect decision to use LIGO 1 OSEMs on PU mass |
| M040099-00.pdf |  | ETM/ITM quad pendulum structure length not to exceed 2005mm | Comply | Current envelope D050266 has 1960 with which we comply. |
| M050397-00.pdf |  | Core Optic sizes, including TMs, BS, FM and RM |  | Covered in PDR #2 |
| M050418-01.pdf |  | Separation of chains in quad suspensions | Comply |  |
| M060043-00 (still in signature cycle) |  | Will not fit sensors on UIM and PM except for the noise prototype. | Will comply | Does not affect Noise Ptype. |

Other areas not covered above

|  | Wedge angles and pitch angles | Should be in ICD SUS/COC? See email from Dennis Coyne of 02 May 2006 | Intend compliance | RODA M050397-00.pdf has “WEDGES: The wedge angles are given in Table 3 of the optical layout T010076-01. However, Mike Smith has noted that the separation distance assumed in the analysis for pick-off beams was inadequate. The result is a larger wedge angle for the ITMs. Wedges are therefore not yet finally defined in this document.” |
| --- | --- | --- | --- | --- |
|  | Design flexibility - reconfigurable | T050005-01 – but did this ever get into any of the DRDs or ICDs? | Comply | See review overview document T060142-00-K. |
|  | Blade matching | We should ensure that mismatching of the blades does not upset the suspension performance or controllability | Comply | The design seems to be quite tolerant of larger errors than we envisage. See cross-coupling paper T040143-00-R |

Are these all “derived requirements”?

|  | Blade internal modes |  | OK | See T010103-05 |
| --- | --- | --- | --- | --- |
|  | Accuracy of setting of d distance and pendulum lengths | d = 0.5 to 2mm for each stage. Silica stage length correct to +/- TBD d distances on any set of four stage must be matched within a 1mm band. Pitch of masses needs to be controlled to allow alignment of OSEMs etc. | Comply | Ref conversation with Norna. See cross-coupling paper T040143-00-R Target Ds changed but we still comply |
|  | Violin mode damping | Must provide mounting points for sensors and allow 50g per sensor. | Comply |  |