## Slide 1: Documenting With E-travelers
Documentation Techniques
Abbott
29 September 2010

## Slide 2: Marking a Circuit Board
On each PCB:
  D-number plus revision
  Short verbal description
  Serial number block (1.25 inch by 3/8 inch)

## Slide 3: Marking a Chassis Front Panel
Short verbal description on front
D-number without revision
Self adhesive S-number sticker (1.25”by 0.375”)
Revisions tracked under S-number

## Slide 4: PCB Documentation In DCC
PDF of schematic and board
Zip of native software files
Manufacturing files (BOM, Gerber, etc.)

## Slide 5: Chassis (Assembly) Documentation In DCC
A Chassis (better named as an assembly) requires:
  Assembly Drawing (what’s inside the box)
  Assembly BOM (what do I need to build it)
  User’s Guide or Quick Start Guide (how not to break it)

## Slide 6: Using the E-traveler
Obtain the latest revision, don’t clone it willy nilly.
  LIGO-F0900053 latest revision
  Put yourself on the “watch this document” list in the DCC
Fill it out per LIGO-T0900520, latest revision
  This records the birth record and life history of a PCB or Chassis
  The E-traveler is saved under the S-number of the device it tracks. Going to an S-number in the DCC should yield related files, one of which is the E-traveler
  Save test data under the S-number file card in the DCC

## Slide 7: Where We Hope To Be
An effort is underway to replace the PDF version with a more convenient DCC interface.
We will eventually try and conveniently link the E-traveler concept to the ICS system (maybe).