DCN No.   E040223-00-W

California Institute of Technology

Sheet    1	 of   1

# Massachusetts Institute of Technology

# Document Change Notice (DCN)

DOCUMENT No.			            	TITLE			            		                                 NEW

A

WHAM7 IOO Table Layout

(DOC-REV-GP.ID)       						                                                                             REV

D000356-00-W

CHANGE DESCRIPTION (FROM/TO):

After the 2/28/01 WA earthquake broke both 2k and 4k MC optic suspension assemblies, we swapped MC Flat suspensions such that the 2k could be quickly vented and fixed.  Since we stole 4k suspensions to do this, the MC1 and MC3 mirror orientations were out-of-configuration (MC1 is supposed to be a “right hand” and MC3 is supposed to be a “left hand” oriented suspension, however both are “right handed” – see T010136).  Therefore, the beam path to SM1 changed horizontally along the HAM7 table surface.  Univ. of Florida recalculated this beam trajectory and revised the WHAM7 table layout drawing.  At this time, they also changed the drawing to reflect the as-built configuration of the steering mirrors which use DLC type rigid mirror mounts, versus the originally designed “Tanner” mounts.

REASON FOR CHANGE:  See above

ACTION:                 Incorporate Change        Attach DCN to Drawings           Other Action (specify):

DISPOSITION OF HARDWARE (IDENTIFY SERIAL NUMBERS)

DCN DISTRIBUTION

Coyne

Reitze

Tanner

SAFETY, COST, SCHEDULE, REQUIREMENTS IMPACT?           NO           YES (If YES, enter CR (CCB) or TCP (TRB) #)

List S/Ns to be retested per this change:

| APPROVALS: | DATE | OTHER APPROVALS (SPECIFY) | DATE |
| --- | --- | --- | --- |

ORIGINATOR: B. Bland

5/18/04

List S/Ns to be reworked/scrapped:

List S/N’s to be built with this change:

No hardware was affected (record change only):

DCC RELEASE:

List S/Ns which comply already:

TASK LEADER: D. Tanner/D. Reitze

GROUP LEADER: D. Tanner/D. Reitze

DCN No.

California Institute of Technology

Sheet    of

# Massachusetts Institute of Technology

CHANGE DESCRIPTION (FROM/TO):

# Document Change Notice (DCN)

# Text boxes

LIGO Form DCN-03 (10/2001)

LIGO Form DCN-03 (10/2001)