| Originator | Cognizant Engineer | Ext./Phone# | Project | Account Number |
| --- | --- | --- | --- | --- |
| Name Stephany Foley | Ken Mason | 617-324-5250 | ELIGO HAM SEI |  |

| Dwg/Part Number | Rev | Part Description / Material | Serial Number | Qty |
| --- | --- | --- | --- | --- |
| D071464 |  | ADE position sensor probes / ceramic, cable- see cleaning insturctions below |  | 6 |

| Used In (next higher assembly): |  |
| --- | --- |

| Vendor Name | PO/Contract Number |
| --- | --- |
| HPD |  |

Data Package, Receiving/Inspection Remarks:

| Inspection Required Y/N | Visual Damage Y/N | Comments | Name/ Initials | Date Comp. |
| --- | --- | --- | --- | --- |

Process Flow:

| # | Operation | Start Date | Work Area | Instructions | Name/ Initials | Date Comp. |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Clean |  | LHO | Ultrasonic clean in methanol for 10 minutes. Soak in isopropyl alcohol for 10 minutes agitating regularly. | B.L (@MIT) | 1-18-08 |
| 2 | Vacuum Bake |  |  | Bake in vacuum at 100oC for 48 hours. (max temp of 100C per ADE, supplier of probes) | T.E. | 1-29-08 |
| 3 | Control Point |  |  | Review/Approve RGA scan | BO’R | 1-30-08 |
| 4 | Wrap & Tag vacuum clean parts |  |  |  | T.E. | 1-31-08 |
| 5 | Ship and Deliver/File paperwork |  |  | Please send to: LHO c/o SEI File one copy of traveler with the DCC. Note: Ship original traveler with these parts. | BO’R | 4-21-08 |
| END: Go to Traveler or procedure associated with next higher assembly processing |

Special Instructions (Handling/Packaging Constraints, Remarks, etc.) or Notes: