LASER INTERFEROMETER GRAVITATIONAL WAVE OBSERVATORY

--LIGO—

California Institute of Technology

Massachusetts Institute of Technology

### This is an internal working note

of the LIGO Laboratory.

| California Institute of Technology LIGO Laboratory, MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-3064 Fax (626) 304-9834 | Massachusetts Institute of Technology LIGO Laboratory, NW17-161 175 Albany St. Cambridge, MA 01239 Phone (617) 253-4824 Fax (617) 253-7014 |
| --- | --- |

Scattering study of 80mm x 120mm LIGO test mass

Below we present preliminary results from imaging scattering in two sapphire samples: the “UWA sample”: a CS sample 60mm x 150mm and the LIGO sample 80mm x 120mm.

The sapphire was illuminated by a normal incidence HeNe laser 10mW and was imaged by a Sony digital camera. Our high sensitivity Meade camera malfunctioned so calibrated scattering intensity data is not available.

Results show that there is one bright point defect every 20 cubic millimetres. Small point defects occur about one per 7 cubic millimetres. A continuous background of scattering is also visible Preliminary estimates put the scattering level at `100 times that of “normal” sapphire material, ~1000ppm/cm.

Experimental Configuration::

Laser beam diameter: 1.5mm

Principal of the experiment:

Six randomly located photos of the LIGO test mass are shown below, followed by a single photo of the UWA sample which shows no detectable signal. All photos show strong surface scattering at the entry and exit points, plus a line of scattering defects.:

Image1, LIGO test mass (UWA, 08/08/02)

Image2, LIGO test mass (UWA, 08/08/02)

Image3, LIGO test mass (UWA, 08/08/02)

Image4, LIGO test mass (UWA, 08/08/02)

Image5, LIGO test mass (UWA, 08/08/02)

Image6, LIGO test mass (UWA, 08/08/02)

Photo of the AIGO test mass:

# Text boxes

80mm

120mm

Laser

Camera

Sapphire

Document Number:      LIGO-T020107-00-Z        Date:   00/00/00

Author(s):  Dr. Li Ju - The University of Western Australia

## Scattering Study of 80mm x 120mm

## LIGO Test Mass