LIGO Laboratory / LIGO Scientific Collaboration

LIGO-T08xxx-0-D	ADVANCED LIGO	6/9/08

AOS: Stray Light Control (SLC) 
Conceptual Design, Stable Recycling Cavity

Michael Smith

Distribution of this document:

LIGO Science Collaboration

This is an internal working note

of the LIGO Project.

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW22-295 185 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 1970 Mail Stop S9-02 Richland, WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

http://www.ligo.caltech.edu/

Table of Contents

1	Introduction	12

1.1	Purpose	12

1.2	Scope	12

1.2.1	Stray Light Control	12

1.3	Definitions	14

1.4	Acronyms	14

1.5	Applicable Documents	15

1.5.1	LIGO Documents	15

1.5.2	Non-LIGO Documents	16

2	Catalog of SLC Design Requirements	17

3	Stray Light Control Conceptual Design Characteristics	18

3.1	COC Wedge Angle Determination	18

3.1.1	Beam Profile in Recycling Cavity	18

3.1.2	Wedge Angles for Unfolded IFO	18

3.1.2.1	BS Wedge Angle	18

3.1.2.2	ITM Wedge Angle	19

3.1.2.3	CP Wedge Angle	19

3.1.2.4	Stay Clear Diameter	20

3.1.2.5	PRM and SRM Wedge Angle	23

3.1.2.6	PR2 and SR2 Wedge Angle	23

3.1.2.7	PR3 and SR3 Wedge Angle	25

3.1.2.8	ETM Wedge Angle	27

3.1.2.9	ETM Reaction Mass Wedge Angle	27

3.1.2.10	COC Wedge Angle Summary, Non-folded IFO	27

3.1.3	Wedge Angles for Folded IFO	27

3.1.3.1	COC Wedge Angle Summary, Folded IFO	28

3.2	Stray Light Control Performance Characteristics	28

3.2.1	Scattered Light Sources	28

3.2.2	Summary of Scattered Light Displacement Noise	31

3.2.3	Output Faraday Isolator	32

3.2.3.1	Faraday Isolator Forward Transmissivity	33

3.2.3.2	Faraday Isolator Reverse Transmissivity	33

3.2.3.3	BRDF of Faraday Surfaces	33

3.2.3.4	Output Faraday Isolator Suspension	33

3.2.3.5	Scattered Light Displacement Noise of Suspended Output Faraday Isolator	35

3.2.3.6	Stay Clear Diameter	35

3.2.4	Arm Cavity Baffle	36

3.2.4.1	Incident Power on Arm Cavity Baffle	36

3.2.4.2	Arm Cavity Baffle Motion	37

3.2.4.2.1	HEPI Displacement	37

3.2.4.2.2	Minimum Arm Cavity Baffle Motion Requirements	38

3.2.4.2.3	Arm Cavity Baffle Suspension Transfer Functions	38

3.2.4.3	Arm Cavity Baffle Surface BRDF	40

3.2.4.4	Arm Cavity Baffle Reflectivity	42

3.2.4.5	Seismic Motion of the Vacuum Manifold	42

3.2.4.6	Scattered Light Displacement Noise of Suspended Arm Cavity Baffle	43

3.2.4.7	Fringe Wrapping of Arm Cavity Baffle Displacement Noise	44

3.2.4.8	Stay Clear Diameter	44

3.2.5	Cryopump Baffle	45

3.2.5.1	Cryopump Blocking	46

3.2.5.2	Cryopump Baffle Suspension	46

3.2.5.3	Cryopump Baffle Motion Requirements	47

3.2.5.4	Cryopump Baffle Surface BRDF	48

3.2.5.5	Cryopump Baffle Reflectivity	48

3.2.5.6	Seismic Motion of the Cryopump Scattering Surfaces	49

3.2.5.7	Scattered Light Displacement Noise of Suspended Cryopump Baffle	49

3.2.5.8	Fringe-wrapping of Cryopump Baffle Displacement Noise	49

3.2.5.9	Stay Clear Zone	50

3.2.6	Elliptical Baffle	51

3.2.6.1	ITM Elliptical Baffle	51

3.2.6.1.1	ITM Elliptical Baffle Seismic Attenuation	51

3.2.6.1.2	Elliptical Baffle Surface BRDF	52

3.2.6.1.3	ITM Elliptical Baffle Reflectivity	52

3.2.6.1.4	Seismic Motion of the Vacuum Chamber	53

3.2.6.1.5	Scattered Light Displacement Noise of Suspended Elliptical Baffle	53

3.2.6.1.6	Stay Clear Diameter	54

3.2.6.2	PRM Elliptical Baffle	54

3.2.6.2.1	Motion of PRM Elliptical Baffle	54

3.2.6.2.2	Power Hitting the PRM Elliptical Baffle from IO Side	55

3.2.6.2.3	PRM Elliptical Baffle Surface BRDF	56

3.2.6.2.4	PRM Elliptical Baffle Reflectivity	56

3.2.6.2.5	Scattered Light Displacement Noise of PRM Elliptical Baffle	56

3.2.6.2.6	Stay Clear Diameter	56

3.2.7	Wide Angle Scatter from COC	56

3.2.7.1	Manifold Baffle	57

3.2.7.1.1	Seismic Motion of Manifold Baffle	57

3.2.7.2	Manifold Wall	57

3.2.7.2.1	Seismic Motion of Manifold Wall	57

3.2.7.3	Back of Arm Cavity Baffle and Cylinder	57

3.2.7.4	BSC Chamber Wall	57

3.2.7.4.1	Summary Scattered Light Displacement Noise of Wide-angle COC Scattering	57

3.2.8	Output Window	60

3.2.8.1	Output Window BRDF	62

3.2.8.2	Seismic Motion of the Output Windows	62

3.2.8.3	Scattered Light Displacement Noise of Output Window	62

3.2.8.4	Reflected Light from Septum Window	63

3.2.8.5	Output Septum Windows Removal	64

3.2.8.5.1	Stay Clear Diameter	64

3.2.9	Hartmann Viewports	64

3.2.9.1	Hartmann Viewport BRDF	65

3.2.9.2	Reflected Light from Hartmann Viewport	66

3.2.9.2.1	Scattered Light Displacement Noise of Ghost Beams	66

3.2.10	ITM GBAR1, GBAR3, and GBAR4 Ghost Beams	66

3.2.10.1	PR2 Cavity Beam Dump BRDF	66

3.2.10.2	PR2 Cavity Beam Dump Reflectivity	66

3.2.10.3	Scattered Light Displacement Noise of Ghost Beams	66

3.2.11	ITM HR, BS AR, AND BS HR Ghost Beams	67

3.2.11.1	Beam Tube Baffle BRDF and Reflectivity	67

3.2.11.2	Scattered Light Displacement Noise of Ghost Beams	67

3.2.12	BS GBHR3P, BS GBHR	69

3.2.12.1	Scattered Light Displacement Noise of Ghost Beams	69

3.2.13	ITMX PO Beam (BS GBAR1)	70

3.2.14	PRM Ghost Beams	70

3.2.14.1	PRM GBAR1	70

3.2.14.2	PRM GBAR3	71

3.2.14.3	PRM GBHR3	71

3.2.14.4	PRM Plate Beam Dump Surface BRDF and Reflectivity	71

3.2.14.5	Scattered Light Displacement Noise of Ghost Beams	71

3.2.15	PR2 Ghost Beams	71

3.2.15.1	PR2 GBAR0t	71

3.2.15.2	PR2 GBAR0t Cavity Beam Dump Surface BRDF and Reflectivity	71

3.2.15.3	BS PO Beam (PR2 GBARt)	71

3.2.15.4	PR2 GBAR3	72

3.2.15.5	PR2 GBHR3	72

3.2.15.6	PR2 Plate Beam Dump Surface BRDF and Reflectivity	73

3.2.15.7	Scattered Light Displacement Noise of Ghost Beams	73

3.2.16	PR3 Ghost Beams	73

3.2.16.1	PR3 GBAR0t	73

3.2.16.2	PR3 GBAR3	73

3.2.16.3	PR3 GBHR3	73

3.2.16.4	PR3 Plate Beam Dump Surface BRDF and Reflectivity	74

3.2.16.5	Scattered Light Displacement Noise of Ghost Beams	74

3.2.17	SRM Ghost Beams	74

3.2.17.1	SRM GBAR3	74

3.2.17.2	SRM GBHR3	74

3.2.17.3	SRM Plate Beam Dump Surface BRDF and Reflectivity	74

3.2.17.4	Scattered Light Displacement Noise of Ghost Beams	74

3.2.18	SR2 Ghost Beams	74

3.2.18.1	SR2 GBAR0t	74

3.2.18.2	SR2 GBAR3	75

3.2.18.3	SR2 GBHR3	76

3.2.18.4	SR2 Plate Beam Dump Surface BRDF and Reflectivity	76

3.2.18.5	Scattered Light Displacement Noise of Ghost Beams	76

3.2.19	SR3 Ghost Beams	76

3.2.19.1	SR3 GBAR0t	76

3.2.19.2	SR3 GBAR3	76

3.2.19.3	SR3 GBHR3	76

3.2.19.4	SR3 Plate Beam Dump Surface BRDF and Reflectivity	77

3.2.19.5	Scattered Light Displacement Noise of Ghost Beams	77

3.2.20	ETM Telescope Baffle	77

3.2.20.1	ETM Telescope Baffle Motion Requirements	78

3.2.20.2	ETM Telescope Baffle Surface BRDF	78

3.2.20.3	ETM Telescope Baffle Reflectivity	79

3.2.20.4	Seismic Motion of the ETM Telescope Baffle Scattering Surfaces	79

3.2.20.5	Scattered Light Displacement Noise of Suspended ETM Telescope Baffle	79

3.3	Stray Light Control Physical Characteristics	80

3.3.1	Faraday Isolator	80

3.3.2	Arm Cavity Baffle	80

3.3.3	Elliptical Baffle	81

3.3.3.1	ITM Elliptical Baffle	81

3.3.3.2	PRM Elliptical Baffle	81

3.3.4	Manifold Baffle	82

3.3.5	Brewster’s Window	82

3.3.6	OMMT	83

3.3.7	ITMX, ITMY, and BS Beam Dump	83

3.3.8	IO Baffle	84

3.3.9	Cryopump Baffle	84

3.3.10	ETM Telescope Baffle	84

3.4	Stray Light Control Interface Definitions	85

3.4.1	Interfaces to other LIGO detector subsystems	85

3.4.1.1	Mechanical Interfaces	85

3.4.1.2	Electrical Interfaces	85

3.4.1.2.1	Suspended Baffles and Beam Dumps	85

3.4.1.2.2	Faraday Isolator	85

3.4.1.3	Optical Interfaces	85

3.4.1.4	Stay Clear Zone	86

3.4.1.4.1	Arm Cavity Baffle	86

3.4.1.4.2	ITMX, ITMY, and BS Beam Dump	86

3.4.1.4.3	Cryopump Baffle	86

3.4.1.4.4	ETM Telescope Baffle	86

3.4.1.4.5	Elliptical Baffle	86

3.4.1.4.6	IO Baffle	86

3.4.2	Interfaces external to LIGO detector subsystems	86

3.5	Stray Light Control Reliability	86

3.6	Stray Light Control Maintainability	86

3.7	Stray Light Control Environmental Conditions	87

3.7.1.1.1.1	Natural Environment	87

3.7.1.1.1.2	Induced Environment	87

3.8	Stray Light Control Transportability	88

4	Stray Light Control Design and Construction	89

4.1.1.1	Materials and Processes	89

4.1.1.1.1	Materials	89

4.1.1.1.2	Processes	89

4.1.1.1.2.1	Cleaning	89

4.1.1.1.3	Component Naming	89

4.1.1.2	Stray Light Control Workmanship	89

4.1.1.3	Stray Light Control Interchangeability	89

4.1.1.4	Stray Light Control Safety	90

4.1.1.5	Stray Light Control Human Engineering	90

4.1.2	Stray Light Control Assembly and Maintenance	90

4.1.3	Stray Light Control Documentation	90

4.1.3.1	Stray Light Control Specifications	90

4.1.3.2	Stray Light Control Design Documents	90

4.1.3.3	Stray Light Control Engineering Drawings and Associated Lists	90

4.1.3.4	Stray Light Control Technical Manuals and Procedures	91

4.1.3.4.1	Procedures	91

4.1.3.5	Stray Light Control Documentation Numbering	91

4.1.3.6	Stray Light Control Test Plans and Procedures	91

4.1.4	Stray Light Control Logistics	91

4.1.5	Stray Light Control Precedence	91

4.1.6	Stray Light Control Qualification	91

5	Quality Assurance Provisions	92

5.1	General	92

5.1.1	Responsibility for Tests	92

5.1.2	Special Tests	92

5.1.2.1	Engineering Tests	92

5.1.2.2	Reliability Testing	92

5.1.3	Configuration Management	92

5.2	Quality conformance inspections	92

5.2.1	Inspections	92

5.2.2	Demonstration	92

5.2.3	Test	93

6	Preparation for Delivery	94

6.1	Preparation	94

6.2	Packaging	94

6.3	Marking	94

7	Appendix A—Scattered Light Noise Theory	95

7.1.1	Scattered Light Noise Theory	Error! Bookmark not defined.

7.1.1.1	Scattered Light Requirement	95

7.1.1.2	Scattered Power into the IFO	96

7.1.1.2.1	Output Faraday Isolator Scatter	97

7.1.1.2.2	Arm Cavity Baffle Surface Scatter	97

7.1.1.2.3	Arm Cavity Baffle Reflected Light	98

7.1.1.2.4	ITM Elliptical Baffle Surface Scatter	99

7.1.1.2.5	ITM Elliptical Baffle Reflected Light	101

7.1.1.2.6	PRM Elliptical Baffle	101

7.1.1.2.7	ITM (ETM) Wide-Angle Scatter	103

7.1.1.2.7.1	Scattering from the Back of Arm Cavity Baffle	103

7.1.1.2.7.2	Scattering from the Cylindrical Baffle	104

7.1.1.2.7.3	Total Scattered Light Displacement Noise from Arm Cavity Baffle and Cylindrical Baffle.	105

7.1.1.2.7.4	Scattering from the Manifold  Baffle	105

7.1.1.2.7.5	Scatter from ITM Manifold Wall	106

7.1.1.2.7.6	Scattering from BSC Chamber Walls	106

7.1.1.2.7.7	Total Wide-Angle Scattered Light Displacement Noise from BSC Chamber, Manifold Walls, and Manifold Baffle	107

7.1.1.2.8	Septum Window Scatter	107

7.1.1.2.8.1	AS Septum Window	107

7.1.1.2.8.2	AS Septum Window Reflection	108

7.1.1.2.8.3	ITMX PO Septum Window	108

7.1.1.2.8.4	ITMX PO Septum Window Reflection	108

7.1.1.2.8.5	RC PO Septum Window	109

7.1.1.2.8.6	RC PO Septum Window Reflection	109

7.1.1.2.9	ITMY Hartmann Beam	110

7.1.1.2.10	ITMX Hartmann Beam	110

7.1.1.2.11	Cavity Beam Dumps	111

7.1.1.2.11.1	Un-dumped Cavity Beam Dump Beam	Error! Bookmark not defined.

7.1.1.2.11.2	ITMYAR1	112

7.1.1.2.11.3	ITMAR3	112

7.1.1.2.11.4	ITMHR3	113

7.1.1.2.11.5	BSAR1	Error! Bookmark not defined.

7.1.1.2.11.6	BSAR3X	114

7.1.1.2.11.7	BSAR3P	114

7.1.1.2.11.8	BSHR3P	114

7.1.1.2.11.9	ITMAR4	115

7.1.1.2.11.10	ITMHR4	115

7.1.1.2.11.11	BSAR4X	115

7.1.1.2.11.12	Cryopump Baffle	115

7.1.1.2.11.13	ETM Telescope Baffle	116

7.1.1.2.12	Fringe-Wrapping	117

7.1.1.2.12.1	Damped Pendulum Example	119

7.1.1.3	Scattered Light Parameters	120

Table of Tables

Table 1: COC Wedge Angles, Non-folded IFO	27

Table 2: COC Wedge Angles, Folded IFO	28

Table 3: Scattered Light Source, Incident Power and Scattered Power	29

Table 4: Faraday Isolator Characteristics	80

Table 5 : Faraday Isolator Suspension Characteristics	80

Table 6: Arm Cavity Baffle Characteristics	80

Table 7: Arm Cavity Baffle Suspension	81

Table 8: ITM Elliptical Baffle Characteristics	81

Table 9: PRM Elliptical Baffle Characteristics	82

Table 10: Manifold Baffle	82

Table 11: Brewster's Window Characteristics	82

Table 12: OMMT M2 Characteristics	83

Table 13: Cavity Beam Dump Characteristics	83

Table 14: IO Baffle Characteristics	84

Table 15: Cryopump Baffle Characteristics	84

Table 16: ETM Telescope Baffle Characteristics	84

Table 17 Environmental Performance Characteristics	87

Table 18: IFO parameter values used for scattered light calculation	120

Table of Figures

Figure 1: AOS System Block Diagram	13

Figure 2: Output beam and ITMX PO beam hitting SR3 mirror	18

Figure 3: ITMX PO Beam from AR surface of BS, with scraper beam dump in front of SR2	19

Figure 4: Scraper beam dump in front of PR2	20

Figure 5: PR2 Cavity Beam Dump, Beam Clearance	21

Figure 6: SR2 Cavity Beam Dump, Beam Clearance	22

Figure 7: PRM beam dumps	23

Figure 8: SRM beam dumps	24

Figure 9: PR2 Plate Beam Dumps	24

Figure 10: SR2 Plate Beam Dumps	25

Figure 11: PR3 AR beam dump	26

Figure 12: SR3 AR beam dump	26

Figure 13: Scattered Light Displacement Noise, Septum Windows in Place	32

Figure 14: Scattered Light Displacement Noise, Septum Windows Removed	32

Figure 15: Initial LIGO Output Faraday Isolator Parts Suspended in a Modified LOS	34

Figure 16: HAM optics table Seismic Motion Requirement	35

Figure 17: Output Faraday Isolator SUS Amplitude Response	36

Figure 18: Scattered Light Displacement Noise from Suspended Faraday Isolator	37

Figure 19: Suspended Arm Cavity Baffle	38

Figure 20: BSC HEPI Motion Spectrum	39

Figure 21: Arm Cavity Baffle Attenuation, Minimum Requirement	40

Figure 22: Transverse Transfer Function, ACB SUS	41

Figure 23: Yaw Transfer Function, ACB SUS	41

Figure 24: Vertical Transfer Function, ACB SUS	42

Figure 25: Seismic motion of vacuum manifold	43

Figure 26: Arm Cavity Baffle Scattered Light Displacement Noise	44

Figure 27: Arm Cavity Baffle Scattered Light Displacement Noise Caused by Fringe-wrapping	45

Figure 28: Conceptual Model of Suspended Cryopump Baffle	47

Figure 29: Cryopump Suspension Amplitude Response	48

Figure 30: Scattered Light Displacement Noise of Suspended Cryopump Baffle	49

Figure 31: Cryopump Baffle Scattered Light Displacement Noise Caused by Fringe-wrapping	50

Figure 32: Suspended Elliptical Baffle	51

Figure 33: Elliptical Baffle SUS Amplitude Response	52

Figure 34: Seismic motion of BSC chamber	53

Figure 35: PRM Elliptical Baffle on HAM3	54

Figure 36: Elliptical Baffle Scattered Light Displacement Noise	55

Figure 37: Manifold Baffle	58

Figure 38: Arm Cavity Baffle with Cylindrical Baffle.	59

Figure 39:Total wide-Angle COC Scattered Light Displacement Noise	60

Figure 40: AS Septum Window Mount	61

Figure 58: Output Septum Window	62

Figure 41: Displacement Spectrum of HAM 6 Flange	63

Figure 42: Output Window Scattered Light Displacement noise	64

Figure 43: Hartmann Viewports	65

Figure 44: ITM GBAR1, GBAR3, and GBAR4 Beam Dump Scattered Light Displacement Noise	67

Figure 45: ITM GBHR Beam Dump Scattered Light Displacement Noise	68

Figure 46: BS GBARX and GBHRX Scattered Light Displacement Noise	69

Figure 47: BS GBAR3P Beam Dump Scattered Light Displacement Noise	70

Figure 48: ITMX PO Beam	Error! Bookmark not defined.

Figure 49: PR2 GBAR0t beam dump	72

Figure 50: SR2 AR0t beam dump	75

Figure 51: PRM, PR2, PR3, SRM, SR2, SR3, Scattered Light Displacement Noise	77

Figure 52: ETM Telescope Baffle	78

Figure 53: Scattered Light Displacement Noise of ETM Telescope Baffle	79

Figure 54: Scattered Light Noise Transfer Functions	96

Figure 55: ARM CAVITY BAFFLE SCATTER	97

Figure 56: ITM ELLIPTICAL BAFFLE SCATTER AND REFLECTION	99

Figure 57: Wide-angle Scatter from ITM (ETM)	103

Figure 59: Noise Waveform at the Onset of Fringe-Wrapping, λ/8	118

Figure 60: Displacement Noise waveform with Fringe-wrapping, λ/4	119

Figure 61: Scattered Light Displacement Noise Caused by Fringe-wrapping	120

Abstract

This document will present the conceptual design for the AOS Stray Light Control subsystem for ADLIGO.

# Introduction

## Purpose

The purpose of this document is to present a conceptual design that meets the SLC Design requirements. Primary requirements are derived (“flowed-down”) from the LIGO principal science requirements. Secondary requirements, which govern Detector performance through interactions between AOS and other Detector subsystems, have been allocated by Detector Systems Engineering.

## Scope

This document will present conceptual designs for the Stray Light Control (SLC) subsystem of AOS under the following assumptions: 1) the recycling cavity is assumed to be stable; 2) all wedge angles for the core optics components are horizontal.

### Stray Light Control

A block diagram showing the principal scattering sources of the AOS System is shown in Figure 1.

AOS is responsible for controlling and reducing the phase noise due to scattered light injected into the IFO mode to acceptable levels.

AOS is not responsible for scattering that occurs in the IO section, which is defined as everything prior to PRM on HAM2 and HAM8, and everything in the ISC section on HAM6, HAM1, HAM12, and HAM7.

The Stray Light Control subsystem will corroborate with the Systems group on the choice of COC wedge angles for producing PO beams.

The Stray Light Control subsystem will provide an ETM telescope baffle to block the excess light transmitted through the ETM that exceeds the clear aperture of the ETM telescope.

Figure 1: AOS System Block Diagram

## Definitions

## Acronyms

AOS - Auxiliary Optics Support

AR - Antireflection mirror coating

AS - anti-symmetric port signal

ASC - Alignment Sensing and Control

BS - Beam Splitter

BSC - Beam Splitter Chamber

CDS – Computer Data Systems

ETMx, ETMy - End Test Mass in the interferometer ‘X’ or ‘Y’ arm

HAM - Horizontal Access Module

HR – Hi-reflectance mirror coating

IFO - LIGO interferometer

IO - Input Optics

ISC- Interferometer Sensing and Control

ITMx, ITMy - Input Test Mass in the interferometer ‘X’ or ‘Y’ arm

LIGO - Laser Interferometer Gravity Wave Observatory

LSC - Length Sensing and Control

LVEA-vacuum equipment area

mm – millimeter

MMT – mode matching telescope

mrad – milliradian

MTBF – mean time before failure

NA – not applicable

nm – nanometer

OSEM – sensor/actuator head

PO - Pick-off

p-p, peak to peak

ppm - parts per million

PRM – Power Recycling Mirror

p-v, peak to valley

Q – quality factor

QPD – quadrant photo diode

RH – relative humidity

rms - root-mean-square

rtHz – square root Hertz

SLC – Stray Light Control

SOS – Small Optic Suspension

SRD - Science Requirements Document

SRM – Signal Recycling Mirror

SW – Solid Works

TBD - To Be Determined

W - Watt

WFS – wave front sensor

## Applicable Documents

### LIGO Documents

- T980027-00, Baffling Requirements for the 4K and 2K IFO

- Rai Weiss, BRDF data, 9/20/95

- E980131-A, Component Specification, Faraday Isolator, 20 mm

- T060013-02, Inputs to Beam Tube Scattering and Optical Surface Roughness Requirement Analysis for Advanced LIGO (table2)

- E950111-A LIGO Naming Convention

- E960022-B LIGO Vacuum Compatibility, Cleaning Methods and Qualification Procedures

- E990303-03 Seismic Isolation Subsystem Design Requirements Document

- L970061-00-D Guidance for Seismic Component Cleaning, Baking, and Shipping Preparation

- LIGO-T960065-03 Seismic Isolation Design Requirements Document

- M060056-06 Advanced LIGO Reference Design

- M060062-00 HAM Single-stage Isolation Baseline Option Review Report

- M950046-F LIGO Project System Safety Management Plan

- MIL-C-104B

- Robert Schofield (11/17/06 LHO ILOG)

- T010076-01 Optical Layout for Advanced LIGO

- T040126-A Baffle Furnace Bake Procedure

- T060073-00 Transfer Functions of Injected Noise

- T060360-02 PO Mirror Assembly & Telescope, and OMMT Conceptual Design Requirements

- T920004-00 Estimation of Special Optical Properties of a Triangular Ring Cavity

- T960151-02 Large and Small Optics Suspension Electronics Design Requirements

- T980104-00 COS Final Design

- T070003-00 Backscattering from the AS Port: A Comparison of P. Fritschel’s Estimate and

AOS T060263.

- T070061-00 AOS: Stray Light Control (SLC) Design Requirements

- reference Hiro RC beam size calculation

- T080064-00 Controlling Light Scatter in Advanced LIGO

- T070089-02 Wide-angle Scatter from LIGO Arm Cavities

### Non-LIGO Documents

# Catalog of SLC Design Requirements

The requirements for the SLC subsystem are derived in T070061-00 AOS: Stray Light Control (SLC) Design Requirements and are referenced below by paragraph number.

- 4.2 Noise Requirements

- 4.2.1 Direct Requirements

- 4.2.2 Implied Requirement for Scattering Surfaces

- 4.3 Faraday Isolator Requirements

- 4.4 IO Baffle Requirement

- 4.5 Cryopump Baffle Requirement

- 4.6 BSC Chamber Components

- 4.7 Clear Aperture Requirements

- 4.8 Generic Requirements

- 4.8.1 Mechanical Characteristics & Standards

- 4.8.2 Electrical Characteristics & Standards

- 4.8.3 Vacuum Compatibility Requirements

- 4.8.4 Acoustic Requirements

- 4.8.5 Earthquake Requirements

- 4.8.6 Operating Environment

- 4.8.7 Quality Assurance

- 4.8.8 Reliability

- 4.8.9 Maintainability

- 4.8.10 Documentation

- 4.8.11 Transportability

- 4.8.11 Safety

# Stray Light Control Conceptual Design Characteristics

## COC Wedge Angle Determination

The COC wedge angles determine the separation between the main beam in the recycling cavity and the ghost beams that will either be intercepted with a pick-off mirror, or dumped on a beam dump.

### Beam Profile in Recycling Cavity

The Beam cross section within the recycling cavity is non-Gaussian, and is determined in the vertical direction by the clear aperture of the PRM, 245 mm, and in the horizontal direction by the clear aperture of the BS, 370 mm diameter by 60 mm thick, tilted at 45 degrees. The beam profile is approximately an ellipse with the horizontal semi-diameter of 107.1 mm and the vertical semi-diameter of 122.5 mm (reference Hiro RC beam size calculation).

### Wedge Angles for Unfolded IFO

#### BS Wedge Angle

The BS wedge angle of 0.04 deg was chosen to cause the prompt reflection from the AR surface of the beam splitter, BS GBAR1 (ITMX PO beam) to hit the center of the signal recycling telescope mirror SR3. See Figure 2.

Figure 2: Output beam and ITMX PO beam hitting SR3 mirror

With this BS wedge angle, the ITMX PO beam separates from the main beam and passes through a hole in the scraper beam dump in front of SR2 mirror and is picked off with a small diameter mirror, as illustrated in the ZEMAX layout in Figure 3. The main, output beam also passes through a hole in the scraper beam dump and is reflected from SR2 back to SRM on HAM6.

Figure 3: ITMX PO Beam from AR surface of BS, with scraper beam dump in front of SR2

#### ITM Wedge Angle

A minimum wedge angle of 0.08 deg was chosen for the ITM, commensurate with metrology of the AR and HR surfaces. With this small wedge angle, the ghost beams from the ITM enter the power recycling and the signal recycling telescopes and are caught by the “scraper” beam dumps in front of the PR2 and SR2 mirrors, as shown in Figure 3, and Figure 4.

#### CP Wedge Angle

The CP wedge angle was chosen to be 0.04 deg, the same as the BS wedge angle, in order to minimize the tooling requirements. The ghost beams from the internal reflections of the CP also will fall within the PR and SR telescopes and will be caught by the scraper beam dumps in front of the PR2 and SR2 mirrors.

Figure 4: Scraper beam dump in front of PR2

#### Stay Clear Diameter

The clearance between the main beam and the ITM and BS ghost beams that land on the PR2 scraper cavity beam dump is shown in Figure 5. The minimum spacing between the main beam and the closest ghost beam is approximately 40 mm.

The clearance between the main beam and the ITM and BS ghost beams that land on the SR2 scraper cavity beam dump is shown in Figure 6. The minimum spacing between the main beam and the closest ghost beam is approximately 25 mm.

The beams are in the vicinity of the telescope’s beam waists and the diameters of the beams will be < 1mm.

This meets the requirement 4.7 Clear Aperture Requirements

Figure 5: PR2 Cavity Beam Dump, Beam Clearance

Figure 6: SR2 Cavity Beam Dump, Beam Clearance

#### PRM and SRM Wedge Angle

The PRM and SRM wedge angles will be 2 deg. This ensures that the ghost beams separate far enough from the main beam to be caught in nearby beam dumps, as shown in Figure 7, and Figure 8.

#### PR2 and SR2 Wedge Angle

The PR2 and SR2 wedge angles will be 2 deg. This ensures that the ghost beams will separate far enough from the main beam to be caught in nearby beam dumps, as shown in Figure 9, and Figure 10.

Figure 7: PRM beam dumps

Figure 8: SRM beam dumps

Figure 9: PR2 Plate Beam Dumps

Figure 10: SR2 Plate Beam Dumps

#### PR3 and SR3 Wedge Angle

The PR3 and SR3 wedge angles will be 0.6 deg. The ghost beams from the AR side will be caught in the beam dump adjacent to the AR surface, as shown in Figure 11, and Figure 12.

Figure 11: PR3 AR beam dump

Figure 12: SR3 AR beam dump

The ghost beams from the HR surfaces of PR3 and SR3 will be allowed to hit the beam tube walls

#### ETM Wedge Angle

The ETM wedge will be 0.08 deg, the same as the ITM wedge, to minimize tooling requirements.

#### ETM Reaction Mass Wedge Angle

The ETM reaction mass wedge will be 0.04 deg, the same as the CP wedge, to minimize tooling requirements.

#### COC Wedge Angle Summary, Non-folded IFO

Table 1: COC Wedge Angles, Non-folded IFO

| Mirror | Wedge Angle, deg | Orientation | Direction | Symmetry |
| --- | --- | --- | --- | --- |
| PRM | 2 | horizontal | thin side -Y | symmetric |
| PR2 | 2 | horizontal | thin side -Y | symmetric |
| PR3 | 0.6 | horizontal | thin side -Y | symmetric |
| SRM | 2 | horizontal | thin side +X | symmetric |
| SR2 | 2 | horizontal | thin side +X | symmetric |
| SR3 | 0.6 | horizontal | thin side -X | symmetric |
| BS | 0.04 | horizontal | thin side -Y | symmetric |
| CPX | 0.04 | horizontal | thin side +Y | symmetric |
| CPY | 0.04 | horizontal | thin side +X | symmetric |
| ITMX | 0.08 | horizontal | thin side +Y | AR face perpendicular to substrate cylindrical axis |
| ITMY | 0.08 | horizontal | thin side +X | AR face perpendicular to substrate axis |
| ETMX | 0.08 | horizontal | thin side -Y | AR face perpendicular to substrate axis |
| ETMY | 0.08 | horizontal | thin side +X | AR face perpendicular to substrate axis |
| ReMX | 0.04 | horizontal | thin side +Y | symmetric |
| ReMY | 0.04 | horizontal | thin side -X | symmetric |

### Wedge Angles for Folded IFO

The wedge angles for the folded IFO are exactly the same as the non-folded IFO.

In addition, the FM wedge angles will be 0.04 deg, the same as the BS, to minimize tooling requirements.

#### COC Wedge Angle Summary, Folded IFO

Table 2: COC Wedge Angles, Folded IFO

| Mirror | Wedge Angle, deg | Orientation | Direction | Symmetry |
| --- | --- | --- | --- | --- |
| PRM | 2 | horizontal | thin side -Y | symmetric |
| PR2 | 2 | horizontal | thin side +Y | symmetric |
| PR3 | 0.6 | horizontal | thin side +Y | symmetric |
| SRM | 2 | horizontal | thin side +X | symmetric |
| SR2 | 2 | horizontal | thin side -X | symmetric |
| SR3 | 0.6 | horizontal | thin side +X | symmetric |
| BS | 0.04 | horizontal | thin side +Y | symmetric |
| CPX | 0.04 | horizontal | thin side -Y | symmetric |
| CPY | 0.04 | horizontal | thin side -X | symmetric |
| ITMX | 0.08 | horizontal | thin side -Y | AR face perpendicular to substrate cylindrical axis |
| ITMY | 0.08 | horizontal | thin side -X | AR face perpendicular to substrate cylindrical axis |
| ETMX | 0.08 | horizontal | thin side -Y | AR face perpendicular to substrate cylindrical axis |
| ETMY | 0.08 | horizontal | thin side +X | AR face perpendicular to substrate cylindrical axis |
| ReMX | 0.04 | horizontal | thin side +Y | symmetric |
| ReMY | 0.04 | horizontal | thin side -X | symmetric |
| FMX | 0.04 | horizontal | thin side -Y | symmetric |
| FMY | 0.04 | horizontal | thin side -Y | symmetric |

## Stray Light Control Performance Characteristics

### Scattered Light Sources

The AOS scattered light sources that contribute to the total scattered light displacement noise are listed in Table 1, together with the incident power and the scattered power. The AOS scattered light displacement noise requirement was taken to be 1/14 of the ADLIGO Science Requirement, which is 50% of the total scattered light displacement noise budget.

Table 3: Scattered Light Source, Incident Power and Scattered Power

| SCATTERING SOURCE | INCIDENT POWER, W | SCATTERED POWER, W |
| --- | --- | --- |
| Faraday | 1.35E-01 | 2.71E-11 |
| AC_Baffle | 7.33E+00 | 7.07E-18 |
| AC_Baffle_Refl | 1.76E-04 | 8.14E-26 |
| AS_Window | 1.35E-01 | 2.20E-17 |
| AS_Window_Refl | 3.38E-04 | 6.88E-19 |
| ITMX_PO_Window | 5.27E-02 | 4.30E-19 |
| RC_PO_Window | 1.35E-05 | 2.20E-22 |
| Cryo_Baffle | 2.77E+00 | 2.67E-18 |
| Cryo_Baffle_Refl | 6.64E-05 | 3.07E-26 |
| ITM_GBAR1_BD | 5.27E-02 | 1.52E-15 |
| ITM_GBAR1_BD_Refl | 1.26E-06 | 1.75E-23 |
| ITM_GBAR3_BD | 5.21E-02 | 1.49E-15 |
| ITM_GBAR3_BD_Refl | 1.25E-06 | 1.71E-23 |
| ITM_GBAR4_BD | 2.59E-06 | 3.68E-24 |
| ITM_GBHR3_ARMBAF | 2.62E-04 | 1.25E-21 |
| ITM_GBHR4_ARMBAF | 1.30E-08 | 3.10E-30 |
| BS_GBAR3X_ARMBAF | 1.32E-04 | 1.12E-22 |
| BS_GBAR4X_ARMBAF | 3.29E-09 | 6.99E-32 |
| BS_GBHR3X_ARMBAF | 1.32E-04 | 1.12E-22 |
| BS_GBHR4X_ARMBAF | 3.29E-09 | 6.99E-32 |
| BS_GBAR3P_BD | 2.63E-02 | 2.68E-16 |
| BS_GBAR3P_Ref | 6.32E-07 | 3.09E-24 |
| BS_GBHR3P_BD | 2.63E-02 | 2.68E-16 |
| BS_GBHR3P_Refl | 6.32E-07 | 3.09E-24 |
| ITM_Ellip_Baffle | 3.70E-01 | 1.26E-21 |
| ITM_Ellip_Baffle | 8.88E-06 | 1.45E-29 |
| BSC_wide_angle | 4.25E-04 | 0.00E+00 |
| manifold_wide_angle | 8.93E-01 | 0.00E+00 |
| Total_BSC_Manifold_Wide_Angle |  | 8.03E-20 |
| AC_Baffle_wide_angle | 4.67E+00 |  |
| AC_Baf_cyl_wide_angle | 2.84E+00 |  |
| Total_AC_Baf_cyl_Wide_Angle |  | 9.66E-18 |
| PRM_Ellip_Baffle | 2.50E-03 | 1.19E-17 |
| PRM_Ellip_Baffle_Refl | 6.00E-08 | 5.02E-29 |
| ETM_Tel_Baffle | 4.88E-02 | 3.32E-19 |
| ETM_Tel_Baffle_Refl | 3.42E-03 | 3.26E-21 |
| manifold_wide_angle | 8.93E-01 | 8.03E-20 |
| AS_Window_Refl | 3.38E-04 | 6.88E-19 |
| ITMX_PO_Window_Refl | 1.32E-04 | 1.34E-20 |
| RC_PO_Window_Refl | 3.37E-08 | 6.88E-24 |
| ITMY_HARTMANN_BS_TRANS | 1.35E-05 | 5.51E-19 |
| ITMY_HARTMANN_VIEWPORT | 3.37E-08 | 1.38E-27 |
| ITMX_HARTMANN_VIEWPORT | 2.63E-04 | 2.15E-19 |
| ITMX_HARTMANN_VIEWPORT_REFL | 3.29E-07 | 1.32E-23 |
| PRM_GBAR1 | 6.25E-03 | 2.70E-19 |
| PRM_GBAR3 | 1.76E-02 | 5.97E-16 |
| PRM_GBHR3 | 4.71E-03 | 4.30E-17 |
| PRM_Total |  | 1.28E-15 |
| PR2_GB0t | 2.11E-01 | 8.59E-15 |
| PR2_GBAR3 | 1.05E-05 | 2.15E-22 |
| PR2_GBHR3 | 1.05E-09 | 2.15E-30 |
| PR2_Total |  | 1.72E-14 |
| PR3_GB0t | 2.11E-01 | 2.86E-15 |
| PR3_GBAR3 | 1.05E-05 | 7.16E-24 |
| PR3_GBHR3 | 1.05E-09 | 1.43E-31 |
| PR3_GBAR_Total |  | 5.73E-15 |
| PR3_GBHR_Total |  | 2.86E-31 |
| SRM_GBAR3 | 2.59E-07 | 2.03E-21 |
| SRM_GBHR3 | 1.08E-08 | 3.52E-24 |
| SRM_Total | 0.00E+00 | 4.07E-21 |
| SR2_GB0t | 1.35E-05 | 5.51E-19 |
| SR2_GBAR3 | 6.75E-10 | 1.38E-26 |
| SR2_GBHR3 | 6.75E-14 | 1.38E-34 |
| SR2_GBHR3 | 6.75E-14 | 1.38E-34 |
| SR2_Total |  | 1.10E-18 |
| SR3_GB0t | 1.35E-05 | 1.84E-19 |
| SR3_GBAR3 | 6.75E-10 | 4.59E-28 |
| SR3_GBHR3 | 6.75E-14 | 9.18E-36 |
| SR3_GBAR_Total |  | 3.67E-19 |
| SR3_GBHR_Total |  | 1.84E-35 |

### Summary of Scattered Light Displacement Noise

A summary of the scattered light displacement noise with all the AOS noise sources mitigated, except for the Septum Window noise is shown in Figure 13. The Scattered Light Noise exceeds the SRD requirement at approximately 26 Hz.

Removing the Septum Window meets the Scattered Light Noise Requirement, 4.2.1 Direct Requirements, at all frequencies, as shown in Figure 14.

Figure 13: Scattered Light Displacement Noise, Septum Windows in Place

Figure 14: Scattered Light Displacement Noise, Septum Windows Removed

### Output Faraday Isolator

The Faraday Isolators that were used for Initial LIGO will be re-used for ADLIGO with a modification to preserve the in-line beam direction and to allow provision for injecting an external beam into the AS port of the IFO.

The scattered light model indicates that the Output Faraday Isolator must be suspended in order to reduce the scattered light noise from the optical surfaces. The optical surfaces are all in a vertical plane, therefore no motion isolation is required in the vertical direction. A conceptual drawing of the modified Faraday Isolator suspended with a modified LOS structure is shown in Figure 15.

The pitch and yaw pointing angles of the Output Faraday Isolator will be pre-set during initial alignment. A remotely controlled Picomotor will provide a small amount of pitch motion to avoid a possible glint from the optical surfaces of the Faraday Isolator into the AS port of the IFO.

#### Faraday Isolator Forward Transmissivity

The measured transmissivity of the Initial LIGO Output Faraday Isolator is 98%.

This meets the requirement 4.3 Faraday Isolator Requirements.

#### Faraday Isolator Reverse Transmissivity

The measured reverse power transmission of the Initial LIGO Output Faraday Isolator is < 0.0001.

This meets the requirement 4.3 Faraday Isolator Requirements.

#### BRDF of Faraday Surfaces

The Output Faraday Isolator has four calcite prism surfaces and one TGG crystal surface on the entrance side. These surfaces will scatter light back toward the antisymmetric port of the IFO. The light scattered by the additional surfaces beyond the Faraday rotator magnet will be attenuated by the reverse transmissivity of the Faraday Isolator and will be ignored.

The BRDF of the TGG surface was estimated using the fractal back-scattering model proposed by R. Weiss; see T920004-00 Estimation of Special Optical Properties of a Triangular Ring Cavity, for incidence angles between 1E-4 and 1E-1 radians.

where

and S is the total integrated scattering loss of the surface.

Assuming an incidence angle on the Faraday Isolator surfaces of 1.7E-2 rad (1 deg) and a total scattering loss per surface of 100 ppm, the estimated BRDF is 5E-4 sr-1.

It was assumed that the calcite prisms have a similar BRDF, and that the scattered light noise injected into the IFO will add in phase.

#### Output Faraday Isolator Suspension

The Output Faraday Isolator will be suspended by a modified LOS as shown in Figure 15. The length of the pendulum is estimated to be 0.4 m. Damping elements will provide damping to reduce the Q < 1000.

The suspension frame will be mounted to the HAM optical table, with the motion requirement shown in Figure 16.

Figure 15: Initial LIGO Output Faraday Isolator Parts Suspended in a Modified LOS

Figure 16: HAM optics table Seismic Motion Requirement

The minimum Output Faraday Isolator motion attenuation requirements were determined using the scattered light model, assuming five surfaces with BRDF of 5E-4 sr-1, and are shown in Figure 17, together with a calculated simple pendulum transfer function.

#### Scattered Light Displacement Noise of Suspended Output Faraday Isolator

The scattered light displacement noise caused by the suspended Output Faraday Isolator is shown in Figure 18.

#### Stay Clear Diameter

The clear aperture of the Faraday Isolator is 20 mm diameter. The AS Gaussian beam diameter at the output of the SRM is approximately 4 mm. The clear aperture of the Faraday Isolator will be pre-aligned within 2 mm of the beam centerline by referencing its position to the center of the ITM.

This meets the requirement 4.7 Clear Aperture Requirements

Figure 17: Output Faraday Isolator SUS Amplitude Response

### Arm Cavity Baffle

#### Incident Power on Arm Cavity Baffle

The power scattered from the far COC mirror, at the opposite end of the arm cavity, into the annular region bounded by the outer radius of the near COC and the inside radius of the Cryopump Baffle will be incident on the Arm Cavity Baffle. It is given by

The Initial LIGO pathfinder COC CSIRO, surface 2, S/N 2 was used to estimate the BRDF.

Figure 18: Scattered Light Displacement Noise from Suspended Faraday Isolator

Where θitm  is				4.25 E-5 rad

θcp  is 					9.612 E-5 rad

and, Pa  is the arm power		8.339 E5 W

Pacb  = 	7.4 W

#### Arm Cavity Baffle Motion

##### HEPI Displacement

The Arm Cavity Baffle shown in Figure 19 will be suspended with a single pendulum from Stage “0” HEPI support ring of the BSC optical table adjacent to the HR side of the ITM and ETM. Earthquake stops will be mounted to the BSC vacuum enclosure.

Figure 19: Suspended Arm Cavity Baffle

We will assume that the x-displacement spectrum of the BSC HEPI isolation system is described by Brian Lantz in the SEI elog entry ID: 596, 3/14/06, as shown in Figure 20.

##### Minimum Arm Cavity Baffle Motion Requirements

With an assumed BRDF of 0.005 sr^-1, the scattered light model indicates that the Arm Cavity Baffle requires 0.05 motion attenuation at frequencies > 10 Hz, as shown in Figure 21.

##### Arm Cavity Baffle Suspension Transfer Functions

The pitch, roll, and yaw resonances of the two-wire Arm Cavity Baffle suspension were estimated using a Matlab model developed by the SUS group, and are all around 1 Hz, as shown in Figure 22, Figure 23, and Figure 24. With these transfer functions, the relative motion will be attenuated by a factor >10 for frequencies > 10 Hz, and will exceed the requirement.

Figure 20: BSC HEPI Motion Spectrum

The hole in the Arm Cavity Baffle for the IFO beam extends in the longitudinal direction because of the tilt angle of the vertical baffle surfaces. The scattering surfaces of the exposed, rough edges of the baffle hole will exhibit a longitudinal motion due to coupling from the vertical motion. The average vertical-to-horizontal coupling factor is estimated to be 0.6.

Vertical springs will attach to the suspension wires to provide a vertical resonance around 1 Hz, shown by the green curves in the figures, which will reduce the vertical motion by a factor >10 and the coupled-longitudinal motion by a factor >17 @ frequencies > 10Hz.

Figure 21: Arm Cavity Baffle Attenuation, Minimum Requirement

#### Arm Cavity Baffle Surface BRDF

The Arm Cavity Baffle will be constructed of porcelainized steel with the first surface inclined at an incidence angle 56 deg and is estimated to have a BRDF < 0.005 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

Figure 22: Transverse Transfer Function, ACB SUS

Figure 23: Yaw Transfer Function, ACB SUS

Figure 24: Vertical Transfer Function, ACB SUS

#### Arm Cavity Baffle Reflectivity

The light that is not absorbed by the Arm Cavity Baffle will reflect from the baffle surface onto the inside walls of the vacuum manifold, where it will scatter from the manifold, reflect again from the Arm Cavity Baffle, and enter the IFO mode at the far COC.

The scattered light model was used to calculate the requirement for the reflectivity of the Arm Cavity Baffle. Assuming a BRDF of the vacuum manifold wall of 0.025 at an incidence angle of 40 deg, the reflectivity of the Arm Cavity Baffle must is < 1%.

The reflectivity of the Arm Cavity Baffle with four internal bounces is estimated to be 2.4 E-5.

#### Seismic Motion of the Vacuum Manifold

The light that reflects from the Arm Cavity Baffle will scatter from the vacuum manifold, which has the seismic motion shown in Figure 25. See Robert Schofield (11/17/06 LHO ILOG).

Figure 25: Seismic motion of vacuum manifold

#### Scattered Light Displacement Noise of Suspended Arm Cavity Baffle

The light that scatters directly from the surface of the suspended Arm Cavity Baffle has a phase noise caused by the seismic motion of the HEPI support structure attenuated by the transfer function of the Arm Cavity Baffle suspension.

The light that reflects from the baffle and subsequently scatters from the vacuum manifold walls will have a phase noise caused by the seismic motion of the walls. The vacuum manifold is assumed to have a BRDF = 0.1 sr^-1

The scattered light noise was calculated using the scattered light model and is shown in Figure 26.

Figure 26: Arm Cavity Baffle Scattered Light Displacement Noise

#### Fringe Wrapping of Arm Cavity Baffle Displacement Noise

The Arm Cavity Baffle has a vertical bounce resonance at approximately 2.3 Hz. The displacement noise at the odd harmonics of the motion due to fringe wrapping was calculated using the fringe wrap model, see Fringe-Wrapping in Appendix A—Scattered Light Noise Theory, assuming a simple pendulum function with a Q = 1000 at the resonant frequency. The fringe wrapping does not cause excessive noise above 10 Hz, as shown in Figure 27.

#### Stay Clear Diameter

The clear aperture of the Arm Cavity Baffle is 346 mm diameter, which is larger than the diameter of the ITM and ETM COC. The clear aperture will be pre-aligned by referencing its position to the center of the HR surface of the COC in the quad suspension frame within 4 mm.

This meets the requirement 4.7 Clear Aperture Requirements.

Figure 27: Arm Cavity Baffle Scattered Light Displacement Noise Caused by Fringe-wrapping

### Cryopump Baffle

A concept for the suspended Cryopump Baffle is shown in Figure 28. It is a single pendulum suspended by springs from the circular, spool piece support ring. Eddy-current or elastomeric damping will be used to damp the pitch, yaw, and vertical motion.

The power scattered from the far COC at the opposite end of the arm cavity into the annular region bounded by the inner radius of the Cryopump Baffle and the beam tube radius is incident on the Cryopump Baffle. The incident power is given by

The Initial LIGO pathfinder COC CSIRO, surface 2, S/N 2 was used to estimate the BRDF.

Where θcp  is				9.612 E-5 rad

θbt  is 					1.327 E-4 rad

and, Pa  is the arm power		8.339 E5 W

Pcp  = 	 2.8 W

#### Cryopump Blocking

The Cryopump Baffle will be placed inside the spool pieces closest to the cryopumps on the ITM side of the arms and the ETM side of the arms. It obscures the interior surfaces of the cryopump from the line of sight as viewed from the ITM and ETM HR surfaces and avoids backscattered light from the surfaces of the cryopump impinging on the ITM and ETM HR surfaces.

This meets the requirements: 4.5 Cryopump Baffle Requirement, and 4.7 Clear Aperture Requirements.

#### Cryopump Baffle Suspension

The Cryopump Baffle consists of a cylinder, a cone, and an annular baffle plate, which are suspended from a single pendulum as shown in Figure 28.

The narrow angle scattered light from the far COC at the opposite end of the beam tube floods into the clear annular region between the shark’s-tooth beam tube baffles and the cryopump baffle cylinder, from the right side in this picture. This light gets trapped by multiple reflections between the cylinder the cone and the annular plate with the viewport holes.

Figure 28: Conceptual Model of Suspended Cryopump Baffle

#### Cryopump Baffle Motion Requirements

Assuming a BRDF of 0.01 sr-1, the minimum Cryopump Baffle motion attenuation requirements were determined using the scattered light model, and are shown in Figure 29. The actual pendulum response function will exceed the requirements.

Figure 29: Cryopump Suspension Amplitude Response

#### Cryopump Baffle Surface BRDF

The Cryopump Baffle will be constructed of porcelainized steel with the first surface inclined at an incidence angle 56 deg and is estimated to have a BRDF < 0.005 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

#### Cryopump Baffle Reflectivity

The light that is not absorbed by the Cryopump Baffle will reflect from the baffle surface onto the insides of the spool piece. There, it will scatter, reflect again from the Cryopump Baffle, and enter the IFO mode at the far COC.

The scattered light model was used to calculate the requirement for the reflectivity of the Cryopump Baffle. Assuming a BRDF of the spool piece wall of 0.1, the reflectivity of the Cryopump Baffle must is < 0.01.

The reflectivity of the Cryopump Baffle is estimated to be 2.4E-5.

#### Seismic Motion of the Cryopump Scattering Surfaces

The surface of the suspended Cryopump Baffle has the seismic motion of the spool piece attenuated by the transfer function of the Cryopump Baffle suspension.

The light that reflects from the Cryopump Baffle will scatter from the spool piece wall, which has the seismic motion shown in Figure 25.

#### Scattered Light Displacement Noise of Suspended Cryopump Baffle

The scattered light displacement noise from the Cryopump Baffle is shown in Figure 30.

Figure 30: Scattered Light Displacement Noise of Suspended Cryopump Baffle

#### Fringe-wrapping of Cryopump Baffle Displacement Noise

The Cryopump Baffle has a pendulum resonance at approximately 0.8 Hz. The displacement noise at the odd harmonics of the motion due to fringe wrapping was calculated using the fringe wrap model, assuming a simple pendulum function with a Q = 1000 at the resonant frequency. The fringe wrapping does not cause excessive noise above 10 Hz, as shown in Figure 31.

Figure 31: Cryopump Baffle Scattered Light Displacement Noise Caused by Fringe-wrapping

#### Stay Clear Zone

The clear aperture diameter of the Cryopump Baffle, 769 mm, is large enough to allow the folded and non-folded IFO beams of 315.4 mm diameter at the 1 ppm diameter to pass through without vignetting. The fractional geometric power loss of a w = 60 mm beam passing once through the Cryopump Baffle is 1.4E-8. With a 4 mm decentering of the baffle, the loss increases to 4E-8. This is negligible compared to the transmission loss through the ETM mirror.

This meets the requirement 4.7 Clear Aperture Requirements.

### Elliptical Baffle

#### ITM Elliptical Baffle

A conceptual drawing of the suspended ITM Elliptical Baffle is shown in Figure 32.

The Cryopump Baffle will be constructed of porcelainized steel with the cone surface inclined at an incidence angle of 56 deg; and therefore, is estimated to have a BRDF < 0.005 sr-1.

##### ITM Elliptical Baffle Seismic Attenuation

The ITM elliptical baffle will be suspended with a single pendulum from the HEPI support ring adjacent to the AR side of the ITM. Earthquake stops will be mounted to the chamber walls.

The required motion attenuation of the Elliptical Baffle is shown in Figure 33.

Figure 32: Suspended Elliptical Baffle

Figure 33: Elliptical Baffle SUS Amplitude Response

##### Elliptical Baffle Surface BRDF

The Elliptical Baffle will be constructed of porcelainized steel with the first surface inclined at an incidence angle 56 deg and is estimated to have a BRDF < 0.005 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

##### ITM Elliptical Baffle Reflectivity

The light that is not absorbed by the ITM Elliptical Baffle will reflect from the baffle surface onto the insides of the vacuum chamber. There, it will scatter from the wall, reflect again from the ITM Elliptical Baffle, and enter the IFO mode at the far COC.

The scattered light model determined that the reflectivity of the ITM Elliptical Baffle must be < 0.001.

The multi-bounce reflectivity of the Cryopump Baffle is estimated to be 2.4E-5.

##### Seismic Motion of the Vacuum Chamber

The seismic motion of the vacuum chamber is shown in Figure 34. See Robert Schofield (11/17/06 LHO ILOG).

##### Scattered Light Displacement Noise of Suspended Elliptical Baffle

The light that scatters directly from the surface of the suspended Elliptical Baffle has a phase noise caused by the seismic motion of the HEPI support ring attenuated by the transfer function of the Elliptical Baffle suspension, which is shown in Figure 33.

The light that reflects from the baffle and subsequently scatters will have a phase noise caused by the seismic motion of the chamber walls.

The vacuum chamber walls are assumed to have a BRDF = 0.1 sr^-1. The Elliptical Baffle surface BRDF < 0.005 sr^-1.

The scattered light displacement noise is shown in Figure 36.

Figure 34: Seismic motion of BSC chamber

##### Stay Clear Diameter

The clear aperture of the Elliptical Baffle is 218 mm horizontal diameter and 249 mm vertical diameter. This is 2 mm larger on all sides than the limiting aperture that is determined by the vertical clear aperture of the PRM and the horizontal clear aperture of the BS, which define the size and shape of the beam in the recycling cavity. The Elliptical Baffle will be aligned within 2 mm of the beam center.

This meets the requirement 4.7 Clear Aperture Requirements.

#### PRM Elliptical Baffle

The PRM Elliptical Baffle will mount to HAM3, and HAM9 optical tables, as shown in the Zemax layout, Figure 35.

Figure 35: PRM Elliptical Baffle on HAM3

##### Motion of PRM Elliptical Baffle

The seismic motion will be the same as the HAM optical table shown in Figure 16.

Figure 36: Elliptical Baffle Scattered Light Displacement Noise

##### Power Hitting the PRM Elliptical Baffle from IO Side

The irradiance of the IO Gaussian beam incident on the PRM Elliptical Baffle is given by

where P0psl is the total power in the IO beam, and w= 0.060 m is the Gaussian beam radius.

The power passing through the hole in the elliptical baffle is given by

The power that hits the elliptical baffle is given by

With a total power input = 125 W, the power hitting the elliptical baffle is = 0.0044 W.

##### PRM Elliptical Baffle Surface BRDF

The PRM Elliptical Baffle will be constructed of porcelainized steel with the first surface inclined at an incidence angle 56 deg and is estimated to have a BRDF < 0.005 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

##### PRM Elliptical Baffle Reflectivity

The light that is not absorbed by the PRM Elliptical Baffle will reflect from the baffle surface onto the insides of the vacuum chamber. There, it will scatter from the wall, reflect again from the PRM Elliptical Baffle, and enter the recycling cavity mode.

The multi-bounce reflectivity of the PRM Elliptical Baffle is estimated to be 2.4E-5.

##### Scattered Light Displacement Noise of PRM Elliptical Baffle

The prompt PSL light that transmits through the PRM and is scraped off by the periphery of the PRM Elliptical Baffle does not build up within the recycling cavity. It is collected by the PR telescope and hits the PRM mirror at an off-axis location where it is re-scattered into the recycling cavity mode.

The scattered light displacement noise is shown in Figure 36.

##### Stay Clear Diameter

The clear aperture of the PRM Elliptical Baffle is 218 mm horizontal diameter and 249 mm vertical diameter. This is 2 mm larger on all sides than the limiting aperture that is determined by the vertical clear aperture of the PRM and the horizontal clear aperture of the BS, which define the size and shape of the beam in the recycling cavity. The PRM Elliptical Baffle will be aligned within 2 mm of the beam center.

### Wide Angle Scatter from COC

The wide-angle scatter from point defects on the ITM and ETM COC mirrors is assumed to have a Lambertian distribution with total integrated scattered power equal to 10ppm fraction of the circulating power in the arm cavity. Much of this scattered light will be intercepted by the back of the arm cavity baffle and the associated cylinder baffle; some of the light will pass through the beam holes in the Arm Cavity Baffle and hit the manifold wall and viewport flange at the end of the manifold, leading to the cryopump.

#### Manifold Baffle

A manifold baffle, shown in Figure 37, will hide the “corner” and avoid the retro-reflection from the viewport flange surface.

##### Seismic Motion of Manifold Baffle

The Manifold Baffle has the motion spectrum of the manifold, as shown in Figure 25.

A preliminary FEA vibration analysis shows that the first resonance of the Manifold Baffle occurs at approximately 120 Hz. The Q is expected to be <1000, so the motion will be acceptable.

#### Manifold Wall

##### Seismic Motion of Manifold Wall

The motion spectrum of the manifold wall is shown in Figure 25.

#### Back of Arm Cavity Baffle and Cylinder

A conceptual design for the Arm Cavity Baffle and the Cylindrical Baffle is shown positioned next to the folded ITM quad suspension in Figure 38.

#### BSC Chamber Wall

##### Summary Scattered Light Displacement Noise of Wide-angle COC Scattering

The calculated displacement noise spectrum by light scattered into the IFO mode from 1) total BSC and Manifold Wide Angle scattering, and 2) total back of Arm Cavity Baffle and Cylindrical Baffle wide angle scatter is shown in Figure 39.

Figure 37: Manifold Baffle

Figure 38: Arm Cavity Baffle with Cylindrical Baffle.

Figure 39:Total wide-Angle COC Scattered Light Displacement Noise

### Output Window

Septum Windows for the AS beam, the ITMX PO beam, and the RC PO beam will be mounted to the HAM1, HAM6, HAM7, and HAM12 septum plates,, which are mounted to the flange of the HAM chamber, as shown in Figure 40 and Figure 41. The compressible bellows between the Septum Plate assembly and the mounting flange of HAM 6 allows the Brewster’s Windows to be removed without moving any other vacuum enclosures.

In addition, the ITMX and ITMY recycling cavity Hartmann beams will enter and exit the vacuum chamber through vacuum viewports located in HAM4 and HAM10. Part of the AS beam that transmits through the SR2 mirror will leak through the ITMY Hartmann coupling beam splitter , and part of the ITMX PO beam will leak through the ITMX Hartmann coupling beam splitter and will scatter from the Hartmann output windows.

Figure 40: AS Septum Window Mount

Figure 41: Output Septum Window

#### Output Window BRDF

The BRDF of the Output Windows were assumed to be the same as the measured BRDF of a super-polished window, 1E-6 sr^-1, see T080064-00 Controlling Light Scatter in Advanced LIGO.

The incidence angle on the Septum Window is 10 degrees.

#### Seismic Motion of the Output Windows

The Output Windows are mounted directly to the HAM1, HAM4, HAM6, HAM7, HAM10, and HAM12 septum plates and doors, and will have a displacement spectrum similar to the HAM6 flange, as shown in Figure 42. See Robert Schofield (11/17/06 LHO ILOG).

#### Scattered Light Displacement Noise of Output Window

The scattered light displacement noise from the Output Windows is shown in Figure 43. The scattered light noise from the AS beam exceeds the AOS requirement and also the ADLIGO Science requirement.

Figure 42: Displacement Spectrum of HAM 6 Flange

#### Reflected Light from Septum Window

The light that reflects from the two surfaces of the Output Septum window will be caught in the cavity beam dumps mounted on HAM chamber optical tables. The cavity beam dump will be made of black glass with the first surface inclined at an incidence angle 56 deg and is estimated to have a BRDF < 0.005 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

The multi-bounce reflectivity of the cavity beam dump is estimated to be < 2.4E-5.

Figure 43: Output Window Scattered Light Displacement noise

#### Output Septum Windows Removal

The Septum Windows are mounted to nozzle pieces with o-rings and a capture flange, and the nozzle piece is mounted independently to the HAM Plenum. Therefore, the nozzle piece can be removed by venting HAM5, with access from the adjoining vented HAM6 chamber, without removing the septum plate.

When the Septum Windows are removed, the total scattered light displacement noise meets the AOS requirement, as shown in Figure 14.

##### Stay Clear Diameter

The clear aperture of the Output Window is > 60 mm diameter. The AS beam, the ITMX PO beam, and the RC PO beam have Gaussian diameters approximately 4 mm.

This meets the requirement 4.7 Clear Aperture Requirements.

### Hartmann Viewports

The ITMX Hartmann beam is superimposed on the ITMX PO beam with a dichroic beamsplitter that transmits mostly visible light and reflects mostly IR light. However, some of the ITMX PO beam power will transmit through the dichroic beamsplitter and scatter from the ITMX Hartmann Viewport, shown in Figure 44.

Similarly, The ITMY Hartmann beam is superimposed on the beam that leaks through the SR2 HR mirror with a dichroic beamsplitter that transmits mostly visible light and reflects mostly IR light. However, some of the SR2 HR leakage beam power will transmit through the dichroic beamsplitter and scatter from the ITMY Hartmann Viewport

Figure 44: Hartmann Viewports

#### Hartmann Viewport BRDF

The BRDF of the Hartmann Viewport is assumed to be the same as the measured BRDF of a super-polished window, 1E-6 sr^-1, see T080064-00 Controlling Light Scatter in Advanced LIGO.

The incidence angle on the Hartmann Viewport is approximately 10 degrees.

The reflectivity of the Hartmann Viewport is estimated to be<0.025%.

#### Reflected Light from Hartmann Viewport

The light that reflects from the two surfaces of the Hartmann Viewport does not cause excessive displacement noise and will be allowed to hit the walls of the HAM chamber.

##### Scattered Light Displacement Noise of Ghost Beams

The scattered light displacement noise from the Hartmann Viewports is shown in Figure 43.

### ITM GBAR1, GBAR3, and GBAR4 Ghost Beams

The ITM GBAR1, GBAR3, and GBAR4 Ghost Beams are collected by the PR and SR telescopes and will be caught in the scraper cavity beam dumps mounted to the HAM optical table in front of PR2, and SR2 mirrors as shown in Figure 5, and Figure 6.

Some of the ghost beam light will reflect from the cavity beam dumps and scatter from the IO and Out tube walls, retracing their paths into the recycling cavity beam.

#### PR2 Cavity Beam Dump BRDF

The PR2 Cavity Beam Dump will be constructed of porcelainized steel with the first surface inclined at an incidence angle 56 deg with an estimated BRDF < 0.005 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

#### PR2 Cavity Beam Dump Reflectivity

The light that is not absorbed by the PR2 Cavity Beam Dump will reflect from the beam dump surface onto the insides of the manifold. There, it will scatter from the wall, reflect again from the PR2 Cavity Beam Dump, and enter the recycling cavity mode.

The multi-bounce reflectivity of the PRM Elliptical Baffle is estimated to be 2.4E-5.

#### Scattered Light Displacement Noise of Ghost Beams

The scattered light displacement noise from the ITM AR ghost beams is shown in Figure 45.

Figure 45: ITM GBAR1, GBAR3, and GBAR4 Beam Dump Scattered Light Displacement Noise

### ITM HR, BS AR, AND BS HR Ghost Beams

The ITM HR3, ITM HR4, BS AR3X, BSAR4X, BSHR3X, AND BSHR4X Ghost Beams will pass through the Cryopump Baffle and hit the beam tube shark’s-tooth baffles inside the arm.

#### Beam Tube Baffle BRDF and Reflectivity

The beam tube shark’s-tooth baffles are made from oxidized, polished stainless steel with the first surface inclined at an incidence angle of 55 deg and are estimated to have a BRDF < 0.005 sr-1. The multi-bounce reflectivity of the PRM Elliptical Baffle is estimated to be 2.4E-5. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

#### Scattered Light Displacement Noise of Ghost Beams

The scattered light displacement noise from the ITM HR3 and ITM HR4X ghost beams is shown in Figure 46.

Figure 46: ITM GBHR Beam Dump Scattered Light Displacement Noise

The scattered light displacement noise from the BS AR3X, BSAR4X, BSHR3X, AND BSHR4X ghost beams is shown in Figure 47.

Figure 47: BS GBARX and GBHRX Scattered Light Displacement Noise

### BS GBHR3P, BS GBHR

The BS AR3P and, BS HR3P are collected by the PR and SR telescopes and will be caught in the scraper cavity beam dumps mounted to the HAM optical table in front of PR2, and SR2 mirrors as shown in Figure 5, and Figure 6.

Some of the ghost beam light will reflect from the cavity beam dumps and scatter from the IO tube and Out tube walls, retracing their paths into the recycling cavity beam.

#### Scattered Light Displacement Noise of Ghost Beams

The scattered light displacement noise from the BS AR3P and, BS HR3P ghost beams is shown in Figure 48.

Figure 48: BS GBAR3P Beam Dump Scattered Light Displacement Noise

### ITMX PO Beam (BS GBAR1)

The ITMX PO beam (BS GBAR1) hits the center of the signal recycling telescope mirror SR3, see Figure 2, then separates from the main beam and passes through a hole in the scraper beam dump in front of SR2 mirror and is picked off with a small diameter mirror, as illustrated in the ZEMAX layout in Figure 44.

### PRM Ghost Beams

#### PRM GBAR1

The PRM AR1 Ghost Beam is the front surface reflection of the PSL beam from the AR surface of the PRM. This beam will scatter from the PRM AR Plate Beam Dump shown in Figure 7. A fraction of this scattered light will reflect from the AR surface and head toward the input Faraday isolator. The scattered light will be deflected by the Faraday isolator toward the REFL detection optics where some of it may reflect or scatter back and retrace its path back through the input Faraday isolator and inject noise into the input beam.

#### PRM GBAR3

The PR2 AR3 Ghost Beam is the first internal reflection of the recycling cavity beam from the HR and AR surfaces that passes out through the AR surface. This beam will scatter from the PRM AR Plate Beam Dump shown in Figure 7. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

#### PRM GBHR3

The PRM HR3 Ghost Beam is the first internal reflection of the recycling cavity beam from the AR surface that passes out through the HR surface. This beam will scatter from the PRM HR Plate Beam Dump shown in Figure 7. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

#### PRM Plate Beam Dump Surface BRDF and Reflectivity

The PRM plate Beam Dump will be constructed of AR-coated black glass. The estimated BRDF < 0.05 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

The reflectivity of the PRM plate Beam Dump is estimated to be<0.025%.

#### Scattered Light Displacement Noise of Ghost Beams

The scattered light displacement noise from the PRM ghost beams is shown in Figure 51.

### PR2 Ghost Beams

#### PR2 GBAR0t

The PR2 AR0t Ghost Beam is the leakage through the HR side of the incident recycling cavity beam from PRM. This beam will scatter from the PR2 GBAR0t Plate Beam Dump shown in Figure 49. A fraction of this scattered light will pass back through PR2 HR surface and inject noise directly into the recycling cavity.

#### PR2 GBAR0t Cavity Beam Dump Surface BRDF and Reflectivity

The PR2 GBAR0t Cavity Beam Dump will be constructed of porcelainized steel with the first surface inclined at an incidence angle 56 deg and is estimated to have a BRDF < 0.005 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

The reflectivity of the PR2 GBAR0t Beam Dump is estimated to be 2.4E-5.

#### BS PO Beam (PR2 GBARt)

The BS PO Beam (PR2 ARt Ghost Beam) is the leakage through the HR side of the returning recycling cavity beam from the BS. This beam will be steered through a septum window onto the ISC detection bench on HAM1 and HAM7.

#### PR2 GBAR3

The PR2 AR3 Ghost Beam is the first internal reflection from the HR and AR surfaces that passes out through the AR surface. This beam will scatter from the PR2 AR Plate Beam Dump shown in Figure 9. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

The recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the recycling cavity.

Figure 49: PR2 GBAR0t beam dump

#### PR2 GBHR3

The PR2 HR3 Ghost Beam is the first internal reflection from the AR surface that passes out through the HR surface. This beam will scatter from the PR2 HR Plate Beam Dump shown in Figure 9. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

The recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the recycling cavity.

#### PR2 Plate Beam Dump Surface BRDF and Reflectivity

The PR2 plate Beam Dump will be constructed of AR-coated black glass. The estimated BRDF < 0.05 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

The reflectivity of the PR2 plate Beam Dump is estimated to be<0.025%.

#### Scattered Light Displacement Noise of Ghost Beams

The scattered light displacement noise from the PR2 ghost beams is shown in Figure 51.

### PR3 Ghost Beams

#### PR3 GBAR0t

The PR3 AR0t Ghost Beam is the transmission of the incident recycling cavity beam from PR2. This beam will scatter from the PR3 AR Plate Beam Dump shown in Figure 11. A fraction of this scattered light will pass back through PR3 HR surface and inject noise directly into the recycling cavity.

The recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the recycling cavity.

#### PR3 GBAR3

The PR2 AR3 Ghost Beam is the first internal reflection from the HR and AR surfaces that passes out through the AR surface. This beam will scatter from the PR3 AR Plate Beam Dump shown in Figure 9. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

The recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the recycling cavity.

#### PR3 GBHR3

The PR3 HR3 Ghost Beam is the first internal reflection from the AR surface that passes out through the HR surface. This beam will be allowed to hit the IO beam tube wall. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

The recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the recycling cavity.

#### PR3 Plate Beam Dump Surface BRDF and Reflectivity

The PR3 plate Beam Dump will be constructed of AR-coated black glass. The estimated BRDF < 0.05 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

The reflectivity of the PR3 plate Beam Dump is estimated to be<0.025%.

#### Scattered Light Displacement Noise of Ghost Beams

The scattered light displacement noise from the PR3 ghost beams is shown in Figure 51.

### SRM Ghost Beams

#### SRM GBAR3

The SRM AR3 Ghost Beam is the first internal reflection from the HR and AR surfaces that passes out through the AR surface. This beam will scatter from the SRM AR Plate Beam Dump shown in Figure 8. A fraction of this scattered light will retrace the path and inject noise directly into the signal recycling cavity.

The signal recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the recycling cavity.

#### SRM GBHR3

The SRM HR3 Ghost Beam is the first internal reflection from the AR surface that passes out through the HR surface. This beam will scatter from the SRM HR Plate Beam Dump shown in Figure 8. A fraction of this scattered light will reflect internally from the AR surface and inject noise directly into the recycling cavity.

The signal recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the signal recycling cavity.

#### SRM Plate Beam Dump Surface BRDF and Reflectivity

The SRM plate Beam Dump will be constructed of AR-coated black glass. The estimated BRDF < 0.05 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

The reflectivity of the SRM plate Beam Dump is estimated to be<0.025%.

#### Scattered Light Displacement Noise of Ghost Beams

The scattered light displacement noise from the SRM ghost beams is shown in Figure 51.

### SR2 Ghost Beams

#### SR2 GBAR0t

The SR2 AR0t Ghost Beam is the leakage through the HR side of the incident recycling cavity beam from SR3. This beam will scatter from the SR2 GBAR0t Plate Beam Dump shown in Figure 49. A fraction of this scattered light will retrace the path and inject noise directly into the signal recycling cavity.

Figure 50: SR2 AR0t beam dump

#### SR2 GBAR3

The SR2 AR3 Ghost Beam is the first internal reflection from the HR and AR surfaces that passes out through the AR surface. This beam will scatter from the SR2 AR Plate Beam Dump shown in Figure 10. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

The recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the recycling cavity.

#### SR2 GBHR3

The SR2 HR3 Ghost Beam is the first internal reflection from the AR surface that passes out through the HR surface. This beam will scatter from the SR2 HR Plate Beam Dump shown in Figure 10. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

The recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the recycling cavity.

#### SR2 Plate Beam Dump Surface BRDF and Reflectivity

The SR2 plate Beam Dump will be constructed of AR-coated black glass. The estimated BRDF < 0.05 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

The reflectivity of the SR2 plate beam dump is estimated to be<0.025%.

#### Scattered Light Displacement Noise of Ghost Beams

The scattered light displacement noise from the SR2 ghost beams is shown in Figure 51.

### SR3 Ghost Beams

#### SR3 GBAR0t

The SR3 AR0t Ghost Beam is the transmission of the incident signal recycling cavity beam from the BS. This beam will scatter from the SR3 AR Plate Beam Dump shown in Figure 12. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

The signal recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the signal recycling cavity.

#### SR3 GBAR3

The SR3 AR3 Ghost Beam is the first internal reflection from the HR and AR surfaces that passes out through the AR surface. This beam will scatter from the SR3 AR Plate Beam Dump shown in Figure 12. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

The signal recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the signal recycling cavity

#### SR3 GBHR3

The SR3 HR3 Ghost Beam is the first internal reflection from the AR surface that passes out through the HR surface. This beam will be allowed to hit the Out beam tube wall. A fraction of this scattered light will retrace the path and inject noise directly into the recycling cavity.

The recycling cavity beam circulating in the opposite direction undergoes a similar scattering event and injects an additional equal amount of noise into the recycling cavity.

#### SR3 Plate Beam Dump Surface BRDF and Reflectivity

The SR3 plate Beam Dump will be constructed of AR-coated black glass. The estimated BRDF < 0.05 sr-1. See T980027-00, Baffling Requirements for the 4K and 2K IFO.

The reflectivity of the SR3 Beam Dump is estimated to be<0.025%.

#### Scattered Light Displacement Noise of Ghost Beams

The scattered light displacement noise from the SR3 ghost beams is shown in Figure 51.

Figure 51: PRM, PR2, PR3, SRM, SR2, SR3, Scattered Light Displacement Noise

### ETM Telescope Baffle

The ETM Telescope Baffle is mounted to the front of the ETM telescope, as shown in Figure 52. The baffle blocks all the transmitted light from the ETM except for the central region. The baffle will be constructed of black glass tilted at 10 deg with a high-efficiency AR coating. Most of the light will be absorbed by the baffle. Less than 0.0025 of the light incident on the baffle will be reflected at an angle toward the ETM. The reflected light will bounce back and forth between the ETM and the baffle until it eventually hits the chamber walls.

The ETM Telescope Baffle will be mounted concentrically with the optical axis of the ETM Telescope within 0.5 mm. The 160 mm diameter aperture in the baffle is the same as the clear aperture of the ETM Telescope.

This will meet the requirement 4.7 Clear Aperture Requirements.

Figure 52: ETM Telescope Baffle

#### ETM Telescope Baffle Motion Requirements

The motion requirement for the ETM Telescope Baffle was determined using the scattered light model. The ETM Telescope Baffle requires no further motion isolation than that provided by the BSC optical table seismic requirement.

#### ETM Telescope Baffle Surface BRDF

The ETM Telescope Baffle will be constructed of black glass with the surface inclined at an incidence angle of 10 deg; the BRDF of the baffle is expected to be < 0.1 sr^-1.

#### ETM Telescope Baffle Reflectivity

The light that is not absorbed by the ETM Telescope Baffle will reflect from the baffle surface onto the insides of the vacuum chamber. There, it will scatter from the chamber, reflect again from the ETM Telescope Baffle, and enter the IFO mode.

The requirement for the reflectivity of the ETM Telescope Baffle was calculated using the scattered light model. The reflectivity of the ETM Telescope Baffle must be < 0.07. This requirement will be met by using either oxidized polished stainless steel or black glass.

#### Seismic Motion of the ETM Telescope Baffle Scattering Surfaces

The light that reflects from the ETM Telescope Baffle will scatter from the vacuum chamber, which has the seismic motion shown in Figure 25.

#### Scattered Light Displacement Noise of Suspended ETM Telescope Baffle

The scattered light noise from the three ETM Telescope Baffle sources is shown in Figure 53.

Figure 53: Scattered Light Displacement Noise of ETM Telescope Baffle

## Stray Light Control Physical Characteristics

### Faraday Isolator

Table 4: Faraday Isolator Characteristics

| Parameter | Value |
| --- | --- |
| Configuration | Single Faraday isolator |
| Wavelength | 1064 nm |
| Clear Aperture | 20 mm |
| Rotator material | TGG crystal |
| Rotator crystal wedge angle front and back surface | 1 deg |
| Total wavefront distortion | <1 λ @ 633 nm |
| Rotator transmissivity across clear aperture | >97 % |
| Input/output polarizer | Calcite, air-spaced Brewster’s angle |
| Polarizer transmissivity per surface | >99.9 % |
| Half-wave rotation plate | Zero-order quartz |

Table 5 : Faraday Isolator Suspension Characteristics

| Parameter | Value |
| --- | --- |
| Frame | Modified LOS |
| Suspension | Four wire marionette |
| Amplitude response | See Figure 17 |
| Damping | Elastomeric |
| Height adjustment | manual |
| Yaw adjustment | manual |
| Pitch adjustment | Remote, Pico Motor |

### Arm Cavity Baffle

Table 6: Arm Cavity Baffle Characteristics

| Parameter | Value |
| --- | --- |
| Aperture diameter | 346 mm |
| Outer diameter blockage | >850 mm |
| Material | Black Glass (#12 grade welder’s glass) |
| BRDF | <0.001 sr^-1 |
| Reflectivity | <0.01 |
| Weight | TBD kg |

Table 7: Arm Cavity Baffle Suspension

| Parameter | Value |
| --- | --- |
| Frame | Aluminum frame |
| Suspension | Two wire, suspended from HEPI stage “0” |
| Amplitude response | See Figure 22, Figure 23, Figure 24 |
| Damping | Elastomeric, Q < 1000 |

### Elliptical Baffle

#### ITM Elliptical Baffle

Table 8: ITM Elliptical Baffle Characteristics

| Parameter | Value |
| --- | --- |
| Suspension | Single pendulum SUS from BSC optical table or HEPI stage “0” |
| Damping | Elastomeric, Q < 1000 |
| Aperture major diameter | 249 mm |
| Aperture minor diameter | 218 mm |
| Material | Black Glass (#12 grade welder’s glass) |
| BRDF | <0.01 sr^-1 |
| Reflectivity | <0.001 |
| Weight | TBD kg |

#### PRM Elliptical Baffle

Table 9: PRM Elliptical Baffle Characteristics

| Parameter | Value |
| --- | --- |
| Suspension | Attached to PRM frame |
| Damping | none |
| Aperture major diameter | 249 mm |
| Aperture minor diameter | 218 mm |
| Material | Oxidized stainless steel |
| BRDF | <0.01 sr^-1 |
| Reflectivity | <0.30 |
| Weight | TBD kg |

### Manifold Baffle

Table 10: Manifold Baffle

| Parameter | Value |
| --- | --- |
| Suspension | Mounted to manifold wall |
| Damping | none |
| Aperture | 570 mm radius |
| Outer diameter | 930 mm |
| Material | Oxidized stainless steel |
| BRDF | <0.01 sr^-1 |
| Reflectivity | < 0.30 |
| Weight | TBD kg |

### Brewster’s Window

Table 11: Brewster's Window Characteristics

| Parameter | Value |
| --- | --- |
| Clear aperture diameter | 60 mm @ 56 deg incidence |
| Wavefront distortion | <0.14 λ @ 633 nm |
| BRDF @ 56 deg incidence | < 5E-6 sr^-1 |
| Reflectivity | <4E-4 |
| Diameter of substrate | 172 mm |
| Thickness | 25.4 mm |
| Material | Grade A fused silica, super polished |
| Attachment to Flange | O-ring seal |

### OMMT

Table 12: OMMT M2 Characteristics

| Parameter | Value |
| --- | --- |
| Mirror scattering loss | < 500 ppm |
| BRDF @ 0.016 rad incidence | <3E-3 sr^-1 |
| Suspension | SOS suspension |
| Damping | OSEM, Q < 10 |
| Clear aperture | 75 mm diameter |
| Weight | TBD kg |

### ITMX, ITMY, and BS Beam Dump

Table 13: Cavity Beam Dump Characteristics

| Parameter | Value |
| --- | --- |
| Suspension | Single pendulum SUS from HEPI stage “0” |
| Damping | Elastomeric, Q < 1000 |
| Aperture | 218 mm horizontal x 249 mm vertical |
| Material | Black Glass (#12 grade welder’s glass) |
| BRDF | <0.001 sr^-1 |
| Reflectivity | < 0.005 |
| Weight | TBD kg |

### IO Baffle

Table 14: IO Baffle Characteristics

| Parameter | Value |
| --- | --- |
| Mounting | HAM table clamp |
| Aperture diameter | 260 mm |
| Outer diameter blockage, segment above HAM table | 1537 mm |
| Material | Polished, oxidized stainless steel |
| Weight | TBD kg |

### Cryopump Baffle

Table 15: Cryopump Baffle Characteristics

| Parameter | Value |
| --- | --- |
| Location | Corner Station-- x arm, y arm End Station-- x arm, y arm |
| Suspension | Single pendulum |
| Aperture diameter | 769 mm |
| Outer diameter | 1133 mm |
| Material | Black Glass (#12 grade welder’s glass) |
| BRDF | <0.01 sr^-1 |
| Reflectivity | <0.01 |
| Weight | TBD |

### ETM Telescope Baffle

Table 16: ETM Telescope Baffle Characteristics

| Parameter | Value |
| --- | --- |
| Aperture diameter | 160 mm |
| Outer dimensions | 340 mm x 340 mm |
| Material | Black Glass (#12 grade welder’s glass) |
| BRDF | <0.1 sr^-1 |
| Reflectivity | <0.0025 |
| Weight | TBD |

## Stray Light Control Interface Definitions

### Interfaces to other LIGO detector subsystems

#### Mechanical Interfaces

The beam dumps will attach to the optical tables or be suspended from the HEPI stage “0” in the HAM and BSC chambers, without interfering with the COC mirror structures. Earthquake stops will attach to the chamber wall.

The ITM Elliptical Baffle will hang from the BSC optics table or from the HEPI stage “0” and will have earthquake stops attached to the chamber wall.

The PRM Elliptical Baffle will mount directly to the PRM SUS structure.

The Arm Cavity Baffles will hang from the ITM and ETM HEPI stage “0”and will have earthquake stops attached to the chamber wall.

The Cryopump Baffle will be suspended from a mounting ring that is held in position inside the spool piece by means of compressive forces.

The Manifold Baffle will be held in position inside the manifold by means of compressive forces.

#### Electrical Interfaces

##### Suspended Baffles and Beam Dumps

All the suspended baffles and beam dumps are passively damped and will require no electrical interfaces.

##### Faraday Isolator

The Faraday Isolator will be suspended from a modified LOS, and appropriate electronic control signals to the Pico Motor will be used for pitch steering.

#### Optical Interfaces

The Cavity Beam Dumps will intercept the ghost beams while maintaining adequate clearance from the main recycling cavity beams.

The PRM elliptical baffle will intercept the main beam incident from the IO input mode matching telescope with a clear aperture slightly larger on all sides than the limiting aperture that is determined by the geometric shadow of the PRM and the BS.

#### Stay Clear Zone

##### Arm Cavity Baffle

The aperture of the Arm Cavity Baffle will be 346 mm, which is larger than the diameter of the ITM and ETM COC. The aperture will be concentric with the COC within 4 mm.

##### ITMX, ITMY, and BS Beam Dump

The Cavity Beam Dumps will have a stay clear zone of >30 mm from the elliptical edges of the main recycling cavity beam.

##### Cryopump Baffle

The Cryopump Baffle will be concentric to the spool piece diameter within 4 mm. The clearance between the 1 ppm edge of the main beam and the centered Cryopump Baffle aperture will be > 7 mm.

##### ETM Telescope Baffle

The clear aperture diameter of the ETM Telescope Baffle is 160 mm, which is the same as the clear aperture of the ETM telescope. The ETM Telescope Baffle will be concentric with the entrance aperture of the ETM telescope to within 0.5 mm.

##### Elliptical Baffle

The clear aperture of the Elliptical Baffle is 2 mm larger on all sides than the limiting clear aperture of the PRM and the BS. The Elliptical Baffle will be concentric with the centerline of the IFO main beam between the BS and the ITM within 2 mm.

##### IO Baffle

The clear aperture of the IO Baffle is 260 mm, which is larger than the diameter of the PRM. The IO Baffle will be concentric with the PRM within 2 mm.

### Interfaces external to LIGO detector subsystems

There are no interfaces external to the LIGO detector.

## Stray Light Control Reliability

All Stray Light Control baffles and beam dumps are passive and are expected to have 100% availability. The MTBF is expected to be equal to the life of the IFO.

The Faraday Isolator will be suspended by a modified LOS. The typical MTBF of an LOS will apply TBD.

## Stray Light Control Maintainability

The following components are susceptible to failure:

- Pico Motor

- Suspension wires

If either of these components fails, the Faraday Isolator suspension assembly will be removed from the vacuum chamber and repaired. The physical location of the suspension will be preserved by means of alignment fixtures. The pointing angle of the Faraday Isolator will be reproduced by means of the initial alignment procedure.

Spare components will be stocked during initial installation for the replacement of long lead-time items such as mirrors.

## Stray Light Control Environmental Conditions

Natural Environment

Temperature and Humidity

The SLC assemblies are designed to operate in the high vacuum environment of the IFO and in the controlled LVEA environment during installation.

Table 17 Environmental Performance Characteristics

| Operating | Non-operating (storage) | Transport |
| --- | --- | --- |
| +20C to +25C, 20-70% RH, non- condensing | 0C to +60C, 10-90% RH, non-condensing | 0C to +60C, 10-90% RH, non- condensing |

Atmospheric Pressure

The Brewster’s window will function with a differential pressure of 1 atmosphere under normal atmospheric pressure conditions.

Seismic Disturbance

The suspended SLC assemblies and the assemblies mounted to the vacuum chambers will withstand ground seismic disturbances.

Induced Environment

Electromagnetic Radiation

NA

Acoustic

NA

Mechanical Vibration

NA

## Stray Light Control Transportability

All items will be transportable by commercial carrier without degradation in performance. As necessary, provisions will be made for measuring and controlling environmental conditions (temperature and accelerations) during transport and handling. Special shipping containers, shipping and handling mechanical restraints, and shock isolation will be utilized to prevent damage. All containers will be movable for forklift. All items over 100 lbs. that must be moved into place within LIGO buildings will have appropriate lifting eyes and mechanical strength to be lifted by cranes.

# Stray Light Control Design and Construction

The design and construction of the Stray Light Control subsystem allow adequate cleaning, either on site or at an appropriate outside vendor, and will fit inside the vacuum baking ovens on site.

#### Materials and Processes

The materials and processes used in the fabrication of the Stray Light Control subsystem will be compatible with the LIGO approved materials list.

Metal components will have quality finishes on all surfaces, suitable for vacuum finishes. Aluminum components used in the vacuum will not have anodized surfaces.

##### Materials

A list of currently approved materials for use inside the LIGO vacuum envelope can be found in LIGO Vacuum Compatible Materials List (LIGO-E960022). All fabricated metal components exposed to vacuum will be made from stainless steel, copper, or aluminum. Other metals are subject to LIGO approval. Pre-baked viton (or fluorel) may be used subject to LIGO approval. All materials used inside the vacuum chamber will comply with LIGO Vacuum Compatibility, Cleaning Methods and Procedures (LIGO-E960022-00-D).

The only lubricating films permitted within the vacuum are dry plating of vacuum compatible materials such as silver and gold.

##### Processes

Cleaning

All materials used inside the vacuum chambers will be cleaned in accordance LIGO-E960022-00-D or LIGO-E000007-00, and Specification Guidance for Seismic Component Cleaning, Baking, and Shipping Preparation (LIGO-L970061-00-D). To facilitate final cleaning procedures, parts will be cleaned after any processes that result in visible contamination from dust, sand or hydrocarbon films.

Materials will be joined in such a way as to facilitate cleaning and vacuum preparation procedures; i. e. internal volumes will be provided with adequate openings to allow for wetting, agitation and draining of cleaning fluids and for subsequent drying.

##### Component Naming

All components will be identified using the LIGO Naming Convention (LIGO-E950111-A-E). This will include identification (part or drawing number, revision number, serial number) physically stamped on all components, in all drawings and in all related documentation.

#### Stray Light Control Workmanship

All components will be manufactured according to good commercial practice.

#### Stray Light Control Interchangeability

Common elements with ordinary dimensional tolerances, will be interchangeable.

#### Stray Light Control Safety

This item will meet all applicable NSF and other Federal safety regulations, plus those applicable State, Local and LIGO safety requirements. A hazard/risk analysis will be conducted in accordance with guidelines set forth in the LIGO Project System Safety Management Plan LIGO-M950046-F, section 3.3.2.

#### Stray Light Control Human Engineering

NA

### Stray Light Control Assembly and Maintenance

Assembly fixtures and installation procedures will be developed in conjunction with the Stray Light Control hardware design. These will include (but not be limited to) fixtures and procedures for:

•	installation and assembly of beam dumps and baffles into the vacuum

•	assembly of the in vacuum components in a clean room (class 100) environment

### Stray Light Control Documentation

The documentation will consist of working drawings, assembly drawings, and alignment procedures

#### Stray Light Control Specifications

Specifications for the purchase of specialized components and assemblies such as Faraday isolator, optical mirrors, windows, and lenses will be developed.

#### Stray Light Control Design Documents

The following documents will be produced:

•	LIGO Stray Light Control Preliminary Design Document (including supporting technical design and analysis documentation)

•	LIGO Stray Light Control Final Design Document (including supporting technical design and analysis documentation)

•	LIGO Stray Light Control Installation Procedures

#### Stray Light Control Engineering Drawings and Associated Lists

A complete set of drawings suitable for fabrication will be provided along with Bill of Material (BOM) and drawing tree lists. The drawings will comply with LIGO standard formats and will be provided in electronic format. All documents will use the LIGO drawing numbering system, be drawn using LIGO Drawing Preparation Standards, etc.

#### Stray Light Control Technical Manuals and Procedures

##### Procedures

Procedures will be provided for the installation, and final alignment of the Stray Light Control elements.

#### Stray Light Control Documentation Numbering

All documents will be numbered and identified in accordance with the LIGO documentation control numbering system LIGO document TBD

#### Stray Light Control Test Plans and Procedures

All test plans and procedures will be developed in accordance with the LIGO Test Plan Guidelines, LIGO document TBD.

### Stray Light Control Logistics

The design will include a list of all recommended spare parts and special test equipment required.

### Stray Light Control Precedence

The relative importance of the positioning of the beam dumps and baffles will be as follows:

- satisfy the stay clear requirements

- align the baffles and beam dumps with the centers of the ghost beams

### Stray Light Control Qualification

N/A

# Quality Assurance Provisions

This section includes all of the examinations and tests to be performed in order to ascertain that the fabricated SLC elements conform to the requirements in section 3.

## General

### Responsibility for Tests

AOS will conduct tests to verify the as-delivered performance specifications of the sub-system.

### Special Tests

#### Engineering Tests

TBD

#### Reliability Testing

No reliability testing is anticipated.

### Configuration Management

Configuration control of specifications and designs will be in accordance with the LIGO Detector Implementation Plan.

## Quality conformance inspections

Design and performance requirements identified in this specification and referenced specifications will be verified by inspection, analysis, demonstration, similarity, test or a combination thereof per the Verification Matrix, Appendix 1 (TBD). Verification method selection shall be specified by individual specifications, and documented by appropriate test and evaluation plans and procedures. Verification of compliance to the requirements of this and subsequent specifications will be accomplished by the following methods or combination of methods:

### Inspections

Manufactured parts with LIGO identification numbers or marks will be inspected to determine conformity with the procurement specification.

Witness samples will be acceptable proof of the properties of HR and AR coatings applied to the optical surfaces.

### Demonstration

The required attenuation characteristics of the assembled Faraday isolator will be demonstrated before installation.

The resonance and damping characteristics of the suspended beam dumps and baffles will be demonstrated before installation.

### Test

Appropriate tests will be implemented to verify the specifications of the purchased components. TBD

# Preparation for Delivery

Packaging and marking of equipment for delivery will be in accordance with the Packaging and Marking procedures specified herein.

## Preparation

•	Vacuum preparation procedures as outlined in E960022-B LIGO Vacuum Compatibility, Cleaning Methods and Qualification Procedures will be followed for all components intended for use in vacuum. After wrapping vacuum parts as specified in this document, an additional, protective outer wrapping and provisions for lifting shall be provided.

•	Electronic components will be wrapped according to standard procedures for such parts.

## Packaging

Procedures for packaging will ensure cleaning, drying, and preservation methods adequate to prevent deterioration, appropriate protective wrapping, adequate package cushioning, and proper containers. Proper protection will be provided for shipping loads and environmental stress during transportation, hauling and storage. The shipping crates used for large items will use for guidance military specification MIL-C-104B, Crates, Wood; Lumber and Plywood Sheathed, Nailed and Bolted. Passive shock witness gauges will accompany the crates during all transits.

For the viewports, the shipping preparation will include double bagging with Ameristat 1.5TM plastic film (heat sealed seams as practical, with the exception of the inner bag, or tied off, or taped with care taken to insure that the tape does not touch the cleaned part). The bag will be purged with dry nitrogen before sealing.

## Marking

Appropriate identification of the product, both on packages and shipping containers; all markings necessary for delivery and for storage, if applicable; all markings required by regulations, statutes, and common carriers; and all markings necessary for safety and safe delivery will be provided.

Identification of the material will be maintained through all manufacturing processes. Each component will be uniquely identified. The identification will enable the complete history of each component to be maintained (in association with Documentation “travelers”). A record for the optical lever support structures will indicate all weld repairs and fabrication abnormalities.

The specification for marking will state that marking fluids, die stamps and/or electro-etching is not permitted. A vibratory tool with a minimum tip radius of 0.005" is acceptable for marking on surfaces that are not hidden from view. Engraving and stamping are also permitted.

# Appendix A—Scattered Light Noise Theory

## Scattered Light Requirement

A DARM signal is obtained when the differential arm length is modulated as a result of a gravity wave strain. The DARM signal was calculated in reference T060073-00 Transfer Functions of Injected Noise, and is defined by the following expression:

Where L is the arm length, hSRD is the minimum SRD gravity wave strain spectral density requirement, P0 is the input laser power into the IFO, and DARM is the signal transfer function.

In a similar manner, an apparent signal (scattered light noise) occurs when a scattered light field with a phase shift is injected into the IFO at some particular location, e.g. through the back of the ETM mirror. The scattered light noise is defined by the following expression:

PSNi is the scattered light power injected into the IFO mode, δSN is the phase shift of the injected field, and SNXXX is the noise transfer function for that particular injection location.

The phase shift spectral density of the injected field due to the motion of the scattering surface is given by

where xs is the spectral density of the horizontal motion of the scattering surface.

In general, the different scattering sources are not coherent and must be added in quadrature. The requirement for scattered light displacement noise can be stated with the following inequality:

The SNXXX/DARM scattered light noise transfer functions for various injection locations within the IFO were calculated by Hiro (T060073-00 Transfer Functions of Injected Noise) and are shown in

Figure 54: Scattered Light Noise Transfer Functions

## Scattered Power into the IFO

The light power scattered into the interferometer from the ith source is calculated as follows:

Where Pin is the power incident on the scattering surface, BRDF is the fraction of incident light that is scattered per unit solid angle, ΔΩ is the solid angle subtended by the mode inside the IFO arm, wIFO is the beam waist of the mode inside the arm, wSN is the beam waist of the beam incident on the scattering surface, and T is the transmissivity of the path from the scattering surface to the injection point in the IFO.

The effective solid angle increases whenever the IFO beam waist has been transformed to a smaller waist by an AOS telescope or some other focusing element in the ISC detection system, because the product of solid angle and beam waist cross-sectional area is proportional to the total radiant flux, which is an optical invariant. Therefore, as the area of the beam waist decreases the solid angle increases proportionally.

### Output Faraday Isolator Scatter

The power incident on the Faraday isolator is given by

GAS is the dark port signal ratio.

The light power scattered into the IFO from the five surfaces before the Faraday rotator magnet is given by

The scattering surface has the seismic motion of the HAM requirement, attenuated by the motion transfer function of the Faraday Isolator requirement.

The scattered light is injected into the SRM mirror, and the appropriate scattered light noise transfer function is ‘SRM’. The displacement noise (m/rt Hz) is

### Arm Cavity Baffle Surface Scatter

The small angle scattered power from the far COC passes through the beam tube to the near COC. The power in the annulus between the cryopump baffle and the ITM (ETM) outside diameter will hit the Arm Cavity Baffle. See Figure 55.

Figure 55: ARM CAVITY BAFFLE SCATTER

The offset between the COC and the beam tube axis will be ignored.

The half-angle from the beam tube centerline to the AC baffle inner edge is

The half-angle from the beam tube centerline to the cryopump baffle outer edge is

Pa is the circulating power in each arm.

The light power scattered from four Arm Cavity Baffle into the mode cross section and re-scattered by the far COC into the IFO mode is given by

The scattering surface is suspended from the BSC HEPI ring and has the seismic motion of the HEPI requirement, attenuated by the motion transfer function of the Arm Cavity Baffle requirement.

The scattered light is injected into the arm cavity, and the appropriate scattered light noise transfer function is ‘ITM_HR’. The displacement noise (m/rt Hz) is

### Arm Cavity Baffle Reflected Light

The power reflected from the Arm Cavity Baffle and incident on the vacuum manifold wall is given by

where Rbd is the net reflectivity of the baffle.

This light will scatter from the wall, reflect again from the Arm Cavity Baffle toward the far COC, and finally scatter from the COC into the mode of the IFO. The scattered power is given by

The scattering surface has the seismic motion of the beam tube.

The scattered light is injected into the arm cavity, and the appropriate scattered light noise transfer function is ‘ITM_HR’. The displacement noise (m/rt Hz) is

### ITM Elliptical Baffle Surface Scatter

See Figure 56. When the IFO arm cavity is on resonance, the power exiting the arm cavity into the recycling cavity through the ITM is exactly twice the power incident on the ITM from the recycling cavity side. The two counter-propagating beams are exactly 180 degrees out of phase and they interfere at the surface of the ITM. The resultant beam, with a power equal to the recycling cavity arm power, appears to reflect from the ITM back into the recycling cavity.

Figure 56: ITM ELLIPTICAL BAFFLE SCATTER AND REFLECTION

However, in the actual LIGO IFO the recycling cavity beam has a truncated Gaussian profile with an elliptical shape. Beyond the edges of the sharp elliptical boundary, the Gaussian shaped beam exiting from the arm cavity is not opposed with a Gaussian recycling cavity beam and will strike the elliptical baffle with twice the irradiance of the recycling cavity beam.

The Gaussian irradiance parameter, P0itm, of the beam exiting the ITM is twice the irradiance parameter, P0rc, of the recycling cavity beam.

The exitance function from the ITM is given by

and the irradiance function inside the recycling cavity arm is given by

The total power exiting from the ITM is

The total power from the exiting ITM beam that passes through the elliptical baffle is

Then, the power that hits the elliptical baffle from the ITM side is the difference

The light power scattered from the two Elliptical Baffles into the IFO mode at the far COC is given by

where Titmhr is the transmissivity of the ITM mirror.

The scattering surface is suspended from the BSC HEPI ring and has the seismic motion of the HEPI requirement, attenuated by the motion transfer function of the ITM Elliptical Baffle requirement.

The scattered light is injected into the arm cavity, and the appropriate scattered light noise transfer function is ‘ITM_HR’. The displacement noise (m/rt Hz) is

### ITM Elliptical Baffle Reflected Light

The power reflected from the Elliptical Baffle and incident on the vacuum manifold wall is given by

where Rellbaf is the reflectivity of the baffle surface.

The light will scatter from the wall, reflect from the Elliptical Baffle, and transmit through the ITM into the mode of the IFO at the far COC. The scattered power is given by

The scattering surface has the seismic motion of the BSC chamber wall.

The scattered light is injected into the arm cavity, and the appropriate scattered light noise transfer function is ‘ITM_HR’. The displacement noise (m/rt Hz) is

### PRM Elliptical Baffle

The prompt Gaussian beam that enters the recycling cavity through the PRM HR surface is expanded by the PRM telescope (PR2 and PR3) and is vignetted into an elliptical cross section by the PRM Elliptical Baffle.

The expanded Gaussian irradiance functions at the PRM Elliptical Baffle, given in terms of radius and Cartesian coordinates are

The total power passing through the PR3 mirror is

The total power passing through the PRM Elliptical Baffle is

The power hitting the baffle is

This power scatters back through the PRM telescope onto the PRM HR surface, where it re-scatters into the de-magnified mode volume of the recycling cavity. The maximum scattering angle at the surface of the PRM is

and m is the magnification of the PRM telescope.

The scattered power into the IFO is given by

where Lprm2 is the distance from the recycling cavity beam waist (near PR2) and PRM, wrc is the

beam radius in the recycling cavity.

The scattering surface is mounted to the HAM table and has the seismic motion of the HAM requirement.

The scattered light is injected into the BS from the PR side, and the appropriate scattered light noise transfer function is ‘BS_from_PR’. The displacement noise (m/rt Hz) is

### ITM (ETM) Wide-Angle Scatter

Point defects in the coatings and dust particles on the surface of the arm cavity mirrors will cause wide-angle scattered light. The scattering function appears to be Lambertian. See T070089-02 Wide-angle Scatter from LIGO Arm Cavities.

The wide-angle scattered light will predominately hit the back of the Arm Cavity Baffle and the Cylindrical Baffle between the mirror and the Arm Cavity Baffle. Some of the light will pass through the hole in the Arm Cavity Baffle and will hit the manifold wall and the manifold baffle. Some of the light will hit the BSC chamber.

Figure 57: Wide-angle Scatter from ITM (ETM)

#### Scattering from the Back of Arm Cavity Baffle

In the following calculations, the offset of the ITM from the centerline of the arm cavity is ignored. The wide-angle scattered light hitting the back of the Arm Cavity Baffle is given by

Where, the half-angle from the ITM centerline to the Arm Cavity Baffle outer edge is

The half-angle from the ITM centerline to the Arm Cavity Baffle inner edge is

and Lacb is the distance from the ITM to the Arm Cavity Baffle.

The power scattered onto the back of the Arm Cavity Baffle is

Where the geometric scattering function is

#### Scattering from the Cylindrical Baffle

The wide-angle scattered light hitting the inside of the Cylinder Baffle is

Where the half-angle from the ITM centerline to the Cylinder Baffle is

and Lacb is the length of the Arm Cavity Baffle, and Lcyl is the length of the Cylindrical Baffle.

The power scattered into the IFO mode is given by

Where the geometric scattering function is

#### Total Scattered Light Displacement Noise from Arm Cavity Baffle and Cylindrical Baffle.

The total scattered light from the Arm Cavity Baffle and the Cylindrical Baffle into the IFO is

The total scattered light displacement noise is

#### Scattering from the Manifold  Baffle

The wide-angle scattered light hitting the Manifold Baffle is

Where the half-angle from the ITM centerline to the Manifold Baffle is

and Lm is the distance from the ITM to the Manifold Baffle.

The power scattered into the IFO mode is given by

Where the geometric scattering function is

#### Scatter from ITM Manifold Wall

The wide-angle scattered light hitting the Manifold wall is

The power scattered into the IFO mode is given by

Where the geometric scattering function is

#### Scattering from BSC Chamber Walls

The wide-angle scattered light hitting the BSC chamber wall is

The power scattered into the IFO mode is given by

Where the geometric scattering function is

#### Total Wide-Angle Scattered Light Displacement Noise from BSC Chamber, Manifold Walls, and Manifold Baffle

The total scattered light from the BSC Chamber, Manifold Walls, and Manifold Baffle into the IFO is

The scattered light is injected into the arm cavity, and the appropriate scattered light noise transfer

function is ‘ITM_HR’. The displacement noise (m/rt Hz) is

### Septum Window Scatter

#### AS Septum Window

The power incident on the AS Septum Window is given by

The light power scattered into the IFO mode from the two surfaces of the AS Septum Window is given by

The scattered light is injected through the SRM, and the appropriate scattered light noise transfer

function is ‘SRM’. The displacement noise (m/rt Hz) is

#### AS Septum Window Reflection

The reflected power incident on the AS Septum Window beam dump is given by

where Rsp is the Fresnel reflectivity of the window surfaces.

The light power scattered into the IFO mode from the AS Septum Window beam dump is given by

The total scattered light displacement noise is

#### ITMX PO Septum Window

The power incident on the ITMX PO Septum Window is given by

The light power scattered into the IFO mode from the two surfaces of the ITMX PO Septum Window is given by

The scattered light is injected into the ITM AR, and the appropriate scattered light noise transfer

function is ‘ITM_AR. The displacement noise (m/rt Hz) is

#### ITMX PO Septum Window Reflection

The reflected power incident on the ITMX PO Septum Window beam dump is given by

The light power scattered into the IFO mode from the ITMX PO Septum Window beam dump is given by

The total scattered light displacement noise is

#### RC PO Septum Window

The power incident on the RC PO Septum Window is given by

where Rpr2hr and Rpr2ar are the Fresnel reflectivity of the HR and AR surfaces of the PR2 mirror, and Grefl is the reflected port signal ratio.

The light power scattered into the IFO mode from the two surfaces of the RC PO Septum Window is given by

The scattered light is injected into the BS from the PRM direction, and the appropriate scattered light noise transfer function is ‘BS_FROM_PRM’. The displacement noise (m/rt Hz) is

#### RC PO Septum Window Reflection

The reflected power incident on the RC PO Septum Window beam dump is given by

The light power scattered into the IFO mode from the RC PO Septum Window beam dump is given by

The total scattered light displacement noise is

### ITMY Hartmann Viewport

The power transmitted through the SR2 HR surface is

The power incident on the Hartmann viewport is

where Rhartybs is the reflectivity of the Hartmann beam splitter.

The light power scattered into the IFO mode from the Hartmann viewport is given by

The scattered light is injected into the BS from the SRM direction, and the appropriate scattered light noise transfer function is ‘BS_FROM_SRM’. The displacement noise (m/rt Hz) is

### ITMX Hartmann Viewport

The power incident on the Hartmann viewport is

where Thartxbs is the transmissivity of the Hartmann beam splitter.

The light power scattered into the IFO mode from the Hartmann viewport is given by

The total scattered light displacement noise is

### Ghost Beams

#### Ghost Beam Naming Convention

The ghost beam naming conventions for the COC mirrors and the beam splitter are shown in the following figures.

Figure 58: PRM, SRM, ITM, and ETM ghost beam naming convention

Figure 59: BS ghost beam naming convention

The GBAR3x’/y’ are superimposed, and are renamed GBAR3P. Likewise, the other superimposed pairs are renamed GBAR4P, GBHR3P, GBAR4P.

#### ITMAR1

The power incident on ITMAR1 Beam Dump is given by

where Ritmar is the reflectivity of the AR surface of the ITM.

The light power scattered into the IFO from the ITM Beam Dump is given by

The scattered light displacement noise is

#### ITMAR1 REFL

The power reflected from the ITMAR1 Beam Dump and incident on the manifold wall is given by

The light power scattered into the IFO from the wall is given by

The scattered light displacement noise is

#### ITMAR3

The power incident on ITMAR3 Beam Dump is given by

where Ritmhr is the reflectivity of the HR surface of the ITM.

The light power scattered into the IFO from the ITM Beam Dump is given by

The scattered light displacement noise is

#### ITMAR3 REFL

The power reflected from the ITMAR3 REFL Beam Dump and incident on the IO tube wall is given by

The light power scattered into the IFO from the wall is given by

The scattered light displacement noise is

#### ITMHR3

The ITMHR3 ghost beam power incident on Beam Tube Baffle in the arm is given by

where Titmhr is the transmissivity of the HR surface of the ITM.

The light power scattered into the recycling cavity through the ITM from the Beam Tube Baffle is given by

The scattered light displacement noise is

#### BSAR3

The BSAR3 ghost beam power incident on Beam Tube Baffle in the arm is given by

where Rbshr is the reflectivity of the HR surface of the BS and Rbsar is the reflectivity of the AR surface of the BS.

The light power scattered into the IFO from the Beam Tube Baffle is given by

The scattered light displacement noise is

#### BSHR3

The power incident on Beam Tube Baffle is given by

The light power scattered into the IFO from the Beam Tube Baffle is given by

The scattered light displacement noise is

#### BSAR3P

The power incident on the BSAR3P beam dump from the two coincident beams is given by

The light power scattered into the IFO from the BSAR3P beam dump is given by

#### BSHR3P

The power incident on the BSHR3P beam dump from the two coincident beams is given by

The light power scattered into the IFO from the BSHR3P beam dump is given by

#### ITMAR4

The power incident on the ITMAR4 beam dump is given by

The light power scattered into the IFO from the ITMAR4 beam dump is given by

#### ITMHR4

The power incident on the ITMHR4 beam dump is given by

The light power scattered into the IFO from the ITMHR4 beam dump is given by

#### BSAR4X

The power incident on the BSAR4X beam dump is given by

The light power scattered into the IFO from the ITMHR4 beam dump is given by

### Cryopump Baffle

The power incident on the Cryopump Baffle is given by

where ηlcp is the scattered loss ratio from the arm power to the Cryopump Baffle surface.

The light power scattered into the IFO from the Cryopump Baffle is given by

The power reflected by the Cryopump Baffle and incident on the spool piece wall is given by

where Rcpb is the reflectivity of the Cryopump Baffle.

The light power scattered into the IFO from the wall is given by

The power incident on the Cryopump Baffle edge is given by

where ηlcpeg is the scattered loss ratio from the arm power to the Cryopump Baffle edge surface.

The light power scattered into the IFO from the Cryopump Baffle edge is given by

### ETM Telescope Baffle

The power incident on the ETM Telescope Baffle is given by

where Pa is the power in the arm cavity,  Tetm is the transmissivity of the ETM mirror, and ηetmbaf is the fractional power that hits the ETM Telescope Baffle.

The light power scattered into the IFO from the ETM Telescope Baffle is given by

The power reflected by the ETM Telescope Baffle and incident on the chamber wall is given by

where Retmbaf is the reflectivity of the ETM Telescope Baffle.

The light power scattered into the IFO from the wall is given by

The power incident on the ETM Telescope Baffle edge is given by

where ηetmbafeg is the scattered loss ratio from the arm power to the ETM Telescope Baffle edge surface.

The light power scattered into the IFO from the ETM Telescope Baffle edge is given by

### Fringe-Wrapping

In the small phase-shift approximation the temporal DARM signal (noise) due to light scattered into the IFO mode is

The motion of the scattering surface is written as the underlying ground seismic motion, xg , times the motion amplitude transfer function of the scattering surface, ASEIi .

The amplitude displacement spectral density is given by the following expression with the transfer coefficient calculated by Hiro (T060073-00 Transfer Functions of Injected Noise)

When the horizontal displacement of the scattering surface exceeds λ/8, the amplitude of the noise no longer increases at the frequency of the scattering surface motion, but becomes non-sinusoidal and is up-converted to noise at odd harmonics of the scattering surface motion frequency. This phenomenon is called fringe-wrapping.

We will assume that the transfer functions SNXXX are valid for large phase-shift signals.

This time function is represented exactly by the Bessel series expansion in odd harmonics of the scattering surface frequency, f0, with amplitudes given by the Bessel functions of integral order n=mn and argument θ.

At the onset of fringe-wrapping, a significant distortion of the noise temporal waveform has already occurred, as shown in Figure 60, with the generation of up-converted noise at odd harmonics of the surface motion. The actual time signal and the Bessel function representation of the time signal are plotted in the figure and agree exactly.

Figure 60: Noise Waveform at the Onset of Fringe-Wrapping, λ/8

If the displacement of the scattering surface is increased to λ/4, the fringe-wrapping becomes clearly visible, as shown in Figure 61. The fundamental and the third harmonic contribute most of the noise, as seen by the coefficients of the Bessel functions in the adjacent table.

Figure 61: Displacement Noise waveform with Fringe-wrapping, λ/4

The displacement spectral density, m/rt Hz, of the fringe-wrapped signal (noise) at an up-converted frequency is given by the Bessel function series

Note that the Bessel function phase is evaluated by using the motion of the surface at the lower frequency that corresponds to an odd multiple of the up-converted frequency.

###### Damped Pendulum Example

Assume that the scattering surface is suspended from a damped, simple pendulum with resonant frequency = 1 Hz, Q = 1000; and the displacement spectral density of the suspension point xg is 1E-7 m/ rt Hz.

The amplitude response of the pendulum is given by

The calculated noise displacement spectral density is shown in Figure 62. The displacement phase of the fundamental disturbance is shown in red, shifted upwards slightly in the graph for clarity. Additional displacement noise caused by fringe-wrapping is evident at the 3rd and 5th harmonics of the fundamental disturbance. The total displacement noise is shown in cyan.

Figure 62: Scattered Light Displacement Noise Caused by Fringe-wrapping

## Scattered Light Parameters

The IFO parameters that were used for the scattered light calculations are listed in Table 18.

Table 18: IFO parameter values used for scattered light calculation

| PARAMETER | VALUE |
| --- | --- |
| IFO_length; | 4.00E+03 |
| IFO_beamwaist; | 1.15E-02 |
| IFO_beam_waist_RC; | 2.10E-03 |
| beam_radius_ITM; | 5.50E-02 |
| beam_waist_photodetector; | 5.00E-03 |
| beam_radius_Faraday; | 2.10E-03 |
| lambda; | 1.06E-06 |
| IFO_diffraction_angle; | 2.95E-05 |
| IFO_solid_angle; | 2.72E-09 |
| laser_power; | 1.25E+02 |
| recycling_cavity_power_gain; | 1.69E+01 |
| reflected_port_power_ratio; | 1.00E-03 |
| dark_port_signal_ratio; | 1.08E-03 |
| recycling_cavity_power; | 2.11E+03 |
| arm_cavity_power; | 8.34E+05 |
| ETM_transmitted_power; | 1.25E+01 |
| reflected_port_power; | 1.25E-01 |
| dark_port_power; | 1.35E-01 |
| ITM_transmissivity; | 5.00E-03 |
| ITM_HR; | 9.95E-01 |
| ETM_transmissivity; | 1.50E-05 |
| ETM_Reflectivity; | 1.00E+00 |
| PRM_AR_reflectivity; | 5.00E-05 |
| PRM_HR_transmissivity; | 2.12E-01 |
| SRM_AR_reflectivity; | 5.00E-05 |
| SRM_HR_reflectivity; | 9.60E-01 |
| SRM_HR_transmissivity; | 4.00E-02 |
| diameter_ETM; | 3.40E-01 |
| diameter_ITM; | 3.40E-01 |
| diameter_PRM; | 2.65E-01 |
| diameter_SRM; | 2.65E-01 |
| diameter_MMT3; | 2.65E-01 |
| Radius_Inner_Cryo; | 3.85E-01 |
| Radius_Beam_Tube; | 5.31E-01 |
| area_arm_cav_baffle; | 6.95E-01 |
| length_armcavbaf_wall; | 4.40E+00 |
| manifold_wall_length; | 1.40E+01 |
| manifold_wall_angle; | 6.64E-02 |
| manifold_wide_angle_scattering_efficiency; | 2.24E-20 |
| manifold_baffle_wide_angle_scattering_efficiency; | 8.84E-24 |
| BSC_wide_angle_scattering_efficiency; | 9.74E-22 |
| AC_Baffle_wide_angle_scattering_efficiency; | 5.83E-19 |
| AC_Baf_cyl_wide_angle_scattering_efficiency; | 1.14E-20 |
| Area_Arm_Cav_Baf_Hole; | 9.08E-02 |
| Length_Arm_Cav_Baf; | 1.00E+00 |
| Solid_Angle_COC_Wide_Angle; | 1.82E-01 |
| AP2_lens_focal_length; | 1.00E-01 |
| lens_AR_reflectivity; | 2.50E-03 |
| scatter_loss_Brewster_window; | 4.00E-05 |
| incident_angle_Faraday_crystal; | 1.70E-02 |
| back_transmission_Faraday_Isolator; | 1.00E-03 |
| Faraday_Tranmission; | 9.00E-01 |
| transmission_ETM_path; | 1.00E-02 |
| BRDF_elliptical_baffle_edge; | 5.00E-02 |
| BRDF_ETM_Tel_Baffle_Edge; | 5.00E-02 |
| BRDF_chamber_walls; | 1.00E-01 |
| BRDF_Nozzle; | 1.00E-01 |
| BRDF_photodetector; | 1.00E-03 |
| BRDF_ITMX_PO_steer_mirror; | 1.00E-05 |
| BRDF_COC_30urad; | 1.36E+03 |
| BRDF_elliptical_baffle; | 5.00E-03 |
| BRDF_arm_cav_baffle; | 5.00E-03 |
| BRDF_cryopump_baffle; | 5.00E-03 |
| BRDF_Brewster_window; | 1.00E-06 |
| BRDF_beam_dump; | 5.00E-03 |
| BRDF_ETM_Tel_Baffle; | 5.00E-02 |
| BRDF_lens; | 1.00E-03 |
| BRDF_Faraday; | 4.92E-04 |
| BRDF_manifold_baffle; | 5.00E-02 |
| BRDF_OMMT2; | 3.00E-03 |
| BRDF_Faraday; | 4.92E-04 |
| BRDF_COC_wide_angle; | 4.76E-06 |
| a; | 1.12E-01 |
| b; | 1.30E-01 |
| w; | 2.10E-03 |
| h; | 1.23E-01 |
| N_Cryopump_Baffles; | 4.00E+00 |
| N_Arm_Cavity_Baffle; | 4.00E+00 |
| N_Elliptical_Baffle; | 0.00E+00 |
| N_ETM_Tel_Baffle; | 2.00E+00 |
| N_Manifold; | 4.00E+00 |
| N_Surfaces_Faraday; | 5.00E+00 |
| N_Surfaces_Brewster; | 2.00E+00 |
| Scatter_Efficiency_Cryo_Baffle; | 3.32E-06 |
| Scatter_Efficiency_AC_Baffle; | 8.79E-06 |
| Scatter_Efficiency_Ellip_Baffle; | 3.51E-04 |
| Scatter_Efficiency_ETM_Tel_Baffle; | 3.90E-03 |
| Scatter_Efficiency_PRM_Ellip_Baffle; | 9.46E-05 |
| Scatter_Efficiency_Wide_Angle; | 1.50E-05 |
| cryopump_sus_length; | 4.00E-01 |
| cryopump_sus_freq; | 7.88E-01 |
| cryopump_sus_Q; | 1.00E+03 |
| arm_cavity_baf_sus_length; | 8.00E-01 |
| arm_cavity_baf_sus_freq; | 2.50E+00 |
| arm_cavity_baf_sus_Q; | 1.00E+03 |
| ellip_baf_sus_length; | 1.00E+00 |
| ellip_baf_sus_freq; | 4.98E-01 |
| ellip_baf_sus_Q; | 1.00E+03 |
| cav_bd_sus_length; | 1.00E+00 |
| cav_bd_sus_freq; | 4.98E-01 |
| cav_bd_sus_Q; | 1.00E+02 |
| Faraday_sus_length; | 4.00E-01 |
| Faraday_sus_freq; | 7.88E-01 |
| Faraday_sus_Q; | 1.00E+02 |
| reflectivity_ellip_baffle; | 2.40E-05 |
| reflectivity_arm_cav_baffle; | 2.40E-05 |
| reflectivity_cryopump_baffle; | 2.40E-05 |
| reflectivity_cavity_beam_dump; | 2.40E-05 |
| Reflectivity_Brewster; | 2.50E-03 |
| reflectivity_ETM_Tel_Baffle; | 7.00E-02 |
| reflectivity_manifold_baffle; | 7.00E-02 |
| Reflectivity_Faraday_AR; | 2.50E-03 |
| PRM_AR_transmissivity; | 1.00E+00 |
| PRM_HR_reflectivity; | 7.88E-01 |
| SRM_AR_transmissivity; | 1.00E+00 |

# Text boxes

Hartmann BS

PR2 GBAR0t

Hartmann BS

REFLECTION

PR2

HAM3

BS PO beam

SCATTER

PRM Elliptical Baffle

ITMX PO BEAM

HAM 4

ITMX PO MIR

SR2

SEISMIC SURFACE

ITM

ARM CAV BEAM

ITM ELLIPTICAL BAF

Septum window

SR3

HAM 5

HAM 3

PR2

PR2 BD

SR2 BD

PRM

PRM HR BD

PRM AR BD

HAM2

SRM HR BD

SRM AR BD

HAM5

SRM

PR2 AR BD

PR2

PR2 HR BD

HAM3

HAM4

SR2 AR BD

SR2

SR2 HR BD

HAM2

PR3 AR BD

PR3

HAM5

SR3 AR BD

SR3

HAM 5

Beam Dump

ITMX PO

SR2 leakage

SR2

Hartmann Viewport

Hartmann Viewport

SR2 AR0t BD

SR2

HAM 6