| AUTHOR(S) | DATE | Document Change Notice, Release or Approval |
| --- | --- | --- |
| Dwayne Giardina, David Shoemaker, Matthew Heintze, Bryan Smith, Bobby Moore, Janeen Romie, Derek Bridges | November 5, 2012 | See LIGO DCC record status |

- Introduction

This document outlines the method of assigning names and serial numbers to parts and assemblies for use with LIGO’s Inventory Control System (ICS).  This document covers the naming and numbering conventions only for the Suspensions subsystem.  The primary goal of these naming and numbering conventions is to establish a uniform system in ICS to be followed at all LIGO sites, so that communication and information sharing within in a site and between sites is faster and simpler.

- Why Follow Naming and Numbering Conventions?

It is critical that the physical aspects of the parts and assemblies match the virtual aspects in ICS.  The locations of parts and assemblies and their clean/bake/assembly status should be accurately recorded in ICS at all times.  It is the responsibility of everyone involved in handling parts to generate and maintain a correct, complete and consistent inventory of the parts in ICS.

The ICS system is not just for the convenience of everyone within LIGO; it is also designed to fulfill an NSF requirement for tracking of their purchases.  LIGO has invested a large amount of time and money in the ICS system for this purpose.  If an NSF auditor arrives at a site next week and asks research scientist "John Doe" to find a particular part in ICS and then locate and show them a part, John Doe should be able to do this without having to track down an Excel spreadsheet that contains data not stored in ICS.  Accurate and timely updates of parts and assemblies and their status in ICS will ensure that LIGO meets these guidelines.

- Naming and Numbering Guidelines

ICS uses the following fields to record information about a given part or assembly.  The naming and numbering of the ICS records is defined for each field below.

  - Assembly or Part Name – This is taken from the title block of the assembly or part drawing on the DCC.

  - Assembly ID (for assemblies) or Drawing (for parts) – This is the drawing number of the assembly or part on the DCC; all drawing numbers start with the letter D.

  - Serial # – This is the serial number of a specific assembly or part; the serial number of an assembly comes from the serial number of a particular part in the assembly, as defined in the following tables

    - Note: Serial numbers of some top-level suspension assemblies (e.g., a Quadruple Pendulum Suspension) will not be taken from a part in the assembly; instead, the serial number will match the number used during assembly and testing (e.g., the second quad built at LLO is referred to as Quad 13 during assembly and testing, so the serial number will be 13).  The serial number will be indicated on the actual assembly in a method TBD (inscribed stainless steel tags?).  Other top-level suspension assemblies (e.g., HLTS and HSTS) will have the same serial number as the structure assembly and may be assembled and tested out of numerical order.

In some cases, it may not be possible to find the serial numbers of some parts after assembly.  If the serial numbers of all of the parts in an assembly are known, but the exact position is not known, enter the part under the lowest-level assembly that is known.  For example, in a Quad Suspension, part number D080167 belongs in the assembly with the Assembly ID of D080166 (with four parts and four assemblies for each Quad Suspension).  If the serial numbers for the four D080167 parts are known, but the exact position is not, enter the D080167 parts under the assembly with the Assembly ID D060341 (which is also where the D0801666 assemblies are entered).

Table 1: Quadruple Pendulum (Quad) Suspension Subassemblies

| Assembly Name | Assembly ID | Part Number Used for Assembly Serial Number | Notes |
| --- | --- | --- | --- |
| Quad Suspension Assembly | D0901346 | N/A | Use the Build Number as the assembly serial number. |
| Tablecloth Assembly | D060310 | D060312 |  |
| OSEM and ECD Adjuster | D060316 | D060318 |  |
| OSEM Adjustment Plate | D060320 | D060321 |  |
| Transverse OSEM Adjuster | D060322 | D060323 |  |
| Blade Cartridge, Top Stage | D060324 | D0901439 | Assemblies can be split into 4 parts, one for each blade (i.e. 001A, 001B, 001C, 001D) |
| Penultimate Mass Assembly, Reaction Chain | D060341 | D060342 |  |
| Pitch Mass Assembly, Penultimate Reaction Mass | D060352 | D060353 |  |
| OSEM Can, Penultimate Reaction Mass | D080166 | D080168 (ETM Only) D1002200 (ITM Only) | For D080166 in ITM suspensions, add 1000 to the serial number. |
| Dummy Test Mass Assembly, Main Chain | D060355 | D060358 | Each D060355 contains 2X D060358; use the lower serial number. |
| Dummy Test Mass Assembly, Reaction Chain | D060356 | D060357 | Each D060356 contains 2X D060357; use the lower serial number. |
| Upper Intermediate Mass Assembly, Main Chain | D060375 | D060376 |  |
| Top Mass Assembly, Main Chain | D060403 | D060430 |  |
| OSEM and ECD Unit | D060409 | D060407 |  |
| Inner Lower Structure | D060454 | D060434 | Each D060454 contains 2X D060434; use the lower serial number. |
| Adjustable Pad Assembly, Long | D060446 | D060447 |  |
| Adjustable Pad Assembly, Short | D060457 | D060459 |  |
| Earthquake Stop Assembly #1, Upper Intermediate Mass, Main Chain | D070540 | D070545 |  |
| Earthquake Stop Assembly #1, Upper Intermediate Mass, Reaction Chain | D070541 | D070546 |  |
| Earthquake Stop Assembly #2, Upper Intermediate Mass, Reaction Chain | D070542 | D070547 |  |
| Earthquake Stop Assembly #2, Upper Intermediate Mass, Main Chain | D070543 | D070544 |  |
| Upper Structure Weldment | D060492 | D060492 | There are parts with the part number D060492; these should be placed in an assembly with same number. |
| Top Mass Assembly, Reaction Chain | D0902031 | D060430 |  |
| Dummy Penultimate Mass Assembly, Main Chain | D0902075 | D060358 | Each D0902075 contains 2X D060358; use the lower serial number. |
| Upper Intermediate Mass Assembly, Reaction Chain | D0902233 | D060376 |  |
| Dummy Thin Compensator Plate, Reaction Chain | D1002204 | D1002205 | Each D1002204 contains 2X D1002205; use the lower serial number. |
| Main Chain Wire Assemblies | D1100041 | N/A | Use the Build Number prefixed by Q as the assembly serial number (i.e. Q11). |
| Top Wire Assembly | D0902643 | D060390 |  |
| Middle Wire Assembly | D0902644 | D060395 |  |
| Bottom/Final Wire Assembly | D0902645 | D060426 |  |
| Reaction Chain Wire Assemblies | D1100042 | N/A | Use the Build Number prefixed by Q as the assembly serial number (i.e. Q11). |

Table 2: Beamsplitter/Folding Mirror (BS/FM) Subassemblies

| Assembly Name | Assembly ID | Part Number Used for Assembly Serial Number | Notes |
| --- | --- | --- | --- |
| Beamsplitter/Folding Mirror Main Assembly | D1000392 | N/A | Use the Build Number as the assembly serial number. |
| Top Mass Assembly | D070435 | D070422 |  |
| OSEM and ECD Unit | D060409 | D060407 |  |
| Pitch Adjuster and Mass, Top Mass | D070424 | D070423 |  |
| Blade Clamp Assembly #1, Top Mass | D080042 | D070418 |  |
| Blade Clamp Assembly #2, Top Mass | D080043 | D070421 |  |
| Lower Structure | D080005 | D080006 |  |
| Top Stage | D080080 | D080081 |  |
| Blade Clamp Assembly, Top Stage | D080082 | D080086 |  |
| Top Tablecloth | D080105 | D080106 |  |
| OSEM and ECD Adjuster | D060316 | D060318 |  |
| OSEM Adjustment Plate | D060320 | D060321 |  |
| Transverse OSEM Adjuster | D060322 | D060323 |  |
| Bottom Tablelcloth | D080111 | D080112 |  |
| Penultimate Mass | D080368 | D080369 |  |
| Upper Structure | D080501 | D080504 |  |
| Top Wire Assembly | D1100039 | D080087/D080088 |  |
| Blade Wire Clamp Assembly, Top Stage | D080087 | D080088 |  |
| Middle/Lower Wire Assembly | D1100040 | D080559/D080560 | Each D1100040 contains 2X D080559; use the lower serial number. |
| Modified D Penultimate Mass Clamp | D080559 | D080560 |  |
| Test Mass Dummy | D1100249 | D080369 |  |

Table 3: HAM Large Triple Suspension (HLTS) Subassemblies

| Assembly Name | Assembly ID | Part Number Used for Assembly Serial Number | Notes |
| --- | --- | --- | --- |
| HLTS Overall Assembly | D070447 | D070442 |  |
| Mounting Pad Assembly, HLTS | D0900626 | D070374 |  |
| Rotational Adjuster, HLTS | D070326 | D070328 |  |
| Upper Wire Assembly, HLTS | D070340 | D020652 |  |
| Upper Mass Assembly, HLTS | D070335 | D020605 |  |
| Intermediate Wire Assembly, HLTS | D070393 | D030149 |  |
| Intermediate Mass Assembly, HLTS | D070334 | D070336 |  |
| Lower Loop Wire Assembly, HLTS | D070438 | D030148 | Each D070438 contains 2X of D030148; use the lower serial number of the 2. |
| Bottom Mass Assembly, HLTS | D070337 | D070338 |  |
| Top Blade Guard Assembly, HLTS | D070308 | D070310 |  |
| Earthquake Stop Assembly, Bottom Mass, Upper, HLTS | D080728 | D070354 |  |
| Earthquake Stop Assembly, Bottom Mass, Lower, HLTS | D1002821 | D1002823 |  |
| Earthquake Stop Assembly, Bridge, Upper, HLTS | D1102071 | D070321 |  |
| Coil Holder Assembly, HLTS | D080677 | D070449 |  |
| Mounting Bracket, Coil Holder, HLTS | D1002133 | D1002135 |  |
| Upper AOSEM Alignment Assembly, Intermediate Mass, HLTS | D0902024 | D0901492 |  |
| Lower AOSEM Alignment Assembly, Intermediate Mass, HLTS | D0901551 | D0901492 |  |
| Upper AOSEM Alignment Assembly, Bottom Mass, HLTS | D0901552 | D0901549 |  |
| Lower AOSEM Alignment Assembly, Bottom Mass, HLTS | D0901553 | D0901549 |  |

Table 4: HAM Small Triple Suspension (HSTS) Subassemblies

| Assembly Name | Assembly ID | Part Number Used for Assembly Serial Number | Notes |
| --- | --- | --- | --- |
| HSTS Overall Assembly | D020700 | D020023 |  |
| Rotational Adjuster Assembly, HSTS | D1000045 | D030447 |  |
| Upper Wire Assembly, HSTS | D0901854 | D020481 |  |
| Upper Mass Assembly, HSTS | D020534 | D020134 |  |
| Intermediate Wire Assembly, HSTS | D0901905 | D0901904 |  |
| Intermediate Mass Assembly, HSTS | D0901873 | D0901792 |  |
| Lower Wire Assembly, HSTS | D0901902 | D020202 (previous design) D1200108 (current design) | Each D0901902 contains two of D020202 or D1200108; use the lower serial number of the two. |
| Metal Lower Mass Assembly (MC), HSTS | D0901791 | D020234 |  |
| Metal Lower Mass Assembly (PR/SR), HSTS | D0902333 | D0902332 |  |
| Metal Lower Mass Assembly (SRM), HSTS | D1200886 | D1200846 |  |
| Top Blade Guard Assembly, HSTS | D0901934 | D0901935 |  |
| Face Earthquake Stop Assembly, Intermediate Mass, HSTS | D0902413 | D0901923 |  |
| Barrel Earthquake Stop Assembly, Intermediate Wire, HSTS | D0902203 | D0901925 |  |
| Barrel Earthquake Stop Bracket Assembly, HSTS | D0902007 | D0902008 |  |
| Barrel Earthquake Stop Assembly, Lower Wire, HSTS | D0902201 | D0902202 |  |
| Face Earthquake Stop Assembly, Lower Mass, HSTS | D0902205 | D0901923 |  |
| Upper Mass and Coil Holder Assembly, HSTS | D020535 | D020239 |  |
| AOSEM Alignment Assembly, Intermediate Mass, HSTS | D0901924 | D0902414 |  |
| Upper AOSEM Alignment Assembly, Lower Mass, HSTS | D0902207 | D0902417 |  |
| Lower AOSEM Alignment Assembly, Lower Mass, HSTS | D0902208 | D0902417 |  |

Table 5: Output Mode Cleaner Suspension (OMC SUS) Subassemblies

| Assembly Name | Assembly ID | Part Number Used for Assembly Serial Number | Notes |
| --- | --- | --- | --- |
| OMC Overall Assembly | D0900295 | N/A | Top-level assembly serial number is to match number used during assembly and testing. |
| Structural Weldment Assembly, OMC | D0900655 | D0900308 |  |
| Rotational Adjuster Assembly, OMC | D030451 | D030447 |  |
| Upper Wire Assembly, OMC | D060536 | D070030 |  |
| Upper Mass Assembly, OMC | D060502 | D060491 |  |
| Lower Wire Assembly, OMC | D060537 | D020132 |  |
| Metal Bench Assembly, OMC | D070035 | D070027 |  |
| Top Blade Guard Assembly, OMC | D070145 | D070146 |  |
| Coil Holder Assembly, OMC | D1201213 | D060530 |  |
| Upper Earthquake Stop Assembly, Optical Bench, OMC | D1201214 | D070049 |  |
| Side Earthquake Stop Assembly, Optical Bench, OMC | D1201215 | D070484 |  |
| Lower Earthquake Stop Assembly, Optical Bench, OMC | D1201216 | D070050 |  |