LASER INTERFEROMETER GRAVITATIONAL WAVE OBSERVATORY

LIGO

CALIFORNIA INSTITUTE OF TECHNOLOGY

MASACHUSETTS INSTITUTE OF TECHNOLOGY

LIGO -E1100491-v6 12/07/11

LLO SLC Mode Cleaner Tube Baffle Install Hazard Analysis

Authors – Mike Smith, Christopher Guido, Lisa C. Austin

LIGO Hanford Observatory		LIGO Livingston Observatory

P.O. Box 1970; Mail Stop S9-02		19100 LIGO Lane

Richland, WA 99352			Livingston, LA 70754

Phone (509) 37208106			Phone (225) 686-3100

Fax (509) 372-8137				Fax (225) 686-7189

E-mail: info@ligo.caltech.edu		E-mail: info@ligo.caltech.edu

California Institute of Technology		Massachusetts Institute of Technology

LIGO – MS 100-36				LIGO – MS NW22-295

Pasadena, CA 91125				Cambridge, MA 01239

Phone (626) 395-2129				Phone (617) 253-4824

Fax (626) 304-9834				Fax (617) 253-7014

E-mail: info@ligo.caltech.edu		E-mail: info@ligo.mit.edu

APPROVAL SIGNATURES

___________________________________________________________

Eric Gustafson, AOS Group leader					  Date

__________________________________________________________

Michael Smith, SLC Task Leader					  Date

__________________________________________________________

David Nolting, LIGO Lab Safety Officer 				Date

__________________________________________________________

John Worden, LHO Site Safety Officer 				Date

__________________________________________________________

Rusyl Wooley, LLO Site Safety Officer 				Date

__________________________________________________________

Brian O’Reilly, Advanced LIGO LLO Installation Lead 		Date

__________________________________________________________

Michael Landry, Advanced LIGO LHO Installation Lead 		Date

__________________________________________________________

David Shoemaker, aLIGO Leader					Date

__________________________________________________________

Albert Lazzarini, LIGO Directorate 					Date

CHANGE LOG

| Date, version | Summary of Changes |
| --- | --- |
| 2011-10-28 V2 | Added more detail to V1 Updated section 2 (Summary of Hazards) Added 3 new hazards and their respective details Updated section 4 (Related Documents) |
| 2011-11-29 V3 | Updated Title Add detail in regards to gloves being pinched Updated Severity table |
| 2011-12-05 V4 | Remove reference to Assembly and Installation version |
| 2011-12-06 V5 | Changed required personnel from 3 to 5 Specified that clean practices must be followed rather than should be followed Added more detail to “Summary of Hazards” (section 2) Updated Related Documents Section |
| 2011-12-07 V6 | Added inspection concerns to section 5.3 Added O2 level check prior to start of installation (section 3) |

- Scope

This document covers safety concerns related to the assembly and installation of the Mode Cleaner Tube Baffles into the manifold tubes for Advanced LIGO. It must be read before beginning the installation of the Mode Cleaner Tube Baffle, and used in conjunction with the SLC Mode Cleaner Tube Baffle Assembly and Installation Procedure, document number LIGO-E1100718.

- Summary of Hazards

There are 4 Hazards to be concerned with in the installation of the Mode Cleaner tube baffles

- Strain from holding/ and lifting the larger parts

- Bumping one’s head or body in the tighter spaces of the viewport adapter flanges and mode cleaner tubes

- Pinching/ Cutting of hands against the parts being assembled

- Contamination hazard of the vacuum system

- Overview

A Solid Works model of one of the Mode Cleaner Tube Baffles (MCA1) is shown in Figure 1. The baffles are installed at each end the mode cleaner tubes. MCA1 is installed next to HAM 2, MCB1 is installed next to HAM 3, MCB2 is installed next to HAM 4, and MCA2 is installed next to HAM 5. Though the baffles are slightly different in design, they are installed with same procedure as described in E1100718.

As work will be done in a semi-enclosed space, O2 levels should be measured in the area of work (Input mode cleaner tube, etc) prior to the start of the work.

The baffles must be installed before both HAM tables (for the respective arm under installation) are occupied with their optics.

At least 5 personnel are required to perform this installation. Two people will be required to remain outside the vacuum chamber, and the other three will be working within the vacuum chamber and tubes.

- The outer support ring for the baffle is inserted and expanded inside the mode cleaner tube.

- In a clean room, the outer annular portion of the baffle is pre-assembled in halves. Afterwards, each half is handed through the HAM chamber opening at the end of the mode cleaner tube to the people inside the viewport adapter tube, who carry it to the person inside the mode cleaner tube.

- The person inside the mode cleaner tube will connect the two halves of the annular portion to the outer support ring, and then exit the mode cleaner tube.

- Inside a clean room, the inner portion of the baffle is pre-assembled in halves and handed to the people standing just outside the opening to the mode cleaner tube. From this position, the inner portion of the baffle will be attached to the annular portion.

During the assembly and installation of the Mode Cleaner Tube Baffle, a task leader shall be assigned to supervise all activities and this person may count as one of the five required personnel.

This assembly and installation requires overall common sense and good lab practices. Personnel must have good working knowledge of how to safely use the tools associated with the build. All personnel must have appropriate safety training to work at a LIGO facility and must be knowledgeable with the contents of E1100718.

Figure 1) Installed MCA1 Baffle by Ham 2

- Related Documentation

- LIGO-E1100718: SLC Mode Cleaner Tube Baffle Assembly and Installation Procedure

- LIGO-M070360: Advanced LIGO Safety: Processes and Guidelines

- LIGO-M950046: LIGO Project System Safety Plan

- LIGO- E0900047: Contamination Control Plan

- LIGO-E000065: Chamber Entry/Exit Checklist

- LIGO-T1000629: aLIGO General Safety Rules for De-Install/Install Activities

# Hazard Analysis

Each hazard and mitigation approach or measure is listed in the severity table in the next section.

5.1 Lifting Strain

Each Piece of the baffle weighs no more than 35 lbs; however, some pieces are as long as 7ft and as wide as 3ft, which may make it cumbersome to hold and pass along. Personnel should be aware of their surroundings when passing pieces along as to not damage nearby objects and the pieces themselves. Should prolong lifting occur, personnel should find a way to cleanly offload the weight or secure the piece to avoid strain. This strain can be mitigated by utilizing two personnel to pass and hold the various pieces.

5.2 Vacuum Spatial Awareness

As there will need to be assembly inside the vacuum chamber, personnel should be mindful of where they stand and move as to not damage nearby objects and bump their heads, knees, etc. Damage from accidental bumps can be mitigated from being spatially aware of the working area and by spotting one another.

5.3 Pinching/Cutting of Hands

The individual pieces of the baffle are thin pieces of metal, and though the edges have been beveled, there is a potential to receive cuts if parts are handled improperly. Not only this, but should a glove tear due to cuts, there is a potential to cause contamination problems. Hands may also be pinched when assembling parts to one another, but this can be mitigated with proper attention to how parts are handled. The team must inspect all parts before handling to identify locations of potential hazards (sharp edges and the like).

5.4 Vacuum Contamination

The vacuum system will be opened during this installation process and has the potential to be contaminated. All work must be done in positive pressure clean rooms and all personnel must be garbed in appropriate Class A garb. Standard Class A procedures must be practiced at all times.

# 6.  Hazard Analysis Severity Table

|  |  |  | PROBABILITY |  |  |
| --- | --- | --- | --- | --- | --- |
| SEVERITY OF | E | D | C | B | A |
| CONSEQUENCE | Improbable | Remote | Occasional | Probable | Frequent |
| 1 |  |  |  |  |  |
| Catastrophic |  |  |  |  |  |
| 2 |  |  |  |  |  |
| Critical |  |  |  |  |  |
| 3 |  |  |  |  |  |
| Marginal |  |  |  |  |  |
| 4 |  |  |  |  |  |
| Negligible |  |  |  |  |  |
| Hazard Risk Index |  |  | Risk Code Criteria |  |
| 1A, 1B, 1C, 2A, 2B, 3A |  | Unacceptable |  |  |
| 1D, 2C, 2D, 3B, 3C |  | Undesirable (Directorate decision required) |
| 1E, 2E, 3D, 3E, 4A, 4B |  | Acceptable with review by Directorate |
| 4C, 4D, 4E |  | Acceptable without review |  |