LASER INTERFEROMETER GRAVITATIONAL WAVE OBSERVATORY

-LIGO-

CALIFORNIA INSTITUTE OF TECHNOLOGY

MASACHUSETTS INSTITUTE OF TECHNOLOGY

LIGO- E1100718-v7 01/05/2012

SLC Mode Cleaner Tube Baffle Assembly and Installation Procedure

Michael Smith, Lisa C. Austin, Tim Nguyen, Stephany Foley, Heidy Kelman

LIGO Hanford Observatory		LIGO Livingston Observatory

P.O. Box 1970; Mail Stop S9-02		19100 LIGO Lane

Richland, WA 99352			Livingston, LA 70754

Phone (509) 37208106			Phone (225) 686-3100

Fax (509) 372-8137				Fax (225) 686-7189

E-mail: info@ligo.caltech.edu			E-mail: info@ligo.caltech.edu

California Institute of Technology		Massachusetts Institute of Technology

LIGO – MS 18-34				LIGO – MS NW22-295

Pasadena, CA 91125				Cambridge, MA 01239

Phone (626) 395-2129				Phone (617) 253-4824

Fax (626) 304-9834				Fax (617) 253-7014

E-mail: info@ligo.caltech.edu		E-mail: info@ligo.mit.edu

1	Scope	3

2	Clean room standards	4

3	Assembly and Installation Overview	5

4	Mode Cleaner Tube Baffle Ring Assembly	7

4.1	Top Ring Assembly (on workbench)	7

4.2	Bottom Ring Assembly (on workbench)	9

5	Mode Cleaner Tube Baffle Framing Assembly	11

5.1	Upper Viewport Framing Assembly (on workbench)	11

5.2	Lower Viewport Framing Assembly (on workbench)	16

Lower assembly viewport for MCA3 (on workbench)	19

5.3	Aperture Framing Assembly (on workbench)	22

6	Installation of Ring Assembly into beam tube	26

7	Install Viewport Framing	30

7.1	Install the Upper Viewport Framing Assembly	30

7.2	Install the lower viewport framing	32

8	Install Aperture Plates of Mode Cleaner Tube Baffle Assembly	35

# Scope

This document describes the assembly and installation procedures for the Mode Cleaner Tube Baffle Ring Assembly, D1002863 and the Mode Cleaner Tube Baffle Assembly, D1002864.

# Clean room standards

For a clean assembly all LIGO standards should be followed, as presented in the latest version of the LIGO Contamination Control Plan (E0900047). Clean room garb including UHV gloves should be worn when working with parts.

All tools that come in contact with assembly should be cleaned to class B standards.

Assembly will be done under a portable clean room. Any time a part of the assembly is not covered by the portable clean room or not being actively worked on it should be covered with appropriate clean covers. (C3 polyester or equivalent).

All parts that will be included in the final assembly must be cleaned to LIGO standards, Class A. The list of parts to be Class A-cleaned includes screws, washers, inserts, and assorted other hardware. All tooling and other parts that are not included in the final assembly, but that contact Class A parts during assembly must be cleaned to LIGO standards, Class B.

Notes for all Subassembly:

Installation requires three people

Installers will be inside the beam tube

The parts weigh between 20-30 lbs

# Assembly and Installation Overview

- Assemble top and bottom outer rings of Mode Cleaner Tube Baffle Ring, D1102863

- Assemble Viewport Framing Assemblies (D1002864)

- Assemble Aperture Framing Assemblies (D1002864)

- Install Ring into tube.

- Install Viewport Framing Assemblies, left and right.

- Install Aperture Assemblies (D1002864)

The Mode Cleaner Tube Baffle Ring (D11002863) is assembled on a workbench and then installed into the input and output mode cleaner tubes.

Three installers will be needed:  One person stands inside the mode cleaner tube; one person stands in the viewport adapter tube; and a third person hands the parts through the door of the HAM chamber. The parts weigh between 20-30 lbs and can be carried by a single person.

The Ring is installed by the person standing inside the mode cleaner tube.

Next, the outer viewport ring assembly, in two semicircular pieces, are passed through the door of the HAM chamber and handed to another person standing in the viewport adapter just outside the opening to the mode cleaner tube, who hands the parts to the person inside the mode cleaner tube.

After the viewport ring assembly is installed, the person inside the mode cleaner tube exits and stands together with the person in the viewport adapter tube.

Next the Mode Cleaner Tube Baffle (D11002864) is assembled on a workbench and installed into the input and output mode cleaner tubes at the location of the newly installed Ring.  The central portion of the Baffle is brought inside the viewport adapter tube in two semicircular pieces. The bottom piece is rested on the bottom of the mode cleaner tube between the viewports and the already installed Ring, as shown in Figure 2.

The top piece is attached to the Ring from the outside; and then the bottom piece is attached to the Ring.

See Figures 1 and 2.

Figure 1: MCA1, H1-L1, HAM2

Figure 2: Bottom Central Portion of Baffle Sitting inside Mode Cleaner Tube

# Mode Cleaner Tube Baffle Ring Assembly

Refer to MODE CLEANER TUBE BAFFLE RING ASSEMBLY Drawing D1002863 for BOM and drawing.

## Top Ring Assembly (on workbench)

### In cleanroom, lay down MC Tube baffle ring _top (D1000777) on the workbench, with chamfer side facing upward.  Position D1000784, Mount standoff spacer on 45 degree to the left, attach with two washers (WF-10) and 10-32 x ¾ L SHCS (C-1012-N).

### Attach D1000780, Center Mount bracket top  at 45 degree to the right on the same ring, attach with two 10-32 x  ¾” L Socket head Cap screw (no washer).

### Screw entire threaded portion of D1000778(Turn buckle screw) into each end of the ring-top, D1000777.

## Bottom Ring Assembly (on workbench)

### Place D1000776 on workbench supported by four D1102164 (3¼” Aluminum block) with chamfer side facing upward. Position D1000779, Center mount bracket bottom at 45 degree to the right on the left, attach with two C-1012-N.

### Attach D1000779 on 45 degree to the left with two 10-32 x ¾ L SHCS (C-1012-N), no washer.

### Attach D1000783, Mount Standoff spacer_ right on 45 degree to the right with two 10-32 x ¾ L SHCS (C-1012-N), no washer.

# Mode Cleaner Tube Baffle Framing Assembly

See Drawing D1002864.

## Upper Viewport Framing Assembly (on workbench)

### Place D1002867 (Mode Cleaner Tube Baffle Upper Brace) on the workbench, with tapped holes facing upward.

### Align D1100121*( Inner upper left brace) to be concentric inside of D1002867.  Make sure four tapped holes face upward.

### * Install D1002869 instead of D1100121 for all baffles except MCA1.

### Attach four D1002871 between D1002867 and D1100121* using BU-2016-N (1/4-20 x 1"L BHCS) with a washer (WF-25) on both ends.  Tapped holes face downward and toward D1100121.

### * Install D1002869 instead of D1100121 for all baffles except MCA1.

### Set D1100277 to be concentric inside of D1002867.  There is a gap between D1100277* and D1100121*.  Two tapped holes face upward.

*  Install D1002869 (instead of D1100277 and D1100121) for  MCA2, MCA3, MCA4, MCB1, MCB2, MCB3, and MCB4 baffles.

Attach two more D1002871 between D1002867 and D1100277 using BU 2016-N (1/4-20 X 1" BHCS) and WF-25 (1/4" washer) on both ends.

### At this time, all BU-2016-N screws are not quite tightened because theymight need to loosen to line up holes.

### Place D1101150* with Super #8 finish facing upward on top of assembled parts.  Match half moon cutout with gap.

* D1003118-00 to be installed for MCA2, MCA3, and MCA4.

D1003118-01 to be installed for MCB1

D1003118-02 to be installed for MCB2

D1003118-03 to be installed for MCB3

D1003118-04 to be installed for MCB4

### Clearance holes in viewport plate should align with tapped holes on rings. Attach with BU-1006-N(10-32 X 5/8"L BHCS, SS) and WF-10 (#10 SS Washer), 14 places.

### Make sure workbench is clear and covered with ??? to protect Super #8 surface.

### Turn the Viewport Framing Assy over and place D1101159 on D1002871 (the spoke). Attach with C-1010-N (10-32 X 5/8"L, SHCS, SS) and WF-10 (#10 Washer, SS), 2 places.

## Lower Viewport Framing Assembly (on workbench)

### Place D1001926 (Mode Cleaner Tube Baffle Lower Brace), on the workbench,  with tapped holes facing upward.

### Set D1002868* to be concentric inside the D1001926 ring.  Use BU-2016-N (1/4-20 X 1"L, BHCS, SS) and WF-25 (#1/4 Washer) to connect 2 rings with D10002871. Make sure these threaded tap holes are facing upward.

*  D1100312 and D1100350 to be used instead of D1002868 for MCA3.

### Attach five D1002871 between D1002867 and D1100121* using BU-2016-N (1/4-20 x 1"L BHCS) with a washer (WF-25) on both ends.  Tapped holes face downward and toward D1100121.

### * Install D1002869 instead of D1100121 for all baffles except MCA1.

At this time, all BU-2016-N hardware is not quite tightened because they might need to loosen to line up holes.

### Prepare to bring D1003119-00* on top of assembled parts.  (MCA1,2,4)

Note:  D1101152 to be installed for MCA3

D1003119-01 to be installed for MCB1

D1003119-02 to be installed for MCB2

D1003119-03 to be installed for MCB3

### D1003119-04 to be installed for MCB4

### Clearance holes in viewport plate should align with tapped holes on rings.  Attach with BU-1006-N (10-32 X 5HCS, SS) and WF-10 (#10 Washer, SS).

BU-1006-N and WF-10

Lower assembly viewport for MCA3 (on workbench)

5.2.1    Place D1100312 to be concentric to D1001926. First and second tapped holes of D1100312 face upward.

5.2.2   Lay D1100350 concentric to D1001926 and match with D1100312.  Last tapped hole at end of D1100350 faces upward.

5.2.3 Repeat step 5.2.4 for fastening outer and inner rings with D1002871.

5.2.4  Set D1101152 on top of assembled parts.  Make sure half-moon cutout match a gap of two inner rings. Super #8 finish side is up

5.2.5  Follow step 5.2.6 to fasten viewport plate to assembled parts.

### Make sure workbench is clear and covered with ??? to protect Super #8 surface.

### Turn the Viewport Framing Assy over and place D1101160 (the spoke). Attach with C-1010-N (10-32 X 5/8"L, SHCS, SS) and WF-10 (#10 Washer, SS), 2 places.

## Aperture Framing Assembly (on workbench)

## Aperture assembly for MCA1 and MCA3.  No framing involved.    Plates attach directly to viewport assembly.

D1100468 and D1100469 to be installed for MCA1

D1100512 and D1100513 to be installed for MCA3

Aperture Framing Assembly (on workbench) for MCA2, 4, MCB1, 2, 3, 4.

MCA2 and MCA4 have same parts and orientation.

Place D1002996, 2 pieces of D1002998 and D1002997 with tapped holes facing upward on workbench.  Use C-1014-NA (10-32 X 7/8"L, SHCS, SS) with WF-10 (#10 washer, SS)  to tighten them together.

D1002998

C-1014-NA & WF-10

5.3.2 Place D1003109 on top of structure frame.

Super #8 finish faces upward.  Be careful to handle aperture plate.

5.3.3 Insert BU-1006-NA with WF-10 to secure the aperture plate to structure frame.

BU-1006-NA with WF-10

5.3.4 Attach D1101973 to ends of the aperture to stiffen aperture assembly when carrying it to the tube.

5.3.5 Use 10-32 screw with wing nut to hold up aperture assembly while carrying them to the tube.

Refer to drawing D1102116_MC Tube baffle, Aperture Support Bar Assembly

Insert 10-32 SHCS with #10 washer though aperture plate and D1101973 and tighten with wing nut.  Do it same for the other end.

10-32 SHCS and wing nut

# Installation of Ring Assembly into beam tube

### Carry the top and bottom ring separately.  Transport D1000776 into the bottom of Mode Cleaner tube section and set in position. Next place D1000777 above D1000776 and align D1000778 (turn buckle) into the holes at the ends of D1000776.  The orientation of the rings are such that the chamfered edges is away from the closest HAM chamber (toward the tube).

D1000778

Clearance hole on D1000776

### Place Alignment tooling, D1101756 between the flat surfaces of these rings against inside wall of the tube.  See view above.

Attach plumb bob:  Attach eyebolt to the top ring with .064 Dia. Wire and plumb bob at the end of the wire.

6.1.4.   Calibrate the plumb bob to line up concentrically to a hole of the bottom ring.  Use plumb bob and alignment block to align rings in the tube.

### Use 3/8” wrench to torque D1000778 (turn buckles screws) evenly so each half ring places against the tube and make sure to remove the D1101756 (alignment tool) when the ring is in place.

### Make sure standoff spacers (D1000783, D1000784) and mount bracket (D1000779, D1000780) are tight.

# Install Viewport Framing

See Drawing D1002864.

## Install the Upper Viewport Framing Assembly

MCA1 at HAM 2-H1

### Bring the upper viewport plate framing through the chamber and into the mode cleaner tube section.  Place diagonally to be mounted to top half of the ring. Be careful to align the upper viewport plate framing behind brackets and standoff spacer.

Tip: For MCA1, the half-moon cutout is shown on the left viewport plate.

Half-moon cutout                 See Fig 7.1.3

See next page                                                         See next page

### Insert one C-1012-N (10-32 X 3/4"L, SHCS, SS) with one WF-10 (#10 washer, SS) to tighten each end of the viewport plate to the brackets.

### Use two C-1012-N to attach the middle of the left viewport plate to the bracket.

## Install the lower viewport framing

MCA1 at HAM2-H1

### Carry the lower viewport plate framing assembly and place it behind the brackets and standoff spacers on the ring. Attach C-1012-N with WF-10 to mount it on the ring.

See Fig 7.2.2

### Insert two C-1012-N without WF-10 to secure the middle of the right viewport plate framing.

Fig.7.2.2

### From the back side of the baffle ring, attach both viewport assemblies with a      C-2024-N(1/4-20 X 1.5"L, SHCS, SS), N-2520-NA (1/4" Hex Nut, SS) and two WF-25 (1/4" Washer, SS).  This applies to all assemblies.

C-2024-N with WF-25 and N-2520-NA

Fig.7.2.3

# Install Aperture Plates of Mode Cleaner Tube Baffle Assembly

(See Drawing D1002864 for complete BOM and drawings)

Assemble aperture plates on viewport ring of MCA1

### Carry D1100468 (MCA1 Upper Aperture) into the tube and set it up against the inner frame.  Use nine of C-1010-N(10-32 X 5/8"L, SHCS, SS) with WF-10(#10 Washer, SS) to bolt the aperture plate to inner frame.*  Make sure cutout of the aperture plate match the half-moon of viewport plate.

*Tip:  Line up visible holes to threaded tapped holes of the inner ring. Secure center top hole with one C-1010-N and WF-10 so it can hang loosely on the inner ring, then insert the rest of C-1010-N with WF-10 into tap holes as shown.

Center top hole

### Match the cutout of D110468 to half-moon on viewport plate.

C-1010-N with WF-10

Leave these tapped holes unscrewed

### Bring in D1100469 to set it so cutouts to be matched to upper aperture and half-moon on viewport plate and align all visible holes*.

C-1010-N with WF-10

*Tip:  After matching cutouts with other plates, let it rest on bottom of the tube.  Hold one side of the aperture and align with a tap hole on the side (either left or right side), then insert a C-1010-N with WF-10 to keep it in place.  Hold up other side to align with tap hole and repeatedly insert C-1010-N with WF-10.

Left side of the aperture                                               C-1010-N plus WF-10

Right side of the aperture

C-1010-N and WF-10

\

### In the process all cutout holes should be aligned as in figure below.

Attach D1100987 (Aluminum Aperture Clip) on chamber side.  Reach in from the spool through cutout to install FA-1010-N (10-32 X 5/8"L, FHCS, SS) into countersunk holes and tighten it into D1100987.

Note:  Use captive Allen wrench to make sure flat head screws DO NOT into fall into the tube. (Wiha: MagicRing Screw Holding-Ball End)

FA-1010-N

FA-1010-N

D1100987

MCA1 at HAM2-H1

Completed assembly viewed from inside the tube

Completed assembly from the spool (chamber).

Make sure viewports match up.

Assemble aperture plates onto viewport ring of MCA2

8.2.1. Bring in assembled aperture plate parts as shown below, upper aperture assembly.

8.2.2 After attaching one C-1016-N(10-32 X 1"L, SHCS, SS) and WF-10(#10 Washer, SS) on center top tapped hole, carefully remove D1101973(Aperture Support Bar) out of the tube.  Continue installing four C-1016-N through the aperture frame to viewport frame.  Next install six C-1008-N(10-32 X 1/2"L, SS) with WF-10 through aperture plate into viewport frame.

Center top tapped hole

C-1016-N with WF-10

C-1008-N with WF-10

8.2.3 Bring in assembled lower aperture plate assemblies as shown below.

Carry assembled aperture assemblies in opposite orientation of upper assembly.

Oval cutout on lower half

8.2.4   Remove D1101973 (support bar) before installing five C-1016-N (10-32 X 1"L, SHCS, SS) through the aperture frame to viewport frame.  Next install six C-1008-N(10-32 X 1/2"L, SS) with WF-10 (#10 washer, SS) through aperture plate into viewport frame.

8.2.5  Attach D1003059 (SS Aperture Clip) on chamber side.  Reach in from the spool       through cutout to install BU-1006-NA (10-32 X 5/8"L, BHCS, Ag-SS) with WF-10 (#10 Washer, SS) into clearance holes and tighten it into D1003059.

D1003059

Note:  Use captive Allen wrench to make sure flat head screws DO NOT fall into the tube. (Wiha: MagicRing Screw Holding-Ball End)

BU-1006-NA with WF-10

8.2.6 Installation of Mode cleaner tube baffle completed of MCA2 and MCA4.

MCA2 at HAM 5-H1

MCA4 at HAM 11-H2

Completed assembly viewed from inside the tube

Completed assembly from the spool (outside the tube).

Make sure viewports match up.

Assemble aperture plates onto viewport ring of MCA3

8.3.1 Match the cutout of D110512 (upper aperture plate, MCA3)to half-moon on viewport plate.  Use nine    C-1010-N(10-32 X 5/8"L, SHCS, SS) with WF-10 (#10 Washer, SS) to bolt the aperture plate to inner ring*.  Make sure cutout of the aperture plate matches the half-moon of the viewport plate.  Repeat for D1100513 (lower aperture plate, MCA3))

*Tip:  Line up visible holes of aperture plate to threaded tap holes of the inner ring. After secure center top hole a C-1010-N with WF-10 so it can hang loosely on the inner ring, then insert the rest of C-1010-N with WF-10 into tap holes as shown.

Center hole

Half-moon

Use nine of C-1010-N with WF-10 to bolt the aperture plate to inner ring.

Make sure cutout of the aperture plate match up lower assembled aperture plate

parts and half-moon of viewport plate.

Half-moon matchups

### 8.3.5   Attach D1100987 (Aluminum Aperture Clip) on chamber side.  Reach in from the spool through cutout to install FA-1010-N (10-32 X 5/8"L, FHCS, SS) into countersunk holes and tighten it into D1100987.

Note:  Use captive Allen wrench to make sure flat head screws DO NOT into fall into the tube. (Wiha: MagicRing Screw Holding-Ball End)

8.3.6 Installation of Mode cleaner tube baffle completed of MCA3.

MCA3 at HAM 8-H2

Completed assembly viewed from inside the tube

Completed assembly from the spool (outside the tube).

Make sure viewports match up.

MCB1 at HAM 3-H1

Completed assembly viewed from inside the tube

Note:  Be aware of odd viewport locations on plates

Completed assembly viewed from the spool (outside the tube)

Make sure viewports match up

MCB2 at HAM 4-H1

Completed assembly viewed from inside the tube

Note:  Be aware of odd viewport locations on plates

Completed assembly viewed from outside the tube

Make sure viewports match up

MCB3 at HAM 9-H2

Completed assembly viewed from inside the tube

Completed assembly viewed from outside the tube

Make sure viewports match up with spool piece

Note:  Be aware of odd viewport locations on plates.

MCB4 at HAM 10-H2

Completed assembly viewed from inside the tube

Completed assembly viewed from outside the tube

Make sure viewports match up with spool piece.

Note:  Be aware of odd viewport locations on plates.

# Text boxes

D1000784

D1000777

D1000780

D1000777

D1000777

D1000778

D1000778

D1000784

D1000777

D1000780

D1102164 4 Places

4

D1000779

D1000776

D1000783

D1000776

D1000779

D1000783

D1000776

D1002867

Tapped holes

D1100121

D1100121

Tapped Holes

D1002871

D1002867

D1100277

Super #8 Finish side

D1101150

Tapped Holes

D1002868

Tapped Holes

D1001926

D1002871

Super #8 Finish side

D1100350

D1100312

D1002871

D1001926

Tapped Holes

D1101152

Half-moon cutout and gap

Super #8 Finish side

BU-1006-N WITH WF-10

D1101160

C-1010-N with WF-10

D1100469

D1100468

D1100513

D1100512

D1002996

D1002997

D1003109*

Super #8 Finish side

D1101973

D100319

Super #8 Finishside

D1002995

Super #8 Finish side

D1001973

Super #8 Finish side

Super #8 Finish side

Super #8 Finish side

MCB 2

D1000776

D1003118-00

C-1012-N

D1003119-00

D1003118-00

D1003118-00

D111152

C-1016-N with WF-10

C-1016-N with WF-10

C-1008-N with WF-10

C-1008-N with WF-10

C-1016-N with WF-10

C-1016-N with WF-10

D1100512

D1100513

D1100987

D1002868

D1001926

D1002867

D1100121

D1002871

D1100277

D1002867

Half moon

Gap

D1101159

D1002871

Super #8 Surface

D1003119-00

* MCA2 & 4

D1003110 for MCB2 & 4

D1002995 for MCB1 & 3

10-32 screws and wing nut

D1000779

D1000777

Mode Cleaner Tube

D1101756

Alignment tooling

Chamfer edge

Eyebolt and wire (.005-.009")

Plumb Bob

D1101150 - (MCA1)

D1003118-00 (MCA2,3,4)

D1003118- 01 (MCB1)

D1003118-02 (MCB2)

D1003118-03 (MCB3)

D1003118-04 (MCB4)

View from Mode Cleaner Tube

D1003119 - (MCA1,2,4)

D1101152-00 (MCA3)

D1003119- 01 (MCB1)

D1003119-02 (MCB2)

D1003119-03 (MCB3)

D1003119-04 (MCB4)

D1100512

D1002867