## Slide 1: To recap
Control theory builds on differential equations
The Laplace transform is a tool to facilitate solving for ODEs.
No need to do actually do the transform
  Lookup tables
System G(s) is stable if
  Its response is bounded and finite
  poles must have negative real parts
Still, how does the cruise control example work?
Getting there…

## Slide 2: Recall
What is the transfer function of a system whose input and output are related by the following differential equation?

## Slide 3: Recall
Given the system’s transfer function
determine the system’s differential equation to input .

## Slide 4: Recall
Determine which of the following transfer functions represent stable systems and which represent unstable systems. Use MATLAB’s step to verify your answer.

## Slide 5: Another example
A simple mechanical accelerometer is shown below. The position y is with respect of the case, the case’s position is x. What is the transfer function between the input acceleration and the output Y?
M
y
k
B
x

## Slide 6: Control Theory 2
The response of a stable system G(s) is characterized by its
Amplitude and Phase shift
to a sinusoidal excitation

## Slide 7: Frequency response
It can be shown that if
then
where
is the amplitude response and
is the phase shift
X
This is how we measure transfer functions

## Slide 8: Frequency response
The dynamic behavior of a physical system can be determined by measuring its transfer function with a sinusoidal excitation
Magnitude and phase response are a function of frequency (
Frequency-response helps to understand the stability criteria

## Slide 9: Graphical analysis tool: Bode Plot
Common graphical representation of transfer function
is complex
  plot of magnitude and phase
Convention
  Log-log scale for magnitude vs. frequency (Hz)
  Semi-log scale for phase (deg) vs. frequency (Hz)
Other conventions
  Magnitude in dB () vs. angular frequency (rad/s)

## Slide 10: Bode plot:
 | → |  | 
 | → |  | 

## Slide 11
bodeexamples.m

## Slide 12: Bode plot:
 | → |  | 
 | → |  | 

## Slide 13
bodeexamples.m

## Slide 14: Bode plot:
 | → |  | 
 | → |  | 

## Slide 15
bodeexamples.m

## Slide 16: Bode plot:
 | → |  | 
 | → |  | 

## Slide 17
bodeexamples.m

## Slide 18: Bode plot:

## Slide 19
bodeexamples.m

## Slide 20
bodeexamples.m

## Slide 21
bodeexamples.m

## Slide 22: Bode plot: SHO

## Slide 23
bodeexamples.m

## Slide 24
bodeexamples.m

## Slide 25
bodeexamples.m

## Slide 26: Bode plots for more complicated TFs? Break it into simpler parts
In general a transfer function can be re-written in terms of simpler ones (of 2nd order at most)
then

## Slide 27: Example
Let’s draw the bode plot for
where

## Slide 28: Example

## Slide 29
0.1Hz
1Hz
10Hz
Log(f)
Log(f)

## Slide 30
0.1Hz
1Hz
10Hz
Log(f)
Log(f)

## Slide 31
bodeexamples.m

## Slide 32
  >> z=-2*pi*0.1;
  >> p=-2*pi*[1 10];
  >> k=500;
  >> G=zpk(z,p,k);
  >> [m,p]=bode(G, w);
bodeexamples.m

## Slide 33: Exercise
Sketch bode plot for the following TF
What is the DC gain (gain for )? What is the gain for ? Confirm results with MATLAB

## Slide 34: Exercise
Sketch bode plot for the following TF
What is the DC gain (gain for )? What is the gain for ? Confirm results with MATLAB

## Slide 35: Exercise
Sketch bode plot for the following TF
What is the DC gain (gain for )? What is the gain for ? Confirm results with MATLAB

## Slide 36: So far…
A system’s TF is a complex function
  Can be represented in terms of its magnitude and phase
Bode plots
  Help visualize the TF
  Plot of magnitude vs. frequency and phase vs. frequency.
  Different conventions
We have explored Bode plots of basic TFs
Bode plot of more complex TFs can be expressed in terms of simpler terms

## Slide 37: General Stability Criterion
The feedback control system is stable if and only if all the poles of the closed loop transfer function have a negative real part. Otherwise the system is unstable.

## Slide 38: In general
c
r
G(s)
e
-
+
H(s)
Open loop gain
Closed loop gain
  Stability: the poles’ real part of must be negative

## Slide 39: Loop stability and design
  If the system is unstable,
    We can’t change but
    We can design a different controller so as to make the system stable
  But how should we change H? Let’s look closely at the root of the problem
c
r
G(s)
e
-
+
H(s)

## Slide 40: The problem
c
r
G(s)
e
-
+
H(s)
If ever becomes then system is unstable

## Slide 41: The general shape of
c
r
G(s)
e
-
+
H(s)
has a limited bandwidth.
Within bandwidth:
Outside bandwidth:

## Slide 42: The general shape of
Log(f)
Log(f)
“Bandwidth”
Unity gain
Unity Gain Frequency (UGF):
DC gain

## Slide 43: Stability Criteria
A closed loop system is stable if the unity gain frequency is lower than the crossing.
Log(f)
Log(f)
UGF
crossing
Stable

## Slide 44: Stability Criteria: Rule of Thumb
The system is (almost always) stable if at the unity gain frequency.
Log(f)
Log(f)
Slope at UGF:
Stable

## Slide 45: Nyquist stability criterion
The closed loop system is stable if the polar plot of the open loop transfer function does not encircle the point.
  >> G=10*tf(10,[1 10];
  >> nyquist(G)
nyquist_example1.m

## Slide 46: Nyquist stability criterion
The closed loop system is stable if the polar plot of the open loop transfer function does not encircle the point.
  Checking the step response of 1/(1+Gol)
nyquist_example1.m

## Slide 47: Back to cruise control
Let’s inspect the system’s loop stability. Recall
Mass m = 1000 kg
Coefficient for air friction b = 50 kg/s
G
v
f
vr
H
K
θ
+
-
e
-
+
c

## Slide 48: Cruise control: Bode plot of
UGF @160 mHz
cruise_freqdomain.m

## Slide 49: Cruise control: Nyquist plot of
cruise_freqdomain.m

## Slide 50
With a little algebra:

## Slide 51: Let’s check step response of
cruise_freqdomain.m

## Slide 52: Example
Is the system with open loop transfer function stable?

## Slide 53
Two poles at 0 Hz
Zero at 10 Hz
Pole at 100 Hz
Pole at 500 Hz
feedback_example4.m

## Slide 54
Stable
by how much?
feedback_example4.m

## Slide 55: Problem
If a system has an open loop transfer function
what values of make it stable? Use MATLAB to confirm this.

## Slide 56: Relative stability
Gain and phase margin
  Measure of “relative” stability
  The larger they are → the “safer we are”
Gain margin
  By how much can the gain increase until the system becomes unstable?
  Defined as
Phase margin
  By how much can the system tolerate a phase change at UGF?
  Defined as
  Rule of thumb: keep the phase margin above

## Slide 57
UGF @30 Hz
Phase margin: 500
Gain margin: 20
feedback_example4.m

## Slide 58
Step response of
feedback_example4.m

## Slide 59
Pole-zero map of
feedback_example4.m

## Slide 60: Performance to noise input d: with no feedback
c
r
G1
d
+
+
e
-
+
G2
H
Noise contribution to signal c

## Slide 61: Performance to noise input d: with feedback
c
r
G1
d
+
+
e
-
+
G2
H
Controlled signal
Suppression factor
Noise contribution to signal c

## Slide 62: Setting the parameters
c
r
G1
d
+
+
e
-
+
G2
H
zeros at 1, 10Hz; poles at 0, 100 Hz, k = 300

## Slide 63
feedback_example6.m

## Slide 64
feedback_example6.m
Controller has a low pass filter at 1kHz

## Slide 65: Suppression factor
feedback_example6.m
Noise term suppression
No suppression
If the DC gain is increased, so is the suppression
Bandwidth

## Slide 66
feedback_example6.m
Control signal, at the output of H.

## Slide 67: How can we correct an unstable loop? Typical compensators
Integral controller
  The output is proportional to the time integral of the input
Derivative controller
  The output is proportional to the time derivative of the input

## Slide 68: Phase-lag compensator
compensator_phaselag.m

## Slide 69: Phase-lead compensator
compensator_phaselead.m

## Slide 70: “Boost”
compensator_boost.m

## Slide 71: Problem
If a system has an open loop transfer function
design a compensator that would make the system stable with an UGF at 100 Hz. Use MATLAB to confirm this.

## Slide 72: Example: locking one LIGO arm
+
+
e
-
+
C
H
S
Reference signal : the cavity “locks” to the laser frequency. For simplicity, units of length.
Noise term : Mirror motion due to seismic noise, units of length

## Slide 73: Example: locking one LIGO arm
+
+
e
-
+
C
H
S
Ligo arm cavity C: a cavity length change is converted to electronic signal e
Controller H: designed in the control room, processes signal e and sends commands to the suspension S
Suspension S: receives the signal from H and drives the mirror, units of length
Noise term : Noise from coil drivers

## Slide 74: Example: no lock
+
+
e
-
+
C
H
S

## Slide 75: Example: locking one LIGO arm
+
+
e
-
+
C
H
S
Suppression factor :
Open Loop gain:
Note on noise term : Noise term appears only when mirrors are driven → limited bandwidth desired

## Slide 76: Example: locking one LIGO arm
Need to design H so as to have
  Enough suppression of noise terms
  Stable
  “Small” bandwidth

## Slide 77: Example: locking one LIGO arm
Cavity transfer function C:
  Pole at 100 Hz
Suspension transfer function S
  Simple harmonic oscillator (SHO) with and quality factor
Shown is
What controller H can we use?
cavityfeedback_exampleA.m

## Slide 78: Example: locking one LIGO arm
Set UGF at 100 Hz
Need H with a zero after 1 Hz and before 100 Hz
Try phase lead
  with and
Bode plot of OL
  UGF at 100 Hz
  PM ~40 deg
  Stable
cavityfeedback_exampleA.m

## Slide 79: Example: locking one LIGO arm
Double check stability
Step response plot of
Step is driven to zero as it should (it is a suppression factor)
In about 10 ms (~1/UGF) response is close to zero
Two oscillation cycles – little ringing
cavityfeedback_exampleA.m

## Slide 80: Example: locking one LIGO arm
Bode plot of the suppression factor
Suppression of ~1500x at 100 mHz
No suppression above 100 Hz
Notice spike at 100 Hz
  This spike is responsible of the ringing in the step response
  decreased if phase margin is increased
cavityfeedback_exampleA.m

## Slide 81: Example: locking one LIGO arm
Let’s increase the low frequency gain with a “boost”
Try H
  with , and
OL bode plot
  UGF at 100 Hz
  PM ~40 deg
  Stable
cavityfeedback_exampleB.m

## Slide 82: Example: locking one LIGO arm
Double check stability
Step response plot of
Very similar response
Step is driven to zero as it should (it is a suppression factor)
In about 10 ms (~1/UGF) response is close to zero
Two oscillation cycles – little ringing
cavityfeedback_exampleB.m

## Slide 83: Example: locking one LIGO arm
Bode plot of the suppression factor
More suppression at low frequencies: at 100 mHz
No suppression above 100 Hz
Notice spike at 100 Hz
  Similar ringing
cavityfeedback_exampleB.m

## Slide 84: Example: locking one LIGO arm
Let’s also “cut-off” the drive to the coils at high frequency
Introduce a low pass LP 6th order Butterworth filter with cut-off frequency at 2 kHz.
Try H
  with , and
OL bode plot
  UGF at 100 Hz
  PM ~30 deg
  Stable
cavityfeedback_exampleC.m

## Slide 85: Example: locking one LIGO arm
Double check stability
Step response plot of
Very similar response
Step is driven to zero as it should (it is a suppression factor)
In about 10 ms (~1/UGF) response is close to zero
~Two oscillation cycles
cavityfeedback_exampleC.m

## Slide 86: Example: locking one LIGO arm
Bode plot of the suppression factor
Same suppression: at 100 mHz
No suppression above 100 Hz
Notice spike at 100 Hz
  A little higher than before
  Similar ringing
cavityfeedback_exampleC.m

## Slide 87: Example: locking one LIGO arm
Increasing the gain by 2x:
OL bode plot
  UGF at ~133 Hz
    Should have gone to 200 Hz but the slope is not 1/f (because of the cavity pole at 100 Hz)
  PM ~20 deg
  Stable but with little phase margin left
cavityfeedback_exampleD.m

## Slide 88: Example: locking one LIGO arm
Step response plot of
Ringing has increased
cavityfeedback_exampleD.m

## Slide 89: Example: locking one LIGO arm
Bode plot of the suppression factor
Suppression has increased
  Gain was increased by factor 2
Notice spike at 100 Hz is more pronounced
cavityfeedback_exampleD.m

## Slide 90: Summary
We have explored the stability criteria
  The feedback control system is stable if and only if all the poles of the closed loop transfer function have a negative real part. Otherwise the system is unstable.
Stability in terms of the open loop gain
  A closed loop system is stable if the unity gain frequency is lower than the crossing.
  Rule of thumb: the system is (almost always) stable if at the unity gain frequency

## Slide 91: Summary
Noise suppression
How close to instability is a system? Gain and phase margin
  Measure of “relative” stability
  The larger they are → the “safer we are”
  Rule of thumb: keep the phase margin to more than
Typical compensators
  Phase-lag
  Phase-lead
  “Boost”
Cavity lock example

## Slide 92: Problem for the afternoon
Identify a (single-input-single-output) control system at LIGO – its plant TF along with its controller TF (LSC, ASC, SUS, MC, PSL, …)
Sketch the block diagram and model the system with MATLAB. Generate the corresponding bode plot.
Can you measure its OL TF? Where is the UGF and how does it compare with the model?
For what range of frequencies can the UGF be placed at by simply adjusting the systems’ gain? What DC gain does it have, what suppression?

## Slide 93: Problem for the afternoon
Optical levers are/were used to damp the fundamental mode of the suspensions. The controller has no DC gain (check this).
Sketch the block diagram and model the system with MATLAB. Generate the corresponding bode plot.
Can you measure its OL TF? Where is the UGF and how does it compare with the model?
For what range of frequencies can the UGF be placed at by simply adjusting the systems’ gain? What DC gain does it have, what suppression?
opticallever.m

## Slide 94: Solutions to problems

## Slide 95
What is the transfer function of a system whose input and output are related by the following differential equation?
Sol: Taking the Laplace transform of the equation
Which can be re-written as

## Slide 96
Given , determine the system’s differential equation to input .
Sol:
or
or

## Slide 97
Determine which of the following transfer functions represent stable systems and which represent unstable systems. Use MATLAB’s step to verify your answer.
  , unstable
  , stable
  , unstable
  , stable
  , unstable

## Slide 98
A simple mechanical accelerometer is shown below. The position y is with respect of the case, the case’s position is x. What is the transfer function between the input acceleration and the output Y?
M
y
k
B
x
Sol:

## Slide 99
Sketch bode plot for the following TF
What is the DC gain (gain for )? What is the gain for ? Confirm results with MATLAB
bodeexcercise1.m

## Slide 100
Sketch bode plot for the following TF
What is the DC gain (gain for )? What is the gain for ? Confirm results with MATLAB

## Slide 101
Sketch bode plot for the following TF
What is the DC gain (gain for )? What is the gain for ? Confirm results with MATLAB

## Slide 102: Solution
If a system has an open loop transfer function
what values of make it stable?
Sol: UGF can be set after the pole at 10 and before pole at 100
Set and . Find corresponding k.
Set and 0. Find corresponding k

## Slide 103: Solution
If a system has an open loop transfer function
design a compensator that would make the system stable with an UGF at 100 Hz. Use MATLAB to confirm this.
Sol: two zeros at 10, decreasing the gain by 3x
H=zpk([],[-10 -10 -10],1e3) * zpk([-10 -10],[],0.3)