## Slide 1: So far…
Signals to sequences
Convolution between sequences and is defined as
  or
Correlation between two sequences and
Impulse response of a system
  Where is the unit sample or impulse response of the LTI system
  System is stable if
  In general, the response sequence to the input sequence can be re-written as

## Slide 2: So far…
Differential to difference equations
  General form of a difference equation
  MATLAB’s filter command to numerically solve difference equations:
    >> y = filter(b, a, x)
  In particular the impulse response of a system can be found
    >> h = filter(b, a, delta)

## Slide 3: Digital Signal Processing 2
In the analog domain, the Laplace transform L
  Relates time-functions to frequency-dependent functions
For the digital domain, the Z transform
  Relates time-sequences to (a different, but related type of) frequency-dependent function

## Slide 4: The Z Transform
This discrete-time equivalent of the Laplace transform is defined as
  where is the complex frequency.
The values of for which the sum converges define a region in the -plane referred to as the region of convergence (ROC).

## Slide 5: Region of convergence (ROC)
The set of z values for which exists is called the region of convergence (ROC)
ROC

## Slide 6: The Z Transform
This transformation is useful in
Solving constant coefficient difference equations
Evaluating the response of an LTI system to a given input, and
Designing linear filters

## Slide 7: Example
Let .
Find its Z transform and its ROC.
or
ROC
Geometric series:
Transfer function: zero at the origin, pole at 1

## Slide 8: Example
Let Find its Z transform and its ROC.
or
ROC
Transfer function: zero at the origin, pole at 2

## Slide 9: Example
Let . Find its Z transform and its ROC.
o
Pole at
Zero at origin

## Slide 10: In general
Many of the signals in DSP have Z transforms that are rational (ratio of two polynomials) functions of :
where is the k-th pole and is the l-th zero of . Each pole is indicated by an ”x” and each zero by an “o” in the -plane.

## Slide 11: Special properties of the Z Transform
Convolution
  Given two sequences and , their time-domain convolution becomes a multiplication process in the frequency domain
Sample shifting

## Slide 12: (Some) Z Transform pairs
 |  | ROC
 |  | Any z
 |  | ROC
 |  | Any z

## Slide 13: And back to sequences: The Inverse Z Transform
Just like in the Laplace domain
Use the partial fraction method to reduce a complex to simpler parts.
Use the table of transform pairs to determine the sequence.
In general
If

## Slide 14: Example
Compute the inverse Z-transform of
Sol:
Re-write in terms of powers of .
At the MATLAB prompt
>> b=[0 1];a=[3 -4 1];
>> [R,p,C]=residuez(b,a)
R =
0.5000
-0.5000
p =
1.0000
0.3333
C =
[]
Using the table of transform pairs

## Slide 15: Example
Compute the inverse Z-transform of
Sol:
Using MATLAB to do the partial fraction
>> b = 1; a = poly([0.9, 0.9, -0.9])
a =
1.0000 -0.9000 -0.8100 0.7290

## Slide 16: Example
>> [R,p,C]=residuez(b,a)
R =
0.2500
0.2500 + 0.0000i
0.5000 - 0.0000i
p =
-0.9000
0.9000 + 0.0000i
0.9000 - 0.0000i
C =
[]

## Slide 17: Example
Using the Z Transform pair table
Sample shifting

## Slide 18: Exercise
Determine the Z-transform of the impulse response

## Slide 19: Exercise
Determine the Z-transform of the impulse response
Sol:
Using the sample shift property

## Slide 20: System function
The system function is simply the Z transform of the impulse response of the system
This means that, given input the output is

## Slide 21: System function from a difference equation
When an LTI system is represented by the difference equation
it can be shown that
where

## Slide 22: System function and MATLAB implementation
The MATLAB implementation, given
The impulse response is simply
>> h = filter(b, a, delta)
While the response to input is
>> y = filter(b, a, x)

## Slide 23: For example
Given the LTI system represented by the difference equation, the determine the impulse response .
Sol: let’s find the system function first.
Taking the Z transform

## Slide 24
Taking the inverse transform
Let’s verify with MATLAB
>> b = [1]; a = [1 -0.9];
>> h = filter(b,a,delta);
and lets plot the two responses.

## Slide 25
ex411.m

## Slide 26: To recap
The Z transform is the digital equivalent of the Laplace transform:
It facilitates the solving of constant coefficient difference equations
It allows to easily evaluate the system’s response
It is critical in designing linear filters
MATLAB commands used
  filter, residuez

## Slide 27: A different transform: DTFT
A very different but very useful representation of a sequence or system is the Discrete-time Fourier Transform (DTFT)
Setting in the -transform
  where is the complex frequency.

## Slide 28: A different transform: DTFT
The DTFT of sequence is defined as
  where
  is a complex valued function
  is a digital frequency ranging from to

## Slide 29: Special property of the DTFT
Just like the Z transform
Convolution
  Given two sequences and , their convolution is a multiplication process in the frequency domain

## Slide 30: Frequency domain representation of LTI systems
The DTFT of the unit sample response is called the Frequency Response or Transfer Function of an LTI system

## Slide 31: Frequency response from difference equations
When an LTI system is represented by the difference equation
Then

## Slide 32: Example
Given difference equation
determine transfer function and plot its magnitude and phase

## Slide 33: Example

## Slide 34
dtft_example3.m
>> w=linspace(-2*pi,2*pi,800);
>> H=1./(1-0.8*exp(-1i*w) );
>> plot(w/pi, abs(H))
>> plot(w/pi,phase(H))

## Slide 35: Example 3.16
A 3rd order low pass filter is described by the difference equation
Plot the magnitude and the phase response of this filter and verify that it is a low pass filter.

## Slide 36
dtft_example316.m
>> b=[0.0181, 0.0543, 0.0543, 0.0181];
>> a=[1.0, -1.76, 1.1829, -0.2781];
>> w=linspace(-2*pi, 2*pi, 1000);
>> num=b * exp(-1i*m'*w);
>> den=a * exp(-1i*l'*w);
>> H=num ./ den;
>> plot(w/pi, abs(H))
>> plot(w/pi,phase(H))

## Slide 37: Example 4.13
An LTI system is described by the following difference equation
Plot the magnitude and the phase response of this filter.

## Slide 38
>> a = [1 0 -0.81];
>> b = [1 0 -1];
>> [H,w]=freqz(b,a,500);
>> plot(w/pi, abs(H))
>> plot(w/pi, phase(H))
dtft_example413.m

## Slide 39: Another transform: The Discrete Fourier Transform (DFT)
The FFT falls into this category
Why more transforms? What is the problem?
  The DTFT and the transform are not numerically computable transforms
    They have infinite sums at uncountably infinite frequencies
The Discrete Fourier Transform (DFT)
  Obtained by sampling the Discrete-Time Fourier Transform (DTFT) in the frequency domain
  “the DFT is just equally-spaced samples of the DTFT”
  Time-consuming numerical computation
Fast-Fourier Transform
  Algorithm for the efficient computation of DFTs

## Slide 40: Example: highlighting the difference between the DTFT and DFT
Let
The corresponding DTFT is

## Slide 41
with M=8
dtft_example.m

## Slide 42
with M=8
>> P=10;
>> wk=(0:P-1) * (2*pi/P);
>> Xfft =fft(x, P);
>> plot(wk/pi, mag(Xfft),’rs’)
dtft_example.m

## Slide 43
with M=8
>> P=50;
>> wk=(0:P-1) * (2*pi/P);
>> Xfft =fft(x, P);
>> plot(wk/pi, mag(Xfft),’rs’)
dtft_example.m
The DFT is just the DTFT at discrete frequency intervals

## Slide 44
Lines at 50 Hz and 120 Hz, contaminated by noise.
dtft_example.m
Advantage of the FFT signal representation: the lines at 50 Hz and 120 Hz are not visible in the time domain representation, but are clear in the FFT representation.

## Slide 45: Power Spectral Density
A graphical representation to easily determine the power of a signal over a particular frequency band.
Uses the fft algorithm
Unfortunately there are many conventions for the normalization, can be confusing…
Let’s use the example of a cosine at 200 Hz
spectraldensity_example.m

## Slide 46: Power Spectral Density (PSD)
In this example, power is computed using
  w=hamming(length(x))
  [Pxx,f]=periodogram(x,wi,'onesided',NFFT,Fs)
Data windowing
  In the fft process, power in one frequency bin “leaks” to nearby bins.
  Filter (with a window filter) the input data stream
The RMS of a sinusiod:
The (running) RMS computed using the PSD (and shown in red)
The computed RMS agrees with the theoretical
spectraldensity_example.m

## Slide 47: Amplitude Spectral Density (ASD)
Plotting the amplitude:
  simply the square root of the power spectral density
spectraldensity_example.m

## Slide 48: Finally – the question on sampling
The Discrete-time Fourier Transform (DTFT) was defined as
where digital frequency
and sampling frequency

## Slide 49: Finally – the question about sampling
The Discrete-time Fourier Transform (DTFT) is defined as
where is the digital frequency.
If you inspect previous plots of DTFTs, you notice a periodicity of .

## Slide 50: Finally – the question about sampling
The sequence represents a continuous-time signal sampled every seconds:
where the digital frequency is
and is frequency in .
Defining the sampling frequency , the periodicity is
The signal repeats every Hz.
is defined as the Nyquist frequency.

## Slide 51
Aliasing

## Slide 52: Sampling Principle
A band-limited signal with bandwidth can be reconstructed from its sample values if the bandwidth is less than the Nyquist frequency
Otherwise aliasing (or distortion) would result in the reconstruction of .

## Slide 53: Effect of sampling
Continuous-time Fourier Transform (CTFT)
Sample
Discrete-time Fourier Transform (DTFT)
Bandwidth
Bandwidth

## Slide 54: Effect of sampling
Continuous-time Fourier Transform (CTFT)
Sample
Discrete-time Fourier Transform (DTFT)
Bandwidth
Aliasing
Bandwidth

## Slide 55: Let’s simulate aliasing
Suppose having an analog signal of the form
Its Fourier transform is

## Slide 56: Aliasing
Plot of vs. time
For and
  No significant energy left
  Let’s set
aliasing_example.m

## Slide 57: Aliasing
Plot of vs. frequency
For
  No significant energy left
  Set
  Reasonable to set the signal’s bandwidth to
To avoid aliasing the sampling frequency must satisfy
aliasing_example.m

## Slide 58: Aliasing
Plot of vs. time along with a sampled sequence ( kHz)
According to the sampling principle
Should not have aliasing…
aliasing_example.m

## Slide 59
Plot of vs. frequency
Plot of DFT
No aliasing is visible
aliasing_example.m

## Slide 60: Aliasing
Plot of vs. time along with a sampled sequence ( kHz)
According to the sampling principle
Should have aliasing…
aliasing_example.m

## Slide 61
Plot of vs. frequency along with the computed DFT
Aliasing is visible
aliasing_example.m

## Slide 62: Recap
The Discrete-time Fourier Transform (DTFT)
  A very different but very useful representation of a sequence or system
  Mapping into frequency space
  in the transform
The Discrete Fourier Transform (DFT)
  Obtained by sampling the DTFT in the frequency domain
  FFT: Fast Fourier Transform
    Algorithm for the efficient computation of DFTs
Power Spectral Density
  power of a signal over a particular frequency band.
Sampling principle
  The signal’s bandwidth must be less than the Nyquist frequency in order to avoid aliasing
Modeling Aliasing