LIGO Laboratory / LIGO Scientific Collaboration

LIGO- E1100847 	                 LIGO                   Mar 18th, 2014

aLIGO BSC-ISI, Pre-integration Testing report,

Phase II (before and after cartridge install)

E1100847– V1

Jim Warner

Distribution of this document:

Advanced LIGO Project

This is an internal working note

of the LIGO Laboratory

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW22-295 185 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 1970 Mail Stop S9-02 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

Table of contents:

1.   Phase IIA	3

2.   Phase IIB............................................................................................................................................4

1.   Hardware changes	4

1.   CPS – E1100369	4

2.   GS13 – E1100740	4

3.   L4C – E1100740	4

4.   T240 – E1100740	4

5.   Cables – E1100822	4

6.   Misc	4

2.   Electronic Inventory	4

3.   Models Modifications	4

4.   Mass distribution	5

5.   Basic functionalities just after installing the BSC-ISI on the teststand	5

1.    Pressure sensors	5

i.   Spectra	6

ii.   Actuators-cables resistance	6

iii.   Offsets CPS Unlocked vs locked 	7

iv.   Offset local drive	7

v.   Offset Cartesian drive	7

vi.   Range of motion	8

vii.   Linearity test	9

6.   Transfer functions.	9

3.   Conclusion Phase II-b	13

Introduction

The BSC-ISI testing is performed in three phases:

1) BSC-ISI, Pre-integration Testing, Phase I (post-assembly, in the staging building)

2) BSC-ISI, Pre-integration Testing, Phase II: Final tests done before insertion in the chamber
3) BSC-ISI, Integration Phase Testing: Procedure and results related to the commissioning in the chamber.

The ISI-BSC2 was moved from the Staging building to the VEA test stand July 2013.

This document presents results of tests (Phase II) performed on the ISI-BSC2 (BS) before installation in the chamber.

All results are posted on the SVN at:

https://svn.ligo.caltech.edu/svn/seismic/BSC-ISI/H1/BS/

The following type of document can be found in the SVN:

- Excell spreadsheet (.xls)

- Data location

- Figures location

- Masses distribution scheme (ppt)

# Phase II-A

Data for the tests on the floor in the LVEA couldn't be found. It may have been overwritten or lost when testing for ITMX was started. All of the required tests were performed once the cartridge was installed in the chamber, so the ISI has been shown to be healthy, regardless. All data in this report is from testing in the chamber.

# Phase II-B

## Hardware changes

### CPS – E1100369

CPS have not been replaced since phase I testing in the staging building.

### GS13 – E1100740

GS13 have not been replaced since phase I testing in the staging building.

### L4C – E1100740

L4C have not been replaced since phase I testing in the staging building.

### T240 – E1100740

T240 have not been replaced since phase I testing in the staging building.

### Cables – E1100822

Further information can be found in E1100822.

### Misc

No hardware changes since phase I testing in the staging building.

## Electronic Inventory

This table reports the electronic equipment used in the LVEA.

## Models Modifications

The model was updated and recompiled since MEDM screens were modified

## Mass distribution

The Payload for this chamber was not recorded before closing. My recollection was that it was not visually different from other chambers.

Test result:                                              Passed:                 Failed:         .   W Waived:  __X

## Basic functionalities just after installing the BSC-ISI in the chamber

## Pressure sensors

All pressure sensors are working.

Table 1 - Geophones Pressure sensors

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### Spectra

Spectra of the instrument can be found in the SVN at:

seismic/BSC-ISI/H1/BS/Data/Spectra/Undamped/

- H1_ISI_BSC2_ASD_CT_LOC_CPS_T240_L4C_GS13_2020_07_24_4 7:9:.mat

seismic/BSC-ISI/H1/BS/Data/Figures/Spectra/Undamped/

- H1_ISI_BSC2_ASD_CT_LOC_CPS_T240_L4C_GS13_2020_07_24_4 7:9:.fig

Figure 1 - Spectra inboard instruments - ISI Unlocked

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### 2. Actuators-cables resistance

Not done. Can be completed outside the chamber if needed.

Test result:                                              Passed:                 Failed:         .   W Waived:   X__

### Offsets CPS Unlocked vs locked

|  | Table locked | Table unlocked | Difference locked - unlocked |
| --- | --- | --- | --- |
| Sensors | Offset (Mean) | Std deviation | Offset (Mean) | Std deviation | Offset (Mean) | mil |
| ST1 - H1 | 240 | 7 | 58 | 28 | 182 | .21 |
| ST1 - H2 | 153 | 6 | -68 | 18 | 221 | .26 |
| ST1 - H3 | -36 | 5 | -93 | 26 | 57 | .07 |
| ST1 - V1 | -710 | 6 | -979 | 24 | 269 | .32 |
| ST1 - V2 | 661 | 10 | 880 | 23 | 219 | .25 |
| ST1 - V3 | -16 | 12 | -42 | 23 | 26 | .03 |
| ST2 - H1 | 302 | 143 | 161 | 40 | 141 | .041 |
| ST2 - H2 | -631 | 129 | -684 | 51 | 53 | .015 |
| ST2 - H3 | -243 | 119 | -206 | 33 | 37 | .011 |
| ST2 - V1 | -1532 | 123 | -1539 | 64 | 7 | .002 |
| ST2 - V2 | -579 | 123 | -559 | 60 | 20 | .006 |
| ST2 - V3 | -221 | 76 | -118 | 66 | 103 | .03 |

Table 2 - Locked vs Unlocked Position

Test result:                                              Passed:  X               Failed:         .   W Waived:   __

### Offset local drive

Skipped due to time.

Test result:                                              Passed:                   Failed:         .   W Waived:   X__

### Offset Cartesian drive

Skipped due to time.

Test result:                                              Passed:                   Failed:         .   W Waived:   X__

### Range of motion

The range of motion of the table is measured by pushing on the table in a direction collinear to the CPS. The Static tests results can be found on the SVN at:

https://svn.ligo.caltech.edu/svn/seismic/BSC-ISI/H1/BS/Data/Static_Tests/H1_ISI_BSC2_Range_Of_Motion_20130419.mat

| Sensor readout (counts) | Negative drive | no drive | Positive drive | Amplitude count | mil |
| --- | --- | --- | --- | --- | --- |
| ST1 - H1 | -15516 | 36 | 16493 | 32008 | 38 |
| ST1 - H2 | -15211 | -43 | 16907 | 32118 | 38 |
| ST1 - H3 | -16688 | -161 | 15523 | 32211 | 38 |
| ST1 - V1 | -14177 | -993 | 12175 | 26352 | 31 |
| ST1 - V2 | -12396 | 850 | 14099 | 26495 | 31 |
| ST1 - V3 | -13327 | -159 | 13004 | 26331 | 31 |
| ST2 - H1 | -9618 | 238 | 10079 | 19697 | 5.9 |
| ST2 - H2 | -10400 | -696 | 9003 | 19403 | 5.8 |
| ST2 - H3 | -9958 | -200 | 9547 | 19505 | 5.8 |
| ST2 - V1 | -13200 | -1581 | 10005 | 23205 | 6.9 |
| ST2 - V2 | -12259 | -663 | 10919 | 23178 | 6.9 |
| ST2 - V3 | -11931 | -222 | 11467 | 23399 | 6.9 |

Table 3 - Range of motion - Actuator drive in the LVEA

Test result:                                              Passed:   X              Failed:         .   W Waived:

### Linearity test

Measurements data can be found in the SVN at:

SeiSVN/seismic/BSC-ISI/H1/BS/Data/Linearity_Test/H1_ISI_BSC2_Linearity_test_20130417.mat

Figure 2. Linearity Test

Test result:                                              Passed:    X              Failed:         .   W Waived:

## Transfer functions and Comparison with measurements done in the staging building.

### At the end station

Measurements data can be found in the SVN at:

SeiSVN/seismic/BSC-ISI/H1/BS/Data/Transfer_Functions/Measurements/Undamped:

- H1_ISI_BSC2_Data_L2L_10mHz_100mHz_ST1_ST2_20130418-205201.mat

- H1_ISI_BSC2_Data_L2L_100mHz_700mHz_ST1_ST2_20130418-161906.mat

- H1_ISI_BSC2_Data_L2L_700mHz_10Hz_ST1_ST2_20130418-223504.mat

- H1_ISI_BSC2_Data_L2L_10Hz_100Hz_ST1_ST2_20130418-134213.mat

- H1_ISI_BSC2_Data_L2L_100Hz_500Hz_ST1_ST2_20130418-122201.mat

- H1_ISI_BSC2_Data_L2L_500Hz_1000Hz_ST1_ST2_20130418-111719.mat

Once the data are processed, they can be found in the SVN at:

/seismic/BSC-ISI/H1/BS/Data/Transfer_Functions/Simulations/Undamped/
- H1_ISI_BS_TF_L2L_Raw_2013_04_18.mat

The transfer functions can be found in the SVN at:

seismic/BSC-ISI/H1/BS/Data/Figures/Transfer_Functions/Measurements/Undamped/

- H1_ISI_BS_TF_L2L_Raw_from_ST1_ACT_to_ST1_CPS_2013_04_18.fig

- H1_ISI_BS_TF_L2L_Raw_from_ST1_ACT_to_ST1_L4C_2013_04_18.fig

- H1_ISI_BS_TF_L2L_Raw_from_ST1_ACT_to_ST1_T240_2013_04_18.fig

- H1_ISI_BS_TF_L2L_Raw_from_ST1_ACT_to_ST2_CPS_2013_04_18.fig

- H1_ISI_BS_TF_L2L_Raw_from_ST1_ACT_to_ST2_GS13_2013_04_18.fig

- H1_ISI_BS_TF_L2L_Raw_from_ST2_ACT_to_ST1_L4C_2013_04_18.fig

- H1_ISI_BS_TF_L2L_Raw_from_ST2_ACT_to_ST1_T240_2013_04_18.fig

- H1_ISI_BS_TF_L2L_Raw_from_ST2_ACT_to_ST2_CPS_2013_04_18.fig

- H1_ISI_BS_TF_L2L_Raw_from_ST2_ACT_to_ST2_GS13_2013_04_18.fig

Figure 3 - TF ST1 ACT to ST1 CPS

Figure 2 - TF ST1 ACT to ST1 T240

Figure 3 - TF ST1 ACT to ST1 L4C

Figure 4 - TF ST2 ACT to ST2 CPS

Figure 5 - TF ST2 ACT to ST2 GS13

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

## Conclusion Phase II-B

Tests performed during Phase II-B don’t show any major anomalies on ISI-BSC2.

Test result:                                              Passed:   X              Failed:         .   W Waived:   _