## Slide 1
1
Towards Advanced LIGO
and the global gravitational-wave detector network
David Reitze
Executive Director
LIGO Laboratory
LIGO G1101200-v2

## Slide 2: Advanced LIGO History
Began in 1999 as an LSC concept paper
Major R&D from 1999-2006
  In anticipation of positive funding outcome, many subsystems through preliminary design phase by 2006
Final baseline review by NSF in November 2007
Advanced LIGO Project officially began on April 1, 2008
Image courtesy of Beverly Berger
Cluster map by Richard Powell
Initial LIGO

## Slide 3: Initial LIGO
5 W
250 W
10 kW
10 kW
LIGO
125 W
700 kW
700 kW
4 kW
Advanced LIGO
Advanced LIGO

## Slide 4: Advanced LIGO overview
What is Advanced?
Parameter | Initial LIGO | Advanced LIGO
Input Laser Power | 10 W (10 kW arm) | 180 W (>700 kW arm)
Mirror Mass | 10 kg | 40 kg
Interferometer Topology | Power-recycled Fabry-Perot arm cavity Michelson | Dual-recycled Fabry-Perot arm cavity Michelson (stable RC)
GW Readout Method | RF heterodyne | DC homodyne
Optimal Strain Sensitivity | 3 x 10-23 / rHz | Tunable, better than 5 x 10-24 / rHz in broadband
Seismic Isolation Performance | flow ~ 50 Hz | flow ~ 12 Hz
Mirror Suspensions | Single Pendulum | Quadruple pendulum

## Slide 5
5
  ISI:
  Two-Stage
  Internal Seismic Isolator
  HEPI:
  Hydraulic External
  Pre Isolator
  ISI:
  Single Stage
  Internal Seismic Isolator
  HEPI:
  Hydraulic External
  Pre Isolator
  HAM Chambers Equipment
  BSC Chambers Equipment
Advanced LIGO Seismic
Isolation

## Slide 6: Advanced LIGO Suspensions

## Slide 7: Advanced LIGO Pre-stabilized Laser

## Slide 8: Advanced LIGO Core Optics

## Slide 9
Strain = DL(f)/L
Displacement = DL(f)

## Slide 10: Coalesence rates /yr for different configurations
m1 / m2 | No SRM, low power | zero detune, low power | zero detune, high power | NSNS Optimal
NS / NS | 17 (358 Mpc) | 12 (323 Mpc) | 32 (445 Mpc) | 40 (481 Mpc)
NS / BH | 5 (757 Mpc) | 3 (680 Mpc) | 9 (926 Mpc) | 11 (1001 Mpc)
BH / BH | 11 (1834 Mpc) | 8 (1632 Mpc) | 19 (2187 Mpc) | 23 (2325 Mpc)
mNS = 1.4 M, mBH = 10 M
Realistic Rates; actual
rates may vary!
0.4/yr < RNS/NS < 400 (NSNS Opt)
A, Weinstein, 2011
Abadie, et al., CQG 2010

## Slide 11: CW sources (AdvLIGO zero detuning high P)
Advanced LIGO can beat the spin-down limit on these red pulsars in 1 year:
Galactic diameter
10
1
10
2
10
3
10
0
10
1
10
2
10
3
10
4
10
5
e
=10
-7
10
-6
10
-5
10
-4
10
-8
gravitational frequency (Hz)
reach, distance (pc)
Crab
Vela
J0537-6910 (LMC)
B1951+32 (CTB80)
J0437-4715
J0737-3039A
J1913+1011
Nearest star
single aL detector
Graham Woan, Ben Owen, 2010

## Slide 12: Advanced LIGO Project Schedule
Commission/
Science Ops

## Slide 13
Sept 2002
March 2007

## Slide 15: Sketch of possible progression for Advanced LIGO sensitivity
Early short run:
25w laser input, no signal recycling ~10x excess low frequency noise BNS Inspiral Range: 60 Mpc BBH Inspiral Range: 227 Mpc Stochastic Omega: 1.5e-7
First extended run:
25w laser input, no signal recycling BNS: 142 Mpc BBH: 1400 Mpc Stochastic Omega: 3e-9
125w laser input, signal recycling BNS Inspiral Range: 200 Mpc BBH Inspiral Range: 1640 Mpc Stochastic Omega: 2.25e-9
Not yet an official plan for the aLIGO
configuration evolution!
CAVEAT:
reaching LF target
sensitivity is challenging
DRAFT
D. Shoemaker, 2011
DRAFT
DRAFT
DRAFT

## Slide 16: Advanced GW Networks
Gravitational-wave astronomy is greatly enhanced by having a multiplicity of interferometers distributed over the globe.
  GW ‘Aperture synthesis’
Advantages include:
  Source localization in near real time
  Enhanced Network Sky Coverage
  Maximum Time Coverage – a fraction of the detectors are‘always listening’
  Detection confidence
  Source parameter estimation
4 properly distributed detectors is better than 3; 5 is even better than 4
source
location
1
2
q
DL = c dt

## Slide 17: Initial GW detector network
B. Sathyaprakash,
S. Fairhurst, Cardiff U., 2011

## Slide 19: Advanced GW detector network
B. Sathyaprakash,
S. Fairhurst, Cardiff U., 2011

## Slide 23
23
23
The Advanced GW Detector Network
GEO 600 (HF)
2011
Advanced LIGO
Hanford
2015
Advanced LIGO
Liviingston
2015
Advanced
Virgo
2015
LIGO India
2020?
LCGT
2017

## Slide 24: LIGO-Australia  LIGO-India
Original plan was to put one of the Hanford interferometers in Australia
  LIGO provides the detector; Australia provides the facility/operations staffing
A major campaign by the LIGO Laboratory, ACIGA, and the NSF to fund LIGO-Australia
  It didn’t work…
As it became clear LIGO-Australia was unlikely to be funded, IndIGO asked the LIGO Laboratory to consider relocating one of the Hanford interferometers to India
Momentum has been building – LIGO-India is under serious consideration as a ‘Mega-Project’ by the Planning Commission
  Mega-Project budget cycle occurs every 5 years, and it’s happening now
  $200M proposed expenditure (infrastructure and operations) over 15 years
Serious evaluation now underway
Lab Go/No-go decision before March 31, 2012

## Slide 25: Conclusions
We are moving toward Advanced LIGO
  Challenges ahead, but we are on time and on budget!
Expect commissioning operations to begin in 2015
Virgo will join in 2015, LCGT in 2017
  Four node GW network
LIGO-India may become a reality by ~2020

## Slide 26: Conclusions
This has been an excellent workshop!
Thanks to the organizers Roy Williams, Christian Ott, Steve Groom and our LIGO Livingston hosts

## Slide 27
George Hobbs,
Dick Manchester, CSIRO
The Gravitational Wave Spectrum
LIGO/VIRGO
NGO