Statement of Work

AO-523 TMS Top Mass Machined Components

LIGO-C1201789-v2

Note to LIGO users: all red text in this template is font type ‘hidden’ and comprises instructions to complete the SOW.  Easier than deleting them, you can hide all red text before saving.  In Word 2010, click File, Options (on the left side), Display (on the left side), and then unclick “Hidden Text”.

The “TEMPLATE” watermark can be removed by clicking Page Layout, Watermark, and then Remove Watermark.

- Scope (AOS Trans Mon Suspension)

This Statement of Work covers the manufacturing of most machined metal class A components used in each LIGO TMS Suspension assembly and installation. Quantities listed are for 6 TMS assemblies, and include spares. Manufacturing is according to LIGO Specification E0900364-v8 wherever applicable.

Briefly describe the work.  For example: Fabrication of Vacuum Pod components for Advanced LIGO BSC-ISI Seismometers.

- Document Access

Many supplemental documents and specifications are incorporated into and made a part this Statement of Work.  Click on the document links to access these documents from the LIGO Document Control Center (DCC) or go on line to the LIGO Public DCC at https://dcc.ligo.org/ to access the DCC#.

- Commercial Terms and Applicable LIGO Specifications:

Note: The documents listed below are invoked for this Statement of Work and comprise additional requirements which are integral to this Statement of Work.

Important: C080185 and Q0900001 apply to all SOWs. Add/delete others as appropriate.

Check to be sure the latest revisions are specified below (please notify QAME or Systems if this template needs to be updated).

- LIGO-C080185-v1	LIGO Commercial Items or Services Contract General Provisions

- LIGO-Q0900001-v5 	Advanced LIGO Supplier Quality Requirements

- LIGO-Q1100003-v1	Acceptable Quality Level (AQL) for Inspection of LIGO Components

- LIGO-E0900364-v8 	Metal Components for use in the Advanced LIGO Vacuum System

- Quality System:

Referring to the above referenced LIGO Specification Q0900001, Suppliers should include a copy of their current ISO 9001, AS9100, or TS16949 certification in their bid package.  Suppliers lacking current certification should send a copy of their Quality Manual with their bid package.

Note 1: Care should be given to the selection of the AQL number.  Consider the amount of time (which equals cost) required to 100% inspect a given number of parts.  Contact QAME for advice.

Note 2: Additional inspection instructions beyond the AQL number can be given – such as 100% inspection of all threaded holes.

- Parts to be manufactured, Quantity Required, and Inspection requirements:

Note: refer to Section 8.0 for delivery schedule and location

## AQL Number is 1.0.

## All tapped holes (100%) must be gauged.

| Item # | Part Number | Rev | Description | Material | Set 1 | Set 2 | TOTAL |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | D060315 | C | ADVANCED LIGO, SUS, QUAD N-PTYPE TABLECLOTH, TABLECLOTH PINCH PLATE, UPPER STRUCTURE | 6061-T6 Al | 12 | 12 | 24 |
| 2 | D060318 | E | ADVANCED LIGO, SUS, QUAD N-PTYPE TABLECLOTH, OSEM AND ECD MOUNTING BRACKET (LOCAL CONTROLS) | 6061-T6 Al | 12 | 12 | 24 |
| 3 | D060321 | D | ADVANCED LIGO, SUS, QUAD N-PTYPE TABLECLOTH, POSITION ADJUSTER FOR FRONT PITCH OSEM | 6061-T6 Al | 3 | 3 | 6 |
| 4 | D060323 | F | ADVANCED LIGO, SUS, QUAD N-PTYPE TABLECLOTH, TRANSVERSE OSEM POSITION ADJUSTMENT PLATE | 6061-T6 Al | 3 | 3 | 6 |
| 5 | D060325 | F | Advanced LIGO, SUS, TOP STAGE N-P TYPE, ROTATIONAL ADJUSTER, STATIC HALF | 304/316 SSTL | 6 | 6 | 12 |
| 6 | D060326-0 | F | Advanced LIGO, SUS, Quad N-Ptype Top Stage, BLADE CLAMP (TOP HALF) | 304/316 SSTL | 6 | 6 | 12 |
| 7 | D060327-0 | F | Advanced LIGO, SUS, Quad N-Ptype Top Stage, BLADE CLAMP (BTM HALF) | 304/316 SSTL | 6 | 6 | 12 |
| 8 | D060328 | v3 | Advanced LIGO, SUS, Quad N-Ptype Top Stage, 3/8-16 UNC T NUT Based on Wixroyd 2418.W120 | 304/316 SSTL | 12 | 12 | 24 |
| 9 | D060329 | E | Advanced LIGO, SUS, Quad N-Ptype Top Stage, Top Stage STIFF BACK | 6061 Al | 6 | 6 | 12 |
| 10 | D060330 | F | Advanced LIGO, SUS, Quad N-Ptype Top Stage, ROTATIONAL ADJUSTER BASE PLATE | 304/316 SSTL | 6 | 6 | 12 |
| 11 | D060331 | F | Advanced LIGO, SUS, Quad N-Ptype Top Stage, JACKING SCREW/Earthquake Stop | 304/316 SSTL | 20 | 20 | 40 |
| 12 | D060333 | F | Advanced LIGO, SUS, Quad N-Ptype Top Stage, WIRE CLAMP BODY, TOP STAGE | 304/316 SSTL | 6 | 6 | 12 |
| 13 | D060336 | v4 | Advanced LIGO, SUS, Penre MASS Quad N-Ptype, 2MM CAM, OSEM ADJUSTER | PH Bronze | 48 | 48 | 96 |
| 14 | D060377 | H | Advanced LIGO, SUS, Quad N-Ptype UI MASS, BLADE TIP Z POSITION ADJ (BTM HALF PART 2) | 6061-T6 Al | 6 | 6 | 12 |
| 15 | D060378 | J | Advanced LIGO, SUS, Quad N-Ptype UI MASS, BLADE TIP Z POSITION ADJ (BTM HALF) | 304, 316 OR 302 SSTL | 6 | 6 | 12 |
| 16 | D060380 | J | ADVANCED LIGO, SUS, QUAD N-PTYPE UI MASS, BLADE CLAMP (TOP HALF) | 304 SSTL | 6 | 6 | 12 |
| 17 | D070140-05 | v3 | Advanced LIGO, SUS, Quad N-Ptype Top Stage, top stage blade wire clamp shim | 6061-T6 Al | 54 | 54 | 108 |
| 18 | D070140-1 | v3 | Advanced LIGO, SUS, Quad N-Ptype Top Stage, top stage blade wire clamp shim | 6061-T6 Al | 54 | 54 | 108 |
| 19 | D070140-2 | v3 | Advanced LIGO, SUS, Quad N-Ptype Top Stage, top stage blade wire clamp shim | 6061-T6 Al | 54 | 54 | 108 |
| 20 | D0901439 | B | Top Stage Modified Backbone Member | 6061 Al | 6 | 6 | 12 |
| 21 | D1000395 | v1 | aLIGO INTERMEDIATE TOP MASS SPACER | 304 SSTL | 9 | 9 | 18 |
| 22 | D1000396 | v1 | aLIGO INTERMEDIATE WIRE CLAMP BODY MIDDLE WIRE | 304 SSTL | 6 | 6 | 12 |
| 23 | D1000407 | v3 | aLIGO_OSEMS_INTERMIDIATE_SUPPORT_RIGHT_SIDE_BRACKET | 6061-T6 Al | 3 | 3 | 6 |
| 24 | D1000408 | v3 | aLIGO_BOSEMS_INTERMIDIATE_SUPPORT_LEFT_SIDE_BRACKET | 6061-T6 Al | 3 | 3 | 6 |
| 25 | D1000409 | v3 | aLIGO_BOSEMS_INTERMIDIATE_SUPPORT_RIGHT_SIDE_TRAY | 6061-T6 Al | 3 | 3 | 6 |
| 26 | D1000410 | v3 | aLIGO_BOSEMS_INTERMIDIATE_SUPPORT_LEFT_SIDE_TRAY | 6061-T6 Al | 3 | 3 | 6 |
| 27 | D1000411 | v3 | TMS Intermediate OSUM Support Plate, Rear | 6061-T6 Al | 3 | 3 | 6 |
| 28 | D1001534 | v1 | Magnetic Plug, BOSEM | 416 SSTL | 42 | 42 | 84 |
| 29 | D1001697 | v1 | Magnet Retainer, BOSEM | 316 SSTL | 42 | 42 | 84 |
| 30 | D1100358 | v1 | TMS Telescope Mass Attachment Screw | Titanium | 100 | 100 | 200 |
| 31 | D1100421 | v1 | TMS Suspension Tablecloth Plate, Front | 6061-T6 Al | 3 | 3 | 6 |
| 32 | D1100573 | v5 | BOSEM Flat Magnet Flag, aLIGO SUS | 6061-T6 Al | 36 | 36 | 72 |
| 33 | D1100574 | v3 | BOSEM Flat Flag Disk | 416 SSTL | 36 | 36 | 72 |
| 34 | D1100712-01 | v2 | TMS Earthquake Stop Screw | 316 SSTL | 25 | 25 | 50 |
| 35 | D1100712-02 | v2 | TMS Earthquake Stop Screw | 316 SSTL | 100 | 100 | 200 |
| 36 | D1100980 | v1 | ALIGO, QUAD, E.STOP SCREW, SPLIT SHAFT COLLAR | SSTL | 6 | 6 | 12 |
| 37 | D1101186 | v1 | aLIGO SUS .500-13 X 1 SHCS Modified | 316 SSTL | 60 | 60 | 120 |
| 38 | D1101273 | v1 | aLIGO SUS Top Mass Stop Bridge | 6061-T6 Al | 6 | 6 | 12 |
| 39 | D1101511 | v1 | aLIGO TMS Upper Mass Top Plate | 304 SSTL | 6 | 6 | 12 |
| 40 | D1101512 | v1 | aLIGO TMS Upper Mass Bottom Plate | 304 SSTL | 3 | 3 | 6 |
| 41 | D1101519 | v1 | aLIGO TMS Top Add Mass Tower | 304 SSTL | 6 | 6 | 12 |
| 42 | D1101520 | v1 | aLIGO TMS Upper Roll Trim Mass | 304 SSTL | 6 | 6 | 12 |
| 43 | D1200312 | v1 | aLIGO TMS Top Add Mass Bar | 304 SSTL | 6 | 6 | 12 |
| 44 | D1200327 | v1 | aLIGO SUS BOSEM Flag Bracket | 6061-T6 Al | 12 | 12 | 24 |
| 45 | D1200328 | v1 | aLIGO SUS BOSEM Flag Center Bracket | 6061-T6 Al | 3 | 3 | 6 |
| 46 | D1200356 | v1 | aLIGO TMS Mass Spacer | 6061-T6 Al | 3 | 3 | 6 |
| 47 | D1200404 | v1 | aLIGO TMS Lower Stage Spring Adjuster Screw | 300 SSTL | 20 | 20 | 40 |
| 48 | D1200405 | v1 | aLIGO TMS Upper Pitch Trim Mass | 304 SSTL | 6 | 6 | 12 |
| 49 | D1200406 | v1 | aLIGO TMS Spring Stop Screw | 300 SSTL | 20 | 20 | 40 |
| 50 | D1200420 | v1 | aLIGO TMS Mass Cable Clamp Bracket | 6061-T6 Al | 3 | 3 | 6 |
| 51 | D1200426 | v1 | aLIGO TMS Mass Wire Clamp Adjustment Block | 6061-T6 Al | 6 | 6 | 12 |
| 52 | D1200427 | v1 | aLIGO TMS Upper SUS Wire Adjuster | 6061-T6 Al | 12 | 12 | 24 |
| 53 | D1200431-01 | v1 | aLIGO TMS Balance Weight | 304 SSTL | 18 | 18 | 36 |
| 54 | D1200431-02 | v1 | aLIGO TMS Balance Weight | 304 SSTL | 18 | 18 | 36 |
| 55 | D1200432-01 | v1 | aLIGO TMS Small Balance Weight | 304 SSTL | 18 | 18 | 36 |
| 56 | D1200432-02 | v1 | aLIGO TMS Small Balance Weight | 304 SSTL | 18 | 18 | 36 |
| 57 | D1200476 | v1 | aLIGO TMS Mass Cable Clamp Screw | 300 SSTL | 20 | 20 | 40 |
| 58 | D1200477 | v1 | aLIGO TMS Mass Cable Clamp Nut | Nickel-Copper Alloy 400 | 20 | 20 | 40 |

List all parts to be made, including the public hyperlink to the latest revision, and the total quantity required.  If you have more than ten parts, create a separate drawing document posted to the DCC as a public document, and link here.

- Manufacturing:

# Requirements:

# Suppliers must refer to the LIGO Specifications referenced in Section 3 for additional, and in some cases, non-industry standard requirements.

# Sub-Contracted Work:

# The Supplier shall be responsible for all sub-contracted work.

## Precedence:

The drawings typically represent the finished part as needed for use in service.  There may be requirements on the drawing (such as coatings) which are specifically defined as not the responsibility of the supplier in this SOW.  Suppliers should always contact a LIGO representative to resolve any discrepancies uncertainties in the documentation or instructions.

## Special Instructions:

- Parts with material call outs for 5083 Aluminum MUST be manufactured with 6061-T6 Aluminum.

- All completed parts must consist of 100% virgin material, free of repairs such as plugs or welds.

- All parts are to be 63 µ Ra.

- Part markings may be laser marked or engraved.Add special manufacturing notes

- Vendor is responsible for electro-polish processing where specified.

- All tapped holes oversized 0.005" unless 1) there is a call-out for heli-coils 2) there is a specific note that says not oversized.

- LIGO must approve source of all ‘make from’ parts.

# Exclusions:  Add/delete as appropriate

# Supplier is NOT responsible for the procurement and installation of Heli-Coils.

- End Item Data Package:  Add/delete lines as necessary

Before delivery of the parts, the Supplier shall provide the following data, as a minimum:

- Any as-built modifications (with approval of the LIGO Contracting Officer) as mark-ups to the drawings

- Material certifications

- Heat Treat and/or Stress Relief certifications, if applicable

- Electro-polish certifications, if applicable

- Pickle/Passivation certifications, if applicable

- Inspection reports of all dimensional features for the number of parts specified per the AQL number and referenced in the AQL table LIGO-Q1100003-v1 and any other inspection requirements detailed in Section 5 of this SOW

- Certificate of compliance for each part number stating conformance to contract and drawing requirements

- Delivery Requirements:

  - Shipping Containers and Packaging:

The contractor is responsible for providing shipping containers and transportation which protects these parts from damage from the transportation environment (weather, handling, accidents, etc.).  Mating edges of parts should be especially protected from damage during shipping.

Note any special packaging requirements here (i.e., wrap in UHV foil and Ameristat).

  - Shipping Destination(s):

The deliveries are FOB at these destinations, i.e. the Supplier has the responsibility for shipping title and control of goods until they are delivered and the transportation has been completed. The contractor selects the carrier and is responsible for the risk of transportation and for filing claims for loss or damage.

Delete shipping destinations that don’t apply to this SOW.  Be sure to reference the shipping abbreviations (i.e., LLO) in the Delivery Schedule if there is more than one shipping destination.

These items will be shipped to:

LIGO Livingston Observatory (LLO)

Attn: Valera Frolov

19100 LIGO Lane

Livingston, LA 70754

LIGO Hanford Observatory (LHO)

Attn: Cheryl Vorvick

127124 North Route 10

Richland, WA  99354

  - Delivery Schedule:

Early and/or partial deliveries are welcome.

- Ship Set 1 to: LIGO Livingston Observatory (LLO)

  - Due 8 weeks ARO

- Ship Set 2 to: LIGO Hanford Observatory (LHO)

- Due 12 weeks ARO

Insert a list or table detailing the delivery requirements (by P/N, as necessary).  Delivery should be specified in weeks ARO (after receipt of order).  Please also specify the shipping destination (i.e. LLO).

Note any first article requirements.  If applicable, the SOW must state upfront that LIGO wants to assemble the first articles for fit check before the rest of the order is completed.

# Text boxes

# LIGO LABORATORY

California Institute of Technology

1200 E. California Blvd.

Pasadena, CA  91125