## Slide 1: Data Acquisition, Diagnostics & Controls (DAQ)
Rolf Bork, CIT
Technical Status
Annual NSF Review of Advanced LIGO Project
April 11 - 13, 2012
LIGO-G1200370-v2
2012 March 28

## Slide 2: DAQ Functions
Provide a global timing and clock distribution system to synchronize all realtime control and data acquisition.
Provide a common Control and Data System (CDS) infrastructure design and standards for use in all aLIGO subsystem controls.
  Real-time applications development tools and code library
    Including “hard” real-time operating system, I/O drivers and inter-process communications.
  Computer and I/O standards
Provide all software necessary to synchronously acquire and archive data.
Provide all computing and networking hardware as necessary to collect data from the various subsystems, format the data and write the data to disk.
Provide a standard set of diagnostic tools for use in all control subsystems, including ability to:
  Inject arbitrary waveforms into realtime control systems
  Set and acquire data from defined testpoints on demand
  Distribute both diagnostic data and acquired data channel to operator stations
  Provide data visualization and analysis tools in support of operations and commissioning.

## Slide 3: DAQ Functions (Continued)
Provide computers, I/O hardware and software for the acquisition of Physical Environment Monitoring (PEM) data.
  New interfaces for existing PEM sensors
Computers and infrastructure software for the Diagnostic Monitoring Tools (DMT)
  Specific application software provided by LSC members
Control room computers and associated networking, including a common set of operations support software.
Provide off-line test and development systems for both sites

## Slide 4: DAQ System Data Acquisition Requirements
Provide a hardware design and software infrastructure to support real-time servo control applications
  Deterministic to within a few μsec.
  High performance to support servo loop rates from 2048Hz to 65536Hz
  Built-in diagnostic and data acquisition features
Acquire and record up to 15MBytes/sec continuously from each interferometer.
  ‘Fast’ data channels at rates from 256 to 32768 samples/sec (Up to 3000/IFO)
  ‘Slow’ data channels at up to 16 samples/sec, with up to 70K channels per interferometer
Provide capabilities to acquire (but not record) an additional 15MB/sec of diagnostic data.
Write data in LSC/VIRGO standard Frame format to disk system provided by Data and Computing System (DCS).
  Provide local disk to allow up to two weeks of data storage
Provide an internal data distribution system to communicate diagnostic and acquired data to operator stations and Diagnostic Monitoring Tool (DMT) computers.

## Slide 5: DAQ System Design Overview
Timing system provides clocks to PCI Express (PCIe) modules in I/O chassis.
PCIe modules interface to control computer via PCIe fiber link.
Control computer acquires data and transmits to DAQ data concentrator (DC) via network.
DC assembles data from all controllers and broadcasts full data blocks every 1/16 second.
FrameWriter computers format data and write to disk (32sec. data frame)
Network Data Server (NDS) provides data on demand either live or from disk.

## Slide 6: Timing Distribution System (TDS)
Contracted to Columbia Univ. for manufacture and test after a joint development effort. Design described in the journal "Classical and Quantum Gravity” under Imre Bartos et al., 2010 Class. Quantum Grav. Vol. 27, No. 8, 084025
Timing Slave provides accurate clocks
At 65536Hz to ADC/DAC modules.
IRIG-B Timing Fanout
Provides accurate time information to computers.

## Slide 7: TDS IRIG-B Distribution Unit
IRIG-B system used to provide time information, in GPS seconds, to DAQ and control computers.
  Includes standard timing slave card to get time information from TDS.
  Outputs IRIG-B standard time code
    DC Level Shift format
  Commercial IRIG-B Receiver modules in computers for accurately setting time in GPS seconds.
  Time accuracy to better +/- 1 μsec.
  Second source of system time verification, along with duotone signal acquired from timing slave in I/O chassis.

## Slide 8: Timing Distribution System Status
Major components for all IFO have been delivered
  L1/H2 systems installed.
  H1 installation in progress.
Remaining deliveries should be complete by June, 2012:
  Timing comparators – in test.
  4 additional IRIG-B fanout units – in production.
Slave-DuoTone pair being tested at Columbia
Master front boards under production

## Slide 9: CDS Standard PCI Express I/O Chassis
Timing Slave
17 Slot
PCIe Bus with
PCIe Uplink
I/O Timing Bus
I/O Interface Module
24V DC Supply
Commercial PCIe expansion motherboards.
Custom I/O timing and interface backplane.
I/O interface modules provide timing and interface between PCIe module connectors and field cabling.
Two fiber optic links.
  To timing distribution system via timing slave module.
  To computer, via fiber optic PCIe link.

## Slide 10: CDS Standard Computers
Supermicro X8DTU-F Motherboards
  Fulfills BIOS PCI-e card mapping and real-time stability requirements
Single Xeon X5680 processor with six cores at 3.33GHz
Up to 4 full height + 1 half-height PCIe slots
Two GigE Ethernet ports
  Separate EPICS/DAQ networks
No disk drives installed in computers used for real-time control
  Operated as diskless-node from central boot server
Operating Systems
  Gentoo with Linux kernel 2.16.34, plus LIGO RT patch
  Ubuntu Linux for CDS servers and other non-real-time computers

## Slide 11: Networking
Ethernet backbones for most applications
  GigE switches with fiber uplinks from end stations
  GigE switches with 10G uplink options for corner station
    10G uplink for DAQ and video connections
  10G switches for DAQ Broadcasts
Low latency networks for real-time data communications.
  Initial LIGO type reflected memory (for long runs to end stations)
  PCIe network, employing reflected memory software (corner station computers)

## Slide 12: PCI Express (PCIe) Real-time Control Network
Low Latency (1.25usec)
High speed (10Gbit/sec)
Cable or Fiber connections
  CX-4 cable to 3 meters
  Multi-core fiber to 100 meters
Stackable 10 port Switches
Reflected Memory Mode
  Data broadcast to same memory location on each computer on the network.

## Slide 13: Corner to End Station Real-time Control Network
Loop topology
Low Latency (700nsec/node)
High speed (2Gbit/sec)
Fiber connections
  Up to 10km
Bypass Switch provided at each location
Reflected Memory
  Data broadcast to same memory location on each computer on the network.

## Slide 14: Networking – Progress
All Ethernet switches have been procured and delivered for all three interferometers.
  All network switches have been configured for L1 and H2.
  H1 switches are being installed/configured.
All real-time networking equipment procured and delivered.
  Systems installed and running at both sites.

## Slide 15: Physical Environment Monitoring Infrastructure
For aLIGO, PEM system will provide control as well as DAQ
  On-line Adaptive Filtering and feed-forward control.
One computer + 1 I/O chassis at each station and at corner station.
Re-use existing PEM sensors
Up to 128 channels of ADC + 8 channels of DAC
  I/O connections via AA/AI chassis with BNC connections.
Progress
  Computers, I/O chassis and ADC/DAC modules have all been procured and delivered.
  9 of the 12 AA Chassis have been built and tested.
  LLO End Station system under test ------------------

## Slide 16: DAQ Computing / Storage Equipment (All Delivered and Installed)
Data Concentrator (DC) (2)
  Collects data from all real-time control computers and broadcasts to 10GigE network.
  One unit on-line, second hot backup
FrameWriter (2)
  Receive data from DC
  Format data into LVC standard Frame format
  Write data to disk
    Local
    Data Analysis group disk farm
Network Data Server (NDS) (2)
  Provides real-time or stored data on request to various control room software tools
    NDS clients also developed for Perl, Python and Matlab
Two computers running Solaris operating system to connect disk systems via QFS.
24 TByte Local Disk

## Slide 17: Control Room and Global Diagnostic Systems
iMac computers w/additional monitor chosen as the standard configuration for operator stations.
  Ubuntu Linux Operating System
Two, dual CPU computers, similar to real-time control computers, in place for Global Diagnostic Monitoring Tool (DMT) applications.
  24TByte disk drive provided for storage of DMT information.
All equipment is in-house and undergoing installation/test.

## Slide 18: Software Real-time Application Support
Continued refinement of graphical tool for real-time code generation (“RCG”).
Allows control application development and documentation without having to know a programming language.
Allows programming staff to concentrate on development and test of common code modules.

## Slide 19: Software Real-time Application Build Process
Build and save RCG model.
make ‘modelName’
  Perl scripts parse the model file to determine signal connections and code flow
  Perl scripts generate EPICS and real-time source code.
  Compiler is invoked to link common code libraries and produce real-time and EPICS executable software.
make install
  Moves executables to target directories for load onto real-time computers.
  Channel descriptor files generated for use by DAQ and GDS
  Basic set of operator displays generated.

## Slide 20: Real-time Core and Patch
aLIGO Real-Time (RT) code not “traditional”
  No pre-emptive operating system scheduler
  No interrupts, semaphores, priorities, ensuing context switching, etc.
Each RT app locked to its own CPU core
  Using custom patch to Linux kernel “play dead” routine
    Notifies Linux scheduler that CPU is going down and unavailable for interrupts/task assignment.
    Inserts RT app code instead of Linux idle routine.
    Removal of RT app brings the CPU “back to life” and reconnects to Linux as a useable resource.
  RT code runs in continuous loop
    Triggered by arrival of ADC data in local memory (polling or MONITOR/MWAIT CPU instructions)
      ADC modules set up to automatically transfer data to computer memory on clock trigger
    Never switched out ie always resident on stack, in cache, memory
For each RT computer, there is a special case model called an Input/Output Processor (IOP)
  Controls startup timing and synchronization.
  Maps and initializes all of the PCIe I/O interfaces
  Triggers and monitors user applications.
  Always running, allowing user apps to come and go, as necessary
Core 0 Linux
Non-RT Tasks
(eg EPICS)
Ethernet
PCIe
Core 1
IOP
ADC Data
Core 2 - N
Usr App

## Slide 21: DAQ System Front-End Software Design
A common DAQ library is compiled into each FE application.
Acquires data at user defined rates and transmits data as 1/16sec data blocks:
  For archive, as described in a DAQ channel configuration file.
  Test point and excitation channel data on demand
    As requested via the arbitrary waveform generator/test point manager (awgtpman)
  Supports aggregate (DAQ+TP) data rate of 2MB/sec per FE processor
  CRC checksums and timestamps sent with all data blocks
Supports various configurations
  (1) Data to FrameWriter/NDS software on same computer via shared memory
    Allows a complete stand-alone system to support various subsystem test stands
  (2) Data to shared memory, with separate network software
    Supports multiple FE applications on same computer
    Relieves RT front end code from network error handling and other possible delays

## Slide 22: DAQ System Backend Software Design
Data Concentrator
  Collects ‘fast’ data from all FE computers via dedicated network
  Collects ‘slow’ (EPICS) data via CDS network
  Broadcasts combined data to upstream computers as 1/16 sec data blocks on to 10Gb Ethernet
FrameWriter
  Format data into standard LIGO Frame using FrameCpp library, with data compression.
  Write data, via QFS, to DCS disk farm (32 second data file)
Network Data Server (NDS)
  Provides live and archived data feeds, on request, to CDS operator stations

## Slide 23: Software Status
“Final” code version tested and released.
  Any new code change requests / bug fixes are to be part of commissioning and operations activities.
“Line by Line” code review in progress by team not involved in the code development.
  Additional outside review planned.
In process of completing/updating documentation necessary to meet system acceptance requirements.

## Slide 24: NSF Review 2011 Concerns
Concern:
  Cyber-security, particularly as it pertains to remote access to LIGO control/DAQ systems.
Action Taken:
  Continuing to work with LIGO cyber-security staff on issues / solutions.
    Presently have a two tier authentication system in place, with access provided to a limited set of staff.
    In process of implementing and testing “one time use” password system.
    Working to develop a method for the site operator to provide final approval for remote logins.

## Slide 25: DAQ System Summary
Software Development
  Complete soon, pending final reviews.
Equipment Procurement
  Complete
Installation
  L1/H2 systems complete and operational.
  H1 system installed; cabling and network setup in progress. Anticipate system will be operational by end of April 2012.