# Document Change Notice (DCN) Title:

| Document No. Doc-Rev |  | New Rev |
| --- | --- | --- |
| D080521-v3 | HEPI Pier Pod Design Change Notice | V4 |

CHANGE DESCRIPTION (FROM/TO):

Initial Release has been changed to v4 by changing R13 from a 2 KOhm resistor to a 33.2K Ohm resistor.  This will change the gain of the L4C channels from 22 to 333.  A thin film resistor should be used for this replacement.  An example of good parts are Digikey P/N:

RNCP1206FTD33K2CT-ND.

REASON FOR CHANGE: To raise the gain of the L4C channels in the Pier Pods.

ACTION:                 Incorporate Change        Attach DCN to Drawings           Other Action (specify):

DISPOSITION OF HARDWARE
(IDENTIFY SERIAL NUMBERS)

DCN DISTRIBUTION

Required:

excomm (Lab Grp Leads, LSC Spokesperson)

Michael Landry (LHO AdL Liaison)

Brian O'Reilly (LLO AdL Liaison)

Bill Tyler (Lab Safety & QA)

| Recommended (AdL Area/Subsys Leads & Cog. Sci./Eng., subsystem email distribution lists): [please delete if/as appropriate for this DCN] |
| --- |
| Ken Mason | Brian Lantz | Richard McCarthy |
| Celine Remet | Mike Fyffe | Vincent L’Huiller |

Additional Distribution List for this DCN:

SAFETY, COST, SCHEDULE, REQUIREMENTS IMPACT?           NO           YES

(If YES, enter CR (CCB) or TCP (TRB) #)

Other disposition/instructions or additional comments:

List S/Ns to be retested per this change:

| APPROVALS: | DATE | OTHER APPROVALS (SPECIFY) | DATE |
| --- | --- | --- | --- |
| ORIGINATOR: Ben Abbott | 4/24/2012 |  |  |
| TASK LEADER: Brian Lantz |  |  |  |
| GROUP LEADER: |  |  |  |
| DCC RELEASE: |  |  |  |

List S/Ns to be reworked/scrapped: All

List S/N’s to be built with this change: all future Chassis.

No hardware was affected (record change only):

(Continue on sheet 2 if needed)

List S/Ns which comply already: None