LIGO Laboratory / LIGO Scientific Collaboration

LIGO-T1200176-v1                                                                                                       4/18/12

LCGT

bLCGT Recycling Cavity Baffles Conceptual Design

Michael Smith

Distribution of this document:

LIGO Scientific Collaboration

This is an internal working note

of the LIGO Laboratory.

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW22-295 185 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 159 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

http://www.ligo.caltech.edu/

Table of Contents

1	INTRODUCTION	5

1.1	Applicable Documents	5

2	WEDGE ANGLES	5

3	RECYCLING CAVITY BAFFLES	5

3.1	Power Recycling Cavity	5

3.1.1	PR3	5

3.1.2	PR2	6

3.1.3	PRM	8

3.2	Signal Recycling Cavity	9

3.2.1	SR3	9

3.2.2	SR2	10

3.2.3	SRM	11

3.2.4	Output Faraday Isolator	11

3.2.5	Ouput Mode Cleaner	12

3.3	Baffle Characteristics	13

3.4	Stray Light Noise	14

3.4.1	Seismic Motion	14

3.4.2	OFI and OMC Suspension Transmissibility	15

3.4.3	Beam Dump Surface BRDF	16

3.4.4	Recycling Cavity Baffles Scatter	17

3.4.4.1	DARM Motion Transfer Functions	17

3.4.4.2	PRM Scatter	18

3.4.4.3	PR2 Scatter	23

3.4.4.4	PR3 Scatter	25

3.4.4.5	BS Ghost Beams and SR2 HR Scatter	28

3.4.4.6	ITM Ghost Beams Scatter	31

3.4.4.7	SRM Scatter	33

3.4.4.8	SR2 Scatter	35

3.4.4.9	SR3 Scatter	38

3.4.4.10	Output Faraday Isolator (OFI) Scatter	41

3.5	Optical Interfaces	44

4	INTERFACE CONTROL DOCUMENT	45

Table of Figures

Figure 1: PR3 HR and PR3AR Baffles; POY Pick-off Beam	6

Figure 2: PR2 HR, PR2 Scraper Baffle, POB Pick-off Beam	7

Figure 3: PRM HR and AR Baffles	8

Figure 4: SR3 HR and AR Baffles	9

Figure 5: SR2 Scraper Baffle, SR2AR Baffle; POX Pick-off Beam	10

Figure 6: SRM, SRM AR Baffles	11

Figure 7: Output Faraday Isolator, MMT2 OMC	12

Figure 8: Output Mode Cleaner, MMT1 OMC	13

Figure 9: Seismic Ground Noise, m/rtHz	14

Figure 10: OFI Transmissibility along beam axis	15

Figure 11: DARM motion transfer functions	17

Figure 12: PRM Ghost Beam Scatter	22

Figure 13: PR2 Ghost Beam Scatter	25

Figure 14: PR3 Ghost Beam Scatter	28

Figure 15: BS and SR2 Ghost beams Scatter	30

Figure 16: ITM Ghost Beam Scatter	32

Figure 17: SRM Ghost Beam Scatter	35

Figure 18: SR2 Ghost Beam Scatter	38

Figure 19: SR3 Ghost Beam Scatter	41

Figure 20: OFI, OMC, OMC Refl, and output PD scatter	44

# INTRODUCTION

This document presents a conceptual design for the bLCGT Recycling Cavity Baffles.

## Applicable Documents

# WEDGE ANGLES

The ITM and BS wedge angles determine the positions of the recycling cavity baffles.

The symmetric BS wedge angle = 0.050 deg is chosen so that the POX beam, which reflects from the AT surface of the BS, will hit the SR3 HR surface and separate from the main IFO beam at the vicinity of SR2, where the POX pick-off mirror will be located. The thick side of the BS mirror faces toward the arms of the IFO.

The ITM wedge angle = 0.025 deg is chosen so that the ITMY GBAR3 hits the PR3 mirror. The thick side of ITMX faces in the –Y direction; the thick side of ITMY faces in the +X direction

# RECYCLING CAVITY BAFFLES

## Power Recycling Cavity

### PR3

Figure 1: PR3 HR and PR3AR Baffles; POY Pick-off Beam

### PR2

Figure 2: PR2 HR, PR2 Scraper Baffle, POB Pick-off Beam

### PRM

Figure 3: PRM HR and AR Baffles

## Signal Recycling Cavity

### SR3

Figure 4: SR3 HR and AR Baffles

### SR2

Figure 5: SR2 Scraper Baffle, SR2AR Baffle; POX Pick-off Beam

### SRM

Figure 6: SRM, SRM AR Baffles

### Output Faraday Isolator

Figure 7: Output Faraday Isolator, MMT2 OMC

### Ouput Mode Cleaner

Figure 8: Output Mode Cleaner, MMT1 OMC

## Baffle Characteristics

Table 1: ? Baffle Characteristics

| Parameter | Value |
| --- | --- |
| Location |  |
| Suspension |  |
| Inside aperture diameter |  |
| Outer diameter |  |
| Material |  |
| BRDF |  |
| Weight |  |

## Stray Light Noise

### Seismic Motion

The ground motion is taken from the Kamioka mine data.

The cryoshield seismic motion is measured data.

The seismic motion of the suspended table, which was modeled as 1/10 the seismic ground motion, can be taken as a minimum requirement.

All of the recycling cavity baffles are mounted to a suspended table in the chamber.

.

Figure 9: Seismic Ground Noise, m/rtHz

### OFI and OMC Suspension Transmissibility

The Output Faraday Isolator (OFI) and the output mode cleaner (OMC) are mounted to the suspended table, but must be suspended by an additional suspension structure. The aLIGO OFI suspension transmissibility was used as a SUS model for these calculations.

Figure 10: OFI Transmissibility along beam axis

### Beam Dump Surface BRDF

Most of the baffles are constructed of polished oxidized steel with the first surface inclined at an incidence angle 57 deg. The measured BRDF is < 0.03 sr-1.

The PRM AR & HR baffle is composed of polished silicon carbide, because it also serves as an errant beam baffle and must absorb the 50 W PSL beam without being damaged. Likewise, the PRM HR baffle is composed of polished silicon carbide, because it also serves as an errant beam baffle and must absorb the reflected beam from PR2 without being damaged.

The output mode cleaner (OMC) Refl beam dump must be made of black glass, with BRDF = 1E-6 sr^-1, in order to reduce the scattering to an acceptable level.

### Recycling Cavity Baffles Scatter

#### DARM Motion Transfer Functions

Figure 11: DARM motion transfer functions

#### PRM Scatter

PRM GBHR3

power incident on PRM HR beam dump from PRM GBHR3

(forward and backward beams),  W

power scattered from  PRM HR3 baffle, W

displacement noise @ 100 Hz, m/rtHz

PRM GBAR3

power incident on PRM AR Baffle (forward and backward beams), W

power scattered from  PRM AR Baffle, W

displacement noise @ 100 Hz, m/rtHz

Scatter of IO Reflected beam from input Faraday isolator

Reflected power from PRM, W

power scattered from  input Faraday isolator surface, W

displacement noise @ 100 Hz, m/rtHz

Scatter from dumped IO Reflected beam

Need SiC surface for beam dump, water cooled

power scattered from  Refl Beam Dump, W

displacement noise @ 100 Hz, m/rtHz

Figure 12: PRM Ghost Beam Scatter

#### PR2 Scatter

PR2 GBHR3

power incident on PR2 scraper baffle from PR2 GBHR3

(forward and backward beams),  W

power scattered from  PR2 GBHR3 toward PR3, W

power scattered from  PR2 GBHR3 toward PRM, W

total power scattered from  PR2 GBHR3

displacement noise @ 100 Hz, m/rtHz

PR2 GBAR1 (POB)

power incident on PR2 AR Baffle (forward  beam), W

PR2 GBAR3

power incident on PR2 AR Baffle (forward  and backward beams), W

power scattered from  PR2 GBAR3 toward PR3, W

power scattered from  PR2 GBAR3 toward PRM, W

total power scattered from  PR2 GBAR3

displacement noise @ 100 Hz, m/rtHz

Figure 13: PR2 Ghost Beam Scatter

#### PR3 Scatter

PR3 GBHR3

power incident on chamber wall from PR3 GBHR3

(forward and backward beams),  W

power scattered from  chamber wall by

PR3 GBHR3 toward BS, W

power scattered from  chamber wall by

PR3 GBHR3 toward PR2, W

total power scattered from chamber wall by

PR3 GBHR3

displacement noise @ 100 Hz, m/rtHz

PR3 GBAR1

power incident on PR3 AR Baffle

(forward and backward beams), W

power scattered from  PR3 AR Baffle toward BS, W

power scattered from  PR3 AR Baffle toward PR3 W

total power scattered from  PR3 AR Baffle, W

displacement noise @ 100 Hz, m/rtHz

Figure 14: PR3 Ghost Beam Scatter

#### BS Ghost Beams and SR2 HR Scatter

BS_GBAR1 (POX)

power incident on SR2 Scraper Baffle from X arm, W

power scattered from  SR2 Scraper Baffle, W

displacement noise @ 100 Hz, m/rtHz

BS_GBAR3P

The stray light from both arms are almost anti-resonant, and the wavefronts overlap; their coherent sum is reduced by the  square of the asymmetry coefficient for common mode field rejection

power incident on SR2 Scraper Baffle from both arms, W

power scattered from  SR2 Scraper Baffle, W

displacement noise @ 100 Hz, m/rtHz

Figure 15: BS and SR2 Ghost beams Scatter

#### ITM Ghost Beams Scatter

ITMX_GBAR1_BD

Part of the ITMX_GBAR1 is caught by the ITMX elliptical baffle,

part reflects from SR2 back through BS and is caught by ITMY ACB.

Power of ITMX GBAR1, W

ITMY_GBAR1_BD

Part of the ITMY_GBAR1 merges with the POX beam and POY beam at PR2,

part of it is caught by the PR3 HR baffle

ITMY_GBAR3 POY

Power incident on POY PO mirror, W

ITMY_GBAR4

2nd order beam can be ignored. Part of the GBAR4 beam is caught on the ITMY Elliptical baf,

part is caught on PR2 scraper baffle

ITMX_GBAR3_BD

power incident on PR2 Scraper Baffle, W

power scattered from  PR2 Scraper Baffle, W

displacement noise @ 100 Hz, m/rtHz

Figure 16: ITM Ghost Beam Scatter

#### SRM Scatter

SRM_GBHR3

power incident on SRM HR baffle,  W

power scattered from  SRM HR baffle, W

displacement noise @ 100 Hz, m/rtHz

SRM_GBAR3

power incident on SRM AR Baffle, W

power scattered from  SRM AR Baffle, W

displacement noise @ 100 Hz, m/rtHz

Figure 17: SRM Ghost Beam Scatter

#### SR2 Scatter

SR2 GBHR3

power incident on SR2 scraper baffle from SR2 GBHR3

(forward and backward beams),  W

power scattered from  SR2 GBHR3 toward SR3, W

power scattered from  SR2 GBHR3 toward SRM, W

total power scattered from  SR2 GBHR3

displacement noise @ 100 Hz, m/rtHz

SR2 GBAR1

SR2 GBAR1 power incident on SR2 AR Baffle (backward beam), W

power scattered from  SR3 AR Baffle, W

displacement noise @ 100 Hz, m/rtHz

SR2 GBAR3

SR2 GBAR3 power incident on SR2 AR Baffle (forward and backward beams), W

power scattered from  SR3 AR Baffle, W

displacement noise @ 100 Hz, m/rtHz

Figure 18: SR2 Ghost Beam Scatter

#### SR3 Scatter

SR3 GBHR3

power incident on wall from SR3 GBHR3 (forward and backward beams),  W

power scattered from  wall by

SR3 GBHR3 toward BS, W

power scattered from wall by SR3 GBHR3 toward SR2 W

total power scattered from SR2 scraper baffle by

from SR3 GBHR3

displacement noise @ 100 Hz, m/rtHz

SR3 AR Baffle

power incident on SR3 AR Baffle

(forward and backward beams), W

power scattered from  SR3 AR Baffle toward BS, W

power scattered from  SR3 AR Baffle toward SR2, W

total power scattered from  SR3 AR Baffle, W

displacement noise @ 100 Hz, m/rtHz

Figure 19: SR3 Ghost Beam Scatter

#### Output Faraday Isolator (OFI) Scatter

Output Faraday Isolator

power incident on Output Faraday Isolator, W

power scattered from  OFI, W

displacement noise @ 100 Hz, m/rtHz

Output Mode Cleaner

TEM00power incident on Output mode cleaner, W

power scattered from  OMC W

displacement noise @ 100 Hz, m/rtHz

Output Mode Cleaner Refl

power reflected from Output mode cleaner, W

power scattered from  OMC Refl BD, W

displacement noise @ 100 Hz, m/rtHz

Output Photodetector

power incident on output photodetector, W

power scattered from  PD, W

displacement noise @ 100 Hz, m/rtHz

Figure 20: OFI, OMC, OMC Refl, and output PD scatter

## Optical Interfaces

# INTERFACE CONTROL DOCUMENT

.