## Slide 1
D. Friedrich
ICRR, The University of Tokyo
K. Agatsuma, S. Sakata, T. Mori, S. Kawamura
QRPN Experiment
with
Suspended 20mg Mirrors

## Slide 2
Objectives
Observation/Reduction of Quantum Radiation Pressure Noise
  Back-action correlates amplitude and phase fluctuations
  Ponderomotive squeezing
Laser light and
vacuum fluctuations
displacement
Laser light and
ponderomotively
squeezed vacuum

## Slide 3
Homodyne detection
Suspended
20mg mirror
@1064nm
Fabry-Perot Michelson ifo
Approach
Topology
  Fabry-Perot Michelson interferometer
  Homodyne detection
Key elements
  High Finesse cavities (F=10000)
  Tiny suspended end mirrors (m=20mg)
20mg
20mg
mirror
≈500W

## Slide 4
Design Sensitivity/Parameter
S.Sakata et al. J.Phys.: Conf. Ser. 122, 012020 (2008)
Observation of QRPN around 1kHz
Reduction @ 1kHz by 6db ponderomotive squeezing
Laser power | 200 mW
Injected laser power | 120 mW
Finesse | 10000
End mirror mass | 20 mg
Diameter of end mirror | 3 mm
Thickness of end mirror | 1.5 mm
Front mirror mass | 14 g
Reflectivity of end mirror | 99.999 %
Reflectivity of front mirror | 99.94 %
Optical loss | 50 ppm
Beam waist of end mirror | 340 mm
Mechanical loss of substrate | 10-5
Mechanical loss of coating | 4×10-4
Length of silica fiber | 1 cm
Diameter of silica fiber | 10 mm

## Slide 5
Initial Experimental Setup
Seismic isolation for core optics is provided by a double pendulum
Fabry-Perot-cavity under vacuum
Front mirror: fixed mirror mounted on a Piezo actuator
End mirror: 20mg mirror suspended by a 10μm diameter silica fiber
S.Sakata, Ph.D. thesis, Ochanomizu University (2008)
End mirror
Front mirror

## Slide 6
Achieved Sensitivity
S.Sakata, GWADW (2008)
Goal sensitivity
Stabilized via PDH-scheme
Sensitivity via calibrated feedback signal
10x @100Hz
100x @1kHz
Cavity parameter:
Finesse = 1400
L = 70mm
RoC1 = 2m
RoC2 = inf

## Slide 7
Angular Anti-Spring in Suspended Cavities
Optical axis is shifted by mirror rotation (yaw/pitch)
  Torque by radiation pressure
  For high circulating power: optical torque > restoring force
  Cavity becomes instable (angular anti-spring effect)
[see e.g. J.A.Sidles, D.Sigg, Phys. Lett. A 354, 167 (2006)]
x
2) Radiation pressure torque
Center of curvature RoC1
Incident light
x
1) End mirror rotation
Center of curvature RoC1
Incident light
small end mirror (flat)
Large front mirror (curved)

## Slide 8
Cavity parameter:
Finesse = 1400
L = 70mm
R1 = 2m
R2 = inf
Measurement of Angular Anti-Spring (Yaw)
S.Sakata et al. Phys. Rev. D 81, 064023 (2010)
Optical anti-spring increases with laser power
Observed via a decrease in yaw eigenfrequency
Data was taken until near instability ( ≈190mW)
kopt: optical anti-spring constant
kΘ2: torsional spring constant

## Slide 9
How to Cope the Angular Anti-Spring
Optimize the cavity geometry:
  Change cavity g-factors
  Change RoC of the front mirror
Restriction:
  Using a flat end mirror*
  Beam radius of 340μm (coating TN)
  Reasonable cavity length ≤ 0.3m
Result:
  Going to smaller RoC1
  Critical power still < 1W
  Circulating Power in final design ≈ 500W
  Angular control is required!
* A curved 20mg mirror is advantageous, but not available so far
Change front Mirror

## Slide 10
Angular Control – Idea
Difficult to apply an external force to the small mirror directly
    Idea: Control the small end mirror via radiation pressure
  Error signal is derived via a quadrant diode (QPD)
x
x
QPD
Method:
Shift optical axis
by
angular control
of the
front mirror
Xspot
Θ2
Θ1
Positive feedback
Negative feedback

## Slide 11
Angular Control - Model
S. Sakata, internal document (2008)
T.Mori, Ph.D. thesis, The University of Tokyo (2012)
Θ2
Θ1
Incident light
xspot
Positive feedback
Negative feedback
Ti: torque, Gi: pendulum transfer function
Model for angular control to suppress xspot (for final design):
  GFB: can provide sufficient gain at low frequencies (zero/pole @ 200/500Hz)
  Need to suppress electronic noise around 1kHz (yaw to longitudinal coupling)
QPD
R1=1m

## Slide 12
Results with a Fully Suspended Cavity
Suspended front mirror
coil-magnet actuators
increase the actuation range
stable longitudinal lock (low power)
sensitivity comparable to prev. setup
T.Mori, Ph.D. thesis, The University of Tokyo (2012)
End mirror
Front mirror
Angular control via front mirror
  control circuit was installed
  stabilization of angular anti-spring
  via RP not demonstrated yet
Goal sensitivity
measured
laser freq.noise (estimated)
Cavity parameter:
Finesse = 1300
L = 80mm
R1 = 1m, R2 = inf

## Slide 13
Summary
Outlook
Goal: Observation and Reduction of QRPN
  Key element: 20mg mirror suspended by a 10μm silica fiber
Fully suspended cavity locked stable (at low power)
  Model/setup for angular control via radiation pressure
Demonstrate angular control (with preliminary setup)
  Investigate feasibility for the final design
Upgrade the vacuum system by an Ion-getter-pump
  More stable working conditions
Setting up the full interferometer
  Common noise rejection

## Slide 14
Thank you
The new lab
Arrival at ICRR, March 2012