## Slide 1: Opto-mechanics with a 50 ng membrane
Henning Kaufer, A. Sawadsky, R. Moghadas Nia,
D.Friedrich, T. Westphal, K. Yamamoto and R. Schnabel
GWADW 2012, 16.5.2012
Notes: ----- Meeting Notes (11.05.12 12:01) -----
Namen hinzufügen, z.B. bei Fus Paper
Kaze hat schonmal darüber geredet (MiSa)
GWADW ist unwichtig

## Slide 2: Radiation pressure noise
Ligo Livingston
Advanced LIGO anticipated strain sensitivty
A limiting factor for low frequencies
Often referred to as back-action noise
Next generation detectors
will observe back-action noise
Is it observeable with tabletop
experiments?
Radiation pressure noise
Shot noise
Notes: ----- Meeting Notes (11.05.12 12:01) -----
RPN regime markieren

## Slide 3: Opto-mechanics
Transfer of photon momentum
T.J. Kippenberg and K.J. Vahala, Science 321, 1172 (2008)
40 nm thickness
meff = 80 ng
Q factor = 500.000
fres = 100 kHz
R = 17 % @ 1064 nm
(refractive index + ethalon effect)
Standard approach:
Build Cavity
1.5 mm
Notes: ----- Meeting Notes (11.05.12 12:01) -----
Cole hat schon über das Bild geredet in der Session
Refl. Fresnel formel

## Slide 4: Michelson-Sagnac interferometer
SIN membrane used as common end-mirror
Recycling mirror in interferometer output
No drawback from low power reflectivity
Laser noise rejection
Notes: ----- Meeting Notes (11.05.12 12:01) -----
4.30 Minuten war ich hier. Hier sollte ich nach 1.30 Minute sein
Fringe zeigen unten links - Pfeile Michelson-und Sagnac Mode

## Slide 5: Experimental setup
Setup features
Arm length = 6 cm
0.5 “ Optics and piezos
Double seismic isolation
Operated at 10-6 mbar
Remote control for alignment
Input
Output

## Slide 6: Currently limited by thermal noise

## Slide 7: Quantum noise
Cryogenic cooling and signal recycling Rsr = 99,97 %
K. Yamamoto et al, Phys. Rev. A 81 , 033849 (2010)
Notes: ----- Meeting Notes (11.05.12 12:01) -----
Bild für hohe T drüber legen. We are here
Reflektivität SR, Signalrecycling haben wir hier

## Slide 8: Ponderomotive squeezing
Requires homodyne readout
(Read out phase quadrature)
0.3 dB @ 500 mW input power
Amplitude <-> Phase fluctuation
Membrane acts as coupling device
Calculation : H. Miao
Notes: ----- Meeting Notes (11.05.12 12:01) -----
H. Miao credit

## Slide 9: Balanced homodyne read out (no recycling)
Notes: ----- Meeting Notes (11.05.12 12:01) -----
balanced homodyne readout, no recycling
Bild von Homodyne Detector, Bild ein bisschen kleiner

## Slide 10: With recycling mirror : Induced oscillations
Cavity operated with Rsr = 99,97 %
Optical linewidth = 30 kHz
Stable and Anti-stable behavior
Induced parametric (de-) amplification of
Membrane motion
Notes: ----- Meeting Notes (11.05.12 12:01) -----
Optical spring effect with recycling

## Slide 11: Optical cooling
Spectra obtained with DC read out
Only slightly improved displacement
sensitivty
Unknown noise background
(most propably laser frequency noise)
Changed oscillator parameters,
Calculated Teff = 7 K and Qeff = 4500
With Rsr = 99 % and Pin = 100 mW
Notes: ----- Meeting Notes (11.05.12 12:01) -----
Optical cooling als Titel

## Slide 12: Thank you for your attention
Questions?

## Slide 13: Dissipative opto-mechanics
Usual idea: use cavity and detune
Supress lower sideband
Eph = hf
Require : lopt << fmech
For strong cooling
Dissipative cooling
Require system with