## Slide 1: Pulsar Timing Arrays Current and Future Instrumentation
Joseph Lazio
Jet Propulsion Laboratory, California Institute of Technology
© 2012 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Pulsar Timing Arrays Current and Future Instrumentation
What are the requirements?
  Timing precision and instrumental performance
What exists?
  Telescopes
  Feeds, receivers, and backends
  IT infrastructure
What is on the horizon?

## Slide 3: Pulsar Timing Arrays Current Results
J1713+0747
30 ns RMS
J1643-1224
1500 ns RMS
J1012+5307
280 ns RMS
Demorest et al. 2012, submitted

## Slide 4: Timing Precision
Assume sTOA ≤ 100 ns
  May be necessary, but not sufficient condition
W  pulse width
SNR  signal-to-noise ratio
Assumes sufficient calibration of telescope system
  Other contributions can include pulse-phase jitter, uncorrected propagation effects
P
W
SNR

## Slide 5: Radio Telescope

## Slide 6: Radio Telescope
Radio Frequency
Local Oscillator
Intermediate Frequency
Local Oscillator
Baseband
Data Acquisition System
Data Storage

## Slide 7: Radio Telescope
Noise Temperature
Replace entire telescope system by resistor in a heat bath
Output voltage equivalent
Not necessarily physical temperature
Tsys = Tsky + Tspill + TRx + …
P = kBTDn
T

## Slide 8: Radiometer Equation
Where can improvements be made?
Tsys portion determined by telescope
  Tsys = Tsky + Tspill + TRx + …
Dn – processed bandwidth
Aeff – effective area of telescope
Dt – observation time
  within limits imposed by pulsar or ISM
Improvements benefit both timing and survey programs
For TPSR << Tsys
S  spectral flux density [W/m2/Hz]
1 Jy = 10−26 W/m2/Hz

## Slide 9: Pulsar Observations
Observational frequency determined by balancing
pulsar spectrum vs.
sky spectrum vs.
scattering
Typically about 1 GHz
Pulsar spectrum
scattering
sky spectrum

## Slide 10: Pulsar Timing Arrays Current Instrumentation

## Slide 11: Pulsar Timing Arrays Current Instrumentation
Discovery of millisecond pulsars (MSPs)
Robert C. Byrd Green Bank Telescope (GBT) dedicated

## Slide 12: Pulsar Timing Historical Context
1974: Hulse-Taylor binary pulsar
  Arecibo telescope @ 430 MHz
  ≤ 8 MHz bandwidth
  175 K system temperature
    Tsky = 25 K @ 430 MHz
1982: first millisecond pulsar (B1937+21)
  Arecibo telescope @ 1400 MHz
  16 MHz bandwidth
  40 K system temperature
    Tsky ~ 7 K @ 1400 MHz

## Slide 13: Pulsar Timing Arrays Current Instrumentation
Typical Parameters
Aeff ~ 100 m
Dn ~ 100 MHz
Tsys ~ 30 K
Dt ~ 15 min.
Current Publications
Yardley et al. 2011, “On detection of the stochastic gravitational-wave background using the Parkes pulsar timing array,” Mon. Not. R. Astron. Soc., 414, 1777
van Haasteren et al. 2011, “Placing limits on the stochastic gravitational-wave background using European Pulsar Timing Array data,” Mon. Not. R. Astron. Soc., 414, 3117
Demorest et al. 2012, “Limits on the Stochastic Gravitational Wave Background from the North American Nanohertz Observatory for Gravitational Waves,” ApJ, in press
Hobbs et al. 2010, “The International Pulsar Timing Array project: using pulsars as a gravitational wave detector,” Class. Quant. Grav., 27, 084013

## Slide 14: Pulsar Timing Arrays Near Future
Instrumentation
Receiver performance reaching fundamental limits, e.g.,
Tsys ≈ 20 K
Dn ~ 1 GHz for observations near 1 GHz
New Pulsars
Major radio pulsar surveys worldwide
  HTRU (Parkes)
  GBNCC (GBT)
  GBT drift scan (GBT)
  P-ALFA (Arecibo)
Multi-wavelength MSPs
  a.k.a. Fermi

## Slide 15: Pulsar Surveys
New pulsars
  Add more arms to PTA, increase sensitivity; or
  For fixed amount of observing time, improve quality of PTA
Survey algorithm
  Observe position on sky
  Search resulting time series for periodic signal at period P with dispersion DM, with orbital parameters
  Loop
a “position” on the sky

## Slide 16: Pulsar Timing Arrays Near Future

## Slide 17: Pulsar Timing Arrays Digital Backends
Green Bank Ultimate Pulsar Processing Instrument (GUPPI)
BEE2 feeds 8 gaming systems w/NVIDIA GPUs
100, 200, or 800 MHz bandwidth
Large improvement in timing precision
~1 TFLOP in real time
operational

## Slide 18: Pulsar Timing Arrays Digital Backends
FPGA-based Reconfigurable Open Architecture Computing Hardware (ROACH), developed by Center for Astronomical Signal Processing and Electronics Research (CASPER, at UC Berkeley)
Wide-bandwidth (1+ GHz), real-time systems implementing RFI mitigation and folding
  (in construction)
Parkes HIPSR
Effelsberg ASTERIX and follow-on
Arecibo PUPPI
  Clone of GBT GUPPI

## Slide 19: Pulsar Timing Arrays New Feed & Rx Systems
GBT Wide-Band Pulsar System
Arecibo Wide-Band System
Effelsberg Ultra-broad Band
Arecibo AO40
Five-hundred metre Aperture Spherical Telescope (FAST) multi-feed system
  19 or 100 feed horns
Tsys ~ 29K (5K sky + 9K spill + 4K coax jct + 7K dewar jct + 3K LNA)

## Slide 20: Pulsar Timing Arrays New Feed & Rx Systems
GBT Wide-Band Pulsar System
Arecibo Wide-Band System
Effelsberg Ultra-broad Band
Arecibo AO40
Five-hundred metre Aperture Spherical Telescope (FAST) multi-feed system
  19 or 100 feed horns
Quasi Self-Complementary Feed
(developed under U.S. SKA auspices)

## Slide 21: Pulsar Timing Arrays New Feed & Rx Systems
GBT Wide-Band Pulsar System
Arecibo Wide-Band System
Effelsberg Ultra-broad Band
Arecibo AO40
Five-hundred metre Aperture Spherical Telescope (FAST) multi-feed system
  19 or 100 feed horns
continuous coverage from 600-3000 MHz
cryogenically cooled receiver
design by Weinreb (JPL/TDP) + MPIfR

## Slide 22: Pulsar Timing Arrays New Feed & Rx Systems
GBT Wide-Band Pulsar System
Arecibo Wide-Band System
Effelsberg Ultra-broad Band
Arecibo AO40
Five-hundred metre Aperture Spherical Telescope (FAST) multi-feed system
  19 or 100 feed horns

## Slide 23
Pulsar Timing Arrays
New Approaches
The European Pulsar Timing Array (EPTA):
100-m class telescopes
Ultimately forming the Large European Array for Pulsars (LEAP)
SRT, Sardinia, Italy
Effelsberg 100-m, Germany
Lovell, Jodrell Bank,
UK
NRT, Nancay, France
WSRT, Westerbork, NL

## Slide 24
Pulsar Timing Arrays
New Approaches
Large European Array for Pulsars = LEAP!
Current status:
- Hardware to record >128 MHz BW, 8 bits, baseband data in
place at all telescopes:
ASTERIX-like systems at Effelsberg and Jodrell Bank
PUMA-II at Westerbork
BON at Nançay
DFB (in APSR-mode, to be tested) at Sardinia
- 24 hr observations at L-band, once per month (in addition
to regular EPTA observations – 30 TB/site/session)
- Data currently shipped by disk, internet tested
- Successful addition of EFF-JB-WSRT,
Nançay added within days/week, SRT in Q4/2012
Almost there: 160-m dish!
Only 10-sec of data:
Notes: 30 M, 0.1-d orbit, e=0.9

## Slide 25: Pulsar Timing Arrays New Approaches
Telescope Infrastructure
Pulsar Sample
For a set of N telescopes and M pulsars, what is the optimal scheduling that maximizes the probability of detecting gravitational waves?

## Slide 26: Pulsar Timing Arrays Future Telescopes
Karl G. Jansky Very Large Array
Five-hundred metre Aperture Spherical Telescope (FAST)
Deff ~ 300 m
19 or 100-beam system
~ 500 new MSPs discovered (projected)
Aeff ~ 130 m
YUPPI backend
  Clone of GUPPI, implemented in existing correlator
Primarily a timing instrument

## Slide 27: Pulsar Timing Arrays Future Telescopes
Australian Square Kilometre Array Pathfinder (ASKAP)
Karoo Array Telescope (MeerKAT)
Aeff ~ 60 m
Phased array feed ~ 30 deg2 field of view
Primarily a search instrument
Aeff ~ 100 m
Primarily a timing instrument

## Slide 28: Square Kilometre Array
Originally: “Hydrogen telescope”
  Detect H I 21-cm emission from Milky Way-like galaxy at z ~ 1
SKA science much broader
  Multi-wavelength, multi-messenger
On-going technical development
International involvement
The Global Radio Wavelength Observatory

## Slide 29: Radio Telescopes and Astrophysical Sources
7 pc
Very Long Baseline Array (VLBA)
B0402+679
Search for additional dual SMBHs, progenitors of GW-emitting binary SMBHs
With VLBA now, SKA in the future
Relevant for future space-based GW mission

## Slide 30: Pulsar Timing Arrays Current and Future Instrumentation
What are the requirements?
  Instrumental performance improving steadily
What exists?
  Powerful set of telescopes
What is on the horizon?
  Increasing capability with new telescopes