## Slide 1: TOBA: Torsion-Bar Antenna
Masaki Ando (Kyoto University)
Small-scale TOBA at Tokyo
Small-scale TOBA at Kyoto
K. Ishidoshiro, K. Okada, W. Kokuyama, K. Yagi, K. Yamamoto,
H. Takahashi, N. Kanda, Y. Aso, N. Matsumoto, K. Tsubono, A. Takamori
SWIM on SDS-1 satellite
Ayaka Shoda (University of Tokyo)
Special thanks to the MANGO members

## Slide 2: Motivation
Low-freq. GW observation  New sciences
・Large amplitude and/or stationary GWs radiated
by sources with large masses and long time-scales.
Novel approach : TOBA (Torsion-Bar Antenna)
・Low-freq. GW obs. even with ground-based config.
・Unexplored band observation with space detector.
・Difficult with ground-based detectors because of
fundamental limitation and seismic disturbances.
・Space-borne detector requires large resources.

## Slide 3
Introduction
Prototype results
- Ground-based TOBA
- Rotating TOBA in space
Next steps
Reference:
- M.Ando, et. al, Phys. Rev. Lett. 105, 161101 (2010)
- K.Ishidoshiro, et. al, Phys. Rev. Lett. 106, 161101 (2011)
- A. Shoda, presentation at GWPAW2011
- W.Kokuyama, in preparation
(A. Shoda)

## Slide 4
TOBA Introduction
Reference: MA+, Phys. Rev. Lett. 105, 161101 (2010)

## Slide 5: TOBA
TOBA : Torsion-Bar Antenna
MA+, Phys. Rev. Lett. 105, 161101 (2010)
Monitors tidal-force fluctuation caused by GWs.

## Slide 6: Detection principle
x
y
z
Changes in tidal forces using free test masses
Conventional IFO antenna
Detect differential length change
GWs
x
y
z
Torsion-bar antenna
GWs
Detect differential rotation
Strain
Angle

## Slide 7: Comparison
Conventional IFO
TOBA
Suspended as pendulum
(Res. Freq. ~1Hz)
Torsion pendulum
(Res. freq ~1mHz)
Long baseline
 High sensitivity
Shorter length
 Simple config.
Common-mode rejection
Obs. band 10Hz-1kHz
Obs. band 10mHz-1Hz

## Slide 8: Fundamental noise level of TOBA
Laser Freq. noise < 10Hz/Hz1/2,
Freq. Noise CMRR>100
Intensity noise < 10-7/Hz1/2,
Bar residual RMS motion < 10-12 m
Bar length : 10m, Mass : 7600kg
Laser source : 1064nm, 10W
Cavity length : 1cm, Finesse : 100
Bar Q-value : 105 , Temp: 4K
Support Loss : 10-10
Practical parameters
(at 0.1 Hz)

## Slide 9: TOBA Sensitivity
Comparison with the other detectors
DECIGO/BBO band: Between ground-based detectors and LISA bands
Characteristic amplitude :
(Dimensionless strain)
SQL

## Slide 10: Observable range
GWs from binary BH mergers
Obs. Range ~10Gpc ( )
Calculation by K.Yagi : BH merger hybrid waveform, spin 0.5/0.5
ET

## Slide 11: And more…
Al bar, Length : 10m, Mass : 7.6 ton
Laser source : 1064nm, 10W
Cavity length : 1cm, Finesse : 100
Bar Q-value : 105 , Temp: 4K
Support Loss : 10-10
Si bar, Length : 25m, Mass : 90 ton
Laser source : 1550nm, 10W
Squeezing 10dB, Finesse : 100
Bar Q-value : 109 , Temp: 4K
Support Loss : 10-9
>10 times better!

## Slide 12: Schematic design
・Example of extreme design
(By Bram Slagmolen)
Si bar, Length : 10m, Mass : 11 ton
Laser source : 1550nm, 100mW
Squeezing 10dB, Finesse : 300
Bar Q-value : 109 , Temp: 4K
Support Loss : 10-9

## Slide 13: Rotating TOBA
wrot
Rotate the detector along its axis
Rotating
TOBA
Tidal force
by GW
・Two independent polarization of GW.
・Allow intermitted observation.
- Avoid low-freq. noises
Observer rotates with the detector
Noises at wrot : not important
- Up-conversion of low-freq. GWs
Low-freq. GW appears at 2 wrot

## Slide 14: Rotating TOBA
Equation of Motion of a test-mass bar
: Dynamic quadrupole moment
: Moment of Inertia
Rotation
GW with very-low freq. (wg) appears
as high freq. (2wrot) signal by up-conversion.

## Slide 15: Sensitivity by R-TOBA
Rot. Freq.
5x10-5 Hz
Bar length : 10m, Mass : 7600kg
Laser source : 1064nm, 1mW
Cavity length : 1cm, Finesse : 1
Bar Q-value : 105 , Temp: 4K
Support Loss : 10-10
Sensitivity example
(Rotation freq. 5x10-5 Hz, Laser power 1mW)
Bridge the Pulsar-timing and LISA

## Slide 16
Results from Prototypes
Reference:
- K.Ishidoshiro+, Phys. Rev. Lett. 106, 161101 (2011)
- A. Shoda, presentation at GWPAW2011
 A.Shoda’s file

## Slide 17
Rotating TOBA prototype
( SWIM on SDS-1 satellite )
Reference: W. Kokuyama, Ph.D thesis

## Slide 18: Rotating TOBA : SWIMmn
Test mass
Photo sensor
Coil
TAM: Torsion Antenna Module with free-falling test mass
(Size : 80mm cube, Weight : ~500g)
Reflective-type optical
displacement sensor
Separation to mass ~1mm
Sensitivity ~ 10-9 m/Hz1/2
6 PSs to monitor mass motion
~47g Aluminum, Surface polished
Small magnets for position control
Spin Axis
(46.5mHz)
80mm
Small Module SWIMmn on SDS-1
Photo：
JAXA
Launched Jan. 2009, Terminated Sept. 2010

## Slide 19: Sensitivity
Though limited by non-fundamental noises,
best as a space-borne GW detector.
By W.Kokuyama

## Slide 20: Observation by SWIM
Continuous data taking
Orbital Period
10mHz LPF
Jun 17, 2010 ~120 min.
July 15, 2010 ~240 min.
Tokyo
Kyoto
Orbital period
~100min.
Observation band
By W.Kokuyama

## Slide 21: Upper Limit on GWB
Upper Limit at two frequencies (two polarizations)
(C.L. 95%, f0 18mHz, BW 4mHz)
By W.Kokuyama
‘Forward’ mode
‘Reverse’ mode

## Slide 22
Next Prototype plan

## Slide 23: TOBA next plan
・Results from two small-scale TOBAs at Tokyo and Kyoto,
and rotating TOBA in space.
One more prototype step
before the 10-m scale TOBA.

## Slide 24: Concepts
・Design concepts
- Should be intermediate step for the 10-m scale TOBA.
- Scientific outcomes.
- Common techniques with KAGRA, ET, …
- Realistic both in technology and the budget.
Medium-scale TOBA for Newtonian noise observation.
- NN monitor sensor
- Take the most advantages of R&Ds
for the next generation detectors.

## Slide 25: Gravity gradient noise
・Newtonian noise by ground motion.
- Coherent plane wave with long wavelength
Same effect as km-scale interferometer
Velocity 5km/s, Frequency 0.1Hz
 wavelength ~ 50km
Plane wave
TOBA
Atmospheric NN may be larger; should be considered.
- NN estimation (by Jan Harms)
Assumption:
Infinite plane wave
Homestake mine seismic level
Newtonian Noise

## Slide 26: Medium-scale TOBA candidates
- Silicon test mass, room-temp. or cryogenic
- Laser 1550nm for two orthogonal bars.
- Readout by interferometers.
- Isolation system : KAGRA technology.
Length Diameter Mass MoI Sensitivity Max IR
10 0.3 1646 1.37x104 3x10-18 800
3 0.2 219 164 3x10-17 150
1 0.15 41 3.4 3x10-16 20
[m] [m] [kg] [kg・m2] [1/Hz1/2 @0.1Hz] [Mpc]
10 0.3 1646 1.37x104 4x10-19 3500
3 0.2 219 164 6x10-18 350
1 0.15 41 3.4 3x10-17 50
Room temp.
(300K)
Cryogenic
(4K)
※ Gravity-gradient noise : ~10-17 [1/Hz1/2] at 0.1Hz
・Sensitivity estimation (only with fundamental noises)

## Slide 27: Sensitivity estimation
Silicon bar, Q-value : 109 , Temp: 300K
Pendulum Q-value : 1010
Pendulum resonance 0.1mHz
Bar length : 3m, Mass : 219kg
Laser source : 1550nm, 10W
Cavity length : 1cm, Finesse : 100

## Slide 28: Medium-scale TOBA design
- Same direction as KAGRA, ET, …
 Effective use of resources and technologies.
Length Diameter Mass MoI Sensitivity Max IR
10 0.3 1646 1.37x104 3x10-18 800
3 0.2 219 164 3x10-17 150
1 0.15 41 3.4 3x10-16 20
[m] [m] [kg] [kg・m2] [1/Hz1/2 @0.1Hz] [Mpc]
10 0.3 1646 1.37x104 4x10-19 3500
3 0.2 219 164 6x10-18 350
1 0.15 41 3.4 3x10-17 50
Room temp.
(300K)
Cryogenic
(4K)
※ Gravity-gradient noise : ~10-17 [1/Hz1/2] at 0.1Hz
・Under discussion, but may be … Cryo. with 1-m scale
(Cryo-system, Suspension, Isolators, Materials)

## Slide 29: Medium-scale TOBA design
・Under discussion, but probably … Cryo. with 1-m scale

## Slide 30
Summary

## Slide 31: Summary (1/2)
・Novel type GW detector : TOBA
 Low-freq. observation (~10-8 – 1 Hz) .
- Observable Range >10Gpc for BH inspirals.
- Rotating TOBA for lower freq. (<1mHz) GWs.
・First prototypes
- Small-scale TOBAs at Tokyo and Kyoto
 First upper limits on GWB at 0.1-0.2Hz band.
- SWIM as a space-borne rotating TOBA
 Upper limit on GWB at 18mHz.

## Slide 32: Summary (2/2)
・Next prototype plan
- Medium-scale TOBA with length ~1m.
- Low-freq. GW detector and also a NN sensor.
- Common techniques with KAGRA, ET, …
Any suggestions are welcome!
・Another plan by Australian group
- Medium-scale TOBA at room temp.
- Please ask Bram Slagmolen!

## Slide 33
End

## Slide 34
Backups

## Slide 35: Detector response
Tidal force
by x-mode GW
Bar rotation
GWs
a : shape factor, between 0 to 1
Dumbbell or thin bar  a = 1
Dimension less,
Independent of matter density
Equation of Motion of a test-mass bar
: Dynamic quadrupole moment
: Moment of Inertia

## Slide 36: Bar shape
・Design of bar shape
- Detector response to GW
Shape factor
Thin bar or dumb-bell
along x-axis  a=1
- Standard quantum limit
Moment of Inertia
Cylindrical bar
Dumb-bell
- Bar thermal noise
When mass is kept,
Shorter is better.
- Suspension thermal noise
When mass is kept,
Longer is better.

## Slide 37: Bar material
・Selection of bar material
- Bar thermal noise
- Electro-magnetic properties
- Availability (production, cost)
Aluminum
Silicon is promising.
Sapphire
Silicon
Q-factor
Young’s
modulus
Availability
○
○
△
<107
108
109
72 GPa
335 GPa
185GPa
Density
2700 kg/m3
3970 kg/m3
2329 kg/m3
Thermal noise
8x10-20 Hz-1/2
1x10-20 Hz-1/2
5x10-21 Hz-1/2
(L=10m, f=0.3m)

## Slide 38: Interferometer configuration
・Readout from reference plate
- Readout by short FP cavities at the bar edge.
- Reference mirrors fixed to isolated base plate.
・MI fixed at bar edges
- Independent measurement
 Linear combination for GW signals.
- Require a seismic-isolated reference plate.
- Form Michelson interferometer at the bar edge.
- Direct angular measurement
- Do not need reference mirrors.
- Coupling from bar displacements.
 Room for improvements

## Slide 39: Seismic noise
・Rotational ground motion
・Coupling from displacement DoF
Coupling 10-3 or CMRR 10-3
 <10-9 isolation is required
at 0.1Hz freq. band.
Horizontal : IP (10mHz) x 5 stages
Vertical : GASF ???

## Slide 40: Bar thermal noise
・Thermal noise of bar mode
Differential readout at the edges
Contribution of odd modes
Readout
By keeping the total mass,
- High Q and low T is better
- Shorter is better
- High Young's modulus is better
8x10-20 1/Hz1/2 at 0.1Hz
Aluminum bar (7.6 ton)
length 10 m, f0.3 m
Temp. 4K, Q 107

## Slide 41: Suspension thermal noise
・Thermal noise of suspension system
- Mechanical loss in suspension fiber
Steel wire
Tungsten wire
Silica fiber
Cryogenic sus.
Superconductor sus.
- Momentum of inertia
Cryogenic suspension, Temp. 4K, g 10-10
- Torque by dissipation (one bar)
Detector response

## Slide 42: Gravity gradient noise
・Newtonian noise by point-like source.
- Assume a dumb-bell mass
and a point-like source mass
f
r
DC torque
(Ex.) Human activity
Ms=100 kg, r=10m,
f=p/2, f=0.1Hz, a= 0.1m
Equivalent noise
(Radial motion, Max. direction, a: amplitude, a, L << r)
Ms
dh ~ 2x10-12

## Slide 43: Open questions…
・Readout scheme
- Better setup to reduce couplings from the other DoF?
- Non-optical readout, such as SQUID?
・Gravity gradient noise
- What happens at an underground site?
- Propagation of seismic waves?
(Cancelation, Scattering, Diffraction)
・Other fancy ideas….
- Detector configuration.
- QND measurement.
・Seismic noise
- Design of isolation system.
- Active controls.

## Slide 44: TOBA prototype example (2)
・Space TOBA
- Silicon test mass, tune at 1mHz.
- Differential measurement using two orthogonal bars.
Length diameter mass MoI Sensitivity Max IR
10 0.3 1646 1.37x104 2x10-17 70
3 0.2 219 164 2x10-16 7
1 0.15 41 3.4 1x10-15 1
[m] [m] [kg] [kg・m2] [1/Hz1/2 @1mHz] [Gpc]
Room temp.
(300K)
※ Acceleration noise is not included.

## Slide 45: Discussions
New motivations for GW research field…
・Optical readout noise
・Low freq. seismic isolation and reduction of Newtonian noise.
・Material, bar shape, and thermal noise
・Cryogenic system
・New possibility as a space mission
・GW sources at different freq. band
- Between pulsar timing and LISA
- Between LISA and ground-based detectors
・Data analysis schemes
- Rotating TOBA configuration
- Distributed multiple detectors

## Slide 46: TOBA prototype plan
・We have two small-scale TOBAs at Tokyo and Kyoto.
- Aluminum test mass, length ~20cm, mass ~300g.
- Room temperature, poor seismic isolation.
- Magnetic levitation using superconductor bulk.
・Next plan concepts
(A) Medium-scale TOBA at room temperature.
- Silicon test mass, length ~1m, mass ~100kg.
- Differential measurement using two orthogonal bars.
- Better isolation system.
(B) Medium/small-scale TOBA at cryogenic temperature.
- Similar configuration to (A), but with a cryogenic system.
- Resonant detector configuration???
(C) Medium-scale TOBA development for a space mission.
- Low-freq. observation by a rotation configuration.
- Several options:
Resonant?, Cryogenic?, Orbit?

## Slide 47: TOBA prototype example (1)
・Medium-scale TOBA
- Realistic configuration with current technology.
- Also works as a gravity-gradient noise monitor,
or a test bench for quantum noise investigation.
- Silicon test mass,
- Differential measurement using two orthogonal bars.
- Isolation system : LCGT type-B SUS, placed at an under ground site.
Length diameter mass MoI Sensitivity Max IR
10 0.3 1646 1.37x104 3x10-18 800
3 0.2 219 164 3x10-17 150
1 0.15 41 3.4 3x10-16 20
[m] [m] [kg] [kg・m2] [1/Hz1/2 @0.1Hz] [Mpc]
10 0.3 1646 1.37x104 4x10-19 3500
3 0.2 219 164 6x10-18 350
1 0.15 41 3.4 3x10-17 50
Room temp.
(300K)
Cryogenic
(4K)
※ Gravity-gradient noise : ~10-17 [1/Hz1/2] at 0.1Hz

## Slide 48: Resonant detector
・Connect two bars by a shaft
 resonant torsion detector
Shaft
- GW signal is enhanced
at resonant frequency by Q.
- Requirements for readout and
bar-thermal noise are relaxed.
- Detector noise is mainly limited
by thermal noise of the shaft.
・Thermal noise level
f0=0.1Hz, Q=109, T=4K,
M=7600kg, L=10m
7.5x10-18 [1/Hz1/2]
At resonant freq.

## Slide 49: Fundamental noise level of TOBA
Laser Freq. noise < 10Hz/Hz1/2,
Freq. Noise CMRR>100
Intensity noise < 10-7/Hz1/2,
Bar residual RMS motion < 10-12 m
Bar length : 10m, Mass : 7600kg
Laser source : 1064nm, 10W
Cavity length : 1cm, Finesse : 100
Bar Q-value : 105 , Temp: 4K
Support Loss : 10-10
Practical parameters
(at 0.1 Hz)

## Slide 50: Optical readout noise
Nd:YAG 1064nm, Power 10W,
Short FP cavity, Finesse 100
・Optical readout noise
- Readout by short FP cavities at the bar edge.
- Reference mirrors fixed to isolated base plate.
Shot noise + Rad. Pressure noise

## Slide 51: TOBA Sensitivity
Comparison with the other detectors
DECIGO/BBO band:
Between ground-based detectors and LISA bands
Characteristic amplitude :
(Dimensionless strain)
SQL

## Slide 52: Fundamental noise level of TOBA
Laser Freq. noise < 10Hz/Hz1/2,
Freq. Noise CMRR>100
Intensity noise < 10-7/Hz1/2,
Bar residual RMS motion < 10-12 m
Bar length : 10m, Mass : 7600kg
Laser source : 1064nm, 10W
Cavity length : 1cm, Finesse : 100
Bar Q-value : 105 , Temp: 4K
Support Loss : 10-10
Practical parameters
(at 0.1 Hz)

## Slide 53: Chirp waveform
・Phenomenological waveform by numerical simulation
- For BH inspiral (no tidal deformation).
- Include chirp, merger, and ring-down.
- Include spin effect.
Inspiral
Merger
Ringdown
GW from BH merger
- 100 Msolar equal mass
- Spin parameter 0.5
- Distance 100 Mpc
(Ajith+ arXiv 0909.2867)

## Slide 54: Observable range
GWs from binary BH mergers
Obs. Range ~10Gpc ( )
Calculation by K.Yagi

## Slide 55: Background GWs
R.Saito and J.Yokoyama,
PRL 102, 161101 (2009)
Beat BBN upper limit
Observable GW
energy density ratio
GW by primordial
tensor perturbation
(1-yr obs. by 2 TOBAs)
TOBA

## Slide 56: Sensitivity by R-TOBA
Rot. Freq.
5x10-5 Hz
Bar length : 10m, Mass : 7600kg
Laser source : 1064nm, 1mW
Cavity length : 1cm, Finesse : 1
Bar Q-value : 105 , Temp: 4K
Support Loss : 10-10
Sensitivity example
Rotation freq. 5x10-5 Hz
Laser power 1mW
Bridge the Pulsar-timing and LISA bands

## Slide 57: Small-scale TOBA
・Optical readout
Mirrors at both edges of the test-mass bar
 Form Michelson interferometer
Sensitive angular sensor
Nd:YAG laser source
Wavelength 1064nm
Power 50mW
・Suspension
Magnetic levitation by pinning
effect of type-II superconductor
Superconductor bulk
f600mm, t 20mm, Tc ~92K
Low-vibration cryo-cooler
Operation temp. ~65K
・Vacuum system
Pressure 10-5 Pa by TMP+RP
Acoustic shield enclosure
・Test-mass bar
Length ~200mm, Weight 160g
Made of Aluminum
Room temperature
Gd1Ba2Cu3O6.9 : 70.9%
Gd2Ba1Cu1O7 : 19.2%

## Slide 58: Small-scale TOBA at Tokyo
Low-vibration
Pulse-tube cryo-cooler
Vacuum tank
φ600mm
Superconductor bulk
(inside a chamber)
Optical bench
Vacuum pump
(TMP + RP)
Acoustic shield
1932mm
1366mm
1498mm
University of Tokyo

## Slide 59: Small-scale TOBA at Kyoto
Cryocooler
Vacuum Tank
Laser source
and input optics
Control circuits
Michelson
interferometer
Test mass
Clean booth
Super-
conductor
Test mass
driver
February 2010 at Kyoto University

## Slide 60: Sensitivity of small TOBA
Small-scale TOBA at University of Tokyo
Sensitivity
at 0.2Hz
Limited by magnetic disturbances and seismic coupling
K.Ishidoshiro et al.,
PRL 106, 161101 (2011)

## Slide 61: GWB observation by small TOBA
・Observation run by small-scale TOBA at the University of Tokyo
One-night observation  7.5 hours’ data
Use stable 3.5 hours’ data
・Data analysis for stochastic background GW
Assume isotropic, unpolarized GWB
Divide obs. data into 120 segments
Hubble constant H0 = 70 [km/s/Mpc ]
GWB energy density ratio
 Average and distribution

## Slide 62: Upper limit on GWB
・Distribution  Averaged power at 0.2Hz
Distribution with
assuming Gaussian dist.
Probability to have
larger result than
Upper limit on
(C.L. 95%)
Conservative upper limit including
calibration error (dh/h ~ 10%)
and the other systematic errors.
Some details…

## Slide 63: Comparison with previous results
New upper limit at unexplored frequency band of 0.2Hz
10m TOBA

## Slide 64: Observation with two detectors
Tokyo
Kyoto
370km
On-line calibration (for monitoring the gain):
10 Hz signal
Monitored GPS signal: 1pps signal
Temperature: ~70K
On-line calibration (for monitoring the gain):
8.7 Hz signal
Monitored GPS signal:
1pps and serial signal
Temperature: ~40K
Kyoto
Tokyo
DATE: 0:00 – 5:00, July 20, 2010
Sampling frequency: 1kHz Direction of Test-mass bar: north-south
Original fig. by
A.Shoda
(GWPAW 2011)
Observation with two detectors places at Tokyo and Kyoto, Japan.
Comparable sensitivity, Separation : 370km
Better upper limit on GWB
Possible detection

## Slide 65: Observation with two detectors
1台の観測では, 背景重力波の検出は極めて困難.
検出器の雑音と背景重力波を区別できない.
複数台での
同時観測, 相関解析を行う.
信号と雑音を区別できる.
感度を向上できる.
程度の向上.
10mスケールのアンテナ 2台で1年間同時観測
プロトタイプ2台で 1年間同時観測
プロトタイプ2台で
5時間同時観測
Fig. By A.Shoda

## Slide 66: Sensitivities
Tokyo
Kyoto
10-2 10-1 1 10
frequency [Hz]
10-4
10-5
10-6
10-7
10-8
10-9
10-10
10-11
strain [Hz-1/2]
Fig. By A.Shoda
One-night observation runs x three times
Data analysis underway  is expected
(1/50 better upper limit than that by one detector)

## Slide 67: 結果の見通し
Fig. By A.Shoda
BBN
COBE
Doppler Tracking by Cassini
Pulsar timing
LIGO
Single TOBA
The estimate of this work
preliminary
-20 -15 -10 -5 0 5
20
15
10
5
0
-5
-10
-15
観測データ (2010年7月) 解析の暫定結果.

## Slide 68: プロトタイプ
(東京大学, 2008年-)
(京都大学, 2010年-)
(地球周回軌道, 2009年-)
ねじれ型重力波検出器A
ねじれ型重力波検出器B
ねじれ型重力波検出器C
試験マス
質量 50g, 長さ 5cm
無重力浮上 +制御
反射型フォトセンサ
スピン + 軌道運動
質量 150g, 長さ 20cm
超電導磁気浮上 +制御
レーザー干渉計
地上静置観測
質量 340g, 長さ 25cm
超電導磁気浮上 +制御
レーザー干渉計
地上静置観測
変動検出
位置・姿勢
SDS-1/SWIM
2つの地上装置, 1つの衛星搭載モジュール

## Slide 69: Rotating TOBA
Very low-freq. GW signal (~10-8 – 10-4 Hz) is
up-converted to 2 x (Rotation freq.)
Rotate the detector along its axis

## Slide 70: Fundamental noise level of TOBA
Laser Freq. noise < 10Hz/Hz1/2,
Freq. Noise CMRR>100
Intensity noise < 10-7/Hz1/2,
Bar residual RMS motion < 10-12 m
Bar length : 10m, Mass : 7600kg
Laser source : 1064nm, 10W
Cavity length : 1cm, Finesse : 100
Bar Q-value : 105 , Temp: 4K
Support Loss : 10-10
Practical parameters
(at 0.1 Hz)

## Slide 71: TOBA Sensitivity
Comparison with the other detectors
DECIGO/BBO band:
Between ground-based detectors and LISA bands
Characteristic amplitude :
(Dimensionless strain)
SQL

## Slide 72: Optical readout noise
Nd:YAG 1064nm, Power 10W,
Short FP cavity, Finesse 100
・Optical readout noise
- Readout by short FP cavities at the bar edge.
- Reference mirrors fixed to isolated base plate.
Shot noise + Rad. Pressure noise

## Slide 73: Bar thermal noise
・Thermal noise of bar mode
Differential readout at the edges
Contribution of odd modes
Readout
By keeping the total mass,
- High Q and low T is better
- Shorter is better
- High Young's modulus is better
8x10-20 1/Hz1/2 at 0.1Hz
Aluminum bar (7.6 ton)
length 10 m, f0.3 m
Temp. 4K, Q 107

## Slide 74: Chirp waveform
・Phenomenological waveform by numerical simulation
- For BH inspiral (no tidal deformation).
- Include chirp, merger, and ring-down.
- Include spin effect.
Inspiral
Merger
Ringdown
GW from BH merger
- 100 Msolar equal mass
- Spin parameter 0.5
- Distance 100 Mpc
(Ajith+ arXiv 0909.2867)

## Slide 75: TOBA Sensitivity
Rot. Freq.
5x10-5 Hz
Bar length : 10m, Mass : 7600kg
Laser source : 1064nm
Bar Q-value : 105 , Temp: 4K
Support Loss : 10-10
Sensitivity example
10W, F 100
0.3W
1mW

## Slide 76: Topic
Homodyne detection
V.B.Braginsky, Ya.B.Zel’dovich, and V.N.Rudenko
Sov. Phys.- JETP Lett. 10 (1969) 280.
Being introduced in:
C.W.Misner, K.S.Thorne, J.A.Wheeler,
‘Gravitation’ W.H.Freedman (1973) pp.1016.
Ideas of :
Bar rotation by tidal acceleration by GW
Detection of Circularly polarized GWs
Heterodyne detection method
Observation with torsion antenna :
Cryogenic torsion antenna to observe
continuous GWs from Grab pulsar
S.Owa, et al.,
‘Cryogenic Detector for Gravitational
Radiation from the Crab Pulsar’
Proceedings of the fourth Mercel Grossmann
Meeting on General Relativity (1986).

## Slide 77: SDS-1衛星での実証
JAXA開発による100kg級の技術実証衛星
SDS-1 (Small Demonstration Satellite - 1)
Size : 70x70x60cm,Weight : 100kg
Power : >100W, Downlink : ~5kbps
Orbit : SSO (~660km)
Spin stabilization and 3-axis attitude control
Mission Lifetime : ~Half year (nominal)
http://www.iat.jaxa.jp/info/prm/2007/019/01.html
SDS-1 and GOSAT
(Press Release, November 4, 2008)
Photo from Mainich Newspaper Web

## Slide 78: SDS-1/SWIM
SDS-1/SWIM
2005年 検討・開発開始.
2009年 1月23日打上げ.
2011年 9月 運用停止.
全ての機器で
full success以上を達成.
写真：JAXA
CPU: HR5000
(64bit, 33MHz)
System Memory:
2MB Flash Memory
4MB Burst SRAM
4MB Asynch. SRAM
Data Recorder:
1GB SDRAM
1GB Flash Memory
SpW: 3ch
SpaceCube2: Space-qualified Computer
SWIMmn : User Module
Processor test board
GW+Acc. sensor
FPGA board
DAC 16bit x 8 ch
ADC 16bit x 4 ch
 32 ch by MPX
Torsion Antenna x2
~47g test mass
Size: 71 x 221 x 171
Weight: 1.9 kg
Power: 7W
Data Rate : 380kbps
Size: 124 x 224 x 174
Weight: 3.5 kg
Power: ~7W
Photo by JAXA
Photo by JAXA

## Slide 79: SWIMmn GW sensor
Tiny GW sensor : Test-mass length ~ 50mm
Launch in Jan. 2009, Decommission in Sept. 2010
Successful operation and data-taking
Test mass
Photo sensor
Coil
TAM: Torsion Antenna Module with free-falling test mass
(Size : 80mm cube, Weight : ~500g)
Reflective-type optical
displacement sensor
Separation to mass ~1mm
Sensitivity ~ 10-9 m/Hz1/2
6 PSs to monitor mass motion
~47g Aluminum, Surface polished
Small magnets for position control
Used for test-mass
position control
Max current ~100mA
2 TAMs
in the frame
SWIMmn Module

## Slide 80: SWIMmn 軌道上実証
SWIM
In-orbit operation
z control on
yaw control on
Operation: May 12, 2009
Downlink: ~ a week
Test mass controlled
Damped oscillation
(in pitch DoF)
Error signal  zero
Signal injection
 OL trans. Fn.
Free oscillation
in x and y DoF
By
W.Kokuyama

## Slide 81: Sensitivity
Observation by SWIM and ground-based detectors
1st run June 17 2010, 2nd run July15 2010

## Slide 82: Dynamic Quadrupole moment
Dynamic quadrupole moment
In case of bar rotation…
: Mode pattern function