## Slide 1: Advanced LIGO Seismic Isolation Status
LVC Meeting Rome 2012
Céline Ramet, for the Seismic Isolation team
September 11th, 2012
G1200910-v4

## Slide 2: Overview
Different aLIGO Seismic Isolation Systems
Assembly & Installation Status
  LIGO Livingston (LLO), LIGO Hanford (LHO), LIGO India (Assembly only)
Commissioning Status
  BSC-ISI & BSC-HEPI (LHO), HAM-ISI (LLO), HAM-HEPI (LASTI)

## Slide 3: Different aligo SEIsmic isolation SySTEMs

## Slide 4: Different aLIGO Seismic Isolation Systems
From the ground to the optical table
Passive isolation (mass-spring) systems with active control (in contrast to iLIGO)
Sensing loops made of blended inertial and capacitive/inductive position sensors (super sensors)
Goal : Isolating optics + provide positioning & alignment
1 Pre-Isolator (present under all chambers)
  HEPI
Two in-vacuum Seismic Isolation systems (ISI)
  HAM-ISI
  BSC-ISI

## Slide 5: LIGO Livingston (LLO)
6 HAM Chambers:
6 HEPI, 5 ISI
5 BSC Chambers:
5 HEPI, 5 ISI
LLO Layout
Courtesy: F. Matichard

## Slide 6: HEPI
One stage of isolation
Isolation from 0.1 Hz to ~ 10 Hz
Out of vacuum
16 sensors
Divided in 4 piers, connected by the support tubes
Hydraulic actuation

## Slide 7: HEPI
HAM-HEPI
BSC-HEPI

## Slide 8: HAM-ISI
One stage of isolation
Effective > ~ 0.2 Hz
In Vacuum
12 sensors
2 per IFO have additional sensors on Stage 0 for feed-forward
Optical table facing up
Carrying Auxiliary Optics
Stage 1
Stage 0

## Slide 9: HAM-ISI

## Slide 10: BSC-ISI
Two stages of isolation
Effective > 0.2 Hz
In vacuum
33 sensors
Optical table facing down
Carrying Core Optics
Stage 2
Stage 0
Stage 1

## Slide 11: BSC-ISI

## Slide 12: Assembly & Installation status
LIGO Livingston (Louisiana, USA), LIGO Hanford (Washington St, USA), LIGO India

## Slide 13: LLO + LHO + India Status
  ISI
  HEPI
  BSC
Assembled: 5/5
  5/5
  3/5
Installed: 5/5
  3/5
Controlled: 4/5
  0/5
Assembled: 6/6
  6/6
  6/6
Installed: 6/6
  5/6
Controlled: 0/6
  0/6
Assembled: 3/5
  3/5
  0/5
Installed: 1/5
  2/5
Controlled: 0/5
  2/5
Assembled: 5/5
  5/5
  5/5
Installed: 5/5
  2/5
Controlled: 0/5
  2/5
  HAM

## Slide 14: LIGO Livingston (LLO)
LLO Layout
represent ISI+HEPI assembly & installation complete

## Slide 15: LIGO Hanford (LHO)
LHO Layout
represent ISI+HEPI assembly & installation complete

## Slide 16: Commissioning
LIGO Livingston, LIGO Hanford, LASTI (Cambridge, Massachusetts, USA)

## Slide 17: HAM-HEPI Commissioning (LASTI)
Courtesy: R. Mittleman
(cavity axis)

## Slide 18: Tracking HAM-ISI Evolution (LLO) L1-HAM 3 Story

## Slide 19: Tracking HAM-ISI Evolution (LLO) L1-HAM 3 Story

## Slide 20: HAM-ISI Commissioning (LLO)
Courtesy: R. De Rosa

## Slide 21: IMC Commissioning (LLO)
Courtesy: R. De Rosa
Input Mode Cleaner

## Slide 22: BSC-ISI+HEPI Commissioning (LHO) Stage 1
Courtesy: V. Lhuillier

## Slide 23: BSC-ISI+HEPI Commissioning (LHO) Stage 2
Courtesy: V. Lhuillier

## Slide 24: Single Arm Commissioning (LHO) Cavity length control signal
Courtesy: V. Lhuillier

## Slide 25: Conclusion
Currently 63% of aLIGO SEI in vacuum components and 100 % of pre-isolators are built
  1/3 of all components will not be installed until India is ready.
Several of each different system (HAM-ISI, BSC-ISI, HAM-HEPI, BSC-HEPI) are installed and under control at either LHO, LLO or LASTI.
About to approve chambers to go through OPS control
Still learning!!!... But closing in on aLIGO requirements

## Slide 26: Thanks / Grazie
All Seismic team at LLO, LHO, LASTI, Stanford, Caltech
Fabrice Matichard, Vincent Lhuillier, Richard Mittleman, Hugh Radkins, Ryan DeRosa
LLO team:
Y’all

## Slide 27: Questions ?

## Slide 28: Extra Slides

## Slide 29: LIGO Hanford (LHO)
H2 HAM Chambers
H2 BSC Chambers
Auxiliary Optics:
10 + 2 Chambers
Core Optics:
10 Chambers
H1 HAM Chambers
H1 BSC Chambers
LHO Layout
Courtesy: F. Matichard

## Slide 30: Tracking HAM-ISI Evolution (LLO) L1-HAM 3 Story

## Slide 31: HAM-ISI Commissioning (LLO)
HAM-ISIs without pre-isolation (HEPI not running yet)
  Starts right after testing after install is approved
Damping (only with seismometer signals)
Blend filters
Isolation
  Level 1 (identical to all chambers and sites)
  Level 2 (minor adjustments for actual resonances)

## Slide 32: HAM-HEPI Commissioning (LASTI)
HEPI limitation?… Non linearity of low amplitude drives
Courtesy: R. Mittleman