## Slide 1: aLIGO QUAD "Level 2" Damping Loop Design (Supplemental to LLO aLOG 6949)
J. Kissel

## Slide 2
aLIGO QUAD "Level 2" Damping Loop Design
Mission Statement
The damping loops installed during the SUS testing phase
merely to prove that the suspensions could be damped
damped quickly and robustly
little-to-no regard to re-injection of sensor noise
very aggressive, but poorly placed elliptic filters to rolloff noise
The mission here was to design a set of loops, that
doesn’t take you years to design and tweak
isn’t on the hairy edge of instability
doesn’t require any “Brett Shapiro” trickery (damping in Modal, Global bases)
doesn’t require and new infrastructure (which Modal and Global damping would),
but still
designed with what modeling experience we’ve gained
gets us close to what we’ll need for aLIGO, primarily focusing on Longitudinal
will be sufficient for the first several stages of integrated testing
Level 1
Level 2

## Slide 3
Stability: Bode plots of Open and Closed Loop Gain Transfer Functions
Cross-Coupling: The above, Modeled both as SISO and MIMO systems, the below as MIMO
Modeled Performance: Compute all DOF’s of Top Mass sensor noise contribution to Test Mass degree of freedom of interest
Compare: with other noise sources, requirements, etc.
Measured Performance: With what we can: Closed Loop TOP2TOP Open and Closed Loop TFs, TOP Sensor ASDs, TOP Control Signal ASDs
Damping Loop Design Model Figures of Merit

## Slide 4: Damping Loop Design Stability (New Filters)
Open Loop Gain TF:
SISO Model = PL * KL
MIMO Model = Full
State Space System
Close Loop Gain:
SISO Model = PL / (1 - GL)
MIMO Model = Full State
Space System
Suppression:
SISO Model = 1 / (1 - GL)
Plant:
SISO Model = PL
Controller:
SISO Model = KL
Unconditionally Stable
Elliptic first, then rolloff
Boost on low-frequency modes to reduce RMS
Not-so-high-Q Elliptic Filter
Not just velocity damping anymore:
[z:p]=[~1:~10] Hz pair for more phase with which to play

## Slide 5: Damping Loop Design All DOF’s TOP Sensor Noise Contribution (New Filters)
Sensor noise contributions to L Test Mass Motion @ 10Hz [m/rtHz]:
L2L = 2.0e-19
R2L = 1.1e-19
P2L = 8.7e-20
T2L = 5.0e-20
L Reqs = 1e-20
When you start carving out the L contribution to L Test Mass Motion, P, R, and T’s contribution are there waiting for you too!
T and R loops are harder to design, because their last resonances are higher in frequency, so can’t be as aggressive with noise roll-off
4th “L” resonsance is a mess of L, T, R, and P

## Slide 6: Damping Loop Design Compare with other Noises (New Filters)
Longitudinal BOSEM Sensor Noise still dominates between 1-30 Hz
PUM Actuator Noise finally takes over at 30 Hz
Residual Seismic Noise
Dominates below 1 Hz
But…
Now only a factor of 5-10 away from residual seismic, instead of 500-1000

## Slide 7: Damping Loop Design Compare with Cavity Displacement (New Filters)
Vertical DOF is also dominated by sensor noise at 10 Hz, and could play a role assuming the 0.001 [m/m] coupling over the 4km arms

## Slide 8: TOP Mass ON/OFF Spectra (New Filters)
Lowest L/P Modes gave us grief in the H2OAT
10-5 [rad]
Longitudinal
Pitch
BUT, ISI is only damped in this measurement, so we’ll probably be fine (as we were once the l.f. performance of the ISIs were tuned)
0.43 Hz
0.56 Hz
0.43 Hz
0.56 Hz

## Slide 9: Level 1 vs.Level 2
Old Sensor Noise takes over at ~0.5 Hz
New Sensor Noise takes over at ~1.0 Hz
Old 0.43 Hz mode from Res. Seis. is squashed entirely
New 0.43 Hz mode from Res. Seis. has a Q of ~10-50, but still not dominating the RMS
Old Sensor Noise is 1.3e-17 [m/rtHz]@ 10Hz
New Sensor Noise is 2.0e-19 [m/rtHz]@ 10Hz
New Sensor Noise is a factor of ~5 better than Old Sensor Noise in between resonces

## Slide 10: Level 1 vs.Level 2
Old 0.43 Hz mode from Res. Seis. is squashed entirely
New 0.43 Hz mode from Res. Seis. has a Q of ~10-50, but still not dominating the RMS
Old Sensor Noise takes over at ~0.5 Hz
New Sensor Noise takes over at ~1.0 Hz
New Sensor Noise is a factor of ~5 better than Old Sensor Noise in between resonces

## Slide 11: Level 1 vs.Level 2
TOP to TOP Mass Transfer Function
New Filters
Old Filters
No Damping
Model
Qs of resonances increased only by a factor of ~10

## Slide 12: Level 1 vs.Level 2
Can’t measure Test Mass noise improvement directly yet…
If sensor noise dominates above 1 Hz both before and after, then TOP control signal should be ~100 times less at 10 Hz.
And it is!

## Slide 13: Remaining Questions
Is it worth keeping Level 1 around?
  (As I installed it at L1 ITMs, I removed Level 1)
Tradition to have the overall gain “tunable” as an EPICs variable. Should it be absorbed in the filter banks?
Would like to look into
  Stability of loops if gains are increased to improve ring-down-time (more tradition)
  Should build infrastructure / standard plot for quantifying ring down

## Slide 14: Bonus Material For the Curious
Remember, for even more text, plots, details see LLO aLOG 6949

## Slide 15: Damping Loop Design OLD Filters

## Slide 16: Damping Loop Design NEW Filters

## Slide 17: Seismic Input Motion
In the absence of real, best-possible performance data from the BSC-ISIs, there are a few choices for Residual Ground Input Motion to the QUAD:
- Use the Requirements for all DOFs
- Use M. Evans’ Model of the “Translation” (same for X, Y, Z) and “Rotational” (same RX, RY, RZ)
- Use not-yet-awesome, but real H2OAT data (different for every DOF, and even between ISIs)
We know every degree of freedom will be different, so I don’t like using the Reqs.
We know the very low frequency data of the H2OAT data is all tilt (if not sensor noise), and we know the mid-frequency band will be better
So I went with Matt’s Model since it seems to fold in the most (optimistic?) realism

## Slide 18: Damping Loop Design All DOF’s TOP Sensor Noise Contribution (Old Filters)
Sensor noise contributions to L Test Mass Motion @ 10Hz [m/rtHz]:
L2L = 1.3e-17
P2L = 3.1e-18
R2L = 2.8e-19
Reqs = 1e-20

## Slide 19: Damping Loop Design Compare with other Noises (Old Filters)

## Slide 20: Damping Loop Design Compare with Cavity Displacement (Old Filters)

## Slide 21: Measured Open Loop Gain TF (New Filters)

## Slide 22: Damping Loop Design Proof that MIMO Matters!!
SISO Model
MIMO Model

## Slide 23: QUAD Performance Modeling All the bits and pieces
Test Mass
Displacement
Top Mass
Sensor Noise
Actuator Noise
Damping Loop
Design
Suspension Point
Residual Seismic Noise
UI Mass
Actuator Noise
PU Mass
Actuator Noise
Steps to computing test mass motion:
Measure / compute every DOF of input noise at every stage
Propogate each stage input DOF to single test mass DOF of interest for cavity (i.e. longitudinal) using SUS model
Add each stage’s input DOF contribution in quadrature