LIGO Laboratory / LIGO Scientific Collaboration

LIGO-T1300639-v2	LIGO	07-19-2013

TMS Primary Mirror Installation Procedure

Ken Mailand

Distribution of this document:

LIGO Scientific Collaboration

This is an internal working note

of the LIGO Laboratory.

| California Institute of Technology LIGO Project | Massachusetts Institute of Technology LIGO Project |
| --- | --- |
| LIGO Hanford Observatory | LIGO Livingston Observatory |

http://www.ligo.caltech.edu/

1

Introduction

Instruction for Mounting the TMS Primary Mirror in the D1102361 Telescope Frame Mirror Nest.

2. TMS Primary Mirror Installation and Hold Down Clamping Procedure ref. Assembly D1102361 This procedure is also the same for the First Article WBSC6-Y

3. aLIGO TMS Primary Mirror Nest and Clamp (3)

1) Mount the Primary Mirror in The Three Standoff Nest (D1102361), and rotate to align the center line scribe with the scribe line in the back plate.

Nest is formed by parts D1002731(item # 15), D1002728 (item # 6) as shown.

2) Add part D1002732 (item # 8) (the common top clamp) with 1/4-20 SHCS (item # 10) and Belleville washer stack in series ( item # 8) as shown.

3) The mirror should be in full back surface contact with the telescope back plate. Turn the set screw in the part D1002731(item # 15) until there is no free play in the nest, do not over tighten, just be sure there is three point contact with the mirror and nest standoffs, with simultaneous back face contact with back plate.

Belleville Spring Data

A Series Stack of 8, .225" ID x .50" OD x .018" thick Stainless Steel

The spring above has a working load of 45 lbs. @ .008"  Deflection.

Ref. McMaster Carr part # 9713K61

Belleville Spring Tightening Procedure Data

Note. Linear load / deflection

The Primary Mirror Mass = 13.5 lbs

Max Working Load, 45 lbs @.008" deflection

13.5 lbs @ .0024" deflection

8 Series Springs = @ 13.5 lb Load = 8 x .0024" = .0192" ~.02"

Screw ( Clamp) ( item # 8)  1/4-20 (twenty turns per inch)

One turn (360 deg.) = .05" Travel

.02" (above deflection @ 13.5 lb)  divided by .05" (360 deg.) = .4

360 deg. times .4 =  144 deg. rotation of screw after all slack and free play is taken up in Clamp assembly.

Ref.

A pie chart tool can be used as a turn angle gage, for this operation.

Ref. Below:

Deflection, Series Stacking, Load