## Slide 1: Hierarchical Control (“Classical” Approach)
J. Kissel, for the Hiers

## Slide 2: Problem Statement
Reduce input spectrum to 1 [nm] RMS using hierarchical feedback to middle two stages of ETMs,
without saturating the DAC
Expected Bandwidth around 10-20 [Hz]
ALS DARM Signal: Differential frequency beat note between two arms as measured by green
1e-9 [m]

## Slide 3: The Toy Model
DARM -- > Treat motion of one test mass
QUAD -- > Double pendulum, parameters roughly of PUM and TST Mass (assuming local damping ON)
UIM & PUM -- > Equal Masses, No Stage Below
Same Actuators with Same Actuator Limits
Same Input Amplitude Spectral Density
Same output scheme (digital compensation of analog electronics, transformation to actuator basis for DAC)
m1 = 40;
m2 = 40;
g = 9.81;
L1 = 0.3;
L2 = 0.6;
k1 = m1*g/L1;
k2 = m2*g/L2;
g1 = 30;
g2 = 30;

## Slide 4: The Prescription The Distributed Hierarchy
Create plant inversion filters (so we can use complementary hierarchy filters)
Design hierarchy filters, check cross-over stability
Design global control filter, check loop gain stability
Compute closed loop performance and RMS, check to meet requirement (1)
Compute control force at DAC, check probability of saturations, RMS, etc. meet requirements (2)
Iterate on Global Control and Hierarchy authority until you get something that meets requirements
Try it on the real thing, see if it works, and tweak if necessary

## Slide 5: Create Plant Inversion Filters
Rely on the fact that you’re blending above the suspension resonance forest -- > Simple Roll-off to the right high-frequency response
“Turn off” compensation at high frequency, so as to not have infinite gain at high-frequency

## Slide 6: Design Hierarchy Filters
Simple Design:
Start with low-pass:
Put corner frequency where you expect upper-stage maximum range to dominate over lower stage. Try a complex pair of poles with a bit of Q … just to make it sassy.
Create high-pass as
HP = (1 – LP).

## Slide 7: Check Cross-over Stability

## Slide 8: Design Global Control, Check Stability
Design Inputs:
Knowledge of input spectral density and where you need gain.
Guess at unity gain frequency.
Compensate for Plant shape for a stable cross-over.
Cut-off high-frequency “quickly” to reduce noise.
Try to minimize gain peaking.
Shoot for 30-45 ish degree of phase margin.
Check for actuator saturation.

## Slide 9: Compute Closed Loop Performance

## Slide 10: Compute Control Forces at DAC
Ask Brett:
What’s the right metric for DAC saturations:
RMS?
Control Force Spectrum?
Probability of Saturation in one time step?
Probability of Saturation over long time?
Probability of Saturating in One Time Step:
M1: 0.0038599
M2: 2.027e-29
Probability of Saturating in One Hour:
M1: 0.0008494
M2: 0

## Slide 11: The Classical Approach
Got it done in 3 days (using 8 years of expert controls knowledge, and intimate knowledge of parameters, having already tried 3 times before, and having a lot of software infrastructure in place)
Lots of steps (though “straight forward” and the math is child’s play)
Needs lots of a priori knowledge, but may inform cost functions
Lots of possible solutions that’ll all get the job done “good enough” to get started