## Slide 1: Control State Definition
March 25, 2014
Daniel Sigg, Chris Wipf, Stefan Ballmer

## Slide 2: Save/Restore
Relying on save/restore yields inconsistent results
  Problem 1: “Everyone needs to keep up the snap file”
  Problem 2: What to restore to? Restore to a “good configuration” is a recipe for disaster
  Problem 3: Restore sometimes skips channels
  Problem 4: Anyone can make a change without save/restore
  Problem 5: No good way to tell how actual differs from snap
  Problem 6: No easy way to make an incremental change
  Problem 7: It scales badly
  Problem 8: No easy way to keep subsystems in sync (EX vs. EY)
  Problem 9: No good way to keep multiple configurations for the same system (e.g. LSC for PRX vs. PRY vs. PRMI, or ASC for PRMI vs. FL)
Relies on everyone doing the right thing all the time
Broken work flow!

## Slide 3: Filter files
This is a work flow which functions well
  Reason 1: All changes are going through a configuration file
  Reason 2: This is the only way to make a change
  Reason 3: There is a GUI to make the changes
  Reason 4: Changes are done incrementally
  Reason 5: You always know what’s running
  Reason 6: We have a record of old filter files
The only way to fix a problem is to actually fix it

## Slide 4: “New” Approach to Save/Restore
Divide slow controls channels into 4 groups
  Readbacks (ignore for now)
  Most of our controls never change
  Some change states in a trivial matter E.g., boost on when lock bit is set, input matrix for PRX, PRY etc.
  Some need to change all the time
Control State Definition is meant for 2 & 3 (some)
  Group 4 requires code, i.e., guardian
CSDef tries to mimic the work flow for filter files

## Slide 5: Scaling is Important
Slow channels:
  ~300,000 slow channels per ifo
  ~100,000 can be set
  ~20,000 do change
  Maybe 10,000 left once you have lookup tables
Good bookkeeping matters!
Configuration needs to be duplicated between identical sub-systems
GUI tool is vitally important to get operators involved
Commissioning team cannot handle ~100,000 variables

## Slide 6: Control State Definition
Configuration file:
  All slow controls channels must be listed
    Even, if they are under outside control
    All unlisted channels are held at zero constant
  Most channels will be set to a constant value (as opposite to manual)
  Includes safe and default values
  Includes lookup tables
    Most lookup table will have 2 states: “Off” and “Init”
  Replacement rules for channel names
  Conditions and Includes for site/location specific configurations
XML GUI editors are available (schema available)
Validating parser exists (C++ code)

## Slide 7: Control State Definition (2)
State machine
  Usual: Init, PreOp, SafeOp and Op modes
  Will set all values to safe in SafeOp
  Will set all values to their default when switching to Op
  Will set values to their configuration when in Op
  Loads a new configuration file upon request
  Implemented as a guardian script or as part of the EPICS ioc
Will initialize all values upon a restart
Checks constantly while in Op mode
A value cannot be changed, if it is set constant
All changes need to go through configuration file
  Of course, many channels will just be set to manual mode
  SM watches configuration file and indicates, if it has changed

## Slide 8: How to support commissioning
Changing the configuration file is as easy as changing a filter
Lookup tables have an “Off” state
  Section a large front-end model into different domains
  Allows to “talk” in states rather than values, e.g., run/acquisition
  Allows to gang filter banks
  Allows for fine grade control
The state machine can be set into PreOp (no writes)
Less time wasted to find out “has this changed?”
Broader user base for keeping up the configuration

## Slide 9: Why not…
Hardcode it all in the front-end
  ECR to change values? Front-end models become very cluttered
Write an incredibly large guardian script
  How can you tell what’s going on w/o reverse engineering the code?
  How can you tell that you didn’t forget a channel?
Use hash values in the front end
  How do you tell what’s wrong?
Use the EPICS access controls
  This is not a security issue!
Resurrect the iLIGO Stat system
  Creates too many secondary channels, CALC records too limited
Just stay with safe/restore and snap files
  Proven to be problematic

## Slide 10: Next on the list
Alarm and error handling
  Problem 1: Alarms are global, should be reserved for real problems
  Problem 2: No clear text messages, why does the IMC not lock?
  Problem 3: Serious problems go unnoticed
  Problem 4: Rediscovering the same issues again and again is a major source of wasted time
Solution with better track record:
  Condition code pioneered for the squeezer/OAT auto-lockers
  Hierarchical error structures (error bit, multi-bit code and msg)
  Each guardian/auto-locker/etc. has a set of conditions which need to be fulfilled to proceed (can be bypassed)
  Clear text messages of what’s wrong
  Required additional sensors in OAT!