## Slide 1
Nathan Z. Zhao
Mentors: Dick Gustafson & Daniel Sigg
Ligo SURF: Enhancement of SHG for Squeezing in aLIGO
Notes: Start: Hello,

## Slide 2: LIGO’s Squeezer
Dominant quantum noise = shot and radiation pressure
Q&M predicts that even in absence of light, the electromagnetic field fluctuates in phase and amplitude, “vacuum fluctuations”
  source of shot noise in LIGO
BUT, the product of quadrature (operators on E-field in phase and A) deviations in phase and amplitude restricted to some minimum value
Squeezing reduces deviations in one quadrature at the cost of increasing it in the other
Poisson Statistics
Notes: Shot noise related to discreteness of light at the quantum level,
Random fluctuations in detection in a photodetector, for example
Radiation pressure noise: uncertainty introduced in position of test mass by pressure fluctuations from the beam itself (greater at high power)
Poisson distribution  normal distribution for large values of the mean (normal distribution becomes a good approximation); poisson models average number of events
“throw some garbage of one into the other”

## Slide 3: Squeezer in LIGO
Improved sensitivity of the interferometer at the shot noise dominated bandwidth (~100 Hz)
  LIGO fundamentally measures changes in relative phase of two beams in light traveling down the two arms of the port
Alternative to boosting beam power to minimize shot noise
Notes: Thermal deformations of the test mass become larger at higher optical powers
Squeezed light is NOT injected into vacuum…but the squeezed vacuum states are.

## Slide 4: Second Harmonic Generation
1) SHG is a nonlinear optical effect arising in dielectrics with a nonlinear susceptibility term proportional to the square of an (applied) electric field
A resonant cavity enhances SHG; higher achievable optical intensities (unconverted beam remains in cavity for more passes)
2) Only in non-centrosymetric crystals
(variant under r -> -r transformation)
3) SHG crystal = Periodically poled KTP
Notes: Time independent term
SHG
Periodic Poling: periodic reversal of orientation in domains in crystal…likely at the coherence length of SHG interaction: achieves quasi phase matching.

## Slide 5: Optical Set-up
Notes: Talk about changes to setup
Cavity Labels
Four Main components: Faraday Isolation and Attenuation, observation, Servo, and Cavity

## Slide 7
Installation
Improvements
Thermistor Wire Slats
Piezo wire Slot
Enlarged Thermistor Ports

## Slide 8
Old SHG (aka SHG 1.0)
Precision Horizontal Translation Set-up for the Mirror Mounts
New SHG (v. 2.0)
1-inch spaced 8-32 tapped holes

## Slide 9: All New Design Changes Documented in SolidWorks2013
Notes: Add picture of real SHG

## Slide 10: Alignment Improvement: Beam Marker

## Slide 11: Inside the Cavity
O-Rings
Piezo-Actuator
Meniscus Mirror
Threaded Brass Rings
Copper Blocks

## Slide 12: SHG 2.0: Cavity Resonated in 3 Days!
Resonances from SHG 1.0;
Not as clean

## Slide 13: Cavity Stabilization
Pound-Drever-Hall servo stabilizes the cavity to peak transmission of 00 resonance.
Gets an indirect measurement of the difference between the resonant frequency versus laser frequency by using the reflectivity of the cavity (mirrors)
Reflection coefficient of the cavity is dependent on this difference:
Derivative with respect to frequency gives an antisymmetric
function about the resonant frequency
  Contains information as to whether the cavity should be shortened or lengthened
  AND the servo is invariant to intensity noise
Chart: Cavity Scan
Mode Mismatch ~ 10%
Control Diagram
Notes: Older servos relied purely on F, but signal had same sign on either side of resonance…had to put in an offset, but his forced the servo to be dependent on the intensity
F(w) = E_ref/E_inc
The phase of the reflected beam actually has a similar antisymmetry characteristic to the derivative of the reflection coefficient…this is what’s actually used.
Mode matching requisite for good conversion efficiency

## Slide 14: Frequency Response (Open Loop)
Data for PDH Frequency Response | 
Unity Gain Frequency | ~170 Hz
PZT Resonance | ~10 kHz
Phase Margin | ~270 degrees
Gain Margin | N/A (can’t tell where -180 degrees really is)
Low frequency gain | 18-20 dB
Notes: Basically looks like a low pass filter with PZT resonances ‘disrupting the response’ at 10 kHz and beyond. Only problem is that the phase behavior does not look like a low pass behavior…normally phase is roughly 0 at low frequencies
Bode stability Criterion: If there is less than 0 dB gain at phase crossover frequency

## Slide 15: Cavity without Lock
Chart: Behavior of SHG 2.0 with No Feedback
Can this be improved structurally? Not much
Falls out of resonance largely due to frequency instability of laser
Amplitude (Volts)
But you can improve noisiness of cavity’s output

## Slide 16
Chart: Comparison of Error Signal and Infrared Beam Lock
Cavity Lock loss generally corresponds with divergence of the control signal
Note how the control Signal Drifts in Time
Chart: Time (1 unit = 5 seconds)
Infrared beam
Control Signal
IR Transmission
Control Signal
Notes: Control Signal Diverges due to limited range of the piezo…as the cavity might drift out of range of the piezo…the control signal gets larger with less and less effect until the cavity loses the lock…but this is a very slow effect, even for a limited range.

## Slide 17
Chart: Cavity Stability with Error Signal Shown
The Integral Control (which in the PDH is assumed by the pre-amp) creates a control signal of the form:
Integrating over time means the integral term will grow with time so long as the error signal is nonzero. Even once the error signal zeroes out, the control signal will remain nonzero, but stable.
‘hiccups’ could be the laser itself shifting in frequency
Notes: Small offset…likely not a real steady state error
Not a real integral controller…just a pre-amp…so there’s not a pole at zero.
IF asked about why previous control signals look noisier…say that a filter was put on signal going to oscilloscope trace

## Slide 18
Chart: Measurement of Green Power Intensity Over Time
Chart: Time Stability of the IR Beam (transmitted)
Chart: Time Stability of IR Beam (Transmitted)
| 0 | 0.00005 | 0.0001 | 0.00015 | 0.0002 | 0.00025 | 0.0003 | 0.00035 | 0.0004 | 0.00045 | 0.0005 | 0.00055 | 0.0006 | 0.00065 | 0.0007 | 0.00075 | 0.0008 | 0.00085 | 0.0009 | 0.00095 | 0.001 | 0.00105 | 0.0011 | 0.00115 | 0.0012 | 0.00125 | 0.0013 | 0.00135 | 0.0014 | 0.00145 | 0.0015 | 0.00155 | 0.0016 | 0.00165 | 0.0017 | 0.00175 | 0.0018 | More
Frequency | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 124 | 945 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 45 Minute Scan of Green Beam Power Distribution
| 0.01 | 0.011 | 0.012 | 0.013 | 0.014 | 0.015 | 0.016 | 0.017 | 0.018 | 0.019 | 0.0191 | 0.0192 | 0.0193 | 0.0194 | 0.0195 | 0.0196 | 0.0197 | 0.0198 | 0.0199 | 0.02 | 0.0201 | 0.0202 | 0.0203 | 0.0204 | 0.021 | 0.022 | 0.023 | More
Frequency | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 3 | 5 | 9 | 19 | 117 | 1479 | 1053 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: Need for INFRARED FROM power meter
Measure frequency noise….using SR-785

## Slide 19
Chart: Oscilloscope Time Stability Measurement of IR and Green Beams
Notes: Stable

## Slide 20
Longest Observed Lock Held = 17 hours

## Slide 21: Stability of Green Light
A good servo lock confirms minimal spread in the green light intensity

## Slide 22: Test with Ophir Power Meter
Chart: 45 Minute Scan of Green Beam Power Distribution
| 0.01 | 0.011 | 0.012 | 0.013 | 0.014 | 0.015 | 0.016 | 0.017 | 0.018 | 0.019 | 0.0191 | 0.0192 | 0.0193 | 0.0194 | 0.0195 | 0.0196 | 0.0197 | 0.0198 | 0.0199 | 0.02 | 0.0201 | 0.0202 | 0.0203 | 0.0204 | 0.021 | 0.022 | 0.023 | More
Frequency | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 3 | 5 | 9 | 19 | 117 | 1479 | 1053 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Distribution of Power in SHG Green Beam
If the lock is not good and the resonance drifts, then the power is ‘jumpy’
Time Range ~ 1 hour
Notes: But it’s likely a digital problem

## Slide 23: Conversion Efficiency vs. Input Power
79% Conversion Efficiency Observed!
Z.Y. Ou et. al
Chart: Output Green Power as a Function of Input Infrared (mW)
| 14.75 | 22.34 | 45.3 | 76.8 | 116 | 67.2 | 10.08 | 52.4 | 112.3 | 103.8 | 85.5 | 147.30000000000001 | 174 | 191.7 | 220.1 | 267.5 | 335
output green (mW) | 0.55 | 2.5 | 8.65 | 24.6 | 46.8 | 16.89 | 0.18 | 11.43 | 50.1 | 43.1 | 30.3 | 70.8 | 99 | 116.5 | 140.1 | 191.6 | 248
At Low Power
Notes: Why does power scale quadratically? Need to use Maxwell’s equations for a nonlinear medium…model input and output beams…impose an approximation (small amplitude deviation)…
get an expression where for perfect phase matching, the amplitude of the output beam scales linearly with z…hence power is quadratic in z…z is variable along length of crystal.
Attenuator…constant slope (same attenuation at all powers)

## Slide 25: New Temperature Controller implemented with Beckhoff electronics
Current Driver
EtherCat Terminals
TEC Interface

## Slide 26: Servo Characterization (in Time Domain)
Chart: Servo Response to Change in Set Temperature
Chart: RMS fluctuations as Servo Stabilizes in Time
Chart: Temp Servo Fluctuations after Settle Time
Time (am/pm)
Temperature (Celsius)
UGF (Unity Gain Frequency) = 0.500
Chart: Set Temperature Response with UGF = 0.01
Notes: Unity gain frequency: frequency where gain = 1

## Slide 27: Unit Step Response
Time (am/pm)
Temperature (Celsius)
Unit Step Response of Temperature Servo in Time
Laplace Transform (time domain <-> frequency domain)
Take inverse Laplace Transform of convolution of the unit step function and the transfer function:
Notes: First order system with one zero and one pole
Constants H(0) and H(inf) are evaluated using initial and final value theorems, but relatively unimportant

## Slide 28
Chart: Phase Matching Curve
| 29 | 29.25 | 29.5 | 29.75 | 30 | 30.25 | 30.5 | 30.75 | 31 | 31.25 | 31.5 | 31.75 | 32 | 32.25 | 32.5 | 32.75 | 33 | 33.25 | 33.5 | 33.65 | 33.75 | 33.85 | 34 | 34.15 | 34.25 | 34.35 | 34.5 | 34.75 | 34.85 | 35 | 35.15 | 35.25 | 35.5 | 35.549999999999997 | 35.65 | 35.75 | 36 | 36.25 | 36.35 | 36.75 | 37 | 37.25 | 37.5 | 37.75 | 38 | 38.25 | 38.5 | 38.75 | 39 | 39.25 | 39.5 | 39.75 | 40 | 40.25 | 40.5 | 40.75 | 41 | 41.25
Green Power (mW) | 0.77 | 0.45 | 0.2 | 0.08 | 0.07 | 0.12 | 0.26 | 0.37 | 0.41 | 0.34 | 0.16 | 0.08 | 0.2 | 0.62 | 1.29 | 2.43 | 3.83 | 5.58 | 6.5 | 7.28 | 7.48 | 7.3 | 6.81 | 5.83 | 5.01 | 4.06 | 2.94 | 1.5 | 0.65 | 0.33 | 0.38 | 0.77 | 3.22 | 3.95 | 5.35 | 7.05 | 12.41 | 18 | 22.13 | 24.78 | 25.08 | 24.85 | 24.38 | 23.85 | 21.66 | 19.69 | 16.83 | 12.15 | 7.22 | 3.3 | 1.03 | 0.16 | 0.07 | 0.35 | 0.55 | 0.69 | 0.29 | 0.07
Phase (mis)matching equation:
Non-symmetric
IR = 78 mW
Phase Matching of Green and Red by Temperature Tuning
Boyd, Nonlinear Optics

## Slide 29: Questions?
Notes: Relative Intensity Noise: -120 dB

## Slide 30: References

## Slide 31: Temperature Servo Introduces Noise

## Slide 32
Return

## Slide 33
Chart: Oscilloscope Tracking of IR, Green Transmission & Control, Error Signal

## Slide 34: Phenomenon seen again in SHG 2.0
Chart: Energy Distribution of Infrared Under Lock (Oscilloscope Measurement)
| 0.481 | 0.482 | 0.483 | 0.484 | 0.485 | 0.486 | 0.487 | 0.488 | 0.489 | 0.49 | 0.491 | 0.492 | 0.493 | 0.494 | 0.495 | 0.496 | 0.497 | 0.498 | 0.499 | 0.5 | 0.501 | 0.502 | 0.503 | 0.504 | 0.505 | 0.506 | 0.507 | 0.508 | 0.509 | More
Frequency | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 30 | 0 | 0 | 104 | 0 | 0 | 0 | 269 | 0 | 0 | 0 | 417 | 0 | 80 | #N/A
Chart: Green Power Intensity Over Time

## Slide 35
Anomalies in the Distribution
Bad Lock
BUT, What are these gaps in the bins

## Slide 36
Chart: Set Temperature Response with UGF = 0.9
Rise Time: ~60 seconds
Settle Time: ~2 mins
Overshoot: 1 degree Celsius
Peak Time: