## Slide 1: Brief Introduction to Advanced LIGO Suspensions
Brett Shapiro
LAAC Session
24 August 2014

## Slide 2
My experience
2001-2005 Undergrad: Penn State Engineering Science
2005-2012 PhD: MIT Mechanical Engineering
Worked on the controls, modeling, assembly, and testing of the prototype quadruple pendulums at the LASTI facility.
2012-now postdoc: Stanford University
Still some involvement in the suspensions group
Mostly working on cryogenic technologies for 3rd generation LIGO observatories
Installing the Quad Prototype at MIT
23 January 2009

## Slide 3
ITM, ETM
PR3, SR3
PRM, PR2, SRM, SR2, IMC
SUS group
Other suspensions
+ TransMon
Courtesy of Jeff Kissel

## Slide 4: BSCs – core optics
active isolation platform (2 stages of isolation)
hydraulic external pre-isolator (HEPI) (one stage of isolation)
quadruple pendulum (four stages of isolation) with monolithic silica final stage

## Slide 5: An aLIGO HAM Chamber
HAM2 (Chamber hidden for clarity)
x
y
z

## Slide 6
SR2, HAM4 – LHO 11 Feb 2014

## Slide 7: HAM Small Triple Suspension (HSTS)
Control
Local – damping at M1
Global – LSC & ASC at all 3
Sensors/Actuators
BOSEMs at M1
AOSEMs at M2 and M3
Optical levers and interferometric signals on M3
Naming: L1:SUS-PRM_M1…
Documentation
Final design review - T0900435
Controls arrangement – E1100109
Purpose
PRM, PR2, SRM, SR2
MC1, MC2, MC3
Location
HAM 2, 3, 4, 5, (8, 9, 10, 11)
M1
M2
M3
T1
T2
T3
SD
LF
RT
UL
UR
LL
LR
UL
UR
LL
LR
L
T
V

## Slide 8: Optical Sensor ElectroMagnet (OSEM)
Magnet Types (M0900034)
BOSEM – 10 X 10 mm, NdFeB , SmCo
10 X 5 mm, NdFeB, SmCo
AOSEM – 2 X 3 mm, SmCo
    2 X 6 mm, SmCo
    2 X 0.5 mm, SmCo
Birmingham OSEM (BOSEM)
Advanced LIGO OSEM (AOSEM)
- modified iLIGO OSEM
BOSEM Schematic

## Slide 9: Quadruple Suspension (Quad)
Main (test) Chain
Reaction Chain
Control
Local – damping at M0, R0
Global – LSC & ASC at all 4
Sensors/Actuators
BOSEMs at M0, R0, L1
AOSEMs at L2
Opt. levs. and interf. sigs. at L3
Electrostatic drive (ESD) at L3
Documentation
Final design review - T1000286
Controls arrang. – E1000617
Purpose
Input Test Mass (ITM, TCP)
End Test Mass (ETM, ERM)
Location
H1 - BSC 1, 3, 9, 10
H2 - BSC 7, 8, 5, 6
L1 – BSC 1, 3, 4, 5
R0, M0
L1
L2
L3

## Slide 10
H1ITMX
LHO alog 12211
10 June 2014
De-install for silica fiber installation

## Slide 11
H1 ITMX – 30 July 2014 - LHO alog 13044

## Slide 12: Suspension Isolation

## Slide 13: Suspension Isolation

## Slide 14: Suspension Isolation

## Slide 15: Suspension Isolation

## Slide 16: Suspension Isolation
Each stage provides 1/f2 isolation
GW band

## Slide 17: The damping challenge

## Slide 18: The damping challenge

## Slide 19: The damping challenge

## Slide 20: The damping challenge
10000 times higher!

## Slide 21: Damping feedback loop

## Slide 22: Damping feedback loop
+
sensor noise
[m]

## Slide 23: Damping feedback loop
Damping feedback filter
+
sensor noise
[m]

## Slide 24: Damping feedback loop
Damping feedback filter
+
sensor noise
[m]
[N]

## Slide 25: Damping feedback loop
Damping feedback filter
+
sensor noise
[m]
[N]

## Slide 26: Damping feedback loop
Damping feedback filter
+
sensor noise
[m]
[N]
Ideal damping filter

## Slide 27: Damping filters in practice
Stable damping filter

## Slide 28: Cavity control
Main (test) Chain
Reaction Chain
Cavity control filters
Drift control
Low frequency control
Medium frequency control
High frequency control

## Slide 29: Resources on control techniques
Damping
  Loop shaping and modal damping - P1200009 http://scitation.aip.org/content/aip/journal/rsi/83/4/10.1063/1.4704459?ver=pdfcov
  Modal damping - P1200057
  Global damping - P1400085, G1200774
Cavity control (aka hierarchical control)
  G1200632
  T1000242
  Using a blended actuator technique, using experience from the SEI group’s sensor blending: G1200692

## Slide 30: Back Ups

## Slide 31: Five Suspension Designs
Ref: G1100434

## Slide 32: Output Mode Cleaner Double (OMCS)
In use during S6
Location
HAM 6, (12)
Control
Local – damping at M1
(true for all SUS’s)
Sensors/Actuators
BOSEMs at top mass
Top mass naming convention
L1:SUS-OMC_M1…
site subsystem unit stage
2
3
3,4
2
Documentation
Final design review - T0900060
HAM SUS controls arrangement – E1100109
Optics
M1
M2
T1
T2
T3
SD
LF
RT
L
T
V
Local coordinates

## Slide 33: TransMon Double
Ref: E1000040
Location
BSC 9, 10
Control
Local – damping at top mass
Sensors/Actuators
BOSEMs at top mass
Top mass naming convention
L1:SUS-TRMX_M1…

## Slide 34: HAM Large Triple Suspension (HLTS)
Control
Local – damping at M1
Global – LSC & ASC at all 3
Sensors/Actuators
BOSEMs at M1
AOSEMs at M2 and M3
Optical levers and interferometric signals on M3
Naming: L1:SUS-SR3_M1…
Documentation
Final design review – T1000012
Controls arrangement – E1100109
Purpose
PR3, SR3
Location
HAM 2, 5, (8, 11)
M1
M2
M3
UL
UR
LL
LR
UL
UR
LL
LR
L
T
V

## Slide 35: Beamsplitter/Folding Mirror (BSFM)
Control
Local – damping at M1
Global – LSC & ASC at M2
Sensors/Actuators
BOSEMs at M1 and M2
Optical levers and interferometric signals on M3
Naming: L1:SUS-FMX_M1…
Documentation
Final design review - T080218
Controls arrangement – E1100108
Purpose
BS, (FMX and FMY)
Location
Beamsplitter – BSC 2, (4)
(Fold Mirror – BSC 6, 8)
M1
M2
M3
UL
UR
LL
LR
F1
F2
F3
LF
RT
SD
L
T
V

## Slide 36: Global Cavity Control (LSC)
Cavity Length
C1
C2
C3
C4
Each stage has limited range, so the control is distributed up the chain with:
Increasing control force
Lower frequency control
ITM
ETM

## Slide 37: Parallel Control of Cavity Length
Cavity Length
C1
C2
With parallel feedback, changing one loop requires changing the others to account for changes in gain and stability.
The stability of all stages are coupled
ITM
ETM

## Slide 38: Hierarchical Control of Cavity Length
Cavity Length
C1
C2’
If each stage’s input is the output of the previous stage, any feedback change is automatically registered by the rest of the loop.
The stability at each stage is independent from the others.
Detailed discussion in T1000242.
ITM
ETM

## Slide 39: Quad MEDM Overview Screen

## Slide 40: Quadruple Suspension ESD
Main (test) Chain
Reaction Chain
The electrostatic drive (ESD) acts directly on the test ITM and ETM test masses.
± 400 V (ΔV 800 V)
  ≈ 100 μN
Each quadrant has an independent control channel
Common bias channel over all quadrants
UL
UR
LL
LR

## Slide 41: Quadruple Suspension ESD
Cartoon diagram illustrating the working principle of the ESD. The upper rectangle represents the test mass containing two polarized molecules; the lower rectangle represents the reaction mass bearing two electrodes. Surface plot shows electrical
potential with electric field lines shown in cyan (John Miller PhD thesis, P1000032).
Test mass
Reaction mass
5 mm
F = αΔV2
α = coupling coefficient, depends on geometry
ΔV = differential voltage across traces
Linearization occurs in the control!

## Slide 42: Quadruple Suspension (Quad)
Main (test) Chain
Reaction Chain
R0, M0
L1
L2
L3
Newly welded monolithic quad at MIT
11 May 2010
Pulling a fiber at MIT
7 May 2010
Fibers

## Slide 43: aLIGO Noise Budget