## Slide 1: Quantum noise in Gravitational Wave Detectors
Koji Arai – LIGO Laboratory / Caltech
LIGO-G1401147-v2

## Slide 2: Introduction ~ Quantum noise?
SHOT NOISE:
Photon counting noise
RADIATION PRESSURE NOISE: Back-action noise caused by random motion of the mirrors
LASER
Photo-Detector
m
Measurement frequency
Slide courtesy of L. Barsotti
Notes: h_shot, h_rad

## Slide 3: “Standard Quantum Limit”
hSQL doesn’t depend on the optical parameters of the interferometer, just on the quantum mechanics of a harmonic oscillator mass
Slide courtesy of L. Barsotti

## Slide 4: Optical noises
Quantum noises
  Standard Quantum Limit (SQL)
- Trade-off Between Shot Noise and Radiation-Pressure Noise
- Uncertainty of the test mass position due to observation

## Slide 5: Introduction ~ Quantum noise?
Quantum noise in Advanced LIGO
  Photon shot noise and radiation pressure noise will limit the detector sensitivity in the end
Shot noise
Radiation
Pressure
Noise

## Slide 6: Introduction ~ Quantum noise?
Quantum noise reduction
  Make the interferometer longer => Needs new facility
  Heavier test masses & more optical power => Stored power of aLIGO will be 800kW
  Have to deal with thermal effects / instabilities
  More complex optical configuration to shape optical response Injection of squeezed states of vacuum

## Slide 7: Introduction ~ Quantum noise?
What is “squeezing”?
Quantized Electromagnetic Fields Quadrature Field Amplitudes Classical Quantum
Coherent State
Heisenberg’s uncertainty principle

## Slide 8: Introduction ~ Quantum noise?
Even when average amplitude is zero, the variance remains => Zero-point “vacuum” fluctuation
Vacuum fluctuations are everywhere => Comes into the interferometer from the open optical port and cause shot and radiation pressure noises

## Slide 9: Squeezing
The noise can be redistributed while keeping the minimum uncertainty product ΔX1 ΔX2 =1 = Squeezed light
Squeezed light is characterized by
  Squeezing factor r How much the noise is squeezed
  Squeezing angle 𝜙sqz Which quadrature is squeezed

## Slide 10: Squeezing
Particularly useful two states
Phase squeezing
(Amplitude anti-squeezing)
Amplitude squeezing
(Phase anti-squeezing)

## Slide 11: Squeezing
In practice, we inject squeezed “vacuum” from the dark port
  Squeezing angle needs to be fixed by a feedback control loop with regard to the field in the interferometer

## Slide 12: Squeezing in action
Actual squeezer (LIGO H1 squeezer)
  Many auxiliary phase lock loops are necessary to fix the squeezing angle
OPO is here!
Sheila Dwyer PhD Thesis (2013)
Squeezed vacuum
is here!

## Slide 13: Squeezing in action
Shot noise reduction in GW detectors has already been realized since 2007
Squeezed light injection experiment at the LIGO 40m
K.Goda et al, Nature Physics 4, 472 - 476 (2008)

## Slide 14: Squeezing in action
Squeezing in GEO600 and LIGO H1 to reduce shot noise
Slide courtesy of L. Barsotti
GEO data are courtesy of H. Grote
3.5 dB
(1/1.5)
2.1 dB
(1/1.27)
LSC, Nature Physics 7, 962 (2011)
LSC, Nature Photonics 7, 613–619 (2013)

## Slide 15: Quantum noise in an interferometer
Ponderomotive effect
  Vacuum fluctuations from the dark port produce amplitude and phase fluctuations in the arm cavities
  Radiation pressure The test mass mechanical system work as a converter from the amplitude fluctuation to the phase fluctuation

## Slide 16: Quantum noise in an interferometer
Ponderomotive effect
  Radiation pressure: The test mass mechanical system work as a converter from the amplitude fluctuation to phase fluctuation
amplitude fluctuation in the arm
phase fluctuation in the arm
radiation pressure
GW
signal
Output fluctuation
amplitude
phase

## Slide 17: Quantum noise in an interferometer
Ponderomotive effect

## Slide 18: Quantum noise in an interferometer
Homodyne detection
  In order to detect the signal (and noise) with a photodetector The output field needs to be mixed with a local oscillator field. cf. RF (or heterodyne) detection using RF sidebands
  Homodyne angle: Changes the projection of the GW signal field and output noise fields into the detection signal
  DC Readout A small (1~10pm) offset from the dark fringe is applied => Useful: The IFO beam itself becomes the LO field ΦH is fixed at zero

## Slide 19: Squeezed vacuum injection
Frequency dependent squeezing
  Rotate squeezing angle to optimize the output noise field
F.D. squeezing
S Danilishin, F Khalili, Living Rev. Relativity, 15, (2012), 5
http://www.livingreviews.org/lrr- 2012- 5

## Slide 20: Squeezed vacuum injection
High finesse detuned “filter cavity” which rotates the squeezing angle as function of frequency
SHOT NOISE
RADIATION PRESSURE
NOISE
GW Signal
Quantum Noise
~30Hz
~30Hz
Frequency dependent squeezing
Slide courtesy of L. Barsotti

## Slide 21: Squeezed vacuum injection: technical issues
The enemies of the squeezing
  Optical Loss Optical losses works as beamsplitters to introduce normal vacuum fluctuation
  Phase noise Wobbling of the squeezing angle causes leakage of the other quadrature into the squeezed quadrature

## Slide 22: Optical loss & Squeezing phase noise
GW
Signal
eLIGO
GEO
We need less than 20% total losses
aLIGO readout now has ~30% (w/o squeezing)
=> Need to reduce!
Target: -10dB
noise reduction
Slide courtesy of L. Barsotti

## Slide 23: Phase noise mitigation
Invac OPOfor aLIGO
Let’s move the OPO into the vacuum envelope on seismic isolated tables!
E. Oelker et al., Optics Express, Vol. 22, Issue 17, pp. 21106-21121 (2014) (P1400064)
Slide courtesy of L. Barsotti

## Slide 24: Summary
Quantom noise in GW detectors
  Shot noise & Radiation pressure noise
Squeezed vacuum injection
  Shot noise reduction already demonstrated.
Radiation pressure
  Will eventually limit the sensitivity
  Frequency Dependent squeezed vacuum injection will mitigate the radiation pressure noise
Technical Issues: Optical loss & phase fluctuation
  R&D on going