## Slide 1: aLIGO HSTS Damping Loops Design Comparison
J. Kissel, for the SUS and ISC Teams

## Slide 2: 3 Different Designs
LHO Current
Began with P. Fritschel’s “resg” design from LLO aLOG 4739
Slight increase of design complexity to strict velocity damping
Some attention paid to sensor noise reinjection
Evolved into disarray on a SUS-by-SUS basis because of
  disjointed install
  disjointed tweaking
  poor version control
LLO Current
Den’s (?) design
(can’t find aLOGs)
Focused on reducing Q’s and impulse response
Consistently installed in all L1 HSTS
Low Noise
Recently designed by Betsy / Kissel
Not implemented anywhere
Focused on 10-20 [Hz] noise performance, attempting to still get a good amount of damping
Remember: there are no optical levers on these SUS

## Slide 3
Resonant Gain at first resonance
AC coupled, rises as f^1,
“velocity”
Various sensor noise roll-off tactics
LLO
LHO
Low Noise

## Slide 4
LLO
LHO
Low Noise
Low-Q design of LHO and LLO produces mode splitting – locking to cage – at 0.7 [Hz]
LHO
LHO
54.6
35.7
67.4
34.9
LN
LN
52.9
29.7
LLO
LLO
Lots of gain means phase margin is pretty tight in LLO design

## Slide 5
Impulse response at top mass is twice as long for M1 to optic for LowNoise design
New FOM!
Even longer for for M2 to optic for LowNoise design
Interesting -- LowNoise and LLO design are comparable at M3 stage – where high freq. lock acquisition impulses happen
1/e ringdown times
Regardless of design – impulse response is worse as you get further from top mass

## Slide 6
New FOM!
Low Noise leaves high-Q features at high freq. in M1 and M2
LLO and LHO designs shift lowest mode frequencies up, and leave with high-Q on all stages

## Slide 7
No surprise here, the LowNoise design is low noise at 10-20 [Hz]
LHO
LLO
LowNoise
Goal for aLIGO Baseline
For LHO and LowNoise designs I’m using increased range M3 driver
Ground Transmission
Sensor Noise
Actuator Noise

## Slide 8
Looking for simple L2P TFs for easy compensation?
No design really gets it, but LowNoise is “better”
High Q features left in LLO and LHO design
New FOM!

## Slide 9
How about simple plant for high-bandwidth WFS control?
Pitch-to-Pitch has high-Q features for ANY design at ANY level
New FOM!

## Slide 10
Regardless of how squashed you make the top-to-top Closed Loop Gain TF
Or how little phase margin …
LHO
LHO
95.1
47.6
58.9
33.2
LN
LN
87.9
28.2
LLO
LLO

## Slide 11
Pitch is bad for impulses, regardless of design
New FOM!

## Slide 12
More Badness
Highest vertical mode @ 27 [Hz] (uncontrollable from top)
Gets kicked for every design – we will always need to notch these for global control
New FOM!

## Slide 13
Roll is just terrible – no stage is well damped at 1.5 [Hz]
And again, highest 40 [Hz] mode gets kicked
New FOM!

## Slide 14
This guy right here
is a “transverse” mode…

## Slide 15
But well damped in Transverse

## Slide 16: What have we learned?
Each design has its pros and cons
As expected, Low-noise design is low noise, Low-Q design (i.e. LLO) reduces Q for Longitudinal but …
Just changing the overall gain is not the answer, nor is paying attention to only Longitudinal
Lots of stuff doesn’t change with design
  Pitch global TFs
  Pitch impulse response
  Exciting of highest Vertical and Roll modes
  Roll impulse response
L (and Y) global transfer functions are more complex for Low-Q, and drastically change depending on design
Remember: there are no optical levers on these SUS

## Slide 17: Conclusions
I haven’t looked yet, but I’m sure the situation will be the same for other SUS types (and the worst for QUADs)
If you want UGFs between 0.5 to 10 [Hz], it’s going to be hard, and will take careful, patient design
Changing damping loop design will impact those global control designs (including L2P and L2Y decoupling filters)
Perhaps we consider switching between designs (i.e. having both on hand, and change the configuration based on IFO needs)?
Should LHO take the global control / decoupling redesign schedule hit and import LLO’s filters?
In the limit of infinite time – can we explore a design that optimizes impulse response at the lowest stage from each stage and simplifies global control TFs and gets the 10-20 [Hz] noise OK?
Do we seriously start considering modal damping? Sure they’re good at noise, but how about these other FOMs?
Suggestions welcome.