## Slide 1: Advanced LIGO status Hiro Yamamoto LIGO lab/Caltech
Introduction
Initial LIGO and advanced LIGO
Sensitivities
Commissioning status
Targeting the first observations
Some slides are from “ET-aLIGO and beyond”, LIGO-G14001331, by David Shoemaker

## Slide 2: Gravitational waves
Gravitational waves are propagating dynamic fluctuations in the curvature of space-time (‘ripples’ in space-time)
Emissions from rapidly accelerating non-spherical mass distributions
  Quadrupolar radiation

## Slide 3: Interferometer for Gravitational Wave detection
L1
L2
h~10-23
L1-L2~10-19m
E1
E2
E1- E2 ∝ L1-L2

## Slide 4: Design Overview
Signal- and Power-recycled Fabry-Perot interferometer
180 W 1064 nm laser
thermal compensation of optics with CO2 laser and Ring-Heater
Arm-Length Stabilization to aid locking
Active Seismic Isolation
Quad Fused-silica suspension
Mode-stable Recycling Cavities
 4km 
Higher-mass, lower-loss, larger test mass optics
 4km 

## Slide 5
5
Advanced LIGO Scope
and Deliverables
Image courtesy of Beverly Berger
Cluster map by Richard Powell
Initial LIGO
Factor 10 better amplitude sensitivity
  (Reach)3 = rate
Factor 4 lower frequency bound
Tunable for various sources
NS Binaries: for three interferometers,
  Initial LIGO: ~20 Mpc
  Adv LIGO: ~300 Mpc, expect one event/week or so
BH Binaries:
  Initial LIGO: 10 Mo, 100 Mpc
  Adv LIGO : 50 Mo, z=2
Stochastic background:
  Initial LIGO: Ω~3e-6
  Adv LIGO ~3e-9

## Slide 6: Noise components iLOGO = seismic + thermal + shot aLIGO = quantum noise + thermal

## Slide 7: Improving sensitivities

## Slide 8: LIGO sites
Hanford
Observatory
(H2K and H4K)
Livingston
Observatory
(L4K)
Hanford, WA (LHO)
located on DOE reservation
treeless, semi-arid high desert
25 km from Richland, WA
Two IFOs: H2K and H4K -> 4k LHO + 4k India
Livingston, LA (LLO)
located in forested, rural area
commercial logging, wet climate
50km from Baton Rouge, LA
One L4K IFO
Both sites are relatively seismically quiet, low human noise - NOT!!
4 km
+ 2 km
4 km

## Slide 9: Logging at Livingston
Less than 3 km a few 100 meters away…
Dragging big logs …
Remedial measures at LIGO are in progress;
this will not be a problem in the future.

## Slide 10: International network
LIGO
Simultaneously detect signal (within msec)
detection confidence
locate the sources
verify light speed propagation
decompose the polarization of gravitational waves
Open up a new field of astrophysics!
GEO
Virgo
KAGRA
LIGO-India

## Slide 11: LIGO vacuums
Beam light path must be high vacuum, to minimize “phase noise”
All optical components must be in high vacuum, so mirrors are not “knocked around” by gas pressure

## Slide 12: aLIGO Test Masses
Half-nm flatness over 300mm diameter
0.2 ppm absorption at 1064nm
Coating specs for 1064 and 532 nm
Mechanical requirements: bulk and coating thermal noise, high resonant frequency
Requires the state of the art in substrates, polishing, coating
Both the physical test mass – a free point in space-time – and a crucial optical element
Test Masses:
34cm ∅ x 20cm
40 kg
40 kg
BS:
37cm ∅ x 6cm
ITM
T = 1.4%
Round-trip optical loss: 75 ppm max
Compensation plates:
34cm ∅x 10cm

## Slide 13: Test mass Optics figure
In-house metrology on 300 mm diameter shows 0.66 nm RMS
  Note spiral from planetary system; about 0.2 nm pk-pk
In-situ measurements of as-built 4km cavity show results are better than requirements!

## Slide 14: Noise injection by the spiral pattern on test mass coatings
Phasemap resolution in simulation
Figure loss by two mirrors
~ 15-20ppm
micro roughness, point scattering ~ 20 ppm
7.83mm
ETM07 map
T1300354 by PF,HY
main beam ⇒
ETM reflection ⇒
larger angle scattering into cone ⇒
reflected by beam tube baffles ⇒
back scattered into ETM ⇒
merged into the main beam

## Slide 15: TCS corrections for LLO PRMI
log11140 CD~400ppm, PRG~45
log#9733 CD~600ppm, PRG~35
RH optimal lens = n(SiO2) x 82km = 1/0.84 x10-5
CP optimal lens = 82km = 1/1.22 x10-5

## Slide 16: (In)Sensitivity on ITM SPTWE + CP lens
ITM08 / ITMY
transmission map in 160mm w/o power
ITM04 / ITMX
-11.6nm
6.6nm
-4.5nm
7.7nm

## Slide 17: Historical perspective: Initial LIGO commissioning
Overall, 4-5 years from locking to design sensitivity
Inauguration
1999
2000
2001
2002
2003
3
4
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
E2
Engineering
E3
E5
E9
E10
E7
E8
E11
First Lock
Full Lock all IFO
10-17
10-18
10-20
10-21
2004
2005
1
2
3
4
1
2
3
4
1
2
3
4
2006
First Science Data
S1
S4
Science
S2
Runs
S3
S5
10-22
4 km strain noise
at 150 Hz [Hz-1/2]
2.5x10-23
10-19
Design sensitivity
1
2
3
2007

## Slide 18: Project Integrated Testing Plan
Integrated testing phases interleaved with installation
Complementary division between LHO and LLO
  Designed to address biggest areas of risk as soon as possible
  H1 focused on long arm cavities; L1 worked outward from the vertex
July 2012
Oct 2012
Jan 2013
Apr 2013
July2013
Oct 2013
Jan 2014
Apr 2014
July2014
One Arm Test 1st arm cavity Green only
Input Mode Cleaner
HIFO-Y Y-arm + corner
Green + PSL IR
HIFO-XY
Both arms + corner
No AS port
Input Mode Cleaner with high power test
Dual recycled Michelson
I
II
III
H1
L1
Full Interferometer
Build & test from the arms backward
Build & test from the laser outward

## Slide 20: LLO Project scope finished
The full interferometer lock was achieved on May 26, 2014
L1 formally met the aLIGO goal of a 2h stable lock
The IFO has been locked for as long as 7.5h
Initial alignment and the lock acquisition are mostly automated
Currently recovering from some in-vacuum work
(Need to complete System Acceptance/documentation)

## Slide 21: LHO installation complete
Now under vacuum at all stations. Dual-recycled Michelson test underway; arms lockable with green Arm Length Stabilization, working toward full lock
Accomplished with huge help from LLO, CIT and MIT
Next: installation acceptance, and get to two-hour-lock milestone
Also, responsibility for 3rd ifo (India) is at Hanford – non-trivial task.

## Slide 22: Targeting the first observations
ER6 slated for start December 8th, 2014
  L1 expected to be locked for multiple-hour intervals, although not at peak sensitivity; H1 not locking yet
  Significant discussion in Joint Run Planning Committee on ER6 readiness (throughout the LSC), start date, calibration/freeze/run durations, and impact on commissioning
O1 observation run slated for as early as mid-July 2015; an evolving discussion as commissioning progress is understood
Important point: we want Both LIGO instruments working at comparable sensitivity for the first observing run
  Catch-up needed at LHO – integrated testing starting ~6 months later than LLO, and e.g., operator/detector support training just getting going; lessons learned will help, but only so much
  Still ‘all hands on deck’ from LLO, MIT, CIT and of course LHO to reach that goal, but with competing needs to complete aLIGO hardware and documentation, work on BeamTube leak repair

## Slide 23: Advanced LIGO: anticipated science runs
2015
2016-2017
Full sensitivity (200 Mpc): end-2018
1st run: 3 months @40-80 Mpc possible detection
2nd run: 6 months @80-120 Mpc likely detection
3rd: 2017-2018