## Slide 1: LIGO-India Detector Master Class Introduction
Koji Arai – LIGO Laboratory / Caltech
LIGO-G1401365-v1

## Slide 2: Who is this guy!?
Ph.D at Univ of Tokyo (1995-1999)
  Design & build of TAMA300 double-pendulum suspensions
  Interferometer length sensing for power recycled Fabry-Perot Michelson Interferometer
Commissioning and science runs of TAMA300 interferometer (1999-2009)
@LIGO Caltech (2009-) Output mode cleaner development eLIGO/aLIGO commissioning

## Slide 3: LIGO-India Detector Master Class: Overview
Mission: To convey technical knowledge necessary for building and operating the LIGO India detector, or similar interferometer, including prototypes
by going through:
  the common technologies in laser interferometer GW detectors
  Detailed description / discussion about the interferometer sensing & control

## Slide 4: LIGO-India Detector Master Class: Overview
Lecture plan
DAY1 General overview of laser interferometer GW detectors
Interferometer configurations
DAY2 Noises in GW detectors
DAY3 Control system & its modeling
DAY4 Interferometer length sensing and control
Feedforward noise cancellation
Quantum noise
DAY5 Higher-order laser modes

## Slide 5: Interferometer GW detection

## Slide 6: Gravitational wave
General Relativity
  Gravity = Spacetime curvature
  Gravitational Wave = Wave of spacetime curvature
GW
  Generated by motion of massive objects
  Propagates with speed of light
  Cause quadrupole deformation of the spacetime
GW
Free mass

## Slide 7: Gravitational wave
What does the balls feel?
  The balls are free mass (= free falling)
  ...Geodesic lines
Q. What happens if the balls are connected by bars
GW
Free mass

## Slide 8: Interferometer GW detection
Michelson-type interferometers are used
Differential change of the arm path lengths
=>change interference
condition
Beamsplitter
Mirror
Mirror
Laser
Interference
Fringe

## Slide 9: Antenna pattern
Antenna pattern (at low frequencies)
Rev. Mod. Phys. 86 (2014) 121-151
http://link.aps.org/doi/10.1103/RevModPhys.86.121 (http://arxiv.org/abs/1305.5188)

## Slide 10: Amplitude of GWs
The effect of GW is very small
h ~ 10-23 => distance of 1m changes 10-23m
Corresponds to:
change by ~0.01 angstrom (or 1pm) for distance between the sun and the earth
1.5 x 1011 m
changes
by 1/100 of a H atom diameter!

## Slide 11: Size of interferometer GW detectors
GW Detection = Length measurement
The longer arms, the bigger the effect
  GW works as strain => dx = hGW x Larm
  Until cancellation of the signal happens
  in the arms
  Optimum arm length
Laser
Photodetector
Mirror
Mirror
Laser
Photodetector
Mirror
Mirror

## Slide 12: Size of interferometer GW detectors
Still shorter than the optimum length
=> Use optical cavity to increase life time of the photons in the arm
LIGO Observatories
Hanford / Livingston 4km
\
c.f. Virgo (FRA/ITA) 3km, KAGRA (JPN) 3km, GEO (GER/GBR) 600m

## Slide 13: Components of the interferometer
“Still simplified” LIGO Interferometer
Laser
Mode
Cleaner
L~16m
Beamsplitter
4km
Fabry-Perot
Cavity
4km Fabry-Perot Cavity
Vacuum Chamber /
Beam tube
Photodetector
Data Acquisition
/Analysis System
Mirror Suspension
Vibration
Isolation
System
Mirror
Digital Control System
Recycling
Mirrors

## Slide 14: Components of the interferometer
3 fundamentals of the GW detector
Mechanics
Optics
Electronics

## Slide 15: Components of the interferometer
3 fundamentals of the GW detector
Mechanics
Optics
Electronics

## Slide 16: What can we do for the detection?
An IFO produces a continuous signal stream in the GW channel
The detector is fixed on the ground => can not be directed to a specific angle
GWs and noises are, in principle, indistinguishable
=> Anything we detect is GW
Reduce noises!
Obs. distance is inv-proportional to noise level
x10 better => x10 farther => x1000 more galaxies

## Slide 17: Sensitivity and noise
Sensitivity (=noise level) of Enhanced LIGO
h= 2x10-23 /rtHz
Laser shot noise
Laser radiation
pressure noise
thermal noise
seismic noise
Laser intensity
/frequency noise
electronics noise
digitization noise
angular control noise
......

## Slide 18: aLIGO sensitivity
aLIGO sensitivity
Preliminary
x= 4x10-20 m/rtHz
h= 1x10-23 /rtHz

## Slide 19: Data Analysis
Compact Binary Coalescence => Chirp signal
  NS-NS binaries Accurate waveforms predictable (Post Newtonian approximation) => Template banks & Matched Filter analysis (amplitude & phase information)
  BH-BH binaries Similar waveforms, but more difficult to predict because of earlier merging
Mat]ched filtering analysis

## Slide 20: Data Analysis
f_ISCO = 1/(pi (6 M)^3/2)
Msolar = 1.989*^30;
c = 2.9979*^8;
G = 6.67*^-11;
c = 299792458; G = 6.67*^-11; m1 = 1.4 Msolar; m2 = 1.4 Msolar; Msolar = 1.989*^30; m = m1 + m2; fISCO = c^3/(6^(3/2)*Pi*G*m)
B. F. Schutz, “Gravitational wave astronomy”, Class. Quantum Grav. 16 (1999) A131.

## Slide 21: Binary range
Binary inspiral range
  Chirp waveform PSD
  ISCO freq (HF cut off freq)
  Horizon range (Integrated SNR of 8)
  In the control room we use D/(2.26) taking all sky average
https://dcc.ligo.org/LIGO-T0900499/public
iLIGO 15Mpc
eLIGO 20Mpc
aLIGO 50Mpc

## Slide 22: Localization capability:
LIGO-Virgo only

## Slide 23: Localization capability:
LIGO-Virgo plus LIGO-India

## Slide 24: Data Analysis
Burst gravitational waves
  Supernovae, binary merger phase, etc Accurate waveforms unpredictable => Find signals with an “unusual” amplitude => Important to distinguish from non-stationary noises
Continuous waves
  Pulsars Sinusoidal signal with some modulations => Longterm integration => Important to distinguish from line noises (Remark: power line freq. US 60Hz, India 50Hz)

## Slide 25: Data Analysis
Stochastic gravitational wave background
  From early universe The waveforms are random => Correlation analysis of the detector network => The total GW flux can be estimated => Or, skymap of the flux is obtained from radiometric analysis
In all cases, it is highly desirable to have the detectors to have comparable sensitivities

## Slide 26: Summary
GWs ~ ripples of the spacetime
Not yet directly detected ~ the effect is so small (h<10-21)
Michelson-type interferometers are used
GW detection is a precise length (=displacement) measurement!
GW effect is very small

## Slide 27: Summary
Basically, the larger, the better. LIGO has two largest interferometers
in the world, and the third one will have very important role in GW astronomy
IFO consists of many components Optics / Mechanics / Electronics
and their combinations (e.g. Opto-Electronics)
Noises and signals are, in principle, indistinguishable. Noise reduction is essential