## Slide 1: Interferometer Length Sensing in Gravitational Wave Detectors
Koji Arai – LIGO Laboratory / Caltech
LIGO-G1401386-v1

## Slide 2: Global control
Interferometer control using the main laser beam
  On the top of the local control, optical path lengths and the mirror alignment need to be kept at the most sensitive state of the interferometer

## Slide 3: Cavity length control
Pound-Drever-Hall (PDH) technique
  We want to keep the cavity at the TOP of the resonance
  Phase of the cavity reflection is linear to the cavity detuning
  Use modulation / demodulation
Drever, R. W. P., et al Appl Phys B 31 97-105 (1983)
http://en.wikipedia.org/wiki/Pound%E2%80%93Drever%E2%80%93Hall_technique
http://www.sjsu.edu/faculty/beyersdorf/Archive/Phys208F07/Sideband%20generation%20in%20LIGO.pdf
  Detuning
  PDH
  Error signal
  Cavity Ref Power
  Cavity Ref Phase

## Slide 4: Modulation
Phasor diagram

## Slide 5: Modulation
Modulation sidebands
  Phase modulation Amplitude modulation

## Slide 6: Modulation
Phasor diagram vs Sideband picture
2nd order? 3rd order?
sidebands rotate
at the rate of 𝜈m
total field shows phase modulation at 𝜈m

## Slide 7: Modulation
Time dependent electric field vs Sideband picture
They are equivalent!

## Slide 8: Modulation
Note: Photodetectors don’t feel phase modulation!

## Slide 9: Modulation
Two quadratures of PM
Two quadratures of AM
Relationship between PM and FM (freq modulaition)

## Slide 10: Demodulation
RF x LO & LPF
Two demodulation quadratures (I&Q)

## Slide 11: RF detection ~ Interferemeter LSC
Use the interferometer as PM-AM converter

## Slide 12: Pound Drever Hall technique
Sideband picture
  Carrier experiences “fast phase change” depending on the length of the interferometer

## Slide 13: Pound Drever Hall technique
Phasor picture
  Reflected field on Resonance Detuned
total field only has phase modulation at 𝜈m
total field has
amplitude modulation at 𝜈m
carrier phase shift
No power modulation
Power modulation at 𝜈m
=> Photocurrent demodulated at 𝜈m shows the linear signal to the detuning!

## Slide 14: Michelson length control
Michelson is operated at the dark fringe for the shot noise and the power recycling
  At the dark fringe, DC signals can’t be a good error signal
  Schnupp asymmetry: Introduce small arm length asymmetry => RF sidebands leaks to the dark port

## Slide 15: Michelson length control
Schnupp asymmetry ~ sideband picture
Because of the asymmetry, the dark port is no longer dark for the sidebands even if the carrier is at dark.

## Slide 16: Michelson length control
Schnupp asymmetry ~ phasor picture

## Slide 17: aLIGO length control
Actual aLIGO Length control scheme

## Slide 18: Resonant conditions
For signal extraction purpose we need to resonate two sidebands (f1 and f2).
  f1 +1/-1 SBs should be resonant in the PRC
  f2 +1/-1 SBs should be resonant in both the PRC and SRC
The carrier, f1 SBs, and f2 SBs needs to go through the resonances of the input mode cleaner. (f1 = n fFSR_MC, f2 = m fFSR_MC)

## Slide 19: Resonant conditions

## Slide 20: Lock Acquisition: Real and Simulated
Transition from non-operational state to the final linear state
  Nonlinear process ~ Lock Acquisition
Before the lock, we can’t make a diagnosis of the control loops Without diagnosis, the lock is difficult. (Chicken & egg problem)
  iLIGO Lock acquisition
  PRMI locked
  Yarm locked
  Xarm locked

## Slide 21: Lock Acquisition: Real and Simulated
Mirror velocity vs Required actuator force
  Mirror momentum: p = m v
  Interaction time: dt = w / v
  Required force: F dt = m v => F = m v^2 / w
For single arm case:
  m: 40kg, v: 1um/s, w: 1nm => 0.04N
For common mode (double cavity) case:
  m: 40kg, v: 1um/s, w: 0.03nm => 1.3N
For DC control of a 1m pendulum for 1um displacement
  F = m g / l x = 0.4 mN
  3000 times smaller!
We want longer interaction time! (quieter mirror)

## Slide 22: Lock acquisition strategy
Probabilistic lock & Deterministic lock
Arm Length Stabilization (aka green locking)
Transmission locking
3f locking
PDH linearization

## Slide 23: Lock acquisition strategy
K. Izumi er al, ”Multicolor cavity metrology”, J. Opt. Soc. Am. A 29 (2012) 2092-2103

## Slide 24: Lock acquisition strategy
Green Locking for one arm (40m prototype)

## Slide 25: Lock acquisition strategy
Transmission locking
Off-resonant
Lock point
Resonant Lock
R. Ward PhD thesis (2009) California Institute of Technology
https://dcc.ligo.org/LIGO-P1400105

## Slide 26: Lock acquisition strategy
3f locking (aka Arai technique!)
K. Arai PhD thesis (2001) Univ. of Tokyo
http://t-munu.phys.s.u-tokyo.ac.jp/theses/arai_d.pdf

## Slide 27: Lock acquisition strategy

## Slide 28: Lock acquisition strategy

## Slide 29: Lock acquisition strategy

## Slide 30: Lock acquisition strategy
PDH linearization
M. Evans PhD thesis (2002) California Institute of Tech
http://www.ligo.caltech.edu/~mevans/lockAcq/thesis.pdf

## Slide 31: Design vs. realization
not needed
not needed

## Slide 32: Locking Process: realized
Find arm
resonances
Offset
arms
Lock
DRMI
Transition
from ALS to
IR signals
Reduce
CARM
offset
Transition
DRMI 3f to 1f
Engage CM/AO
Transition to reflection RF signal (REFL9I)
Align
recycling
mirrors
>95% coupled into IFO