## Slide 1: Low Vibration Cryogenics for LIGO Voyager
Brett Shapiro
Stanford University
Notes: I’m going to talk to you about some new directions for the cryogenics that we’ve been discussing recently at Stanford.
So I am going to propose a number of changes, and not just from a cryogenics point of view.
So I really want to encourage you to interrupt me with questions, comments, throughout the talk.

## Slide 2: LIGO III Cryosystem
ISI Stage 2
124 K Silicon test mass
…
Notes: First, here is the way we have been thinking about the cryogenics for the passed couple of years with the 124 K test mass

## Slide 3: LIGO III Cryosystem
ISI Stage 2
124 K Silicon test mass
…
Heat shield at 80 K
Notes: cooled with a radiative heat shield mounted to ISI

## Slide 4: LIGO III Cryosystem
Room temperature
ISI Stage 2
124 K Silicon test mass
…
Heat shield at 80 K
Notes: Everything else is kept at room temperature

## Slide 5: LIGO III Cryosystem
Room temperature
ISI Stage 2
Vacuum flange
Cold link
124 K Silicon test mass
…
Heat shield at 80 K
Notes: The shield is cooled with a long cold link that weaves through the stages of the ISI on its way to the vacuum flange

## Slide 6: LIGO III Cryosystem
Room temperature
Heat shield at 80 K
ISI Stage 2
Vacuum flange
Cold link
10 m
124 K Silicon test mass
…
Beam tube shield at 80 K
Notes: The laser beam passes through a 10 m long beam tube heat shield that is rigidly attached to the main shield.

## Slide 7: LIGO III Cryosystem
Room temperature
Heat shield at 80 K
ISI Stage 2
Vacuum flange
Cold link
10 m
124 K Silicon test mass
…
Beam tube shield at 80 K
Challenge – integrating cryo and seismic
  Seismic shorts
  cold link modes
  Long heat path
  Thermal drifts
Notes: There are a number of challenges to overcome to make this work.
Such as integrating the cryogenic and seismic systems. For example the cold link will introduce seismic shorts and vibrational modes….

## Slide 8: LIGO III Cryosystem
Room temperature
Heat shield at 80 K
ISI Stage 2
Vacuum flange
Cold link
10 m
124 K Silicon test mass
…
Beam tube shield at 80 K
Challenge – integrating cryo and seismic
    Seismic shorts
    cold link modes
    Long heat path
    Thermal drifts
Challenge – balance 10 m shield from suspended platform
Notes: Also, there is the challenge of balancing a 10 m beam tube shield from a suspended platform.
So I am going to propose a different approach, where we solve these issues by separating the overall system into dedicated pieces.

## Slide 9: Actively controlled shield (ETM)
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Cryo pump
124 K test mass
Notes: And here is a sketch of that approach showing the End station vacuum envelope.
Here’s the test mass inside the BSC.
By the way, I plan to spend at least half this talk on just this figure. I’ll point out the various features 1 by 1.

## Slide 10: Actively controlled shield (ETM)
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Cryo pump
124 K test mass
80 K heat shield and lower structure
Notes: Here’s the heat shield surrounding the lower suspension as before.

## Slide 11: Actively controlled shield (ETM)
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Cryo pump
124 K test mass
80 K heat shield and lower structure
Blade springs
Notes: However, you’ll note that the shield is attached to stage 0, rather than stage 2, and it is suspended from springs.
This means the issue of integrating the cryo and seismic systems is solved by physically decoupling them.

## Slide 12: Actively controlled shield (ETM)
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Cryo pump
124 K test mass
Cold link
80 K heat shield and lower structure
Blade springs
Notes: One immediate benefit of this, the heat transfer can be done with a short and simple cold link that goes right to the vacuum wall.

## Slide 13: Actively controlled shield (ETM)
Stage 2
St0
St0
124 K test mass
Cold link
Gate Valve
z
80 K heat shield and lower structure
Gate Valve
Cryo pump
Sensors between heat shield and stage 2
Blade springs
Notes: However, a complication of hanging the heat shield from stage 0, is that it may not be isolated enough for scattered light. So it will need active control.
To do this, you would put sensors between the shield and stage 2, which is well isolated.

## Slide 14: Actively controlled shield (ETM)
Stage 2
St0
St0
124 K test mass
Cold link
Actuators between stage 0 and heat shield
Sensors between heat shield and stage 2
Gate Valve
z
80 K heat shield and lower structure
Gate Valve
Cryo pump
Blade springs
Notes: You’d then have actuators between stage 0 and the heat shield.
The control would then lock the heat shield to stage 2, without actually touching it.

## Slide 15: Actively controlled shield (ETM)
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Cryo pump
124 K test mass
Cold link
80 K heat shield and lower structure
80 K baffled beam tube shield
10 m
Actuators between stage 0 and heat shield
Sensors between heat shield and stage 2
≈ 900 mm dia
Blade springs
Notes: Another feature of this approach is that the issue of balancing a long beam tube shield from a suspended platform, is avoided again, by physical decoupling.
Here the beam tube shield is not connected to the main shield at all, it’s physically separated with some gap and supported by the beam tube instead.
We can get away with this by maximizing the its diameter and length. Here it is basically making use of all the available space.
You’ll also note, that this beam tube shield incorporated angled baffles along its length. These serve both to block scattered laser light, as well as scattered warm radiation leaking through the opening.
These baffles by the way, are very similar to those used by KAGRA, which is not a coincidence.

## Slide 16: Actively controlled shield (ETM)
Stage 2
St0
St0
Gate Valve
z
Gate Valve
10 m
Cryo pump
124 K test mass
Cold link
80 K heat shield and lower structure
ACB in suspended HS
Actuators between stage 0 and heat shield
Sensors between heat shield and stage 2
≈ 900 mm dia
80 K baffled beam tube shield
Blade springs
Notes: Speaking of baffles, thing we can actually simplify from aLIGO is the removal of the ACB suspension. Here the ACB is simply integrated into the suspended heat shield.

## Slide 17: Actively controlled shield (ETM)
Stage 2
St0
St0
Gate Valve
z
Gate Valve
10 m
Cryo pump
124 K test mass
Cold link
80 K heat shield and lower structure
ACB in suspended HS
Room temp upper structure, disconnected from cold lower
Actuators between stage 0 and heat shield
Sensors between heat shield and stage 2
≈ 900 mm dia
80 K baffled beam tube shield
Blade springs
Notes: The last feature in this figure is the warm upper structure of the quad, which is physically disconnected from the lower structure. It’s not clear here, but the lower quad structure is meant to be a part of the heat shield.
Now, it may seem scary at first to suspend the lower structure. But keep in mind that the aLIGO structure is also suspended because its on the ISI. If you ever get the chance to work on a suspension when the ISI is free this immediately becomes obvious as soon as you touch it.
The only difference here is that the 2 structures are suspended from different places.
I’ll speak about a bit more about this later.

## Slide 18: Pros/cons of separate cryo and seismic
Pros
  No seismic isolation impact
  Shorter heat transfer path
  Much greater choice of heat transfer methods
  Allows more science payload (bigger test masses)
Cons
  Requires another active control system with many additional sensors and actuators per BSC
Notes: …
We can put more mass into our suspensions.
Because the ISI has a finite payload, and because it no longer has to support the cryogenics, more payload is available for the suspension system.
Of course we do pay for all this by having yet another active control system with a full compliment of sensors and actuators.

## Slide 19: To make 1 structure or 2?
 | Temperature of cold part | Thermal stress + alignment of warm part | Vibrational mode frequencies | Damping of vibrational modes | Relative complexity of construction
1 structure |  |  |  |  | 
2 structures: warm & cold |  |  |  |  | 
Good
Fair
Risky
Show stopper
Note:
For 1 structure, the heat shield is not integrated. It cools the lower structure radiatively, along with the suspension.
For 2 structures, the heat shield is fully integrated into the lower structure as 1 unit.
- in the case of a suspended heat shield
Notes: So now I’d like to address the question of separating the cold lower structure from the upper.
…
So what you see is that in the first case, these challenges become difficult because they are all competing with each other.
As has become the theme of this talk, the second case simplifies these challenges by physically decoupling them.

## Slide 20: To make 1 structure or 2?
 | Temperature of cold part | Thermal stress + alignment of warm part | Vibrational mode frequencies | Damping of vibrational modes | Relative complexity of construction
1 structure |  |  |  |  | 
2 structures: warm & cold |  |  |  |  | 
?
Good
Fair
Risky
Show stopper
Note:
For 1 structure, the heat shield is not integrated. It cools the lower structure radiatively, along with the suspension.
For 2 structures, the heat shield is fully integrated into the lower structure as 1 unit.
- in the case of a suspended heat shield
?

## Slide 21: Conceptual LIGO III SolidWorks Sketches

## Slide 22
aLIGO LLO Y End SolidWorks Model
5 m
10 m
5 m

## Slide 23
ISI
LIGO III End Station Conceptual Model
Gate valve
Gate valve

## Slide 24
ISI
Stage 0
LIGO III End Station Conceptual Model
Gate valve
Gate valve

## Slide 25
ISI
Stage 0
LIGO III End Station Conceptual Model
Gate valve
Gate valve
Suspended heat shield / lower quad structure 80 K

## Slide 26
ISI
Stage 0
LIGO III End Station Conceptual Model
Gate valve
Gate valve
Suspended heat shield / lower quad structure 80 K
Transmitted
beam shield

## Slide 27
ISI
Stage 0
LIGO III End Station Conceptual Model
Gate valve
Gate valve
Suspended heat shield / lower quad structure 80 K
Transmitted
beam shield
Arm Cavity Baffle integrated
with suspended heat shield, 80 K

## Slide 28
ISI
Stage 0
LIGO III End Station Conceptual Model
Gate valve
Gate valve
Suspended heat shield / lower quad structure 80 K
Transmitted
beam shield
Arm Cavity Baffle integrated
with suspended heat shield, 80 K
Beam tube shield mounted to beam tube, 80 K

## Slide 29
ISI
Stage 0
Arm Cavity Baffle integrated
with suspended heat shield, 80 K
Suspended heat shield / lower quad structure 80 K
Beam tube shield mounted to beam tube, 80 K
LIGO III End Station Conceptual Model
Cryo pump, cools this
section of shield,
and maybe everything else
Gate valve
Gate valve
Transmitted
beam shield

## Slide 30
34 m
2 m
aLIGO LLO corner station SolidWorks model

## Slide 31: Conclusions: Work/info needed for a low vibration cryo system
Stage 2
St0
St0
Gate Valve
z
Gate Valve

## Slide 32: Conclusions: Work/info needed for a low vibration cryo system
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Beam tube shield
Backscatter of coatings (BRDF)
Heat leak simulation with ray tracing.

## Slide 33: Conclusions: Work/info needed for a low vibration cryo system
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Beam tube shield
Backscatter of coatings (BRDF)
Heat leak simulation with ray tracing.
Optical coating emissivity

## Slide 34: Conclusions: Work/info needed for a low vibration cryo system
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Beam tube shield
Backscatter of coatings (BRDF)
Heat leak simulation with ray tracing.
Optical coating emissivity
Transmitted beam?

## Slide 35: Conclusions: Work/info needed for a low vibration cryo system
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Beam tube shield
Backscatter of coatings (BRDF)
Heat leak simulation with ray tracing.
Optical coating emissivity
Transmitted beam?
Getting optical levers through shield?

## Slide 36: Conclusions: Work/info needed for a low vibration cryo system
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Beam tube shield
Backscatter of coatings (BRDF)
Heat leak simulation with ray tracing.
Optical coating emissivity
Transmitted beam?
Getting optical levers through shield?
How to handle thermal drifts of
Stops
Sensors
fibers

## Slide 37: Conclusions: Work/info needed for a low vibration cryo system
Stage 2
St0
St0
Gate Valve
z
Gate Valve
Beam tube shield
Backscatter of coatings (BRDF)
Heat leak simulation with ray tracing.
Optical coating emissivity
Transmitted beam?
Getting optical levers through shield?
How to handle thermal drifts of
Stops
Sensors
fibers
Demonstrate an active cryo shield will work

## Slide 38: Stanford Active Heat Shield Experiment

## Slide 40
Stage 1
Stage 2
Stage 0 spring post

## Slide 45
6 OSEMs between shield and table

## Slide 46
2 coil actuators and 2 witness geophones in each of the 3 corners
6 OSEMs between shield and table

## Slide 47
2 coil actuators and 2 witness geophones in each of the 3 corners
6 OSEMs between shield and table
Optic suspended from stage 2 with a warm blade spring

## Slide 48
Construction well underway!
Photo taken 12 March 2015

## Slide 49: BackUps

## Slide 50
LIGO III end station back view model
Suspended heat shield / lower quad structure, 80 k
BSC floor, room temp
Upper quad structure, room temp
Stage 0, room temp
Beam tube shield mounted to beam tube, 80 K
Transmitted
beam shield, 80 K
ISI
Heat shield blade springs, room temp

## Slide 51
Vibrational modes of support structure

## Slide 52: Heat Shield Requirements
Beam tube length
Scattered light (much uncertainty to overcome)

## Slide 53: Radiation leak from Beam Tube

## Slide 54: Light scattering noise estimates

## Slide 55: Scattered light modeling for shield
Linear regime – differential displacement between cavity and scattering surface much less than light wavelength. Only worry about > 10 Hz
Nonlinear regime – differential displacement comparable to or greater than a wavelength. Upconversion is an issue, must worry about large amplitude low frequency motion.

## Slide 56: Linear regime scattered light References
T940063 - Noise due to backscatter off baffles, the nearby wall, and objects at the far end of the beam tube; and recommended actions – Flanagan and Thorne.
  This is a useful reference for the basic theory and derivations.
T1300354 - Scattered light noise due to the ETM coating ripple – Fritschel and Yamamoto
  Good example of applying the equations in T940063
T1300332 - Noise from baffle motion with the current ETM coating – Rai
  Complements the example of T1300354

## Slide 57: Nonlinear regime scattered light References
P1100117 - The impact of upconverted scattered light on aLIGO – Ottaway, Fritschel, and Waldman

## Slide 58
Ref T1000747-v4, pg 41
in aLIGO

## Slide 59: Linear scattered light noise estimates
Small angle scatter across beam tube length – beam tube parameters in E940002 and P990007
Parameters of calculation following notation in T1300354
Calculated heat shield displacement requirement from small angle scatter

## Slide 60: Linear scattered light noise estimates
Large angle scatter in local heat shield – assuming 150 W of local scatter out of 3 MW cavity
Parameters of calculation following notation in T1300354
Calculated heat shield displacement requirement from large angle scatter

## Slide 61
T0900312

## Slide 62
T0900312
10 Hz heat shield scattered light requirement

## Slide 63
T0900312
10 Hz motion with 3 Hz suspension
10 Hz heat shield scattered light requirement

## Slide 64
T0900312
OSEM noise
10 Hz motion with 3 Hz suspension
10 Hz heat shield scattered light requirement

## Slide 65: KAGRA Cryo System

## Slide 66
KAGRA’s cryogenic system
(pulse tube)
Yusuke Sakakibara et al 2014 Class. Quantum Grav. 31 224003
http://iopscience.iop.org/0264-9381/31/22/224003/

## Slide 67
KAGRA beam tube heat shield
Quote from text pages 2-3: “In CLIO, thermal radiation through the duct shield (described in section 4 ) was 1000 times larger than our expectation because we had neglected reflections from the duct shield. To
reduce this heat load, donut-shaped structures (called baffles) were introduced.”

## Slide 68: Annealed Pyrolitic Graphite (APG)
K core technology from thermacore
~ 3 times the conductivity of copper, in plane, but magnetic

## Slide 69
http://www.thermacore.com/thermal-basics/advanced-solid-conduction.aspx
See a brief video introhttps://www.youtube.com/watch?v=kMD0GUZmoy0
The graphite can be made flexible by making it into thin strips
Vacuum compatible, at least to NASA specs for outgassing
Conductive peak around 120-150 K
The graphite is highly diamagnetic
Annealed Pyrolitic Graphite (APG)
Cu 99.999%

## Slide 70: Shorter shield with cryo baffle
Stage 2
St0
St0
80 K suspended cryo baffle
124 K test mass
Cold link
Actuators between stage 0 and heat shield
Sensors between heat shield and stage 2
Gate Valve
Oplevs: require steering mirrors or openings to enter shield
Room temp upper structure, disconnected from cold lower
Arm cavity baffle part of suspended HS
80 K, non suspended beam tube shield
80 K heat shield and lower structure

## Slide 71: Cold SUS structure configurations
 | Temperature of cold part | Thermal stress + alignment of warm part | Vibrational mode frequencies | Damping of vibrational modes | Relative complexity of construction
1 structure |  |  |  |  | 
2 structures: warm & cold |  |  |  |  | 
Cold suspended from warm |  |  |  |  | 
Low freq sus modes
Good
Fair
Risky
Show stopper

## Slide 74
BSC ISI Stage 0-1 lockers - D1000854
Something like this could be used to limit the suspended heat shield / lower quad structure range of motion. The design makes it impossible for the suspension to fall in the event of a wire or spring failure.
Stage 1
Stage 0

## Slide 75
Possible arrangement of lower-structure-to-upper-structure lockers considering thermal contraction
Top view of lower structure (square cross-section). Thermal contraction occurs along an unconstrained DOF of the lockers, for a spatially uniform lower structure temperature. The clearance in the lockers will set a requirement on the maximum thermal gradient in the structure.
Warm dimensions
Cold dimensions

## Slide 76: How much cooling is lost if the shield is warmer than 80 K?