## Slide 1
State observers and Kalman filtering
High performance vibration isolation systems
Prof.dr. J.F.J. van den Brand
GWADW, May 19, 2015
jo@nikhef.nl

## Slide 2
Multi-stage attenuation systems
Bench low frequency control
  Mark Beker
    Paper, see:
    http://www.nikhef.nl/pub/services/biblio
/theses_pdf/thesis_M_G_Beker.pdf
  Vertical DOF

## Slide 3
LISA
Least squares
  Minimizes the sum of squares of the errors
  Has no “knowledge” of the system
Wiener filter
  x[n] = s[n] + w[n] -> “estimate s[n] so as to minimize the error”
  Stationary processes – The statistical properties of the inputs don’t change in t
  Causal, length grows, (generally) non-recursive
  For discrete samples reduces to least squares solution
Kalman filter
http://www.ws.binghamton.edu/fowler/fowler%20personal%20page/EE522_ﬁles/EECE%205
Generalization for Wiener filter to non-stationary processes – The signal is
characterized by a dynamical model
Recursive – don’t need to re-evaluate all data at each step
Uses prior knowledge of the system
  System is described by state vector x (unobservable)
  State can be estimated based on ẍ previous data z and model
  Requires a dynamic (state space) model
! ["]
2
!ˆ[5]
1
3 4 5
"
Wiener vs Kalman filtering

## Slide 4
Eric Hennes
4
IP leg modes
Where needed passive eddy current dampers can be used to lower Q-factor of higher order resonances
1.6 Hz
Finite element models used to identify all modes
of the system

## Slide 5
Non-rigid leg modes
Higher order GAS modes
84 Hz
252 Hz
340 Hz
357 Hz
Finite element model: Higher order modes

## Slide 6
Simulated performance
Vertical transfer function

## Slide 7
Vertical to horizontal coupling will dominate performance above 10 Hz
Simulated performance
Horizontal transfer function

## Slide 8
Simulated performance
Horizontal to tilt coupling

## Slide 9
LISA
State space model
  Imperative to have an accurate model
FEA
  Detailed description of the system
  Tune model to measured transfer functions
Optimal control: state observer

## Slide 10
Advanced Virgo
Questions?

## Slide 11: System identification with bayes theorem and non gaussian distributions
G. Cella
We will take each single bit of information
If it does not cost too much!

## Slide 12: Three basic rules
Law of total probability
Bayes’ theorem
The product of two (multivariate) gaussian distributions is proportional to a (multivariate) gaussian distributions:

## Slide 13: A simple example: a suspension (pendulum) with uncertain length
Description in the phase space:
We measure the state (position and velocity). Maybe with some measurement error.
We enlarge the space, adding the unknown parameter
We model our ignorance with a joint probability distribution
We assume we have a good model…
…which can be used to calculate the time evolution (RULE 1 at work)

## Slide 14: A simple example: a suspension (pendulum) with uncertain length
Description in the phase space:
We measure the state (position and velocity). Maybe with some measurement error.
We enlarge the space, adding the unknown parameter
We model our ignorance with a joint probability distribution
We assume we have a good model…
…which can be used to calculate the time evolution (RULE 1 at work)

## Slide 15: A simple example: a suspension (pendulum) with uncertain length
Description in the phase space:
We measure the state (position and velocity). Maybe with some measurement error.
We enlarge the space, adding the unknown parameter
We model our ignorance with a joint probability distribution
We assume we have a good model…
…which can be used to calculate the time evolution (RULE 1 at work)

## Slide 16: A simple example: a suspension (pendulum) with uncertain length
Description in the phase space:
We measure the state (position and velocity). Maybe with some measurement error.
We enlarge the space, adding the unknown parameter
We model our ignorance with a joint probability distribution
We assume we have a good model…
…which can be used to calculate the time evolution (RULE 1 at work)

## Slide 17: A simple example: a suspension (pendulum) with uncertain length
Description in the phase space:
We measure the state (position and velocity). Maybe with some measurement error.
We enlarge the space, adding the unknown parameter
We model our ignorance with a joint probability distribution
We assume we have a good model…
…which can be used to calculate the time evolution (RULE 1 at work)

## Slide 18: A simple example: a suspension (pendulum) with uncertain length
This is no more a gaussian distribution (in general). How to parameterize it?
  Each horizontal line is a gaussian distribution
  Gaussian misture can be a good representation:
Now, we measure the position and the velocity again, and we use RULE 2 and RULE 3

## Slide 19: A simple example: a suspension (pendulum) with uncertain length
This is no more a gaussian distribution (in general). How to parameterize it?
  Each horizontal line is a gaussian distribution
  Gaussian misture can be a good representation:
Now, we measure the position and the velocity again, and we use RULE 2 and RULE 3

## Slide 20: This could have several applications
Tracking the Pound Drever signal
  Identify optical parameters
  Improve locking
Systems with nonlinear dynamics
  Radiation pressure
Adjusting noise models:
Selection strategy needed
  Elements with low weight must be removed
  Gaussian misture not necessarily a good representation in all cases

## Slide 21: Suspension Parameter Estimation for State Space Models Brett Shapiro GWADW – 19 May 2015

## Slide 22: State space from physical values
Inertia
Stiffness
Length
MATLAB
Energy methods convert
parameters to matrices
Gradient of potential energy
Gradient of kinetic energy
See T020205
Notes: The state space models are parameterized by the physical values, such as mass, stiffness, and length. A Mathematica script solves the state space matrices in terms of these parameters using energy the gradients of the suspension kinetic and potential energy.
Since most of our analysis tools are in actually in MATLAB, that solution is then exported to MATLAB, along a with a parameter file listing listing all the parameter values. Finally, a script in MATLAB produces the actual state space model.

## Slide 23: Parameter Estimation Algorithm
J = Jacobian matrix of error gradients wrt parameters
e = % error between modeled and measured resonant frequencies
p = parameter value (mass, stiffness, length, etc)
Mismatch between model and measurement
Notes: Once the state space model is in MATLAB, we still have to fit the parameter values to the measured data. Critical to this fitting algorithm is the Jacobian matrix. This matrix is just a list of the gradients of the model error with respect to the model parameters like mass and stiffness. As before the errors are given by the resonant frequencies.
The gradients are calculated numerical, simply by moving each parameter a small amount and measuring how much the error changes.

## Slide 24: Parameter Estimation Algorithm
J = Jacobian matrix of error gradients wrt parameters
e = % error between modeled and measured resonant frequencies
p = parameter value (mass, stiffness, length, etc)
Gauss-Newton algorithm – an modification of Newton’s method (2nd order)
Update the parameter list, p, with step size α
Update the descent direction d with the psuedo-inverse of J.
References: T1000458 and “Selection of Important Parameters Using Uncertainty and Sensitivity Analysis”, Shapiro et al.
Notes: Once we have the Jacobian, we can apply a fitting algorithm. The suspensions use a Gauss-Newton algorithm, which is an approximation of Newton’s method.
In this method, the descent direction is given by the psuedoinverse of the Jacobian matrix. For reference, gradient descent would be the same except it would use the transpose.

## Slide 25: Before Parameter Estimation
Notes: So using this algorithm, we can adjust update the model that so it goes from one a mismatch like this…

## Slide 26: After Parameter Estimation
Notes: To one like this.