## Slide 1
PSL Presentation at UF
September 4th, 2015
GM
Source Material:
  G1100452
  Optics Express, Vol 20(10), 10617 (2012)
  Dissertation presentation Jan Pöld (AEI, 2014)
  G1100837 (PSL Training Session, incl. movies)

## Slide 2
Advanced LIGO
EOM
Laser
200W
Cavity-enhanced,
dual-recycled Michelson interferometer
125W
~600kW

## Slide 3
Advanced LIGO
EOM
Laser
4km long Cavities

## Slide 4
Advanced LIGO
EOM
Laser
Short MI:
4 to 5m long
~4cm difference

## Slide 5
Advanced LIGO
EOM
Laser
~55m power recycling cavity
~55m signal recycling cavity

## Slide 6
Why this design?
MI:
  optimum geometry (∂l-meter)
  equal arms = common mode rejection of noise
Cavities in arms
  amplify phase shift
    Trade-off between gain and BW
Power Recycling
  builds up power
  cleans up mode
Signal Recycling
  builds up signal
  Trade-off between gain and BW
∂l(f)
Log f
MI
MI+Cav
MI+Cav+PR
MI+Cav+PR+SR
Peak frequency tunable
(SR mirror position)
Advanced LIGO

## Slide 7
Displacement Sensitivity: Shot Noise only
Power Recycling:
MI-Phase sensitivity:
Arm cavity gain:
In length and strain:
Low pass filter of cavity:
Advanced LIGO: Back on the envelope

## Slide 8
Advanced LIGO: Back on the envelope
Shot Noise

## Slide 9
Advanced LIGO: Back on the envelope
Displacement
Noise
Displacement Noise:
Seismic motion
Environmental vibrations
Thermal noise
  Coating
  Substrate
  Suspension
Radiation Pressure Noise
  Fundamental (Quantum)
  Technical
    Unbalanced Arms
Newtonian or Gravity gradient noise

## Slide 10
Advanced LIGO
EOM
Laser
200W
125W
~600kW
Key systems:
PSL
IO
Core Optics
Suspensions
SEI
Main IFO
  Mode matching
  ISC, ASC
Output Optics
TCS
AOS
Photon calibrator
…

## Slide 11
PSL
PSL: Prestabilized Laser System
Designed, developed, tested, installed by
Albert Einstein Institute, Hannover, Germany
Development Lead: Benno Willke
PSL-Lead at project-level: Peter King
PSL-Officer at LLO: Matt Heintze

## Slide 12
PSL
Requirements:
  Stand alone Laser system
  Stabilized system
Requirement flow down:
  Top level:
      125W TE00 injected into IFO spatial mode
          < 5W in higher order modes as defined by IFO
              Saturates detectors
              Creates stray light

## Slide 13
PSL
Requirements:
  Stand alone Laser system
  Stabilized system
Requirement flow down:
  Top level:
      125W TE00 injected into IFO spatial mode
      Laser frequency noise relative to CARM
          relative to CARM

## Slide 14
PSL
Requirements:
  Stand alone Laser system
  Stabilized system
Requirement flow down:
  Top level:
      125W TEM00 injected into IFO spatial mode
      Laser frequency noise relative to CARM
      Laser Amplitude noise = Relative Intensity Noise (RIN)

## Slide 15
PSL
Requirements:
  Stand alone Laser system
  Stabilized system
Requirement flow down:
  Top level:
      125W TE00 injected into IFO spatial mode
      Laser frequency noise relative to CARM
      Laser Amplitude noise
measured at input of IFO at 125W input power

## Slide 16
PSL
Requirements:
  Stand alone Laser system
  Stabilized system
Requirement flow down:
  Top level:
      125W TE00 injected into IFO spatial mode
      Laser frequency noise relative to CARM
      Laser Amplitude noise = Relative Intensity Noise (RIN)
      Beam pointing = beam jitter
        Maintain alignment into IFO (active or passive)

## Slide 17
PSL
Requirements:
  Stand alone Laser system
  Stabilized system
Requirement flow down:
  Top level
  ‘Propagate’ back through IO to PSL
      IO filters Laser noise
        reduces requirements of stand-alone laser
  IFO and IO provide control signals to suppress laser noise
      Requires appropriate actuators within PSL (and IO)

## Slide 18
PSL
Requirements:
  Stand alone Laser system
    Power output: Deliver 165W TEM00 to IO
    <5% of power in higher order modes

## Slide 19
PSL
Requirements:
  Stand alone Laser system
    Power output: Deliver 165W TEM00 to IO
    <5% of power in higher order modes
    laser frequency noise

## Slide 20
PSL
Requirements:
  Stand alone Laser system
    Power output: Deliver 165W TEM00 to IO
    <5% of power in higher order modes
    laser frequency noise
    RIN
2nd-Stage: Signal from IFO
1st-Stage: PSL internal

## Slide 21
PSL
Requirements:
  Stand alone Laser system
    Power output: Deliver 165W TEM00 to IO
    <5% of power in higher order modes
    laser frequency noise
    RIN
    Laser frequency drift: < 100kHz over 100s
    Laser power drift: < 5% over 24h

## Slide 22: advanced LIGO laser - layout
2W
35W
180W
165W in TEM00
eLIGO laser
4

## Slide 23: advanced LIGO laser - layout
2W
35W
180W
165W in TEM00
eLIGO laser
4
NPRO: Non-planar ring oscillator
Ultra-stable master (passive)
Laser crystal: Nd:YAG
Diode laser pumped (808nm)
~10kHz/rtHz @ 1Hz
Same lasers we have in lab!
808nm

## Slide 24: advanced LIGO laser - layout
2W
35W
180W
165W in TEM00
eLIGO laser
4
EOM:
Phase modulation
Phase correction
AOM:
Power stabilization
FI:
Suppress back reflection
808nm

## Slide 25: eLIGO laser
2W
35W
180W
165W in TEM00
eLIGO laser
4
808nm

## Slide 26: eLIGO Laser System
4 stage Nd:YVO4
water cooled
fiber coupled pump diodes
pump power 4 x 32 W
seed power 1.7 W
output power 35 W
pump light pickups
laser pickups
temperature monitoring
Amplifier
Pump
power

## Slide 27: eLIGO Laser System
4 pump diodes
water cooled heat sink
temperature interlocks
diode power supplies
peltier driver boards with power supply
Beckhoff interface
Diode Box
Pump diodes
located in different room.
Fiber coupled

## Slide 28: advanced LIGO laser - layout
2W
35W
180W
165W in TEM00
eLIGO laser
4
EOM:
Phase modulation
Phase correction
AOM:
Power stabilization
FI:
Suppress back reflection
808nm

## Slide 29
PSL

## Slide 30
PSL
eLIGO Laser =
aLIGO front end
Nd:YVO4 crystals
pumped by 808nm diode lasers

## Slide 31
PSL
Injection locked ring laser, forced to emit on the injected laser frequency
  laser frequency identical to master laser
  Pumped by four ~200W diode laser arrays, fiber coupled

## Slide 32
PSL
Ring laser:
‘Point’ design. Requires certain pump power to create thermal lens in Nd:YAG rods to stabilize laser resonator.
Water-cooled
Laser system can only operate at full power
  Current low power operation (25W input at PRM) works w/o high power oscillator (slave laser)!

## Slide 33
PSL
Auxiliary parts of PSL:
Diagnostic Breadboard (see Paul for details)
Pre-mode cleaner: Bow tie cavity to spatially filter laser field
1st Stage intensity stabilization system (ISS)
  Sensor prior to Input Optics!!

## Slide 34
PSL
DBB:
Mode Analyzer Cavity
Power monitor
Pointing monitor (QPD1&2)
  with respect to PMC
ISS:
PDA: Creates error signal
PDB: Out of loop signal
QPD to maintain alignment
  PD sensitivity depends on position on active element

## Slide 35
PSL
High power laser beam:
Fairly bad spatial mode quality (thermal distortions …)
  incl. beam jitter
Pre-Mode Cleaner (PMC) filters spatial distortions
  Locked to laser frequency via PDH signal
To Ref.Cav.
To IO
To ISS in PSL

## Slide 36
PSL
Reference Cavity:
Glass cavity in thermally isolated vacuum tank
1st Frequency stabilization system
Offset lock:
  SB generated in AOM, locked to cavity
  Sideband frequency tunable

## Slide 37
PSL
Sensors external to PSL:
Frequency:
  Input Mode Cleaner (IMC)
  Common Arm Cavities (CARM)
Intensity:
  2nd ISS uses signal in HAM2 after IO

## Slide 38
PSL
four photodiodes per detector
  In-loop
  Out of loop
each aligned to lowest pointing coupling
50mA photocurrent per photodiode
in dust-free environment with reduced pointing fluctuations
installed in HAM 2

## Slide 39
PSL
Sensors external to PSL:
Frequency:
  Input Mode Cleaner (IMC)
  Common Arm Cavities (CARM)
Intensity:
  2nd ISS uses signal in HAM2 after IO
General issues with PSL:
Beam pointing from PSL table (out of IO) might be higher than expected due
    Acoustic noise and water flow shakes IO periscope
2nd ISS loop not yet 100% functional
    Sees also stray light from IOT2R
    Needed for high power operation only (not yet)
…