## Slide 1: O1 DARM Loop Design Comparisons and Critiques
J. Kissel, for the ISC and Calibration Teams

## Slide 2: DARM Open Loop Gain TF (Big Picture)
H1 has notched WAY more features
H1 needs more gain at low frequency
Roughly the the same UGF
Good compromise on aggression of filtering

## Slide 3: DARM OLGTF (UGF Zoom)
L1 UGF: 56.6 [Hz]
H1 UGF: 40.1 [Hz]
L1 UGF: 40.3 [Hz]
H1 Phase Margin: 42.2 [deg]
Good compromise on aggression of filtering

## Slide 4: DARM Open Loop Gain TF
1 / (1+G)
H1 has a couple of orders of magnitude less suppression around the microseism
H1 Max Suppression: 1.5
L1 Max Suppression: 1.7
Both have plenty of gain margin

## Slide 5: Actuator Strength Comparison

## Slide 6: Actuator Strength Comparison
Small(-ish?) OOPS:
(L1 Forgot to include all possible harmonics in model)
Different ESD Bias Sign,
Different PUM COILOUTF convention  PUM and TST have different signs

## Slide 7: Actuator Comparison (Hierarchy Filters)
Both sites have a mish-mash of “offloaded” vs. “distributed” hierarchy filters due to staggered design
L1 does more loop shaping in the DARM bank (because of all the notching done at H1)
Note the difference in HF cut-off filter for all stages…

## Slide 8: The DARM Filter and Sensing Function
Digital gains (and a sign) are distributed differently on the sensing side,
so DARM filter gain and sign compensate, otherwise pretty similar…
But because of the different design choices, with frequency response and gains all over the place, tough to get a feel for the loop shaping from just one filter or plot
H1 boosts LF in the DARM bank
actual optical gain: ~3 [mA/pm] at both sites

## Slide 9: L1 Actuator Authority (Big Picture)
“Strength” = from DRIVEALIGN OUT to Test Mass Displacement
“Authority” = from LOCK IN to Test
Mass Displacement
Authority re-mathed to show it as a Distributed system, so “cross-over” frequencies mean something
L1 does all their LF boosting in the actuator filters
Just a bit of light notching,
not too aggressive of a HF cut-off

## Slide 10: L1 Actuator Authority (X-over Zoom)
PUM / TST
Cross-over: 15 [Hz]
UIM/PUM
Cross-over: (Ill-defined, but PUM is rolled off by) 0.45 [Hz]
Cross-over stability pretty good!
Cross-over stability kinda risky here, but it’s hard!

## Slide 11: L1 Actuator Authority (HF Roll-off Zoom)
PUM is nicely rolled off above cross-over, but there’s still some phase interaction that causes some icky wiggles in the total TF of the “super actuator”
some icky wiggles

## Slide 12: H1 Actuator Authority (Big Picture)
Shown to same scale as L1 on Slide 9
Don’t be alarmed: remember H1 does its boosting in the DARM bank (will show with DARM filter later)
Interesting: UIM Bounce and Roll notches aren’t as aggressive…
Loooooot of high-frequency notching, plus a ridiculous cutoff filter

## Slide 13: H1 Actuator Authority (X-over Zoom)
Shown to different scale from L1 on Slide 10
PUM / TST
Cross-over: 30 [Hz]
UIM/PUM
Cross-over: (Ill-defined, but PUM is rolled off by) 0.45 [Hz]
Similarly risky cross-over here, but it’s hard!

## Slide 14: H1 Actuator Authority (HF Roll-off Zoom)
YUCK.
PUM phase is still interacting with TST phase out to 300 Hz
Notches + HF Cut-off causes all sorts of nastiness.

## Slide 15: Authority Including DARM Filter (scaled by optical gain)
Looks pretty DARM clean!

## Slide 16: Authority Including DARM Filter (scaled by optical gain)
Even with DARM filter boost, there’s still lots more to go to get to L1’s level of boosting
Looks pretty DARM messy!

## Slide 17: Conclusions
H1 DARM Loop needs some tune-up and clean-up
  More boosting at low-frequency
  Better / simpler distribution filters
  Less notching?
Frequency response is splayed out everywhere at both sites, evident that “design” was staggered and piecemeal
  Both sites should consider consolidating, for easier analysis of performance

## Slide 18: Bonus Material: Calibration Parameter Time Dependence Clues of “real” IFO parameters changing -- confirmation from alternative measurements

## Slide 19: Comparison Between Relative ESD Actuation Strength
LHO aLOG 22991
Relative ESD Actuation Strength
Time
Aug
Sep
Oct
Nov
Tracked via PCAL
Tracked via Oplevs

## Slide 20: Comparison Between Relative Optical Gain Measurements
LHO aLOG 23147
Tracked via PCAL
Tracked via Arm Power
PCAL Estimation of the change in optical gain from 330 [Hz] PCAL lines
Arm Power (divided by PRM transmittion), normalized by the start of the lock stretch