## Slide 1: C02 Calibration Uncertainty Material For Review
Craig Cahillane for the Calibration Team
(edited by Jeff Kissel)

## Slide 2: Where’s the Original Source Material?
Craig has done all the work. Thanks Craig!
For the original source material, see LHO aLOG 26889 and LLO aLOG 25950
Results have been produced by
  aligocalibration/trunk/Runs/O1/Common/Scripts/Uncertainty/
  NumericalUncertaintyBudget.m
  Further instructions on locations and how to run the code can be found in comments to above aLOGs
Kissel was able to reproduce all plots from the aLOGs with a local checkout of repo.
Kissel’s plots (those not found in Craig’s aLOGs) are produced from text files attached to the aLOG, and plotted with
  aligocalibration/trunk/Common/Documents/G1601003_C02Review/plot_GW151225_uncertainty_forG1601003.m

## Slide 3: What’s new in C02 Uncertainty since GW150914
Now have Uncertainty for GW150914, LVT151012, and GW151226
  And they’re different on the level of ~5% / 5 deg
Now have plots where you can easily read off the “pair of numbers” to quote in papers.
  However, we continue to aggressively encourage search groups to fold all of our knowledge into future analyses
Scalar, time-dependent corrections (kappa_c, kappa_tst, and \kappa_pu) have been applied to h(t), but still impact the uncertainty.
  Informed by noise leftover from de-trending the time series of these parameters
  Fluctuations are a function of time, because SNR of CAL lines are a function of time
  Not large, but now included in overall statistical uncertainty
Time-dependent cavity pole remains uncompensated
  That means the systematic error (because the value of the pole is known) is time dependent
Plots showing the uncertainty evolution over the entire run instead of just at event times
  Spectrograms (systematic error, statistical uncertainty, maximum uncertainty & error)
  Percentile Plots (maximum uncertainty & error)
  Time series (of maximum uncertainty & error)
Eventually (but not yet): including 1-4.5 kHz data

## Slide 4: What do we need?
CBC / PE group needs a one-sentence statement about the uncertainty, in the usual “pair of numbers” format
  Boxing Day Event Paper (just at time of event; Dec 26, 2015 03:38:53 UTC)
  BBH Search Paper (For the all three events)
  Rates Statements (All of O1; focused on how Inspiral Range varies)
Frequency range needs for all of the above is now confirmed to be 20 – 1000 Hz
Current statement: (Boxing Day Paper, Lines 70-73) “The calibration is continuously monitored and measured to an uncertainty (1 σ) of less than 10% in amplitude and 10 degrees in phase [11].”

## Slide 5: GW151226 C02 Total Uncertainty and Error
Components of Systematic Error:
Time-independent model vs. measurement discrepancy
Uncompensated change in DARM coupled cavity pole
Frequency-independent Systematic Error in PCAL
Components of Statistical Uncertainty:
Weighted Uncertainty (i.e. coherence) from several frequency-domain transfer functions
Uncertainty in change in time-dependent parameters

## Slide 6: GW151226 C02 Total Uncertainty and Error
L1 Uncertainty is larger than H1 because of the limited number of measurements they were able to obtain
H1 error at high frequency is poorly understood, (More on this later…) but doesn’t significantly impact “CBC” or “event-like” frequency band
H1 error below 20 Hz is due to poorly understood deviation from flat sensing function (L1 doesn’t have enough low-freq data points to resolve it)
L1’s error below 20 Hz is due to poorly resolved frequency dependence of PUM stage (again, due to lack of low-freq measurement)

## Slide 7: GW151226 Maximum 1-s Error and Uncertainty
GW Event PRL’s don’t have the space to say – and/or
Searches and PE aren’t yet sophisticated enough to include – more than
A pair of frequency independent numbers “Uncertainty is less than XX% and YY deg.”
Take data from previous plot
Subtract 1.0 (to turn “relative correction factor” error into “additive systematic correction” error)
Take the absolute value of solid lines; (syst. error + stat. uncertainty) as well as (syst. error - stat. uncertainty)
Plot the maximum as a function of frequency
Find the maximum value (for magnitude and phase) over the frequency range of the search and parameter estimation

## Slide 8: GW151226 C02 Maximum 1-s Error and Uncertainty
 | 20-1000 Hz
H1 | 4.3% / 3.1 deg
L1 | 7.4% / 4.7 deg
This is the final answer for GW151226
Why is L1 larger than H1?
In brief:
PUM actuator: systematic errors between measurements at high freq
TST actuator: low freq outliers
Sensing function determined totally differently between sites
SEE APPENDIX B

## Slide 9: What about for all of O1?
Components of Systematic Error:
Time-independent model vs. measurement discrepancy
Uncompensated change in DARM coupled cavity pole
Frequency-independent Systematic Error in PCAL
Components of Statistical Uncertainty:
Weighted Uncertainty (i.e. coherence) from several frequency-domain transfer functions
Uncertainty in change in time-dependent parameters
This makes the systematic error time-dependent
This makes the statistical uncertainty time-dependent
We must at least make plots of how the uncertainty evolves as a function of time, to see if “less than 10% and 10 deg” holds for all data over the entire run.
The next pages walk through all of the plots that have helped us quantify this time dependence.

## Slide 10: Systematic Error for All of O1, L1
For L1:
Even though we’ve compensated for scalar systematic error, the remaining frequency dependent error (from the changing DARM coupled cavity pole) changes as a function of time.
For a given frequency, extreme of change is on the order of 3% / 2 deg at ~300 Hz from beginning to the end of run
Z, color axis range is limited to the max and min of value from 5 to 3000 Hz: [-3% to +5%] and +/-2 deg
Change in value is smaller…

## Slide 11: Systematic Error for All of O1, H1
Similar but worse story at H1
Even though we’ve compensated for scalar systematic error, the remaining frequency dependent error (from the changing DARM coupled cavity pole) changes as a function of time.
For a given frequency, extreme of changes are on the order of 3% / 2 deg at ~300 Hz from beginning to the end of run.
Changes from cavity pole are larger (over this frequency range) in H1 because the pole frequency is lower, and it varies more because alignment was more poorly controlled
5 to 3000 Hz Range is [-5% to 9%] and +/- 2.5 deg but the change is smaller

## Slide 12: Statistical Uncertainty for All O1, L1
Measurements of the time-dependent parameters are based on SNR of PCAL and ESD Calibration Lines
Sensitivity changes as a function of time  statistical uncertainty is a function of time
Worst at low frequency for L1, where we lost sensitivity throughout the run. At 30 Hz, varies also at the level of 3% / 2 deg.

## Slide 13: Statistical Uncertainty for All O1, H1
Measurements of the time-dependent parameters are based on SNR of PCAL and ESD Calibration Lines
Sensitivity changes as a function of time  statistical uncertainty is a function of time
At H1, variation is smaller and most prevalant at the DARM UGF, as the ESD actuation strength changed throughout the run (including BIAS flip in mid-October). At 50 Hz, varies also at the level of 0.5% / 1 deg.

## Slide 14: Maximum Statistical Uncertainty and Systematic Error as a Function of Time
Because both statistical uncertainty and systematic error are frequency dependent and a function of time – how do we convey this as a pair of numbers for all O1?
Calculate the maximum over time, and show spectrograms, time-series of a horizontal slice and frequency-dependent percentiles covering all time

## Slide 15: Maximum Stat. Unc. and Syst. Err., L1
Max Magnitude Uncertainty and Error Spectrogram, Time Series, and Percentile plots
(i.e. pg 7 as a function of time)
Because L1’s cavity pole doesn’t change much (better alignment control)
Uncertainty & Error are large, but quantifiably quite stable.
Only significant time-dependence is a trend due to \kappa_TST value.
Even though it’s corrected for, it still folds into uncertainty partial derivatives.
Now limited to 20 -1000 Hz!

## Slide 16: Maximum Stat. Unc. and Syst. Err., L1
99%
Phase [deg]
95%
68%
Center
Largest excursion is on Oct 10th (marked w/ green circle and arrow)
This is a result of L1 turning off linearization, and reducing the ESD bias voltage:
LLO aLOG 24573
Corrected for in h(t), but
Again, the value of \kappa_TST still plays into the uncertainty via partial derivatives
Now limited to 20 -1000 Hz!

## Slide 17: Maximum Stat. Unc. and Syst. Err., H1
H1’s has a lower-frequency (~341 Hz) and more dynamic cavity pole
Therefore the percentile bounds for the run are significantly different above cavity pole frequency
However, the deviations are sporadic, likely because of lock-to-lock differences in alignment
(Note the ylim range on time series is half that of L1)
Now limited to 20 -1000 Hz!

## Slide 18: Maximum Stat. Unc. and Syst. Err., H1
99%
95%
68%
Center
The phase shows the same story: the largest deviation is at the cavity pole frequency
Largest deviation is around Nov 14th, which had several problems with wind, TCS laser and RF45 noise, e.g.
LHO aLOG 23385
(Again, be weary of ylim range on time series – it’s half that of equivalent L1 plot)
Now limited to 20 -1000 Hz!

## Slide 19: Things Left to Do
Establish a pair of numbers for 20-1000 Hz region using maximum deviation plot for all of O1 DONE
  Actually nail down from search groups what frequency they want! (Still waiting to hear from Burst, CW, and Stochastic Groups)
Need to include 1-4.5 kHz data In Progress
Request to “think out of the box” for what we might not be accounting (never really) DONE
None of these to-do items impact review for GW151226.

## Slide 20: C02 Maximum 1-s Error and Uncertainty
 | H1 Reviewed, including T.Dep. Statistical Unc. | H1 Used in PE Runs (from EVNT aLOGs) | L1 Reviewed, including T.Dep. Statistical Unc. | L1 Used in PE Runs (from EVNT aLOGs)
GW150914 | 4.5% / 3.1 deg | 4.82% / 3.158 deg | 9.3% / 5.4 deg | 8.23% / 4.196 deg
LVT151012 | 4.5% / 3.1 deg | 4.19% / 2.667 deg | 9.6% / 5.6 deg | 8.32% / 4.283 deg
GW151226 | 4.3% / 3.1 deg | 4.22% / 2.71 deg | 7.4% / 4.7 deg | 6.88% / 3.573 deg
All O1 | 6.89% / 4.0 deg | (n/a) | 11.6% / 6.4 deg | (n/a)
Over a 20 – 1000 Hz frequency range:
Recall, PE group used numbers for EVNT aLOGs 11578, 11576, and 11580, which was before Craig corrected and implemented the median subtracted time-dependence statistical uncertainty
  “Using methods as described in [GW150914 CAL companion paper], the calibration uncertainty (1 sigma) in both detectors is better than 8% in amplitude and 5 degrees in phase at the time of GW151226.”

## Slide 21: Conclusions
Here’s the “final” (as usual grossly over-simplified) answer for GW151226:
Given the above frequency range, the calibration uncertainty still satisfies the “less than 10% and 10 deg” statement for all event and candidates (GW150914, LVT151012, and GW151226), but not for all of O1.
Landry, Kissel, and Vitale have agreed on
  “Using methods as described in [GW150914 CAL companion paper], the calibration uncertainty (1 sigma) in both detectors is better than 8% in amplitude and 5 degrees in phase at the time of GW151226.”
for Boxing Day Paper.
There is still more work to do to refine 1-4.5 kHz for other searches
All of O1 uncertainty is a function of time. We have plots to show how it evolves. We wait for discussion with search groups on how to fold this information into analysis (e.g. Rates group and BBH Paper).
 | 20-2000 Hz | 30-1000 Hz | 20-1000 Hz
H1 | 5.5% / 3.1 deg | 4.3% / 3.1 deg | 4.3% / 3.1 deg
L1 | 7.4% / 4.7 deg | 7.4% / 4.3 deg | 7.4% / 4.7 deg

## Slide 22: Appendix A: Overall C02 Uncertainty Plots for GW150914, LVT151012, and GW151226

## Slide 23: GW150914 C02 Total Uncertainty and Error

## Slide 24: LVT151012 C02 Total Uncertainty and Error

## Slide 25: GW151226 C02 Total Uncertainty and Error

## Slide 26: GW150914 C02 Maximum 1-s Error and Uncertainty

## Slide 27: LVT151012 C02 Maximum 1-s Error and Uncertainty

## Slide 28: GW151226 C02 Maximum 1-s Error and Uncertainty

## Slide 29: Appendix B: Why is L1 Uncertainty Larger than H1?

## Slide 30: Why is L1’s statistical Uncertainty Larger than H1’s? Let’s follow the Rabbit Down the Hole, taking GW151226 as the example…
 | 20-1000 Hz
H1 | 4.3% / 3.1 deg
L1 | 7.4% / 4.7 deg

## Slide 31: Why is L1’s Statistical Uncertainty Larger than H1’s?
TST Magnitude
TST Phase
Sensing
Magnitude
H1 Stat. Unc. Components
L1 Stat. Unc. Components
(Rel. Magnitude)2
(Phase [deg])2
5
10
15
20
25
100
102
101
PUM
Phase
(Rel. Magnitude)2
(Phase [deg])2
100
102
101
1
2
3
4
5
6
7
101
102
103
101
102
103
PUM & TST actuation, and function uncertainties are larger. Why?

## Slide 32: Why is L1’s Statistical Uncertainty Larger than H1’s? *NOT* because of less measurements!
Scatter doesn’t too different either!
So why?
Because L1 took data out to higher frequency, and the residual systematic error between measurements was not consistent
That means *overall* systematic error removed still is non-Gaussian and just taking “std” of residual-with-overall-systematic-removed is a poor estimate, an over estimate at best, of statistical uncertainty.

## Slide 33: Why is L1’s Statistical Uncertainty Larger than H1’s? Because of L1 PUM violin-mode systematics that aren’t modeled well.

## Slide 34: Why is L1’s Statistical Uncertainty Larger than H1’s? Compare against H1 PUM results which have much more Gaussian fluctuations.

## Slide 35: Why is L1’s Statistical Uncertainty Larger than H1’s? For the TST Stage, the L1 data have two issues
L1 TST Stage
Standard deviation of all (residual – systematic error) frequency points from all measurements is used as frequency-independent statistical uncertainty.
L1 Low-frequency outliers skew the standard deviation
L1 data taken over months, and not compensated for known actuation strength change. Makes measurement-to-measurement non-Guassian, which means std is not a good estimate of uncertainty
The low frequency outliers go out to 25% and 15 deg, doubling the standa deviation.
H1 measurements tightly grouped in time
L1 measurements spread over months

## Slide 36: Why is L1’s Statistical Uncertainty Larger than H1’s? Actuation Summary
Actuation Summary:
Standard deviation of all (residual – systematic error) frequency points is used as frequency-independent statistical uncertainty.
L1 TST and PUM have a factor of 2 larger uncertainty than H1 for different reasons:
  PUM because of high-frequency violin mode systematics between measurements at L1 that H1 just didn’t measure
  TST because L1 it has low frequency outliers which skew the standard deviation
  L1 TST also larger, because 4 measurements were taken over 4 months and not compensated for known actuation strength change (H1 data all taken within 1 week.)
Advice for the future:
Weight frequency points contributing actuation coefficient uncertainty by
  coherence
  distribution filter / contribution to over all actuation strength

## Slide 37: Why is L1’s Statistical Uncertainty Larger than H1’s? How about the Sensing Function Uncertainty?
Again – not at all an issue of lack of measurements.
  (Actually, H1’s uncertainty estimation missed measurements from 2015-10-15, 2015-12-01, and 2015-12-21  )
Why, then?
  Because of H1’s non-linear magnitude residual, a “rolling standard deviation” was used, so the uncertainty is much smaller in the bucket.

## Slide 38: Why is L1’s Statistical Uncertainty Larger than H1’s? L1’s sensing uncertainty was treated exactly like actuation uncertainty:

## Slide 39: Why is L1’s Statistical Uncertainty Larger than H1’s? H1’s sensing’s magnitude systematic error and uncertainty were treated totally differently:

## Slide 40: Why is L1’s Statistical Uncertainty Larger than H1’s? H1’s sensing function uncertainty is estimated totally differently than L1
H1 Stat. Unc. Components
L1 Stat. Unc. Components
(Rel. Magnitude)2
100
102
101
(Rel. Magnitude)2
100
102
101
H1
L1
Sensing Summary:
Differences in assessment of uncertainty are essential incomparable, unfortunate for L1
Tough to say if H1 is under or L1 is over estimated

## Slide 41: Why is L1’s Statistical Uncertainty Larger than H1’s? Conclusions
Kissel had claimed that L1’s statistical uncertainty suffered from too few measurements. This is just not true (I hear you now Shivaraj!)
For Actuation L1 took (PCAL Actuation) data out to higher frequency, which (for the PUM stage) includes violin modes.
Revisiting the data, L1’s PUM uncertainty is large because systematic errors (from PUM stage violin modes) were not consistent between data sets. Remaining systematic after subtracting out an overall fit to all measurements still left significant, non-Gaussian residual spread, miss-construed as large statistical fluctuation.
L1’s TST stage measurements have a few low-frequency outliers (remaining systematics?) that doubled the standard deviation w.r.t. H1, and includes 4 months worth of actuation strength change making measurement-to-measurement results non-Gaussian.
Sensing function uncertainty is treated differently between sites. Could say L1 is over estimated, or H1 is underestimated.
For the future:
Both sites *need* to measure out the the same frequency band (H1 should go higher!)
If combining multiple measurements for TST, make sure clustered tightly in time or compensated for long-term drift.
Need to look into a better treatment of residuals for determining statistical uncertainty that is less sensitive to systematic error fits, time-dependence and outliers.
Need to treat the uncertainties the same between sites. If we see inconsistencies between measurements – investigate why!