## Slide 1: Gravitational wave detection with laser interferometers
Koji Arai – LIGO Laboratory / Caltech
LIGO-G1601395-v1

## Slide 2: Introduction

## Slide 3: Gravitational wave
General Relativity
  Gravity = Spacetime curvature
  Gravitational wave = Wave of spacetime curvature
Gravitational waves
  Generated by motion of massive objects
  Propagates with speed of light
  Cause quadrupole deformation of the spacetime
  Measure strain between
  free masses to detect GWs
GW
Free mass

## Slide 4: GW: Generation, Propagation, and Detection
Generation:
Change of quadrupole moment
Post-newtonian, NR
Propagation:
wave equation of
the spacetime metric
Detection:
Quadrupolar “displacement” of the masses
1/R

## Slide 5: GW Detection
Measure strain between free masses
GW
free
mass
free
mass

## Slide 6: GW Detection
Measure strain between free masses
  GW does not appear in the local motion
  Changes optical distance between the masses
Longer the baseline, the bigeer change
  (displacement dx) = (Strain h) x (baseline L)
We need to measure phase of the laser light => use “laser interferometry”
GW
L->L(1+dh)

## Slide 7: Quadrupole nature of GWs
Differential motion => Michelson interferometer
Longer baseline -> bigger change
  (displacement dx) = (Strain h) x (baseline L)
Need to measure phase of the laser light => use “laser interferometry”

## Slide 8: GW telescope?
A continuous signal stream from an interferometer
Fixed on the ground, can not be directed
Poor directivity => More like an antenna

## Slide 9: GW telescope?
A continuous signal stream from an interferometer
GWs and noises: in principle, indistinguishable
=> Anything we detect is GW
Reduce noises!
  Obs. distance is inv-proportional to noise level
  x10 better => x10 farther => x1000 more galaxies

## Slide 10: Actual GW detector
High
Power Laser
Mode
Cleaner
Recycling
Mirrors
4km FP arm cavities
Signal
Readout
Scheme
Data Storage
Data Analysis
Analog Electronics
Digital Control
Seismic Attenuation
Vacuum Envelope
Mirror Suspension
(Quad Pendulum)
Mirror & Coating
Fused Silica fiber

## Slide 11: Components of the interferometer
3 elements of a GW detector
  Mechanics
  Optics
  Electronics

## Slide 12: Components of the interferometer
3 elements of a GW detector
  Mechanics
  Optics
  Electronics

## Slide 13: Sensitivity and noise
Sensitivity (=noise level) of Advanced LIGO
Design

## Slide 14: Sensitivity and noise
Sensitivity (=noise level) of Advanced LIGO
Current sensitivity
h= 8x10-24 /rtHz

## Slide 15: Sensitivity and noise
Sensitivity (=noise level) of Advanced LIGO
Noise budget
h= 2x10-23 /rtHz

## Slide 16: Optical configurations of laser interferometer GW detectors

## Slide 17: Introduction ~ Interferometer?
Interferometry
  Utilize characteristic of a Michelson interferometer as a length comparator
Michelson
Interferometer
Advanced LIGO
Dual-Recycled Fabry-Perot Michelson Interferometer
In reality...
Fabry-Perot cavity
No worries: It’s just a combination of MI and FPs

## Slide 18: Michelson interferometer
Light intensity at the output port
  Difference of the electric fields from the arms
  Output intensity is sensitive
  to the differential phase

## Slide 19: Michelson interferometer
Frequency response of the Michelson to GWs
Jean-Yves Vinet,et al
Phys. Rev. D 38, 433 (1988)
Frequency response
of the Michelson interferometer
Ω: optical angular frequency, λOPT laser wavelength
ω: angular frequency of GW, λGW wavelength of GW

## Slide 20: Michelson interferometer
Frequency response of the Michelson to GWs
DC Response
longer -> larger
Cut off freq
longer -> lower
Notch freq
f = n c / (2 L)
  Michelson arm length optimized for 1kHz GW -> 75km, too long!

## Slide 21: Fabry-Perot optical resonator
Storing light in an optical cavity
  Field equations
Very fast phase response

## Slide 22: Fabry-Perot optical resonator
Storing light in an optical cavity
Finesse
DC Response
amplification
Cutoff freq “Cavity pole”
  1. FP increases stored power in the arm
  2. FP increases accumulation time of the signal
  => Above the roll-off, increasing F does not improve the response

## Slide 23: Fabry-Perot Michelson Interferometer
Differential nature of the Michelson + Longer photon storage time of Fabry-Perot cavities = Fabry-Perot Michelson Interferometer
Basic form of the modern interferometer GW detector

## Slide 24: Optical Recycling Technique
Power recycling
  When the Michelson interferometer is operated at a “dark fringe”, most of the light goes back to the laser side

## Slide 25: Optical Recycling Technique
Power recycling
  Let’s reuse the reflected light
  Place a mirror in front of the interferometer to form a cavity with the Michelson (compound mirror) “Power Recycling Mirror”
  The internal light power is increased = equivalent to the increase of the input laser power
compound mirror

## Slide 26: Optical Recycling Technique
Power recycling
  BTW, all the output ports are made dark. Where does the light go?
  In the ideal power recycling, all input power is internally consumed via optical losses (absorption & scattering)

## Slide 27: Optical Recycling Technique
Power-recycled Fabry-Perot Michelson Interferometer
  Internal light power in the arms is increased
From the laser side /
common arm length change
It looks like a three mirror caivty
= high finesse cavity
For the differential motion (=GW)
It looks like just an arm cavity

## Slide 28: Optical Recycling Technique
Common mode
= high finesse three mirror cavity
Differential mode (=GW)
= low (or high) finesse three mirror cavity
Dual-recycled Fabry-Perot Michelson Interferometer
  Another mirror is added at the dark port “Signal Recycling Mirror”
  Dual recycling allows us to set different storage times for common and differential modes

## Slide 29: To tuned or not to tune
Bandwidth of the detector can be changed
  by changing the resonant phase of the signal recycling cavity (SRC)
Optimize the curve depending on the noise shape
Dynamic signal tracking
Signals: resonant in SRC
(Resonant Sideband Extraction)
Signals: anti-resonant in SRC
(Signal Recycling)

## Slide 30: Signal Readout
Interferometer response is nonlinear
How do you read the GW signal (and other signals)? => Signal readout scheme

## Slide 31: Signal Readout
Signal readout scheme
RF phase modulation / demodulation or DC Readout

## Slide 32: Signal Readout
RF Readout and DC Readout
DC Readout is good for GW channel
  removes nonstationary shot noise
  mitigates technical noises associated with the RF sidebands

## Slide 33: Pound-Drever-Hall technique (PDH)
RF signal readout scheme for cavities
  Phase modulation -> RF optical sidebands
  Reflected beam -> detected / demodulated
Laser
Electro-Optic
Modulator
Faraday
Isolator
or
Pick-off mirror
dL or f
V

## Slide 34: Summary
Optical phase measurement => Interferometry
Michelson interferometer: requires too long arm
Fabry-Perot arm: longer light storage time
Optical recycling technique: - more power in the arms - allows us to taylor the detector response to GW signals
Optical read-out schemes

## Slide 35: Advanced topics
Angular & frequency response of an interferometer
  Up to this point GWs from the zenith was assumed.
  What is the response to GWs with an arbitrary angle?
  What is the frequency response of the detector for such GWs?
  Draw an arbitrary optical path. What is the angular and frequency response of such a path?
  Can we use numerical “optimization” for certain criteria? e.g. better sky coverage, directive beaming, for certain source frequency, etc…
GW
GW
GW

## Slide 36: Advanced topics
Angular & frequency response of an interferometer
  R. Schilling, Class. Quantum Grav. 14 (1997) 1513-1519

## Slide 37: Noises in Gravitational Wave Detectors

## Slide 38: Introduction ~ Noise?
GW detection Data stream of differential arm strain
Once recorded: Signals and noises are indistinguishable What we can do is to catch “likely” features
Reduce any kind of noises!

## Slide 39: Introduction ~ Noise?
Time domain vs frequency domain
Noise
Reduction
Time domain: transient noises Frequency domain: stationary noises

## Slide 40: Introduction ~ Noise?
Power Spectral Density (PSD) Double sided PSD (-Infinity < f < Infinity)
Single sided PSD (0 <= f < Infinity) [xunit2 / Hz]
Linearized PSD: [xunit/ sqrtHz]

## Slide 41: Introduction ~ Noise?
Parseval’s Theorem for signal RMS and PSD
Root Mean of x(t): average signal power density (per sec)
(cf. variance, std deviation)
PSD Sx(f):
power density per frequency (per sec)

## Slide 42: Introduction ~ Noise?
Example
PSD [fm/sqrtHz] in log-log scale, RMS [fm] ~ 50fm = 0.05pm
PSD [fm/sqrtHz] in log-lin scale
RMS [fm]
Time series [pm]

## Slide 43: Noise categories
3 fundamentals of the GW detector
Mechanics -> Displacement noises
Optics -> Optical noises
Electronics -> Electrical noises
Optical
Optical
Displacement
Displacement
Electrical
Electrical
Electrical

## Slide 44: Sensitivity and noise
Sensitivity (=noise level) of Advanced LIGO
Noise budget
h= 2x10-23 /rtHz
Laser shot noise
Laser radiation pressure noise
Thermal noise
Seismic noise
Laser intensity /frequency noise
Electronics noise
Digitization noise
Angular control noise
......

## Slide 45: Displacement noises

## Slide 46: Displacement noise
Mechanical displacement sensed by a laser interferometer
The longer the arm length, the smaller the strain noise
  Seismic noise
  Thermal noise
  Newtonian Gravity noise

## Slide 47: Displacement noise
Seismic noise
  Even when there is no noticeable earth quake…
http://link.aps.org/doi/10.1103/RevModPhys.86.121 (http://arxiv.org/abs/1305.5188)
Target disp. noise
10-20m/rtHz

## Slide 48: Displacement noise
Vibration isolation ~ utilize a harmonic oscillator
  A harmonic oscillator provides vibration isolation above its resonant frequency
w0=1Hz
|x/X|~1/1000@30Hz

## Slide 49: Displacement noise
How to get more isolation?
Damping
Lower the peak height
Worse isolation
Lower resonant freq
Better isolation
Complex to realize
Multi stage
Steeper isolation curve
More peaks
f -2
f -4
In practice: employ combination of these measures

## Slide 50: Displacement noise
iLIGO vibration isolation
Hydraulic active isolation / Isolation stack / Single Pendulum

## Slide 51: Displacement noise
aLIGO vibration isolation
Hydraulic active isolation / Invacuum Active Isolation Platforms / Multiple Pendulum

## Slide 52: Displacement noise
Virgo: super attenuator
  8m high
  9 stages in horizontal
  6 stages in vertical
8m

## Slide 53: Displacement noise
http://link.aps.org/doi/10.1103/RevModPhys.86.121 (http://arxiv.org/abs/1305.5188)

## Slide 54: Displacement noise
Question:
n-stage multiple pendulum with fixed height of H
How many stages n do we need to realize the vibration isolation of A at frequency of f?
For a given A what is the minimum f, we can realize by increasing n?
(Mass distribution)
  For equal m for each stage or
  For arbitrary mass mi and length hi

## Slide 55: Displacement noise
Thermal noise:
System in thermal equilibrium
  the system can dissipate its energy to the heat bath
  the system is thermally excited by thermal fluctuation
Mechanical thermal noises
  suspension thermal noise
  mirror substrate thermal noise
  mirror coating thermal noise

## Slide 56: Displacement noise
Fluctuation Dissipation Theorem
Friction: interaction with “bath” = huge number of d.o.f.
Fluctuation force: produced by huge number of d.o.f.
Dissipation and fluctuation have certain relationship
system description (Langevin equation)
q: generalized coordinate m: generalized mass
R: friction (dissipation)
F: internal force (restoring force, etc)
F’(t): fluctuating force from heat bath
Power spectrum density (PSD) of the fluctuation force

## Slide 57: Displacement noise
Transfer function approach
Equivalently, the fluctuation of the system can be obtained from the response of the system
where Z(w) and H(w) are the impedance and
force-to-displacement transfer function of the system

## Slide 58: Displacement noise
Question:
- Velocity damping of a pendulum
- Structure damping
loss angle: 0 < 𝜙 ≪ 1
- How anti-spring changes the thermal noise spectrum?
anti-spring parameter: 0<𝛼<1

## Slide 59: Displacement noise
In some cases, calculating the system response is complicated (e.g. deformation of an elastic body)
Systems response (impedance) at a certain freq:
Average rate of energy disspation
We don’t need to
know Z(w)!

## Slide 60: Displacement noise
Sensing of the mirror surface deformation with a laser beam (with intensity profile of f(r))
Apply periodic pressure with profile of f(r)
This induces deformation of x(r) which is different
from our sensing profile of f(r), but that’s OK
Calculate the rate of dissipation Wdiss
analytically, using FEA, or etc
Put this into the formula
We don’t need to
know Z(w)!
Y. Levin PRD 57, 659-663 (1998)

## Slide 61: Displacement noise
Mirror substrate thermal noise
  Brownian motion Mechanical loss associated with the internal friction Thermally excited body modes Optical coating (high mechanical loss) will be limiting noise source in aLIGO
  Thermo elastic noise Elastic strain & thermal expansion coefficient => cause heat distribution & flow in the substrate Temperature fluctuation causes mirror displacement
  Thermo-refractive noise Temp. fluctuation causes fluctuation of refractive index
We don’t need to
know Z(w)!

## Slide 62: Displacement noise
Suspension thermal noise
  Brownian motion Mechanical loss of the suspension fiber Thermally excited pendulum modes
  Thermo elastic noise Elastic strain of the fiber & thermal expansion coefficient => cause heat distribution & flow in the fiber Temperature fluctuation causes mirror motion
We don’t need to
know Z(w)!
<- Monolithic suspension
for high pendulum Q

## Slide 63: Displacement noise
Question
  Induced current damping (electro-mechanical system) 1. How does the Q factor of the system depend on R? 2. How much is the thermal noise displacement of the mass? 3. How does the thermal noise of the resister shakes the mass? 4. How are the above questions with a capacitive coupling instead of the coil?
  Cold damping 1. If the resister is cooled, how does the thermal noise motion change? 2. Is the pendulum actually cooled? Down to what temperature? 3. How fast the pendulum recovers the original temperature once R is returned to the room temp.?
We don’t need to
know Z(w)!

## Slide 64: Displacement noise
Newtonian Gravity noise
  Mass density fluctuations around the test masses => test mass motion via gravitational coupling
  Dominant source of Newtonian noise = Seismic surface wave
  Mitigation 1) Going to quiet place (underground) 2) Feedforward subtraction 3) Passive reduction by shaping local topography
NN
aLIGO
sensitivity
J Driggers, et al, PRD 86, 102001 (2012)
J Harms, et al, Class. Quantum Grav. 31 185011 (2014)

## Slide 65: Displacement noise
Mechanical upconversion noise
  Large low frequency (f < 1Hz) motion => upconverted to 10~100Hz motion via nonliner processes
  Barkhausen noise => low freq mirror actuation cause BH noise and upconversion Select better magnet materials (e.g. SmCo)
https://www.nde-ed.org/

## Slide 66: Optical noises

## Slide 67: Optical noises
Noises that contaminate the readout signal
  Quantum noises (shot noise, radiation pressure noise)
  Laser technical noises (frequency/intensity noise)
  Modulation noises
  Scattered light noise
Optical
Optical

## Slide 68: Optical noises
Quantum noises: Shot noise
  Noise due to photon counting statistics
  N detected photon => standard deviation √N
  Increasing the incident power Pin, => The shot noise is increased by √Pin => The signal amplitude is increased by Pin
  In total, the signal-to-noise ratio is improved by

## Slide 69: Optical noises
Quantum noises: Shot noise
  Photon shot noise associated with photodetection
  Michelson interferometer
  Michelson response (@DC)
at the limit of d𝜙->0
  iDC : DC Photocurrent
  η : PD Quantum Efficiency
  ν : Optical Frequency
Shot-noise limit of the Michelson phase sensitivity
  1.3x10-20 1/sqrtHz
  @1W, 1064nm, 4km
Michelson
Strain Sensitivity

## Slide 70: Optical noises
Supplemental slide ~ Shot noise derivation

## Slide 71: Optical noises
Quantum noises ~ Radiation pressure noise
  Photon number fluctuation in the arm cavity => Fluctuation of the back action force
  Quantum noise of the input laser => Common noise for two arms => cancelled and does not appear in the signal
  Vacuum fluctuation injected from the dark port => Differentially power fluctuation => Cause the noise in the GW signal

## Slide 72: Optical noises
Quantum noises
  Standard Quantum Limit (SQL)
- Trade-off Between Shot Noise and Radiation-Pressure Noise
- Uncertainty of the test mass position due to observation

## Slide 73: Optical noises
Laser frequency noise
  Laser wavelength (λ = c / ν) = reference for the displacement measurement
  Optical phase 𝜙 = 2 pi ν L / c d𝜙 = 2 pi / c (L dν + ν dL) <= indistinguishable
  dL/L target 10-24 => dν = 10-24 x 300 THz (1064nmYAG laser) = 3 x 10-10 Hz/rtHz

## Slide 74: Optical noises
Laser frequency noise
  Target: dνeff = 3 x 10-10 Hz/rtHz
  Laser stability dν = 10~100 Hz/rtHz @100Hz
3-stage cascaded laser frequency stabilization
iLIGO
  Michelson’s differential sensitivity provides Frequency noise cancellation of 1/100~1/1000 “Common Mode Rejection”

## Slide 75: Optical noises
Laser intensity noise
  Relative Intensity Noise (RIN): dP/P
  Sensor output V = P x => dV = P dx + x dP <= indistinguishable
  Requirement: RIN = 10-9 1/√Hz xofs=10e-12 (DC Readout) => dx=1e-20 m/√Hz

## Slide 76: Optical noises
Laser intensity noise ~ intensity stabiliaztion
  Requirement: RIN = 10-9 1/√Hz
  2-stage cascaded intensity stabilization control
  Challenge: requires 300mA of photodetection
  Shot noise limited RIN
  In-vacuum 8-branch Photodiode array
P. Kwee et al, Optics Express 20 10617-10634 (2012)

## Slide 77: Optical noises
Modulation noises
  RF Residual Amplitude Modulation
  Modulation Oscillator Phase Noise
  Modulation Oscillator Amplitude Noise
Produce noise sidebands on the modulation sidebands
Mitigation
  For the GW signal: Use DC readout and eliminate them by an “output mode cleaner cavity”
J. Camp et al JOSA A 17 120-128 (2000)

## Slide 78: Optical noises
Scattered light noise
  Scattered light recouples to the interferometer beam with an arbitrary phase => causes amplitude and phase fluctuation
  Two effects: 1. Small motion regime: linear coupling of the phase fluctuation 2. Large motion regime: low freq large motion of the scattering object => upconversion via fringe wrapping
  Mitigation
    Reduce scattered light
    Vibration isolation of the scattering object

## Slide 79: Electrical noises

## Slide 80: Electrical noises
General rules for electrical noises
  Electrical noise in photo detection
  Digitization noise (ADC/DAC) / Aliasing
Control noise
Actuator noise

## Slide 81: General rules for electrical noises
Low noise amplification at the beginning
Give necessary gain as early as possible
Don’t attenuate (and amplify again)
Gain G1
Gain G2
input noise: v1
input noise: v2
output noise: v1 G1
output noise Vout:
Sqrt[(v1 G1 G2)2+(V2 G2) 2]
Input equivalent noise
Vout / (G1 G2)
= Sqrt[v12+(v2/G1) 2]
Signal
Lessons
  The input referred noise is determined by v1
  It won’t become better by the later stages
  If G1 is big enough, we can ignore the noise of later stages

## Slide 82: Noise in photodetectors
Photodiodes
  PIN photodiodes (InGaAs for near IR, Si for visible)
    Good linearity
    Low noise
    High Quantum Efficiency (>90%)
InGaAs Quadrant PD
(𝜙3mm)
InGaAs PD (𝜙1mm)
P-layer
I-layer
N-layer
Anode
Cathode
“Photodiode Amplifiers”, J. Graeme (McGrawHill 1995)
Photocurrent

## Slide 83: Noise in photodetectors
Photodetectors are the first electrical block of the control chains
  It is important to have low input-referred current noise
Photo detection
  AF (Audio Frequency 0~100kHz)
    Prenty of light (photocurrent ~mA) Not a big electrical issue
  RF (Radio Frequency 10~200MHz)
    Large diode aperture -> high RF noise Need careful consideration

## Slide 84: Noise in photodetectors
input referred noise current
Noise in photodiodes
  Photodiode equivalent circuit
    Shunt Capacitance RD (~100MΩ) Usually not a problem
    Junction Capacitance CD (1pF~1nF)
    Series Resistance RS (1Ω~100Ω)
  The diode aperture size needs to be ~mm => Cd tends to be big.
  2mm InGaAs PD: Rs~10Ω, Cd~100pF => i_Rs = 20 pA/sqrtHz @100MHz
  (equivalent to the shot noise of 1mA light ~ 1.3mW@1064nm)

## Slide 85: Analog/Digital interface
Restriction of signal digitization
  Voltage quantization: quantization noise => limited dynamic range => Requires whitening/dewhitening filters
  Temporally discrete sampling: aliasing problem => limited signal bandwidth => Requires anti-aliasing (AA) / anti-imaging (AI) filters
  Typical signal chain

## Slide 86: Digitization (Quantization) noise
Analog signals (~+/-10V) -> Digital signal
  Digitized to a discrete N bit integer number
  Quantization causes a white noise e.g. +/-10V 16bit => Δ = 0.3mV => Vn ~ 100 μV/sqrtHz cf. Input noise of a typical analog circuit 10nV/sqrtHz
http://www.analog.com/static/imported-files/tutorials/MT-229.pdf
quantization
quantization error

## Slide 87: Digitization (Quantization) noise
Whitening
  Amplify a signal in the freq band where the signal is weak
Dewhitening
  Amplify a signal in the freq band where the signal is weak

## Slide 88: Control induced noise
Noise couplings from auxiliary loops
  e.g. Angle control feedback -> noise injection to the GW channel
  Mitigation 1) Make the coupling smaller 2) Make the noise itself smaller 3) Limit the control bandwidth of the aux loop

## Slide 89: Actuator noise
Actuator noise appears in the GW signal as an external disturbance
  Mitigation 1) Make the noise itself smaller 2) Make the actuator response smaller
  We need to keep sufficient actuator strength for lock acquisition => Transition to a low-noise mode after achieving lock

## Slide 90: Summary

## Slide 91: Summary
Summary
  There are such large number of noises
  They are quite omnidisciplinary
  Even only one noise can ruin our GW detection
  GW detection will be achieved by
    Careful design / knowledge / experience
    Logical, but inspirational trouble shooting
  Noise “hunting”