## Slide 1: Gravitational-Wave Detectors in India
Fred Raab, for the LIGO Scientific Collaboration and the Virgo Collaboration

## Slide 2: Einstein’s General Relativity re-wrote the rules of space and time
A massive object shifts apparent position of a star
Rendering of space stirred by two orbiting black holes
Empty space and time are things, with real physical properties. Space has a shape, a stiffness and a maximum speed for information transfer.

## Slide 3: Gravitational waves: hard to find because space-time is stiff!
K ~ 10-44 N-1
 Wave can carry huge energy with miniscule amplitude!
K~[G/c4] is combination of G and c with units of 1/N
Following I.R. Kenyon, General Relativity

## Slide 4: Expected order-of-magnitude strength
Strain from a binary neutron star pair
  M = 1.4 M,
  r = 1023 m (15 Mpc, Virgo),
  R = 20 km
  forb = 400 Hz
Event rate is proportional to hmin-3.

## Slide 5: Gravitational Waves; a well-understood transmitter
Neutron Binary System – Hulse & Taylor
PSR 1913 + 16 -- Timing of pulsars
·
·
17 / sec
Neutron Binary System
separated by 106 miles
m1 = 1.4m; m2 = 1.36m; e = 0.617
Prediction from general relativity
spiral in by 3 mm/orbit
rate of change orbital period
~ 8 hr
Emission of gravitational waves
J.M. Weisberg, D.J. Nice, J.H. Taylor, Astrophys. J., 722, 1030 (2010).

## Slide 6: Basic idea for detection is simple
GW amplitude h = (Rx-Ry)/R
Spatial asymmetry induces relative phase shifts on light in arms

## Slide 7: Expected event rates
Rates paper: Class. Quant. Grav,
27 (2010) 173001
Binary neutron stars
Initial LIGO reach: 15Mpc; rate ~ 1/50yrs
Advanced LIGO ~ 200Mpc
‘Realistic’ rate ~ 40 events/yr
Notes: From i) observations of double neutron stars in our galaxy, and
ii) Population synthesis modeling.
Suffers from small sample size, and the assumption the sample is representative
Suffers from unknowns like birth velocities, companion mass distribution etc

## Slide 8
LIGO (Washington)
LIGO (Louisiana)
The Laser Interferometer
Gravitational-Wave Observatory
Brought to you by the National Science Foundation; operated by Caltech and MIT; the research focus for more than 1000 LIGO Scientific Collaboration members worldwide.

## Slide 9
Observed on Sep 14, 2015
PRL 116, 061102 (2016)

## Slide 11: A signal from a binary black hole merger
PRL 116, 061102 (2016)

## Slide 12: GW150914: a signal from a binary black hole merger

## Slide 13
SXS Simulation of GW150914 aginst a field of stars
Notes: 13
13

## Slide 14: Discovery Timeline – Advanced LIGO’s 1st Observations
Courtesy Caltech/MIT/LIGO Laboratory

## Slide 15: Advanced LIGO’s First Observations
ArViv:1606.04856; see also PRL 116, 241103 (2016) for GW151226.

## Slide 16: Known Stellar-Mass Black Holes – June 2016
Courtesy Caltech/MIT/LIGO Laboratory

## Slide 17: Now what?
These first observations open up access to a vast new frontier for exploration
How and where have these objects been formed?
Initial observations indicate that stellar-mass or “heavy” black hole binaries merge hourly somewhere in the universe
What can these mergers teach us?
Where is the matter?
  No “known” form of matter can explain LIGO’s early discoveries, and they behave like black holes.
  Can we prove that these objects are black holes?
  Where are the neutron stars and how do they behave?

## Slide 18: Sources of Gravitational Waves
Accelerating Quadrupole Mass Moments

## Slide 19: Astrophysical Sources of Gravitational Waves
Casey Reed, Penn State
Credit: AEI, CCT, LSU
Coalescing Compact Binary Systems: Neutron Star-NS, Black Hole-NS, BH-BH
- Strong emitters, well-modeled,
- (effectively) transient
Credit: Chandra X-ray Observatory
Asymmetric Core Collapse Supernovae
- Weak emitters, not well-modeled (‘bursts’), transient
NASA/WMAP Science Team
Cosmic Gravitational-wave Background
- Residue of the Big Bang
- Long duration, stochastic background
Spinning neutron stars
- (nearly) monotonic waveform
- Long duration
Notes: LIGO is designed to be an observatory, not a one-off proof that GWs exist. What do we look for?
There are number of predicted astrophysical sources of gravitational radiation, and most of them involve cataclysmic events.
Binary systems – NSs and BHs, most likely source, theoretically well understood with known waveforms
Bursts – GW emissions that are not well modeled or understood. These include asymmetrically core collapse supernova, cosmic strings, and perhaps unknown sources
The residual GW background
Continuously emitting sources such as spinning neutron stars, which have a pure monotone emission.

## Slide 20: Astrophysical Sources of Gravitational Waves
Casey Reed, Penn State
Credit: AEI, CCT, LSU
Coalescing Compact Binary Systems: Neutron Star-NS, Black Hole-NS, BH-BH
- Strong emitters, well-modeled,
- (effectively) transient
Credit: Chandra X-ray Observatory
Asymmetric Core Collapse Supernovae
- Weak emitters, not well-modeled (‘bursts’), transient
NASA/WMAP Science Team
Cosmic Gravitational-wave Background
- Residue of the Big Bang
- Long duration, stochastic background
Spinning neutron stars
- (nearly) monotonic waveform
- Long duration
✓
Notes: LIGO is designed to be an observatory, not a one-off proof that GWs exist. What do we look for?
There are number of predicted astrophysical sources of gravitational radiation, and most of them involve cataclysmic events.
Binary systems – NSs and BHs, most likely source, theoretically well understood with known waveforms
Bursts – GW emissions that are not well modeled or understood. These include asymmetrically core collapse supernova, cosmic strings, and perhaps unknown sources
The residual GW background
Continuously emitting sources such as spinning neutron stars, which have a pure monotone emission.

## Slide 21: Frequency-Time Characteristics of GW Sources
frequency
time
Bursts
Ringdowns
Broadband Background
CW (quasi-periodic)
Chirps
time
frequency
Earth’s orbit
frequency
time
Earth’s rotation

## Slide 22
The rate of future discovery in gravitational-wave astronomy will be determined by the number and sensitivity of gravitational-wave detectors and the number and skill of GW experimentalists. For India to be successful in this field will require quickly growing a sufficiently large community of its own GW experimental experts.

## Slide 23: Sky Localization Is Poor With Only Two Detectors
Image credit: LIGO (Leo Singer) /Milky Way image (Axel Mellinger)

## Slide 24
24
24
The advanced GW detector network:
2015-2025
GEO600 (HF)
2011
Advanced LIGO
Hanford
2015
Advanced LIGO
Livingston
2015
Advanced
Virgo
2017
LIGO-India
2024
KAGRA
>2018

## Slide 25: LIGO-India Concept
Started as a partnership between LIGO Laboratory and IndIGO collaboration to build an Indian interferometer
  LIGO Lab (with its UK, German and Australian partners) provides components for one Advanced LIGO interferometer (H2) from the Advanced LIGO project
  LIGO Lab provides designs and design assistance for facilities and vacuum system and training for Indian detector team
  India provides the infrastructure (site, roads, building, vacuum system), staff for installation & commissioning, operating costs
LIGO-India would be operated as part of LIGO network to maximize scientific impact
Major enhancement to the global network and to the capabilities for GW astrophysics and Multi-messenger Astronomy

## Slide 26: Improved Localization: LIGOVirgoLIGO-India
GW150914: LIGO only
GW150914: LIGO LV LVI
(Preliminary)
375°  9.3°  7.8°
(99% confidence level)

## Slide 27: Improved Localization: LIGOVirgoLIGO-India
GW150914: LIGO only
GW150914: LIGO LV LVI
(Preliminary)
375°  9.3°  7.8°
(99% confidence level)
Assumes detectors of comparable sensitivity!

## Slide 28: The international GW network will not stay frozen in time.
The detector now in storage for LIGO-India is 2015 technology.
At best, LIGO-India will not be ready for joining observing runs until early 2024.
At present, the LIGO H1 and L1 detectors are at 1/3 of design sensitivity.
H1 and L1 should reach design sensitivity years before LIGO-India is ready for observing, probably by 2019.
LIGO Laboratory will share knowledge gained getting to design sensitivity, but India’s experimental community needs to implement them.

## Slide 29: LVC Observing Scenario (arXiv:1304.0670)

## Slide 30: Sensitivity and Noise
The keys to improving detectors are sensitivity and noise.
Range is proportional to sensitivity.
Event rate is proportional to volume, which is proportional to Range cubed.
Thus a factor of 2 in sensitivity gives a factor of 8 in event rate (nearly an order of magnitude).

## Slide 31: Noise cartoon
R. Adhikari

## Slide 32: What Limits Sensitivity of Interferometers?
Seismic noise & vibration limit at low frequencies
Atomic vibrations (Thermal Noise) inside components limit at mid frequencies
Quantum nature of light (Shot Noise) limits at high frequencies
Myriad details of the lasers, electronics, etc., can make problems above these levels
DESIGN
COMMISSIONING
Typical early LIGO noise estimates

## Slide 33: Optical configuration
Complete detector description in Class. Quantum Grav. 32 (2015) 074001

## Slide 34
Better
seismic
isolation
Higher
power
laser
Better
test masses
and
suspension
Notes: Sathya pointed out need to mitigate gravity gradient noise.
We need Krishna’s tiltmeters! Testing at endstation.
Tilt-to-length coupling in an inertial sensor.

## Slide 35
Ground Motion at 10 [Hz] ~ 10-9 [m/rtHz]
Need 10 orders of magnitude
Test masses are suspended from 7 stages of active and passive vibration isolation
Seismic Isolation
Matichard, F., et al. Proc. ASPE (2010)
Aston, S. M., et al. CQG 29.23 (2012): 235004.
2
4
5
6
7
1
3
Last two stages are monolithic
to improve Brownian noise
Cumming, A. V., et al. CQG 29.3 (2012): 035003.

## Slide 36: Initial S6 / Advanced O1 Design / A+ Upgrade
~3 x the sensitivity made the difference
~3 x to go!
And we can go beyond
https://dcc.ligo.org/public/0113/T1400316/004; https://dcc.ligo.org/LIGO-G1500623

## Slide 37: Science drives Requirements
Stellar Evolution at High Red-Shift: Black Holes from the first stars (Population III)
  Reach z>~10
  At least moderate GW luminosity distance precision
Independent Cosmology and the Dark Energy Equation of State
  Needs precision GW luminosity distance and localization for EM follow-ups (for redshift)
Checking GR in extreme regime
  High SNR needed
  GW luminosity distance and localization not essential

## Slide 38: What will it take to improve detectors?
Clever experimental physicists and engineers, capable of solving multi-dimensional problems at the forefront of basic measurement science
Advanced LIGO detectors are complex:
  Approximately 350 high-performance servomechanisms
  Many of these are multiple-input, multiple output
  Sensors and actuators for these are operating at or beyond commercial limits
Developing ways to work around fundamental limitations:
  Quantum nature of light
  Atomic nature of matter
A single example: working around the classical and quantum nature of light

## Slide 39: Principal noise terms
Radiation-Pressure Dominated Background
Shot-Noise Dominated Phase Noise

## Slide 40: Nothing Is Easy: Classical Challenges to High-Power Operation
Thermal lensing and compensation
R Lawrence et al (2004)
Opt Lett 29(22)2635-2637
J Sidles, D Sigg, Phys. Lett. A.
354, 167-172 (2006)
Angular radiation pressure
instabilities
M Evans et al (2015) Phys. Rev. Lett. 114, 161102
Parametric instabilities

## Slide 41: Quantum Noise is Fundamental, Caused by Vacuum Fluctuations
Laser
C Caves (1981) Phys. Rev. D 23, 1693
EM Vacuum Fluctuations Cause Shot Noise and Radiation Pressure Noise

## Slide 42: Vacuum squeezing: a partial work-around
Laser
LIGO Scientific Collaboration, Nature Photonics 2013
doi:10.1038/nphoton.2013.177

## Slide 43: A better work-around: frequency-dependent squeezing
M Evans et al, (2013) PRD 88 022002
Original idea: J Kimble et al (2001) Phys. Rev. D 65, 022002
Practical designs: T Corbitt et al (2004) Phys. Rev. D 70, 022002
Demonstration in regime applicable to LIGO: E Oelker et al (2016) Phys. Rev. Lett. 116, 041102

## Slide 44: Advanced LIGO upgrade path
Advanced LIGO is limited by quantum noise & coating thermal noise
Squeezed vacuum to reduce quantum noise
Options for thermal noise:
  Better coatings
  Cryogenic operation
  Longer arms (new facility)

## Slide 45: Upgrade possibilities
https://dcc.ligo.org/public/0113/T1400316/004; www.et-gw.eu

## Slide 46
Credit: NASA

## Slide 47: Summary
1st observing run of LIGO’s 2nd-generation detectors have initiated Gravitational-Wave Astronomy, opening a new frontier for exploration.
An emerging international network of detectors soon will provide more accurate positions of sources to enable EM follow-ups of GW events.
There is still room within the laws of physics to develop more powerful generations of detectors and much physics still to be harvested from their observations.
The role played by India in these developments will depend strongly on India’s ability to supply quickly both GW observatory facilities and a team of brilliant experimentalists in India with expertise in the commissioning of state-of-the-art GW detectors.