## Slide 1
Acoustic Emissions in Metals
Searching for Crackling Noise in aLIGO Suspensions
Danielle Frostig
Mentor: Gabriele Vajente

## Slide 2: Overview
Motivation
Crackling Noise
Previous Work
Microphone Calibration Experiment
  Process and problems encountered
  Data analysis and initial results
Conclusions and Future Work

## Slide 3: Motivation
Quadruple pendulum system with three stages of Maraging steel blades for vertical isolation
Crackling Noise
  When a system responds to slowly changing external conditions with discrete energy events at higher frequencies
  E.g. Earthquakes on fault lines, stock market fluctuations, a crumpling piece of paper.

## Slide 4: Motivation Continued
Low frequency noise
  Residual seismic motion
  Up-converted to GW band
Vertical displacements couple with horizontal displacements to cause noise in the data

## Slide 5: Previous Work
Maraging and high carbon steel blades loaded with 11kg and 16kg masses
  Imitates aLIGO suspensions
  Suspect crackling noise related to stress
Driven with a sinusoidal displacement
  No difference found between on and off periods
  Implies any crackling noise occurred below the noise floor

## Slide 6: Microphone Calibration
Ultrasonic acoustic emissions microphones used to collect crackle data
  We expect to detect discrete crackling events in releases of acoustic energy
If crackling noise is detected, we want to know the energy of the event.
We can calibrate the output of the microphones to energy input by a known system
  E.g. a ball drop experiment

## Slide 7: Experimental Setup

## Slide 8: Experimental Setup
Aluminum ball release mechanism

## Slide 9: Motion Tracking
Videos of ball drop experiment analyzed with MATLAB
  Single object tracking based on Kalman Filtering
  Script built around kalmanFilterForTracking1 function in MATLAB
1http://www.mathworks.com/help/vision/examples/using-kalman-filter-for-object-tracking.html

## Slide 10: Motion Tracking
Can analyze position, velocity, and acceleration from motion.
Can obtain estimates of kinetic energy from velocity.

## Slide 11: Microphone Output
The integral of an event’s root mean squared (RMS) plot gives energy recorded.

## Slide 12: Summary and Future Work
Ball drop experiment and motion tracking were set up to analyze energy of a known system for microphone calibration.
Next Steps:
  Correlate data to calibrate microphones
    Energy was tested with variable heights, test with variable distances
  Continue to run AE crackle detection experiments

## Slide 13: Acknowledgements
Gabriele Vajente
Crackle and Suspension Labs
LIGO
Caltech
NSF

## Slide 14: Electronic Setup

## Slide 15: Electronic Setup

## Slide 16: Kalman Filtering
An algorithm that uses measurements and noise to estimate unknown variables.
https://en.wikipedia.org/wiki/Kalman_filter

## Slide 17: Microphone Saturation

## Slide 18: Microphone Saturation

## Slide 19: Maraging Steel
Maraging steels are carbon free iron-nickel alloys with additions of cobalt, molybdenum, titanium and aluminium. The term maraging is derived from the strengthening mechanism, which is transforming the alloy to martensite with subsequent age hardening.
http://www.imoa.info/molybdenum-uses/molybdenum-grade-alloy-steels-irons/maraging-steels.php

## Slide 20: Various Fits on Velocity