## Slide 1: Study of Optical Scatterers within Coating Layers of LIGO Test-Mass Mirrors
Lamar Glover(1,3), Eddy Arriaga(1), Erik Barragan(1), Riccardo DeSalvo(1,3), Eric Do(1), Cameron Fajardo(1), Michael Goff(1), Jignesh Patel(1), Innocenzo Pinto(3), Travis Sadecki(2), Richard Savage(2), Ethan Villarama(1)
Related doc: LIGO-G1600431
1 – Cal State LA 2 – LIGO Hanford
3 – Uni. Sannio

## Slide 2
Observation of Optical Scatterers illuminated by LIGO stored beam
Feasibility study of scatterer observation with microscope

## Slide 3: Brief Summary
We are analyzing, at Cal State LA, scattering points detected in beam-illuminated photos of Advanced LIGO mirrors
A large number of scatterers were observed where few were expected, likely extending through the depths of the coating layer stack
Perhaps the problem of scatterers can now be better understood

## Slide 4: Method
Individual scatterers were identified using an astronomer’s algorithm for stars in galaxies
Extract apparent amplitude and position of each scatterer
Fit the stored beam position and profile to determine the illumination power on each scatterer.
Track changes in scatterer position and luminosity distribution in order to determine motion amongst test mass, stored beam and camera

## Slide 5: Daophot Mechanism: Point Spread Templates
“daophot” creates a point spread template from selected sources within the image.
The template is used to search scatterers
Magnitude data is derived for each identified source.
Point Spread Template for an exposure time of 1.25 x 10-4 s

## Slide 6: Daophot Mechanism: Problems
Good
Badly saturated

## Slide 7: Identifying/subtracting scatterers
Black dots mark the place where bright scatterers have been excised
“dirt” does not fit template is ignored by daophot and is less bright
Original Photo
256
256
100
Subtracted Photo
Dark pixels
expanded pixel scale
Fluffy dirt
ignored

## Slide 8: Daophot subtraction effectiveness and magnitudo resolution
Pixel amplitude histogram of original Image
Residual pixel amplitude histogram after scatterer extraction
In a good image, “daophot” is very effective in extracting all scatterers
Width of residuals (2-3 pixels FWHM) illustrates “daophot’s” good resolution
100
200
50
-50
Notes: Note for you, the central pixel does not count because it is just the black background that daophot ignores, but this is log scale, ignoring the central pixel you get 2-3 pixel FWHM

## Slide 9: Scatterer light intensity distribution @ Exposure Time = 0.0125 sec
70
40
5000
20000
The number of reconstructed scatterers grows rapidly at low amplitude.
Integrated count

## Slide 10: Number of Scatterers vs. Exposure Time
Number increases almost linearly with exposure
Exploring smaller scatterers
But also deeper in the dielectric coating layers ! !
Exposure Scatterers (1st Run)
@ 0.125 ms 76
@ 1 ms exposure 624
  @ 400 ms exposure 127,774
Scatterer count plateaus due to saturation.

## Slide 11: Apparent size: Depth in stack effect
There are two depth attenuation components:
Attenuation of impinging light due to reflections through depth of coating layers
Back-reflection on front layers attenuates Scattered light
Scattered light detected by CCD
Image: Stuart Reid, Iain Martin, 2016
Back reflected scattered light

## Slide 12: Rapid drop of laser light impedes: Measurement of size of scatterers Detection of scatterers below first 2-3 layers Need different exploration method

## Slide 13: Ongoing work
Two steps proposed:
Analyze more images from LIGO Hanford/Livingston to mitigate saturation.
Study spare ad-LIGO witness samples to determine scatterer’s depth distribution through layers and size distribution

## Slide 14: 1st feasibility study
  Idea:
Analyze more low exposure images from LIGO and add them up coherently to mitigate the saturation
  Problems:
Camera moves w.r.t. mirror, scatteters change pixel position
Beam moves w.r.t. mirror, scatterers change luminosity
  Byproduct:
Independent detection of motions of stored beam, camera and/or test mass.

## Slide 15
Initial Analysis of Scatterer Motion Tracking
The scatter of the points (standard deviation) =
~11µm
positioning error of “daophot”

## Slide 16
Initial Analysis of Scatterer Motion Tracking
The mean offset (-58 ±1.3µm in X 31 ±1.3µm in Y) is attributed to the relative motion of the camera and the test mass.
Calibration 1Pixel = ~80 µm

## Slide 17: Luminosity Shifts in Images
Divide an image into two halves with approximately equivalent luminosity
Compare the relative change in luminosity in a subsequent picture
Initial analysis with the only two images of similar time exposures (both approx. 1.3 millisecond)
SPLIT | INITIAL DIFFERENCE | FINAL DIFFERENCE | Luminosity Shift | Apparent Stored Beam Shift
Left compared to Right | Left – Right = -0.0070 | Left – Right = -0.0062 | -0.0008 | 0.02 mm
Bottom compared to Top | Bottom - Top = -0.0278 | Bottom - Top = -0.0550 | 0.0272 | 0.6 mm
VERY PRELIMINARY

## Slide 18: Next Steps
Analyze exposure-optimized images from LIGO Hanford or Livingston to:
Mitigate saturation
Extract Test Mass vs. Camera position
Extract Stored Beam vs. Test Mass position

## Slide 19: Depth scatterer exploration
Study a spare ad-LIGO witness samples to determine
the scatterer’s depth distribution through the layers
the size distribution

## Slide 20
1
3
2
50% Reflector
@ 45°
AdLIGO Multi-Layered Mirror
CCD Camera
Microscope
lens
White light LED
X, Y Axis micropositioning
Z Axis piezo focusing

## Slide 21
Grid scan of Mirror
X1
X2
…
Xn
Y1
Y2
Yn
…
Raster scan X-Y of microscope frames on mirror surface to identify rough scatterer position
Defocused
Scatterers

## Slide 22
No scatterer present:
  No reflected light
Scatterer present out of f-plane
  Low illumination density
  Defocused scatterer image
Z-zoom with piezo-movement to bring focal plane on scatterer:
  Brighter illumination
  Focused airy disk image
Method for Depth determination by Z-focussing
+Z
-Z
Defocused
Scatterer
Defocused
Scatterer
Focused
Scatterer
Maximum Brilliance

## Slide 23
  Depth of field 0.6 µm / n
  Sub-wavelength
  Z-position determination from Z-feedback fit
Potential depth resolution
+Z
-Z
Maximum Luminosity
Defocused
Scatterer
Defocused
Scatterer
Focused
Scatterer
Nikon lens calculator
http://www.microscopyu.com/tutorials/java/depthoffield/
Notes: For your information, n is the refraction index of the material, in Ta2O5 or TiO2 it is between 2.5 and 3

## Slide 24
Feasibility Study of Z sensitivity
Use a slightly tilted grating
At 100x magnification, monitor the line sharpness as a function of x position

## Slide 25
Z Axis Calibration – line widths
Areas with sharp lines are on the focal plane
Blurry areas are either above or below the focal plane
The sharpness is measured by the apparent width of the grating lines in the luminosity graph

## Slide 26
The plotted widths have a minimum at the focal plane
The parabolic fit parameter error gives the depth resolution of the focal plane.
A depth resolution of about 30 nm is observed.
Feasibility Study: Z AxisCalibration

## Slide 27: Potentiality
Depth of scatterers in the coating layers can be measured if sufficient contrast is available.
Scatterer “size” can be corrected for the depth attenuation effect
The large angle and wide light spectrum of the light used by the microscope may allow exploration of scatterer distribution deeper than the first 2-3 layers

## Slide 28: Next steps
Continue the feasibility study on a aLIGO witness sample mirror using a piezo actuator scanner in the microscope

## Slide 29: Conclusions 1
A very large population of scatterers was found on aLIGO mirrors under high-power illumination.
They contribute to large angle optical scattering,
if the observed points are the locus of mechanical dissipation, they may explain the anomalous mechanical dissipation observed in sputtered coatings.
The discovery is a good diagnostic tool, perhaps indicating possible ways to improve the Sensitivity limitation of Gravitational Wave detectors

## Slide 30: Conclusions 2
Methods are being developed to monitor
mirror to camera and
beam to mirror micro-movements
Both can be valuable diagnostic tools at the observatory