## Slide 1: SMEE Project Update
Vincent Roma
2016

## Slide 2
PSL Periscope Noise in O1

## Slide 3
Filter applied through convolution in the time domain.
Target data: y(k) with N samples
Witness data: x(k)
Our filter: f(l) with L + 1 coefficients
E represents the mean square error between target data and predicted data.
Create our filter by minimizing the mean square error. That means setting derivative with respect to each filter coefficient to zero.
Wiener Filter

## Slide 4
Derivative constraints lead to the Wiener-Hopf equation.
Rxx is auto-correlation matrix of witness data, x(k) where k = [0,..., L]
cyx is cross-correlation matrix between witness and target data.
Signals are real so the auto-correlation matrix is symmetric, resulting in a Toeplitz structured system of equations. Solution obtained with the Levinson-Durbin algorithm.
Output data, r(k), is predicted data subtracted from target data.

## Slide 5
Blue: Original, Red: Subtracted Data
Witness Channel:
H1:IMC-WFS_B_I_YAW_OUT_DQ
1 hour of data used to train filter

## Slide 6
300 – 400 Hz

## Slide 7
Injected 16 waveforms from the Murphy catalog (2009) and 128 waveforms from the Dimmelmeier catalog (2008)
Each waveform injected at 10 evenly spaced intervals over a 24 hour period to explore entire antenna pattern. 1440 total injections.
Two sets of PCs, Dimmelmeier and Murphy.
6 PCs for Dimmelmeier, 9 for Murphy
Injections

## Slide 8
Original Data
Data points: 1016
Avg Bdm = 2.7399e5
Correctly Identified: 1016 / 1016 (100%)
Incorrectly identified waveforms: 0 / 1016 (0%)
Undecided: 0 / 1016 (0%)
Filtered Data
Data points: 1063
Avg Bmd = 2.7481e5
Correctly Identified: 1063 / 1063 (100%)
Incorrectly Identified: 0 / 1063 (0%)
Undecided: 0 / 1063 (0%)
Dimmelmeier .2 kpc

## Slide 9
Original Data
Data points: 128
Avg Bdm = 1.4e4
Correctly Identified: 112 / 128 (88%)
Incorrectly identified waveforms: 15 / 128 (12%)
Undecided: 1 / 128 (<1%)
Filtered Data
Data points: 145
Avg Bmd = 1.3663e4
Correctly Idenified: 127 / 145 (88%)
Incorrectly Identified: 16 / 145 (11%)
Undecided: 2 / 145 (1%)
Murphy .2 kpc

## Slide 10
Original Data
Data points: 1090
Avg Bdm = 2.657e3
Correctly Identified: 1078 / 1090 (99%)
Incorrectly identified waveforms: 0 / 1016 (0%)
Undecided: 12 / 1090 (1%)
Filtered Data
Data points: 1153
Avg Bmd = 2.552e3
Correctly Identified: 1137 / 1153 (99%)
Incorrectly Identified: 0 / 1153 (0%)
Undecided: 16 / 1153 (1%)
Dimmelmeier 2 kpc

## Slide 11
Original Data
Data points: 145
Avg Bdm = 115
Correctly Identified: 68 / 145 (47%)
Incorrectly identified waveforms: 9 / 145 (6%)
Undecided: 68 / 128 (47%)
Filtered Data
Data points: 145
Avg Bmd = 119
Correctly Idenified: 69 / 145 (48%)
Incorrectly Identified: 11 / 145 (8%)
Undecided: 65 / 145 (45%)
Murphy 2 kpc

## Slide 12
Original Data
Data points: 1152
Avg Bdm = 96
Correctly Identified: 719 / 1152 (62%)
Incorrectly identified waveforms: 0 / 1052 (0%)
Undecided: 433 / 1152 (38%)
Filtered Data
Data points: 1153
Avg Bmd = 98
Correctly Identified: 719 / 1153 (62%)
Incorrectly Identified: 0 / 1153 (0%)
Undecided: 434 / 1153 (38%)
Dimmelmeier 10 kpc

## Slide 13
Original Data
Data points: 145
Avg Bdm = -1.5
Correctly Identified: 7 / 145 (5%)
Incorrectly identified waveforms: 16 / 145 (11%)
Undecided: 122 / 145 (84%)
Filtered Data
Data points: 145
Avg Bmd = -1.32
Correctly Idenified: 7 / 145 (5%)
Incorrectly Identified: 16 / 145 (11%)
Undecided: 122 / 145 (84%)
Murphy 10 kpc

## Slide 19
Fix recoloring issues
Study future detectors in depth
Try Multi-Coherence method
Examine other noise sources (LLO noise breathing, current LHO jitter, etc)
Add new non-catalog waveforms
Current/Next Steps